## Slide 1
Remote Controlled Submarine
Students
Osama Naji Abu-Omar
Hakam Marwan Risheh
Supervisor
Dr. Luai Malhis
An-Najah National University
Computer Engineering Department

## Slide 2: Overview
Project idea
Body design
Drivers and Wireless communication
The microcontroller
The remote
Non-stationary water mode
Demo
Conclusions and future work

## Slide 3: Project idea
Small remote controlled submarine
Mainly built as an entertaining project for mini games underwater
Can moves in three dimensions
Controlled via a wireless connection
Can Hold Position in non-stationary water

## Slide 4: Body Design
Initial submarine body:

## Slide 5
The new body shape:

## Slide 6
Considerations taken:
Size fits the components
Light enough for motors
Balanced in water (horizontal position)
Directional motors give enough torque
Protection from hitting the propellers

## Slide 7: Motor drivers
Free / stall motor current draw:
Motor rating | Free (no load) mA | Stall (stopped) mA
M1 (Forward) | 220 | 1300
M2 | 250 | 1500
M3 (Up/ Down) | 750 | 1700
M4 (Left/ Right) | 50 | 500
M5 | 350 | 1200

## Slide 8: Choosing the Driver
The L298N dual h-bridge motor driver was chosen
Can supply up to 4 amps of current
Control in both directions
Speed control using PWM

## Slide 9: Wireless Control
Controller communicates via Bluetooth
fits the requirements of the project
  Short distance controlling
  Easy to implement (less time)
  BT module is available and relatively cheap
  Control using an application (any phone)

## Slide 10: The Microcontroller
Arduino Uno R3

## Slide 11: Block Diagram

## Slide 12: Command Messages
UI Command | event | String command | Notes
up arrow | Press | F,1,SPEED | Thrust speed
Up arrow | Release | F,0,SPEED | Thrust speed
Down arrow | Press | B,1,SPEED | Thrust speed
Down arrow | Release | B,0,SPEED | Thrust speed
Left arrow | Press | R,1 | No speed
Left arrow | Release | R,0 | No speed
Right arrow | Press | L,1 | No speed
Right arrow | Release | L,0 | No speed
D | Press | D,1,DSPEED | Diving speed
D | Release | D,0,DSPEED | Diving speed
S | Press | S,1,DSPEED | Diving speed
S | Release | S,0,DSPEED | Diving speed
ON | Click – toggle 1 | O,1 | On/off
OFF | Click – toggle 2 | O,0 | On/off
H | Click – toggle 1 | H,1 | Hold or Auto
H | Click – toggle 2 | H,0 | Hold or Auto

## Slide 13: Controller Operation

## Slide 14: The Remote
We Build an Android application as a remote control for the submarine.

## Slide 15: The Remote

## Slide 16: Non-stationary water mode
Submarine gets HOLD POSITION command
Water streams push the body
Accelerations (forces) are detected
The submarine responds by pushing to the opposite direction of the water stream
Returns to it’s initial position

## Slide 17: Non-stationary water mode
We used an Accelerometer sensor
It detects Accelerations applied to the submarine
The ADXL335 3-axis accelerometer

## Slide 18: Enhancements
Custom body, better material
Custom remote control, radio frequency operation (more range)
Brushless Motors
Smaller components (smaller whole size)
Special water propellers

## Slide 19: Future work
Grabber arm (for other types of games)
Auto obstacle avoidance (protection from crashes)
Hooking up other sensors, an off line camera.
Think of others ?...

## Slide 20: Conclusion
Submarine operation in static water tested and worked as expected with acceptable results.
Accelerometer is barely accurate enough to detect water streams in water
in the final testing stage, water (moisture) leaked into the components and some damaged, due to poor isolation.

## Slide 21
Demo

## Slide 22
Thank you