## Slide 1
COMPU
SHADE
Nagham Hanani - Marah Dwikat

## Slide 2
PROMBLEM
Shade matching is an important aspect of restorative dental medicine
It relies on the doctors sikills and lightening
manual selection is prone to errors and mismatches

## Slide 3
MAIN IDEA
Automate shade selection and dispensing
Utilize image processing and mechanincs
Add material tracking features and remote control

## Slide 4
STAGES
Capturing the tooth and analyizing the shade
Releasing the disposable cup on the belt
Cutting and delivering
Tube selection and disposing
1
2
4
3

## Slide 5
STAGE 1
We custom made a cone and fixed lightening to eliminate errors
An image of the tooth is taken, then processed to get compared with VITA shade guide samples
The selected shade is sent as a serial signal to the Arduino to start the dispensing

## Slide 6
STAGE 1
We took pictures of the samples in the shade guide as reference to ensure standard environment and resolution

## Slide 7
STAGE 1
COMPONENTS
Raspberry Pi 4
Raspberry Cam V2

## Slide 8
STAGE 2
A disposable cup is dispensed on the belt upon starting
The belt moves the cup to be under the tubes to catch the material

## Slide 9
STAGE 2
COMPONENTS
Nema 17 motor
L298N Driver
Arduino Mega
Hall-effect sensor

## Slide 10
STAGE 3
The gear of the tubes moves a certain angle based on the shade selected
Then a filling is pushed out of the selected tube
After the cutting is done the gear moves back to home position to close the tubes again so the material wouldn’t dry

## Slide 11
STAGE 3
COMPONENTS

## Slide 12
STAGE 4
The material is cut by the wire and falls into the cup
the cup then moves to the end for the doctor to pick up
we notify them by printing a statement on the LCD and ringing a buzzer

## Slide 13
STAGE 4
COMPONENTS
LCD 16x2
Buzzer
cutting wire

## Slide 14
Empty cups detection
01
FEATURES
Empty Tubes detection
01
Remote control (App)
01

## Slide 15
EMPTY CUPS
The device can detect when there are no cups left
the doctor is notified using the LCD and the buzzer to refill them

## Slide 16
EMPTY TUBES
We counted the rotations of the tube needed to empty it, and stored it in the EEPROM of the Arduino
with each dispensing of the tube a counter is incremented
before running, we check the counter if its over the limit then the tube is empty and the doctor is asked to replace it

## Slide 17
APP
We built an app and connected it to the Arduino using HC-05 bluetooth module
the app allows the doctor to remotely run the device and get any shade they want

## Slide 18
APP
in case of an empty tube, after notifying the doctor to replace it, they’re asked to reset it using the app

## Slide 19
CONSTRAINTS
The nature of the composite material
Time
Cost

## Slide 20
THANK YOU !