## Slide 1
An-Najah National University
Faculty of Engineering and Information Technology
Building Engineering Department
Graduation Project (II)
Nablus Municipality
Prepared by:
Manar Shorbaji
Amneh Badawie
Ola Taha
Supervisor Name:
Eng. Nermeen Albarq

## Slide 2: Content :
Introduction
Site Analysis
Architectural Aspect
Environmental Aspect
Structural Aspect
Mechanical work
Electrical work
Quantity & Estimate Serving
1

## Slide 3: Introduction
In this project, an integrated municipality design was created that keeps pace with the development of the times and meets basic needs.
New integrated design is introduced taking all strengths into consideration and demolishing all weaknesses.
2

## Slide 4: Site Analysis
The land on which the municipality will be built is located on Haifa Street, located in the Rafidia district in Nablus.
3
Areas and slope
Area of land which municipality is built on equals to (3380) m² with slope less than 6 % approximately.

## Slide 5: Site Analysis
5

## Slide 6: Architectural Aspect
General Information
Floors , Elevations and Sections
7

## Slide 7: General Information
The Nablus Municipality includes Five story.
Total area equals to 6770 m2.
8

## Slide 8: Architectural Aspect
Area 6670. m2
Floor Height 4 m
9

## Slide 9: Architectural Aspect
10

## Slide 10: Architectural Aspect
14

## Slide 11: Architectural Aspect
20

## Slide 12
20

## Slide 13: Architectural Aspect
23

## Slide 14: Environmental Aspects As any aspect , environmental design is very important and it should be taken into consideration
Solar radiation
Daylight factor (DF)
Sun path diagram
Shadow
DesignBuilder
Acoustics
48

## Slide 15
Western elevation solar radiation (after)
54
Eastern elevation solar radiation(after)
North elevation solar radiation (after)
South elevation (after )
Solar radiation

## Slide 16: Daylight factor (DF)
Ground floor
59
Sun path
Sun path diagram in winter from 8:00 am to 4:00 pm
Sun path diagram in summer from 8:00 am to 4:00 pm

## Slide 17: Shadow
shadow at 8:00 am
Shadow at 12:00 pm
Shadow at 3:00 pm
61

## Slide 18: DesignBuilder
we will analyze the municipality building from a thermal point of view, and add insulators in the ceilings, floors, roofs, partitions, external and internal walls. To become an isolated Palestinian building.

## Slide 21: Heating design:

## Slide 22
Cooling design:
The Cooling Load consists of the envelop transmission (U-value), solar gain, internal gains including (humans, lighting and equipment).
We put vertical louver in east and west elevation:

## Slide 23
Cooling design:

## Slide 24
Simulation
The simulation analysis It is a simulation of reality. It takes the whole building in all its details
These sum result according to Air temperature:

## Slide 25: U-value of wall equal = 0.369 which is good less than recommended value 0.5
Energy per conditioned area =122 less than base line =150 KWh/m2 (standard for office building) so the building is energy efficient

## Slide 26
HVAC design
The system used here is VAV (variable air volume) HVAC system.

## Slide 29
Acoustic analysis

## Slide 30: Sound pressure level:
The intensity level can be expressed as the sound pressure level (SPL):
Effect of distance on sound level :
Sound level decreases when moving away from a sound source.

## Slide 31
Engineering office:
Engineering office plan
Noise in room
Room RT60
Direct SPL

## Slide 32
ALC
STI Eng. room
Total SPL

## Slide 33
INSUL

## Slide 34
STC value
Total STC

## Slide 35: Internal wall
Partition Sound Transmission Class (STC) standard

## Slide 36: Ceiling

## Slide 37: Structural Aspect

## Slide 38
Structural Aspects
This chapter explains the structural design of the building.
At the beginning, the building was divided into two blocks
as shown in the figure, and then by using ETABS program,
each block was modelled and analysed, also the preliminary
design of the structural elements such as columns, walls,
beams and slabs was determined and checks.
Two-way ribbed slab with drop beams,
Slab thickness (h)=400 mm ribbed slab pattern
Beam 1: 800 mm in depth and 800 mm in width
Beam 2: 400 mm in depth and 800 mm in width 700 x 400 mm cross sectional for column
Thickness of shear wall 1 = 200 mm
Thickness of shear wall 2 (basement wall) = 300 mm
Thickness of shear wall 3 = 400 mm
Preliminary design

## Slide 39
Basement
Ground
First
Second
Column design

## Slide 40
Modeling and analysis
By using ETABS we need to modeling and analysis first & second block check
Compatibility check

## Slide 41
Equilibrium check
Load pattern |  | Load (KN) |  | Error %
 |  | Manual | ETABS | 
Live |  | 15419.5 | 15419.8 | 0.002
SID | on slab | 16961.45 | 28624.75 | 0.029
 | walls | 11655 |  | 
 | Total SID | 28616.45 |  | 
Dead | Columns | 1680 | 34943.92 | 2.825
 | Beams | 12848 |  | 
 | Slab | 17855.78 |  | 
 | Walls | 3576 |  | 
 | Total Dead | 35959.78 |  | 
Load pattern |  | load |  | Error %
 |  | Manual | ETABS | 
Live |  | 14035 | 14039.42 | 0.031
SID | on slab | 15438.5 | 27816.06 | 0.031
 | walls | 12369 |  | 
 | Total SID | 27807.5 |  | 
Dead | Columns | 2492 | 38709.8 | 2.87
 | Beams | 12384 |  | 
 | Slab | 16252.53 |  | 
 | Walls | 8724.8 |  | 
 | Total Dead | 39853.33 |  | 
Equilibrium check model for first block
Equilibrium check model for secondary block

## Slide 42
Structural Models
Internal forces check :
column | Axial load (KN) |  |  | Error%
C1 | Manual- load due to |  | ETABS | 
 | beams | 1155 | 3358 | 1.82
 | slab | 2152 |  | 
 | Self- weight | 112 |  | 
 | Total | 3419 |  | 
C2 | beams | 682 | 4910 | 2.08
 | slab | 4217.92 |  | 
 | Self- weight | 112 |  | 
 | Total | 5011.92 |  | 
Beam | manual |  |  | ETABS | Error %
B1 | moment (KN.m) | M(-) | 96.04 | 121 | 20.63
 |  | M(+) | 104.00 | 95 | 8.65
 |  | M(-) | 185.41 | 136.7 | 26.27
 | shear (KN) |  | 201.5 | 175.14 | 13.08
B2 | moment (KN.m) | M(-) | 684.03 | 560.7 | 18.03
 |  | M(+) | 368.32 | 542.13 | 32.06
 |  | M(-) | 684.03 | 885.64 | 22.76
 | shear (KN) |  | 569.91 | 532.44 | 6.57
internal force checked for columns
Internal force check for beams in block 1
Internal forces in first block
Span | manual |  |  | ETABS | Error %
S1 | M22 (KN.m) | M(-) | 13.54 | 12.06 | 10.93
 |  | M(+) | 48.24 | 45.7 | 5.26
 |  | M(-) | 59.24 | 55.6 | 6.14
 | M11 (KN.m) | M(-) | 24.13 | 22.6 | 6.33
 |  | M(+) | 25.98 | 30.07 | 15.73
 |  | M(-) | 28.95 | 26.32 | 9.10
Explains internal force for slab in block 1

## Slide 43
Structural Models
ETABS Checks
Deflection check for block 1: Live load deflection:
Limit = (11.30*1000)/360 = 31.40 mm Displacement from (D+L) load which equals 29.03 mm shows in Figure
Δlive = ΔD+L - ΔD
= 29.03 – 11.90
= 17.13 mm
17.13 < 31.40 ok
45.87 < 47.10
Thus, long-term deflection was acceptable

## Slide 44
Seismic Checks
Load combination
Seismic effect on Block 1
Seismic effect on Block 2

## Slide 45
Mass participation check:
Sum x =96% and Sum y =94%, and both are more than 90%.
Sum x =91% and Sum y =98%, and both are more than 90%. (Block 2)
Drift check
Drift check for Block 1
Drift check for Block 2

## Slide 46
Base shear check
Manual and ETABs calculation for (V)s Value on block 1
Check Period:
Values of time Period in Block 1
T method (A) =
T from Etabs = 0.57s
1.4*0.426 = 0.59 > T from ETABs = 0.57 → Check is OK
Manual and ETABs calculation for (V)s Value on block 2
T method (A) =
T from Etabs = 0.502s
1.4*0.426 = 0.59 > T from ETABs = 0.5 → Check is OK
Values of time period in Block 2

## Slide 47
Design element
Design of column
The reinforcement of columns in block 1

## Slide 48
Design of beam
Check for doubly reinforcement for the beams in block 1
beam to calculate the shear in block 1
Distributions of the Beams

## Slide 49
Design of slab

## Slide 50
Design shear wall
Stair shear wall
shear wall in block 1

## Slide 51
Design of footing
Isolated footing
detailing of columns and footing in Block 2
detailing of columns and footing in Block 1

## Slide 52
Design of Retaining wall
The project involves a basement floor, which results in various levels in the property, necessitating the construction of a retaining wall.

## Slide 53
Stair design:
The loads will use to design the stair:
Live load = 5 KN/m2 ,,,, SID load = 5.5 KN/m2
Dead load = 0.2 * 25 = 5 KN/m2 (assume the slab thickness = 20 cm).
Ultimate loads on stair equal (1.2D + 1.6L) = (1.2 × (5.5+ 5)) + (1.6 ×5) = 20.6 KN/m2

## Slide 54
Water tank
Detailing of water tank

## Slide 55
Electro-Mechanical Aspect
1- Mechanical work
Water supply system
Drainage system
Fire system
2- Electrical work
Power design
Low voltage design
Photovoltaic system design
PV Sys
RET screen
Earthling system
Main circuit breakers
Elevator
Lighting design (DILUX)

## Slide 56: Mechanical work
Water supply
This building contains hot & cold water. The cold water comes from tanks situated on the rooftop, and heated water comes from boilers. In this building water put away in-ground tank water.
Consumption | fresh water | Flushing water | Raining water
Daily | 21.09 | 2.96 | (-)
Yearly | 4850.7 | 680.8 | 926.27
annual consumption water in building CM
weight of fixture units

## Slide 57
Water Supply System
Use two tanks of (10*7*5m), So two tanks for flushing = 700 m3
Fresh water tank = (6*5*4m) = 120 m3
Pipe selection |  |  |  | 
Type | water |  | Gray water | 
 | diameter(inch) | Losses (psi) | diameter(inch) | Losses (psi)
Vertical | 2.5 | 7.67 | 2 | 16.51
Horizontal 1 | 2.5 | 0.39 | 1.5 | 1.57
Horizontal 2 | 2.5 | 0.15 | 1 | 0.94
Horizontal 3 | 2 | 0.24 | 1 | 6.24
Horizontal 4 | 2 | 0.22 | 1 | 1.6
Branch | 1 | 0.701 | 0.75 | 2.19
Total |  | 9.371 |  | 29.05
Pipe selection
Types of pipes:
Stainless Steel for Vertical pipes
PVC for horizontal and branch pipes

## Slide 58
Water supply plan by AutoCad

## Slide 59
Drainage system
Water Drainage System
Three types of drainage water systems:
Black water
We use 4 inch stakes with slope 1% for all WC's.
Grey water
We use 2 inch with slope 2% for lavatories.
Rain water
We use 4 inch with slope 1%
We use 6 inch with slope 1% between manholes.

## Slide 60
Drainage plan

## Slide 61
Firefighting system
Designing the building to protect against fire has become an important necessity for the engineer
Firefighting system
Introduction
Facilities Classification
In your building the category is category C
Fire detecting and alarm system
-Smoke detector
- Heat detector
Requirements for prevention and self-protection (Jordanian code)
Emergency fire escape (Jordanian code)

## Slide 62
Firefighting system
Design of fire system:
Hazard classification | High hazard | Medium hazard | Low hazard
coverage area(m2 ) | 9 | 12 | 18-20
Maximum distance(m) | 3.6 | 3.9 | 4.6
Sprinkler
Sprinkler to sprinkler maximum distance = 4.6 m by NFPA 13 CODE (National Fire Protection Association)
Fire detector alarm
Heat detector symbol
Smoke detector symbol

## Slide 63
Fire fighting
Hose station
FM200 classes

## Slide 64
Basement
Ground
Sprinkler plan
First
Second

## Slide 65
Fire system distribution
SD
Basement fire system
First floor fire system

## Slide 66
Electrical work
1- PV sys
Calculated the number of panel that we have distribution direction by landscape design and got 270 panels, height of module = 1.5 m to ignore shadow and to allow passage man maintenance.
The capacity of system = 270*400 Wp = 108000 Wp = 108 KWp.
Active Area = 270 x (2.031x 1.011) = 554.5 m2

## Slide 67
1- PV sys
Pvsys program simulation result
Energy Cost
NIS/KWh = 0.7
Convert NIS/KWh to $/KWh = 0.7/3.5 =0.2 $
So 1 MWh = 200$
Energy cost =51774 $/year from RET screen Program
PV system Cost:
Power system consist of:
1) Cost of modules
=No. of module x watt x price/watt
=270 x 400 x 0.1$/watt= 10800 $
Custom fees: assume an interest of 1.3 to delivered to Palestine so &
The cost of modules = 1.3 x 10800 = 14040 $
2) cost of inverter
Inverter cost=Price x # of inverter
= 1140 $ x 30 = 34200 $

## Slide 68
Earthling system
The earthing system for buildings is not designed in the Nablus Municipality building because it is provided by the Electricity Company.
In municipality Nablus building we can use TN-S earthling system

## Slide 69: Low voltage drop

## Slide 70
Power design
DF: diversity factor for lighting = 0.90
DF: for socket =0.30.
SF: safety factor = 1.20.
220: electrical voltage for 1 phase.
380: electrical voltage for 3 phase.
current load
In this building, the electrical design is intended to provide adequate power for all sockets and luminaires, and every system requires electricity, so these are the results obtained after performing all calculations and applying the equation of electric.in this section we provide the power design, Electrical sockets, circuit breaker boards and earthling system.
HVAV system need 240.62 kW.
Elevator calculation
Power of elevator = mass in kg x acceleration x (h final – h initial)/ speed (m/sec)
Power of one elevator = [(1200 x 9.81 x (20.3 – 0)] / 2 = 119486 watt
Total power for ground floor = 23185.7 W
Total power for first floor = 21806 W
Total power for second floor = 26304.3 W
Total power for third floor = 19809 W
Calculation power design

## Slide 71
Power design
Ground floor

## Slide 72
Main circuit breaker for building
Main Circuit Breaker |  |  |  |  |  |  |  | 
Floor | Circuit board name | Total Power (W) | Iload (A) | I C.B (A) | I cable (A) | Circuit Breaker (A) | Cable Cross- secton area | Phase
Master | DB.0 | 23185.7 | 94.85 | 109.08 | 125.44 | 125 | 50 mm^2 | 3 Phase
First | DB.1 | 21806 | 89.21 | 102.59 | 117.98 | 125 | 50 mm^2 | 3 Phase
Second | DB.2 | 26304.3 | 107.61 | 123.75 | 142.31 | 125 | 50 mm^2 | 3 Phase
Basement | DB.3 | 3300 | 13.50 | 15.53 | 17.85 | 15 | 4 mm^2 | 1 Phase
Third | DB.4 | 19809 | 81.04 | 93.19 | 107.17 | 125 | 50 mm^2 | 3 Phase
HVAC | M.C.B | 240620 | 290.00 | 333.50 | 383.53 | 400 | 240 mm^2 | 3 Phase
Elevator | M.C.B | 35316 | 144.47 | 166.15 | 191.07 | 66 | 25 mm^2 | 3 Phase
M.C,B |  | 370341 | 506.41 | 582.37 | 669.72 | 723 | 550 mm^2 | 3 Phase

## Slide 73
options | 2500/350 | 2500/400 | 3000/350 | 3000/400 | 3500/350 | 3500/400
p | 13 | 13 | 16 | 16 | 19 | 19
RT | 90 | 83 | 106 | 99 | 109 | 105
Hc=(300 x p)/RT | 46 | 43 | 45.28302 | 48.48485 | 52.29358 | 54.28571
N | 2.354343 | 2.5186 | 2.391625 | 2.233688 | 2.071 | 1.995
N* | 3 | 3 | 3 | 2 | 3 | 2
PHC | 20.79% | 14.49% | 20.35% | 10.90% | 17.63% | 24.06%
I | 22.5 | 27.66667 | 26.5 | 49.5 | 36.33333 | 35
Vertical transportation (Elevator)
So we need three elevators with car capacity 2500 Ib and speed 400 fpm needed.

## Slide 74
Lighting System
DIALux program was used to design lighting system in Municipality
Lighting System
Public hall
Isoline chart for the Perpendicular illuminance in public hall.

## Slide 75
Result for public hall
Type and specification of used luminaire in public hall
The result of simulation in public hall.

## Slide 76
Basement
Ground floor
First floor

## Slide 77: Quantity surveying & cost estimate
62
After calculating the quantities and costs of materials and workers for all works in the building, the total cost is equal (14043896.93 NIS)
Cost per m2 = 2204.693391 NIS/ m2

## Slide 78
END OF PRESENTATION