## Slide 1
Auto Parallel Parking Car

## Slide 3
We created a Car that can identify a parking space and parallel park by itself. The Car drives down a street searching for a parking space to its right using a distance sensor. When the car has identified a space, the car checks to see whether that space is large enough to park in

## Slide 4
If it determines that there is sufficient space, the car will begin parallel parking into that space. It uses information from sensors placed on front, right, and rear of the car to direct the car into the parking space. Once the car has parked, it will remain in that position until it is reset.

## Slide 5
Move Car
Detect Parking
Park Car
Sensor Data
Logical Structure

## Slide 6: Hardware
Car.
Motors of the Car.
Microcontroller.
H-bridge L298HN .
Distance Sensors .

## Slide 7
We used three infrared distance sensors to determine the distance between our car and nearby objects. We placed a sensor on the front, the right side, and the rear of the car. For the front and rear, we used 4-50cm sensors. For the right side, we used we used a 7-80cm sensor. We decided to use a sensor with a larger range for the side so that we could more easily detect a parking space.
Distance Sensors

## Slide 9
we measured the output of each sensor at various distance values, linearized the plot, curve fit the line, and implemented an analog to digital conversion so that we had reliable distance values.

## Slide 10
Chart: Digital Value
| 1024 | 430 | 240 | 170 | 120 | 100 | 85 | 70 | 60 | 50 | 40
Sensor 50 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50

## Slide 11
Chart: Digital Value
| 1024 | 430 | 240 | 170 | 120 | 100 | 85 | 70 | 60 | 50 | 40
Sensor 50 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50

## Slide 12
Chart: Digital Value
| 1024 | 610 | 410 | 300 | 230 | 200 | 160 | 140 | 125 | 120 | 110 | 100 | 90 | 80 | 70 | 60 | 50
Sensor 80 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80

## Slide 13: How we take the data from sensors ?
X=Digital value from sensor.
X0<X <X1.
(X0,Y0) ,(X1,Y1).
Interpolate function:
value = ((y0 - y1) * (X -x0))/(x1 -x0)
value = y0 – value // distance in cm.

## Slide 14: How to Park the CaR
Forward until Detect Park
Go back until bigginning of Gap
Go forward /stop
Turn wheel left
turn wheel right go back inside space
Turn left go back to side wall/ sensor
turn right close to rear wall
ReSet
Go Forward /sensor

## Slide 16: Thank You