## Slide 1
Under supervision of:
Dr.Ibrahim Arman.
Prepared by:
Rania Fawzi Daraghmeh.
Layth Ibrahim Obeid.
Du'a Mohammad Hotaree.
Spring 2022.
STRUCTURAL ANALYSIS AND DESIGN OF JERUSALEM TWIN TOWERS
GRADUATION PROJECT-2
AN-NAJAH NATIONAL UNIVERSITY
Faculty of Engineering
DEPARTMENT OF CIVIL ENGINEERING

## Slide 2
CONSTRAINS
The complexity of the project plans.
Modeling the structure was not easy.
Various and continuous changes of levels and structural elements of each story.
Different zones were taken in the computation of loads due to the multiple usages for each story.
Run time was consuming, it takes more than 3 hours.

## Slide 3
Project Outline
CHAPTER 1
Introduction.
CHAPTER 2
CHAPTER 3
CHAPTER 4
Preliminary Design.
Three Dimensional Modeling.
Structural Design.

## Slide 4
CHAPTER 1: INTRODUCTION.
OUTLINE
PROJECT PLANS AND SITE LOCATION
FLOORS HEIGHTS, AREAS AND USAGES
CODES AND STANDARDS
SOFTWARE PROGRAMS
MATERIALS
GEOTECHNICAL INVESTIGATIONS
LOADS
(GRAVITY AND LATERAL LOADS)
LOAD COMBINATIONS

## Slide 5
CH1:INTRODUCTION
+783m AMSL of the north.
Location: Jerusalem city –Palestine.
Elevation of the site.
+777m AMSL of the south.
SITE LOCATION

## Slide 6
CH1:INTRODUCTION
NORTHERN FACADE

## Slide 7
CH1:INTRODUCTION
FLOORS USAGE

## Slide 8
Floor NO. | Area of each tower | Total area | Height m
-3 | - | 2704.4 | 4.3
-2 | - | 2704.4 | 3
-1 | - | 2704.4 | 4.4
1 (Ground floor) | - | 2704.4 | 3.85
2 | - | 2349 | 3.15
3 | - | 2107.7 | 3.15
4 - 17 | 595.5 | 1191 | 3.15
18 | 595.5 | 1191 | 3.3
19, 20 | 595.5 | 1191 | 3.5
21 | 595.5 | 1191 | 2.95
22 (Roof) | 595.5 | 1191 | 2.5
Floor NO. |  |  | Height m
-3 | - | 2704.4 | 4.3
-2 | - | 2704.4 | 3
-1 | - | 2704.4 | 4.4
1 (Ground floor) | - | 2704.4 | 3.85
2 | - | 2349 | 3.15
3 | - | 2107.7 | 3.15
4 - 17 | 595.5 | 1191 | 3.15
18 | 595.5 | 1191 | 3.3
19, 20 | 595.5 | 1191 | 3.5
21 | 595.5 | 1191 | 2.95
22 (Roof) | 595.5 | 1191 | 2.5
CH1:INTRODUCTION
FLOORS AREAS AND HEIGHTS

## Slide 9
CH1:INTRODUCTION
PROJECT PLAN OF FLOOR - 02

## Slide 10
CH1:INTRODUCTION
SECTION VIEW

## Slide 11
CH1:INTRODUCTION
PROJECT PLAN OF FLOOR 04:

## Slide 12
ASCE 7-10
IBC 2018
ACI 318-14
ASTM 2016
CODES AND STANDARDS:
LOADS COMPUTATIONS
LOADS COMPUTATIONS
ANALYSIS AND DESIGN
MATERIALS SPECIFICATIONS
JORDANIAN CODE FOR LOADS – 2006
ONLY FOR SNOW LOAD
CH1:INTRODUCTION

## Slide 13
ETABS 2016
AUTOCAD 2019
MICROSOFT OFFICE 2020
  1
  2
  3
CH1:INTRODUCTION
SOFTWARE PROGRAMS:
ANALYSIS AND DESIGN THE MODEL
DRAWING PROGRAM.
PREPARING REPORTS & TABLES

## Slide 14
Structural element | Concrete Type | fcʹ (MPa)
Walls, columns and footings | B500 | 40
Beams, slabs and stairs | B400 | 32
Yield strength (Fy) | 420 MPa
Ultimate strength (fu) | 620 MPa
Steel grade | 60
Modulus of elasticity (Es) | 200 GPa
CONCRETE
A. STRUCTURAL ELEMENTS MATERIALS:
REINFORCEMENT STEEL
CH1:INTRODUCTION
MATERIALS

## Slide 15
Material | Unit weight γ (Kn/m^3)
Masonry stone | 26.5
Cement Mortar & Plaster | 23
Partition blocks | 15
Filling material aggregate | 18
Glass | 25
Aluminum | 26
Porcelain tiles | 24
Marble tiles | 27
B. NON-STRUCTURAL ELEMENTS MATERIALS:
CH1:INTRODUCTION
MATERIALS

## Slide 16
CH1:INTRODUCTION
SOIL INVESTIGATION
The characterization of soil is Marl soil with equal levels of strength and density of limestone.
The soil is reported to be "TYPE C" .
The foundation of the tower will be made using mat foundation.
The bearing capacity equals 500KN/m .
2
K coefficient = 0.35 up to a depth of 3m ,and k=0.15 below that depth.
Surcharge load=20KN/m .
2

## Slide 17
CH1:INTRODUCTION
ASSUMPTIONS
Different elements will be represented as lines and areas in the program.
The structure is analyzed and designed for the critical load cases
The foundation of the tower will be mat foundation.
The supports to the model are fixed.
The wind and rains loads will not be the dominant load case as the seismic forces are larger.

## Slide 18
LOADS
CH1:INTRODUCTION

## Slide 19
Live Load (KN/) | Occupancy
5 | Lobbies
3 | Apartments
5 | Balconies
3 | Garage (Passenger vehicle only)
5 | Ramp
6 | Storage Rooms (light)
5 | Gardens
15 | Trash room
12 | Generator
5 | Roof
5 | Stairs
 | Occupancy
5 | Lobbies
3 | Apartments
5 | Balconies
3 | Garage (Passenger vehicle only)
5 | Ramp
6 | Storage Rooms (light)
5 | Gardens
15 | Trash room
12 | Generator
5 | Roof
5 | Stairs
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
1.Dead load: self weigh of the struture
2.Live loads: According to ASCE7-16 code.

## Slide 20
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
3.Super imposed loads on slabs:
S = 5.52 KN/m .
DL partition

## Slide 21
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
3.Super imposed loads on slabs:
S = 5.52 KN/m .
DL partition

## Slide 22
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
3. Super imposed dead loads on slabs.

## Slide 23
Material | Masonry stone | Aluminum | Glass | Block | Plain concrete
Unit weight (KN/m3) | 26.5 | 26 | 25 | 15 | 23
Thickness (cm) | 5 | 0.2 | 0.4 | 10 | 5
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
3. Super imposed dead loads on exterior walls.

## Slide 24
Structure Elevation AMSL (h) in meters | Site Snow Load (S_0) (KN/m2)
h < 250 m | 0
250 < h < 500 | (h-250)/800
500 < h < 1500 | (h-400)/320
A.GRAVITY LOADS:
CH1:INTRODUCTION
LOADS
4. Snow load:

## Slide 25
B. Temperature load:
CH1:INTRODUCTION
LOADS
Temperature load has been used rather than using of expansion joint.
Temperature load equals to 15 °C due to the average change of the temperature during the day.

## Slide 26
C. LATERAL load:
CH1:INTRODUCTION
LOADS
1.Earthquake load:
From maps:
Spectral response acceleration:
= 0.38g , = 0.1g.
Site coefficient:
=1.7, =1.2.
Spectral acceleration:
= × =0.456.
= × =0.17.

## Slide 27
C. LATERAL load:
CH1:INTRODUCTION
LOADS
1.Earthquake load:
The design spectral acceleration parameters:
=𝑆_𝑀𝑆=0.456.
= =0.17.

## Slide 28
C. LATERAL load:
CH1:INTRODUCTION
LOADS
1.Earthquake load:
Risk category (III). (ASCE 7-16).
Importance factor () = 1.25. (ASCE 7-16).
Seismic design category (SDC) → C. (ASCE 7-16).
Redundancy factor (ρ) = 1.0. (ASCE 7-16).

## Slide 29
C. LATERAL load:
CH1:INTRODUCTION
LOADS
1.Earthquake load:
Seismic forces resisting system:
Bearing wall system-ordinary reinforced concrete shear wall.
Response modification coefficient (R) = 4.
Over-strength factor () = 2.5.
Deflection amplification factor () = 4.

## Slide 30
C. LATERAL load:
CH1:INTRODUCTION
LOADS
1.Earthquake load:

## Slide 31
C. LATERAL load:
CH1:INTRODUCTION
LOADS
2. Soil load:
The soil report has specified the following points:
K = 0.35 up to depth 3m.
K = 0.15 below 3m.
Surcharge load = 20 KN/.
𝛾 = 20 KN/.
Soil lateral pressure: P = 𝛾 × 𝐻 ×
Soil seismic load: ∆𝑃 = 0.4 × × 𝛾 × 𝐻𝑏
= = 0.456.
= 2.5 = 0.182.

## Slide 32
C. LATERAL load:
CH1:INTRODUCTION
LOADS
2. Soil load:
=
+

## Slide 33
Load
Combination:
Service load combinations:
1. D + F + H + 0.75T.
2. D + L + F + H + 0.75T.
3. D + + F + H + 0.75T.
4. D + S + F + H + 0.75T.
5. 1.0 D + 0.7 + 0.7 + F + H + 0.75T.
6. 1.0 D + 0.525 + 0.525 + 0.75 L + F + H + 0.75T.
7. 0.6 D – 0.7 + 0.7 + 0.6F + 0.75T.

## Slide 34
Load
Combination:
Strength design combination.
1. 1.4 D + 1.4 F + 1.6H + T.
2. 1.2 D + 1.6 L + 0.5 +1.2 F + 1.6H + T.
3. 1.2 D + 1.6 L + 0.5 S +1.2 F + 1.6H + T.
4. 1.2 D + 1.6 + L + 1.2F + 1.6H + T.
5. 1.2 D + 1.6 S + L +1.2 F + 1.6H + T.
6. 1.2 D + + + L + 0.2S + 1.2F + 1.6H + T.
7. 0.9 D –+ + 0.9F + 1.6H + T.

## Slide 35
CHAPTER 2: Preliminary Design.
Slab structural system.
Preliminary slab thickness.
Preliminary dimensions of columns and walls.

## Slide 36
CH2:Preliminary Design.
Slab preliminary design:
Slab type is flat slab.

## Slide 37
CH2:Preliminary Design.
Floor -02:

## Slide 38
CH2:Preliminary Design.
Floor 04:

## Slide 39
CH2:Preliminary Design.
Slab preliminary design:
Floor | Level (m) | Preliminary slab depth (mm)
-2 | -7.40 | 350mm
 | -8.40 | 450mm
Under-ramp | -7.40 | 1000mm
-1 | -5.25 | 450mm
 | -4.40 | 350mm
01( GF) | -2.5 | 300mm
 | -1.4 | 300mm
 | 0.00 | 300mm
02 | +2.80 | 350mm
 | +3.70 | 350mm
03 | +5.85 | 350mm
 | +6.85 | 350mm
04 - 21 | +10.0 to +70 | 350mm

## Slide 40
CH2:Preliminary Design.
Walls and columns preliminary dimensions:
Structural element | Preliminary dimensions
Walls | Thickness = 300mm
Circular columns | R = 400mm
Square columns | 700*700

## Slide 41
CHAPTER 3: Three – Dimensional Analysis and Design.
Structural modeling of the building.
Verification of the structural analysis.
Deflection computations.
Slab shear check.
Structural irregularity.
Effect of P-delta.

## Slide 42
Structural Modeling.

## Slide 43
Section modifiers for flexure and torsion:
Slab modifiers = 0.25.
Beams modifiers = 0.35.
Wall modifiers = 0.7.
Columns modifiers = 0.7.
Ramp and stairs modifiers = 0.001.

## Slide 44
Load Definition:

## Slide 45
Load Definition:
Parameters of seismic forces in X and Y direction.
The values of SS, S1 and site class coefficient were changed in both directions until the values of SDS and SD1 reached the previously calculated values.

## Slide 46
Load Definition:
Functions:
Response Spectrum function was defined in ETABS software based on ASCE 7-10 code.

## Slide 47
Masses:
The total seismic load (w) includes: 100% from dead loads and superimposed dead loads, in addition to 25% from live loads.

## Slide 48
Pier and spandrel labeling:
Walls must be assigned to pier or spandrel label before obtaining either output forces or design.
Piers will report the forces and preform the design at the top and bottom of each object for each story.
Spandrel label on the other hand output the forces and the design ate the left and right ends of the object.

## Slide 49
Verification of structural analysis:
1.
Compatibility check:

## Slide 50
Verification of structural analysis:
2. Equilibrium check:
Load | Manual value (KN) | Etabs value (KN) | Difference %
Dead | 669,965.15 | 674,199.8542 | 0.63
Live | 128,650.78 | 128,695.9069 | 0.04
Snow | 1055.73 | 1039.2415 | 1.56
Super imposed (stone) | 37,041.20 | 37,122.901 | 0.22
Super imposed (slab) | 159,380.3 | 159,417.9765 | 0.02

## Slide 51
Verification of structural analysis:
1st -ve moment =-3.384KN.m. +ve moment= +2.64KN.m.
(-29.93,10.23,25.90) (-27.70,10.23,25.90)
3.
Stress – strain check

## Slide 52
Verification of structural analysis:
3.
Stress – strain check

## Slide 53
4.
Stress – strain check
Verification of structural analysis:

## Slide 54
4.
Deflection check:
Verification of structural analysis:

## Slide 55
Verification of structural analysis:
5.
Slab shear check:

## Slide 56
Verification of structural analysis:
6.
Punching shear check :

## Slide 57
Verification of structural analysis:
6.
Punching shear check :

## Slide 58
Upper portion :
Two staged – Analysis and Design:
1.
2.
Lower portion :

## Slide 59
Verification of structural analysis:
Principles of running the analysis:
A.
Mass participation ratio in each direction at least 90%.
This condition was fulfilled in the upper portion.
Note: In the lower portion the equivalent static method was implemented.
Case | Mode | Period | UX | UY | Sum UX | Sum UY
 |  | sec |  |  |  | 
Modal | 34 | 0.065 | 0 | 3.84E-06 | 0.9234 | 0.9118
B.
Scaling of forces:
If equivalent statict base shear value (V) is larger than response spectrum base shear value(Vt) , the forces shall be multiplied by
𝑉/𝑉𝑡 .

## Slide 60
Verification of structural analysis:
Principles of running the analysis:
C.
Period check for the lower portion:
D.

## Slide 61
Verification of structural analysis:
7.
Drift check:

## Slide 62
Verification of structural analysis:
8.
P – Delta effect:

## Slide 63
Verification of structural analysis:
9.
Horizontal structural irregularities:

## Slide 64
Verification of structural analysis:
10. Vertical structural irregularities:

## Slide 65
Verification of structural analysis:
Seismic force (Base Shear):
A.
Upper portion:
Weight of structure = 287692.6 KN.

## Slide 66
Verification of structural analysis:
Seismic force (Base Shear):
B.
Lower portion:
Weight of structure = 819906.1KN.

## Slide 67
Verification of structural analysis:
Seismic force (Base Shear):
A.
Base shear results for the upper portion:
Base shear | Manual (KN) | Etabs (KN) | % Difference
Vx | 14528.2 | 14528.031 | 0.001182
Vy | 23298.28 | 23294.463 | 0.016367
A.
Base shear results for the lower portion:
Base shear | Manual (KN) | Etabs (KN) | % Difference
Vx | 116153.641 | 111954.205 | 3.61
Vy | 116836.6228 | 112715.709 | 3.52
Notes: Base shear
Manual (KN)
Etabs (KN)
% Difference
Vx
14528.2
14528.031
0.001182
Vy
23298.28
23294.463
0.016367

## Slide 68
Verification of structural analysis:
Seismic force distribution for the upper portion X- direction:

## Slide 69
Structural Design.

## Slide 70
CHAPTER 4: Structural Design.
Design of slabs.
Design of columns.
Design of walls.
Design of footings.
Design of stairs.
Design of ramp.
Design of
non-structural elements.

## Slide 71
Design
of slabs:

## Slide 72
Design
of slabs:

## Slide 73
Design
of slabs:
Reinforcement in X-Direction of story 16 of the upper portion “left side”

## Slide 74
Design
of slabs:
Reinforcement in Y-Direction of story 16 of the upper portion “left side”

## Slide 75
Design
of slabs:
Reinforcement of punching shear in story -1:

## Slide 76
Design of Diaphragm:
Diaphragm:

## Slide 77
Design of Diaphragm:
Diaphragm:

## Slide 78
Design of Diaphragm:
Diaphragm:
Section cuts with 1 meter increments.

## Slide 79
Design of Diaphragm:
Diaphragm:

## Slide 80
Design of Diaphragm:
Diaphragm:
shear check:

## Slide 81
Design of Collector
Collector elements:
1. Shall be provided that are capable to transfer the seismic forces. 2. they are affected with tension and compression forces (F11 & F22).
Collector:

## Slide 82
Design of Collector
Points where maximum values of tension and compression
Collector:

## Slide 83
Design of Collector
Collector:

## Slide 84
Design of Collector
Collector:

## Slide 85
Design of Walls:

## Slide 86
Design of Walls:
Flexural verification:
Bressler’s Reciprocal load method shall be applied to verify the wall section for the biaxial moments.
CSI SAP 2000 was used to obtain the moment – axial interaction diagram (P-M-M).

## Slide 87
Design of Walls:
Chart: P-M3
| 0 | 8326.1782999999905 | 13671.731000000009 | 17529.902999999998 | 19994.238000000001 | 21252.953000000001 | 23395.945000000018 | 24703.796999999999 | 20211.778999999999 | 14299.538 | 0
 | 36034.4 | 36034.4 | 34194.9 | 29111.42 | 23859.34 | 18319.46 | 17025.24 | 15028.08 | 9866.3 | 4759.91 | -4939.1567

## Slide 88
Design of Walls:
Chart: P-M2
| 0 | 1428.2447 | 2409.8474000000001 | 3052.3577000000023 | 3359.7903000000001 | 3347.1235000000001 | 3622.8825000000002 | 3649.1843999999987 | 2675.6320000000001 | 1399.7909 | 0
 | 36034.4 | 36034.4 | 34036.5 | 28679.5 | 23115.29 | 17145.49 | 15033.26 | 11956.24 | 6052.81 | 210.4749 | -4939.1567

## Slide 89
Design of Walls:

## Slide 90
Design of Walls:
Flexural verification:

## Slide 91
Design of Walls:

## Slide 92
Design of Walls:

## Slide 93
Design of Spandrel:

## Slide 94
Design of Spandrel:

## Slide 95
Design of Spandrel:

## Slide 96
Design of Spandrel:

## Slide 97
Design of Spandrel:

## Slide 98
Design of Spandrel:
m

## Slide 99
Design of Spandrel:

## Slide 100
Design of Mat Foundation:

## Slide 101
Design of Mat Foundation:

## Slide 102
Design of Mat Foundation:

## Slide 103
Design of columns:
Column C15 in story3 was chosen to be verified and designed :
Length= 2.15m.
Diameter= 650mm.

## Slide 104
Design of columns:
Interaction diagram at 0 degrees.
Mu3 = -55.93 KN.m → ØPn3 = 6480 KN.
Chart: P-M
| 0 | 174.82410000000004 | 358.74059999999969 | 504.55529999999999 | 585.09119999999996 | 593.17950000000053 | 624.39009999999996 | 598.8288 | 400.90789999999993 | 158.60850000000002 | 0
 | 6480.0959 | 6480.0959 | 6480.0959 | 5382.8311 | 4133.3828 | 2782.276 | 2200.9896 | 1464.8203 | 374.2065 | -664.8469 | -1227.5387

## Slide 105
Design of columns:
Interaction diagram at 90 degrees.
Mu2 = -53.73 KN.m → ØPn2 = 6480 KN. (positive values are compression).

## Slide 106
Design of columns:
Column C15 in story3 was chosen to be verified and designed :

## Slide 107
Design of columns:
Column C15 in story3 was chosen to be verified and designed :

## Slide 108
Design of Stairs:

## Slide 109
Design of Stairs:

## Slide 110
Design of Stairs:

## Slide 111
Design of Stairs:

## Slide 112
Design of Stairs:

## Slide 113
Design of Ramps:

## Slide 114
Design of Ramps:

## Slide 115
Design of Ramps:

## Slide 116
Design of Ramps:

## Slide 117
Design of Ramps:

## Slide 118
Design of Ramps:

## Slide 119
Design of Ramps:

## Slide 120
Design of Ramps:

## Slide 121
Design of Ramps:

## Slide 122
CHAPTER 2
Design of non-Structural elements:تعدييييييييييل

## Slide 123
CHAPTER 2
Design of non-Structural elements:

## Slide 124
CHAPTER 2
Design of non-Structural elements:

## Slide 125
CHAPTER 2
Design of non-Structural elements:
Steel angle:

## Slide 126
CHAPTER 2
Design of non-Structural elements:تعدييييييييييل

## Slide 127
CHAPTER 2
Design of non-Structural elements:

## Slide 128
CHAPTER 2
Design of non-Structural elements:
Design of partition wall:

## Slide 129
CHAPTER 2
Design of non-Structural elements:
Design of partition wall:

## Slide 130
Thank you for listening..
Any questions?