## Slide 1
Integration of LCCA & Energy simulation for green building using eQUEST as energy modeling software and Royal Wings Hotel as a case study
Prepared by:
Danya Al-Madani
Hiba Mansour
Ruba Adnan
Supervisors:
Dr.Mohammad Al Sayed
Dr.Yahya Saleh

## Slide 2
Contents:
Introduction
Methodology
Data collection
Model Inputs
Results
Conclusion
Future works

## Slide 3
Introduction

## Slide 4
A great development took place in various fields in the last few years, which made electricity an indispensable need for the individual.
Introduction

## Slide 5
Introduction
Dramatically increased development and its increasing correlation with energy consumption have had unfortunate consequences:
Negative impacts on the environment have increased .
Depletion of non-renewable energy sources.
High expenses spent on generating needed energy.

## Slide 6
Factors that qualified Buildings to be the third sector next to the industry and transport sector :
population growth.
high requirement of services and comfort levels in the buildings.
rise in time spent inside buildings.
Energy consumption sectors
Transport
Buildings
Industry

## Slide 7
Green building definition
green building means buildings that achieve a balance between the biosphere and the occupants of the building, as the building is designed within the local climate in which it is held on to reduce the amount of water used in building construction, reducing energy in works, reducing materials consumed upon construction and after completion, encouraging recycling and contributing to the creation of high-efficiency, healthy and sustainable buildings that are affordable and environmentally friendly.

## Slide 8
Life-Cycle Cost Analysis (LCCA)
Life-cycle cost analysis (LCCA) is a method for assessing the total cost of facility ownership.
The study is conducted over a specific period of the building's life.
The picture becomes clearer and more comprehensive of the long-term cost (operating cost ).

## Slide 9
eQuest simulation software
eQUEST program is an energy modeling and simulation program that gives us finally the energy consumption rate and all detailed information on building energy consumption, it indicates the rate of effect each parameter on energy performance (electric and gas consumption during the life span of a building).

## Slide 10
Methodology

## Slide 12
Replacement of the Lighting system
Case One
Base Case
Combination of case one and two.
Case Three
External wall Insulation
Case Two
Energy conservation measures -Cases

## Slide 13
Data collection

## Slide 14
Data collection
Physical data
Cost data
Construction cost
Monthly bills
Maintenance cost
Inflation rate
Occupancy Data
Activity area
Hour of use
HVAC system
Name Here
Manager
Lighting system
Building
envelope
Water heating system
Walls type and insulation
Windows and doors type
Capacity, type &EER
Type& LPD
Capacity & type

## Slide 15
Model inputs

## Slide 16
External wall
U=0.401BTU/h.ft^2.F
Roof
construction
8 in. concrete
Doors construction
Steel Urethane foam
Windows type
Double clear
Aluminum frame
Light source
Fluorescent
Avg LPD =0.496 W/ft^2
HVAC
EER =8.2
Base Case
No insulation
External wall
U=0.401BTU/h.ft^2
Roof
construction
8 in. concrete
Doors construction
Steel Urethane foam
Windows type
Double clear
Aluminum frame
Light source
LED
Avg LPD =0.326
HVAC
EER =8.2
Case
One
No insulation
Inputs to eQUEST for all Cases

## Slide 17
External wall
Roof
construction
8 in. concrete
Doors construction
Steel Urethane foam
Windows type
Double clear
Aluminum frame
Light source
Fluorescent
Avg LPD =0.496
HVAC
EER =8.2
Case
Two
Polystyrene insulation
U=0.401BTU/h.ft^2
Roof
construction
8 in. concrete
Doors construction
Steel Urethane foam
Windows type
Double clear
Aluminum frame
Light source
LED
Avg LPD =0.326
HVAC
EER =8.2
Case
Three
No insulation
External wall
Polystyrene insulation

## Slide 18
Results

## Slide 19
Base Case
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 76.3 | 23.7
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 13.15 | 86.85
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.9 | 91.1
40%
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 1.65 | 98.35
Space cooling & Ventilation
Equipment
Pumps & heating
Lighting
1.4%
0.25%

## Slide 20
Verification and Validation
Simulation
Hotel
Actual bills
Hotel & Restaurants
Month | Actual (hotel& restaurants)
Jan | 22689.31
Feb | 27639.11
Mar | 29352.64
Apr | 29697.21
May | 37695.52
Jun | 26375.98
Jul | 41793.95
Aug | 40041.01
Sep | 36667.24
Oct | 32328.55
Nov | 26286.36
Dec | 40253.47
Month | Actual (hotel)
Jan | 8086.22
Feb | 7334.82
Mar | 10184.36
Apr | 14080.08
May | 18056.72
Jun | 22125.84
Jul | 26877
Aug | 27744
Sep | 23998.56
Oct | 19744.48
Nov | 10750.8
Dec | 8265.4

## Slide 21
Actual bills
Simulation bills
Chart: Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Actual Bills (including Restaurants) | 22689.31 | 27639.11 | 29352.64 | 29697.21 | 37695.52 | 26375.98 | 41793.95 | 40041.01 | 36667.24 | 32328.55 | 26286.36 | 40253.47
Simulation Bills for hotel only | 8086.22 | 7334.82 | 10184.36 | 14080.08 | 18056.72 | 22125.84 | 26877 | 27744 | 23998.56 | 19744.48 | 10750.8 | 8265.4
It was noticed that the actual electric bills were higher than the simulated bills because of the consumption of the restaurants, which had been increased at a constant rate during most of the year except the period between May and June
Error factors
Due to limitations in software and Palestinian weather data.
The software cannot predict occupants’ behavior
The deference of the exchange rate of the dollar during the year.

## Slide 22
Review
Fluorescent lamps
No insulation
Base Case
Case One
Case Two
Case Three
LED lamps
No insulation
Fluorescent lamps
Polystyrene insulation
LED lamps
Polystyrene insulation

## Slide 23
The total electric consumption saving was about 15470 kWh/year, which means that the annual bill dropped from 204762 NIS to 195480 NIS , about 4.5% saving.
Comparison between Base Case and Case one
 | Base Case (kWh *1000) | Case One (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 263.54 | -0.58%
Space heat | 0.87 | 0.88 | 1.1 %
Area lights | 30.35 | 16.40 | -46%
Total |  |  | -45.48%

## Slide 24
The total electric consumption saving was about 32130 kWh/year, which means that the annual bill dropped from 204762 NIS to 185383 NIS , about 9.4% saving.
Comparison between Base Case and Case Two
 | Base Case (kWh *1000) | Case Two (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 233.26 | -12%
Space heat | 0.87 | 0.55 | -36.8 %
Total |  |  | -48.8%

## Slide 25
The total electric consumption saving was about 47400 kWh/year, which means that the annual bill dropped from 204762 NIS to 176322 NIS , about 13.9% saving.
Comparison between Base Case and Case Three
 | Base Case (kWh *1000) | Case Three (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 231.56 | -12.6%
Space heat | 0.87 | 0.56 | -35.6%
Area lights | 30.35 | 16.76 | -44.8
Total |  |  | -93%

## Slide 26
Case One
325800 kWh/year
Base Case
341270 kWh/year
Case Two
309140 kWh/year
Case Three
293870 kWh/year
Simulation results
01
YOUR CONTENTS

## Slide 27
Conclusion

## Slide 28
Conclusion
eQuest software was used to simulate the energy performance of the Royal wings Hotel in Nablus, Palestine. Through the process of calibrating the baseline model, the validity of the software was discussed. A comparison was made between the actual electric bills and the software resulting bills. The results of the comparison approve that the software was accurate and could be reliable for energy simulation.
Different parameters influence the energy consumption in the hotel. The first parameter discussed this semester is the lighting system. The replacement of the fluorescent lamps with led lamps made an annual bill saving 8000 NIS, which equivalent to 3.2%.

## Slide 29
Future works

## Slide 30
Future works
Modeling and discuss case two and three
LCCA for all cases using different funding methods
Design a solar PV system to cover the bills and study the LCCA for this case

## Slide 31
THANK YOU