## Slide 1: Building a bridge in Nablus city
Prepared by : Monawwar Abdulrahman.
Noor Hussein.
Under supervision of : Dr.Mohammad Ghazal.

## Slide 2: contents
Introduction.
Site Description.
 Problem definition.
Site investigation.
Design of bridge foundations.
 Column footing design.
 Retaining wall footing design.

## Slide 3: Introduction

## Slide 4
The main task of our project is to design foundations for abridge instead of the roundabout at the intersection of of Haifa Road and Mohammad Bin Rashid Al-Maktoom Road at the western entrance of Nablus city.

## Slide 6: The intersection

## Slide 7: Areal View

## Slide 8: Problem definition

## Slide 9
High Traffic Load
Urbanization Expansion
Educational Hospital of NNU
The New Campus of NNU
High Traffic Loads from Tulkarm and Jenin Governorates
Congestion Problems
Increase in the Average Delay Per Vehicle
Limited Capacity
Accidents increase

## Slide 10
SITE INVESTIGATION

## Slide 11
Site investigation purposes
Site description
Laboratory tests results
Water table

## Slide 12: Site description
The site consists of layers of sedimentary brownish silty clay of high plasticity with pebbles and boulders of varying sizes. Wastewater open channel passes through the site its southern part.

## Slide 13: Laboratory tests results
BH No. | Sample No. | Depth M | Nature moisture % | Liquid limit % | Plastic limit % | Plasticity index | Angle of internal friction | Cohesion (from unconfined compression test ) Kg/cm2
1 | 1 | 0.0-5.0 | 14 |  |  |  |  | .85
 | 2 | 5.0-7.5 | 15 |  |  |  |  | .7
 | 3 | 7.5-13 | 23 |  |  |  |  | 
2 | 1 | 0.0-5.0 | 21 | 61 | 33 | 28 |  | .93
 | 2 | 5.0-9.0 | 7 |  |  |  |  | 
3 | 1 | 0.0-4.0 | 17 | 54 | 28 | 26 |  | 
 | 2 | 4.0-6.0 | 7 |  |  |  |  | 
 | 3 | 6.0-9.0 | 6 | 35 | 19 | 16 |  | 

## Slide 14
The recommended bearing capacity is 3.5 Kg/cm2.
Cohesion in average equal to 0.8.
Lateral earth pressure at rest (K0) =0.5.

## Slide 15: Water table
Ground water table was found at 5 m depth.

## Slide 16: Design of bridge foundations

## Slide 17
A bridge is a structure that spans horizontally between supports and provides passage over obstacles such as valleys, rough terrain or water…. Etc.
A foundation is the element which connects the structure (here: bridge) to the ground, and transfers its loads to the ground. Foundations are generally considered either shallow or deep.
The foundations of a bridge is particularly critical because they must carry the traffic loads and the weight of the bridge itself.

## Slide 18: Loads on the bridge
Loads
Dead
Live
Soil
Wearing
Breaking force

## Slide 19: 3-D model for the bridge on sap2000 program

## Slide 20: Definitions Of Material.
  fˋc=32 MPa
CONCRETE
  fy=420 MPa.
STEEL

## Slide 21
COLUMNS
80 cm Diameter
70 cm Thickness.
7.8 m Height.
RETAINING WALL
Design and dimensions

## Slide 22: Footing of the bridge
Columns Footing
Retaining Wall Footing
Bridge Footing
9 Ø 20/m.
Dimensions
13.3*5.8*1.5
15*8*0.6
Area of steel
7 Ø 20/m for toe.
6 Ø 20/m for heal.
6 Ø 12/m for stem.
6 Ø 16/m for shrinkage .

## Slide 23: Columns footing design
The footing of the columns is combined one.
The Dimensions and distances of the columns as shown.

## Slide 24
An excel sheet was made to check the ability of the suggested footing to carry the loads from the bridge by applying an equation to compare the stress comes from columns with the allowable bearing capacity .
The stress equation:
σ = ± ±

## Slide 25
Stress2 | Stress1 | M2 | M1 | Axial Force
-210.2 | -167.819 | -608.434 | 731.7037 | 13071.89
-207.259 | -170.76 | -608.434 | 1182.476 | 13071.89
-170.437 | -137.95 | -468.026 | 571.5184 | 10664.01
-168.288 | -140.098 | -468.026 | 900.9273 | 10664.01
-143.928 | -118.037 | -374.421 | 464.7282 | 9058.748
-142.307 | -119.658 | -374.421 | 713.2283 | 9058.748
-55.1672 | -13.8092 | -375.579 | -713.228 | 2385.205
-53.5462 | -15.4302 | -375.579 | -464.728 | 2385.205
-59.4854 | -7.66544 | -469.473 | -900.927 | 2322.077
-57.3367 | -9.81416 | -469.473 | -571.518 | 2322.077
-65.9628 | 1.55021 | -610.315 | -1182.48 | 2227.387
-63.0224 | -1.39016 | -610.315 | -731.704 | 2227.387
All values of stress on the suggested footing are lower than the allowable bearing capacity which is equal to 350 KN/m2. So it's ok.

## Slide 26
Columns Footing :
An area of (13.3m length×5.8m width) was suggested as shown below.

## Slide 27: 3-d model for columns footing

## Slide 28: Check Wide beam Shear
qu =207 KN/m2.
qall = 350 KN/m2.
Footing area = 77.14 m2 .
Let d =1.4m.
L1=2.5m.
.
Vu= qu(L1-d)= 227.7 KN.
.
ØVc =0.75 * ∗ 1∗ * b*d / 1000= 989.95 KN.
ØVc =0.75 * 𝟏/𝟔∗ 1∗ √𝐟ꞌ𝐜* b*d / 1000= 989.95 KN.
.
Vu= qu(L1-d)= 227.7 KN.
.
Vu < ΦVc …. OK

## Slide 29: Check Punishing Shear
.
Vup= Pu- qu A1=12285.29 KN.
.
ØVcp = 0.75 * ∗ 1∗ * 2π *( +r )*d= 13670.4 KN.
ØVcp = 0.75 * 𝟏/𝟑∗ 1∗ √𝐟ꞌ𝐜* 2π *( 𝒅/𝟐 +r )*d= 13670.4 KN.
.
Vup= Pu- qu A1=12285.29 KN.
.
Pu= 13071.89 KN.
A1= (r+ )2*π =3.8 m2 .
Thickness of the footing :
h=1.5m.
Vup < ΦVc p ….OK.

## Slide 30: Check of deflection
Max deflection in Footing = 9.82 mm < 10 mm …… OK

## Slide 31: Check Stress under Footing
..OK

## Slide 32: CHECK SHEAR FROM ULTIMATE LOAD
Section Cut at d
ϕ Vc =989.95 KN
Vu=5560.45/13.3=418 KN
Capacity of section ok

## Slide 33: REINFORCMENT STEEL OF COLUMNS FOOTING
Mu= qu=
ρ=8.8*10-4 .
ρmin =0.0018.
As= ρ b d =0.0018 *1000*1500 = 2700 mm2/m.
Use 9 Ø 20/m.

## Slide 34: DESIGN OF RETAINING WALL FOOTING
The retaining wall is chosen to be cantilever one, which consists of a relatively thin stem and a base slab. The base is also divided into two parts, the heel and toe. The heel is the part of the base under the backfill. The toe is the other part of the base. This type of retaining walls has many advantages such as:
Use much less concrete than gravity walls, but require more design and careful construction.
Generally, it's economical.
Can be precast in a factory or formed on site.

## Slide 35
- Back filling material unit weight of 20 KN/m².
- Friction angle = 0º.
- Live load = 12 KN/m².
- fc’ = 32 and fy = 420 Mpa.
- Concrete unit weight = 25 Mpa.
- h=8.4m.
The Preliminary Dimensions of the Retaining Wall is Shown in the Figure:

## Slide 36: Check of the overturning for the wall:
ka = 1−sin (Ø)/1+sin (Ø) = 1
q1 = Ɣ * h * ka = 168 KN/m².
q2 = W * ka =12 * 1 = 12 KN/m2 .
P1 = 0.5 * q1 * h = 705.6 KN .
P2 = 0.5 * q2 * h= 50.4 KN.
Pt = P1 + P2 = 756 KN.
M(ov.) = P1(8.4/3) + P2(8.4/2) = 2187.63 KN.m

## Slide 37
The following table shows the moment resistance calculation:
Weight Name | Unit weight | Weight | Force arm | Moment Ris.
W1 | 25 | 136.5 | 4 | 546
W2 | 25 | 120 | 4 | 480
W3 | 20 | 146 | 1.825 | 266.45
W4 | 20 | 569.4 | 6.175 | 3516.04
Total |  | 971.9 |  | 4808.495
F.S =
F.S = 2.198 > 2 …so it is Ok.

## Slide 38: Check of bearing capacity
a = = = 2.5 m .
M = (4 –2.5)*(971.9) = 1457.85 KN.
q1 = ± = -260.064 KN/m2 .
q2= -121.472 KN/m2 .
Stress less than 350 ….So its Ok.

## Slide 39: Check deflection of stem
Max deflection < 10 ...OK.

## Slide 40: Check shear for the stem
ØVc = 0.75 * 1/6 * λ * √𝑓𝑐′ * bw * d
= 0.75 * 1/6 * 1 * √32 * 1000 *630
= 445.5 KN.
All Vu values < ØVc
so it is ok

## Slide 41: Flexural design for the stem
Moment on the stem from ultimate loads:
Mu from SAP = 470 KN.m
ρ = 0.0032
As = 0.0032*1000*630 = 2020.4 mm2
Use 7 ø 20 /m.
Use shrinkage steel in other direction at each face
As = 2.
Use 6 ø 12 / m

## Slide 42: Check deflection for retaining wall footing.
Max deflection in Footing:
4 mm < 10 mm
SO its Ok.

## Slide 43: Check stress under footing
A tension stress appear on the heel ,so a tension equation was applied to check the stress values due to tension , The stress under footing was less than bearing capacity of soil so the footing is safe.
The tension equation :
σ = * Where e =

## Slide 44: Check shear for the heal and toe from the ultimate load.
ϕ Vc = 0.75*()*32) *1000*530 = 374 KN
(from manual calculation).
ALL value of shear less than 375 KN.
So its ok.

## Slide 45: Reinforcement steel in the toe
Mu= = 406 KN.m
ρ=0.004
As= ρ b d
=0.004*1000*5300
= 2087 mm2/m .
Use 7 Ø 20/m

## Slide 46: Reinforcement steel in heel
Mu= = 342.4
ρ=0.0033
As= ρ b d = 0.003*1000*530
= 1751 mm2/m
Use 6 Ø 20/m.
use in other direction of footing:
Shrinkage steel :
0.0018*1000*600= 1800 mm2
Use 6 ø16/m

## Slide 47: Thank you!