## Slide 1
Integration of LCCA & Energy simulation for green building using eQUEST as energy modeling software and Royal Wings Hotel as a case study
Prepared by:
Danya Al-Madani
Hiba Mansour
Ruba Adnan
Supervisors:
Dr.Mohammad Al Sayed
Dr.Yahya Saleh

## Slide 2
Agenda
01
Retrieve Project 1
02
Simulation Results
03
04
Sensitivity Analysis
05
Financial Analysis Results
Economical Inputs
06
Recommendations

## Slide 3
Retrieve Project 1

## Slide 4
Review
Fluorescent lamps
No insulation
Base Case
Case One
Case Two
Case Three
LED lamps
No insulation
Fluorescent lamps
Polystyrene insulation
LED lamps
Polystyrene insulation

## Slide 5
Simulation Results

## Slide 6
The total electric consumption saving was about 15470 kWh/year, which means that the annual bill dropped from 204762 NIS to 195480 NIS , about 4.5% saving.
Comparison between Base Case and Case one
 | Base Case (kWh *1000) | Case One (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 263.54 | -0.58%
Space heat | 0.87 | 0.88 | 1.1 %
Area lights | 30.35 | 16.40 | -46%
Total |  |  | -45.48%

## Slide 7
The total electric consumption saving was about 32130 kWh/year, which means that the annual bill dropped from 204762 NIS to 185383 NIS , about 9.4% saving.
Comparison between Base Case and Case Two
 | Base Case (kWh *1000) | Case Two (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 233.26 | -12%
Space heat | 0.87 | 0.55 | -36.8 %
Total |  |  | -48.8%

## Slide 8
The total electric consumption saving was about 47400 kWh/year, which means that the annual bill dropped from 204762 NIS to 176322 NIS , about 13.9% saving.
Comparison between Base Case and Case Three
 | Base Case (kWh *1000) | Case Three (kWh *1000) | % diff from Base Case
Space Cool | 265.07 | 231.56 | -12.6%
Space heat | 0.87 | 0.56 | -35.6%
Area lights | 30.35 | 16.76 | -44.8
Total |  |  | -93%

## Slide 9
Case One
325800 kWh/year
Base Case
341270 kWh/year
Case Two
309140 kWh/year
Case Three
293870 kWh/year
Simulation results
01
YOUR CONTENTS

## Slide 10
Economical Inputs

## Slide 11
Economical data
  Initial cost = 0
Estimated life =13000 hrs.
Case
One
Lamp replacement cost= 9 Nis/lamp
Operating hours =4015 hrs./year
# of lamps=741
Base Case
  Initial cost = 10395 Nis
Estimated life =50000 hrs.
Lamp replacement cost= 13 Nis/lamp
Operating hours =4015 hrs./year
# of lamps=741

## Slide 12
  Initial cost =20000
Case
Three
Case Two
  Initial cost = 30395 Nis
Estimated life =50000 hrs.
Lamp replacement cost= 13 Nis/lamp
Operating hours =4015 hrs./year
# of lamps=741
Electricity cost =0.6 Nis/kWh
Increase in Electricity cost =0.5%/year
MARR=10%
i=5%
Loan Payment =80%
Loan Period =3 years
Lifetime=25 years

## Slide 13
Financial Analysis Results

## Slide 14
01
Case1
03
Case3
02
Case2
Feasibility Analysis Results |  | Decision
Present value [Nis] | ₪62,603.14 | Feasible
Annual Worth [Nis/year] | ₪6,896.87 | Feasible
Simple payback Period [year] | 1.50 | 
Discounted Payback period [years] | 1.50 | 
Internal Rate of Return [%] | 71.8% | Feasible
Feasibility Analysis Results |  | Decision
Present value [Nis] | ₪162,618.41 | Feasible
Annual Worth [Nis/year] | ₪17,915.36 | Feasible
Simple payback Period [year] | 1.5 | 
Discounted Payback period [years] | 1.5 | 
Internal Rate of Return [%] | 97% | Feasible
Feasibility Analysis Results |  | Decision
Present value [Nis] | ₪234,827.07 | Feasible
Annual Worth [Nis/year] | ₪25,870.45 | Feasible
Simple payback Period [year] | 1.50 | 
Discounted Payback period [years] | 1.50 | 
Internal Rate of Return [%] | 91.5% | Feasible
LCCA for the 3 cases
01

## Slide 15
What if the project was funded with a loan?
The bank usually takes very high guarantees and is satisfied with a little interest rate, and while the investor pumps this loan In a project like this, and he is confident of his profits, he begins to pay back the loan payments from what has been saved as a result of the implementation of the project, and after repaying the entire loan to the bank, he begins to reap the net profit that will be gained from the savings.

## Slide 16
Comparison between cash &loan results
71.8% Case1
97% case 2
91.5% Case 3
6896.14 NIS Case 1
17915.36 NIS Case 2
25870.45 NIS Case 3
187% Case 1
340% Case 2
300% Case 3
6976.4 NIS Case 1
18068.37 NIS Case 2
26102.99 NIS Case 3
Cash Results
Loan Results
Chart: 
| Category 1
Series 1 | 71.8
Series 2 | 97
Series 3 | 91.5
IRR
AW
Chart: 
| Category 1
Series 1 | 6896.14
Series 2 | 17915.36
Series 3 | 25870.45
IRR
AW
Chart: 
| Category 1
Series 1 | 187
Series 2 | 340
Series 3 | 300
Chart: 
| Category 1
Series 1 | 6976.4
Series 2 | 18068.37
Series 3 | 26102.99

## Slide 17
Sensitivity Analysis

## Slide 18
Sensitivity Analysis
Chart: Operating hours
| 2500 | 3000 | 3500 | 4015 | 4500 | 5000
Case 1 | 34790.3142 | 44461.5337 | 56553.2802 | 62603.1447 | 79641.4538 | 86395.6649
Case 3 | 207014.2384 | 216685.458 | 228777.2044 | 234827.0689 | 251865.378 | 258619.5892
Chart: Electricity cost [Nis/kWh]
| 0.3 | 0.6 | 0.9
Case 1 | 33131.6364 | 62603.1447 | 92074.6529
Case 2 | 71309.2059 | 162618.4118 | 253927.6177
Case 3 | 109243.5985 | 234827.0689 | 360410.5394
The effect of operation hours on NPV (cash)
The effect of electricity cost on NPV (cash)

## Slide 19
Sensitivity Analysis
Interest rate
Chart: i
| 0.05 | 0.1 | 0.15
Case 1 | 63325.0288 | 62603.1447 | 61861.4915
Case 2 | 164007.3182 | 162618.4118 | 161191.4697
Case 3 | 236937.8594 | 234827.0689 | 232658.4737
Chart: i
| 0.05 | 0.1 | 0.15
Case 1 | 1.8734 | 1.7651 | 1.6576
Case 2 | 3.3992 | 3.2633 | 3.1244
Case 3 | 2.9972 | 2.8658 | 2.732
Interest rate VS NPV
Interest rate VS IRR

## Slide 20
Sensitivity Analysis
Loan period
Chart: Loan period
| 1 | 3 | 5
Case 1 | 62981.1447 | 63325.0288 | 63637.8529
Case 2 | 163345.6845 | 164007.3182 | 164609.1925
Case 3 | 235932.3417 | 236937.8594 | 237852.5578
Chart: Loan period
| 1 | 3 | 5
Case 1 | 1.1667 | 1.8734 | 2.3037
Case 2 | 2.038 | 3.3992 | 3.9262
Case 3 | 1.7937 | 2.9972 | 3.5087
Loan period VS NPV
Loan period VS IRR

## Slide 21
Sensitivity Analysis
Loan payments
Chart: Loan payment
| 0.2 | 0.5 | 0.8 | 0.9
Case 1 | 62783.6157 | 63054.3222 | 63325.0288 | 63415.2643
Case 2 | 162965.6384 | 163486.4783 | 164007.3182 | 164180.9315
Case 3 | 235354.7666 | 236146.313 | 236937.8594 | 237201.7083
Chart: Loan payment
| 0.2 | 0.5 | 0.8 | 0.9
Case 1 | 0.81118 | 1.0592 | 1.8734 | 3.0668
Case 2 | 1.1339 | 1.5973 | 3.3992 | 6.3981
Case 3 | 1.0574 | 1.4628 | 2.9972 | 5.5256
Loan payments VS NPV
Loan payments VS IRR

## Slide 22
Recommendations

## Slide 23
Limitations
The biggest challenge in the Life Cycle Cost Analysis study is that it takes place over a long period of the project’s life.
In order to be able to build the calculator on excel, we had to recalculate some of the given values in a ready-made way through the eQuest simulation program, which formed a slight difference in the final results.
.
Recommendations for the hotel owner
Adding occupancy sensors.
Decreases frequency of switching and restart for the lighting system.
Use a different types of doors.
Take into consideration the presence of insulators in designing the HVAC system.
Reduce the number of windows and repair any cracks .
Install PV system to cover the load.

## Slide 24
THANK YOU