## Slide 1: Smart lighting control
Done by :
Haya Salah
Esraa Nabulsi
Eman Dwikat
Under the supervision of:
Dr. Kamil Subhi

## Slide 2: Background

## Slide 3: Why A Smart lighting control?
Energy consumption is in a great increase all over the world so that required us to use engineering techniques to reach the optimum consumption of electricity by having the building automatically controlled (by using sensors, dimmable lighting units and controllers. ….. etc).

## Slide 4: Why A Smart lighting control?
Lighting of a room for its intended use at the exact lighting level can help sufficiently saving energy.

## Slide 5
Methodology

## Slide 6: What about our project?
We will control the dimming of the light load according to dimmer theory by using:
zero crossing circuit.
dimmer circuit .
light sensor circuit.
Microcontroller (arduino) .

## Slide 7: Theories and analyses
Project is built according to the dimmer theory based on power electronics as illustrated bellow.

## Slide 8: What does dimmer theory mean?
A dimmer is a device that is originally created to control the brightness of lamps.
This is done by altering the total power delivered to the lamp and thus the brightness.

## Slide 9: basic type of dimmer
The following schematic demonstrates a basic type of dimmer:

## Slide 10: Operation principles
The operation of the dimmer is based on the fact that, during a full cycle of an AC waveform, a triac will only allow a part of the waveform to be delivered to the load (lamp).
Take a look at the following waveforms:

## Slide 12: designing the Electrical circuits
This consists of the components and the operation of each circuit we built and these circuits are:
Zero cross detection circuits
Dimmer circuit
Light sensor circuit

## Slide 13: Zero cross detection circuit components
Transformer
Full-wave rectification
Optocoupler:
its a combination of two distinct Devices:

## Slide 14: Zero cross detection circuit components
light-emitting diode
Phototransistor
The two are Separated by a transparent barrier which blocks any electrical current between them

## Slide 15: Zero cross detection circuit operation
First, the sine wave goes through double phased rectification.
Then this wave will pass via an optocoupler which gives pulse at every zero crossing.
This pulse then can be used to trigger an interrupt in the Arduino.

## Slide 16: Zero cross detection circuits

## Slide 17: Dimmer circuit components
MOC3021: The MOC3021 is optically isolated triac driver devices.These devices contain an intrafid emitting diod and a light activated silicon bilateral switch,which fuctions like a triac.
components we used in this circuit are :

## Slide 18: Dimmer circuit components
Triac:The TRIAC is an ideal device to use for AC switching applications because it can control the current flow over both halves of an alternating cycle.So It is possible to view the operation of a TRIAC in terms of two thyristors placed back to back.

## Slide 19: Dimmer circuit operation
The output pulse of arduino goes through a MOC321 that opens and triggers the tiac.
Then the triac will open for a number of microseconds delay starting from the zero crossing therefore gives a predictable level of dimming.

## Slide 20: Dimmer circuit

## Slide 21: Light sensor circuit components
LDR( Light Dependent Resistor)
Transistor

## Slide 22: Light sensor circuit operation
A light detector senses light. As the light level increases and LDR meets the lowest threshold resistance, the circuit automatically turns on the LED D1. We can adjust the sensitivity using the resistor R2.

## Slide 23: Light sensor circuit operation
We connect this circuit to arduino by connecting the collector of transistor to the analogue Pin of arduino (A0).
LDR writes an analog value (PWM wave) to a pin, and so it can be used to light a LED at varying brightnesses.

## Slide 25: Hardware

## Slide 26: Hardware

## Slide 27: Microcontroller Arduino Uno

## Slide 28: Arduino Uno
When the AC voltage crosses the zero, the Microcontroller will be interrupted and therefore detects the zero crossing .
We can reach to the required voltage by triggering the triac after a specific Delay.

## Slide 29: If keypad value<sensor value
Interrupt service routine code contain delay to
Control the output pulse from arduino to control firing angle
Enter the required illumination from keypad and compare it with sensor value
If keypad value>sensor value
If keypad value=sensor value
Increase the lamp lightening
Decrease the lamp lightening
No change in lamp lightening

## Slide 30: Results

## Slide 31: The input of the optocoupler(the output of full wave rectifier)
We get this result because we used full wave rectifier that converts alternating current (AC), which periodically reverses direction, to direct current (DC), which flows in only one direction.

## Slide 32: the output of optocoupler/ input of the arduino.
When the rectified signal reaches zero the optocoupler give pulse.
This signal then can be used to trigger an interrupt in the Arduino(pin2).

## Slide 33: Synchronizing
Synchronizing between the output of the arduino (pin 13) and the output of optocoupler.
We control the output of the arduino by change the delay (in ms) after the zero crossing to give pulse.
Blue signal:output of optocoupler. Red signal: output of the arduino

## Slide 34: The output of the moc
At Dely =50 ms.

## Slide 35: 2. At delay 150ms

## Slide 36: 3. At delay 200ms

## Slide 37
We notice by changing the delay we control the firing angle (alpha).
When the α becomes smaller, then the dimmer becomes conductive sooner and the lamp is brighter.
When the α becomes larger, then the triac delays more to become conductive and thus the lamb is dimmer.

## Slide 38: The output of Triac
At delay 50ms

## Slide 39: 2. At delay 150ms

## Slide 40: 3. At delay 300ms

## Slide 41: 4. At delay 550ms

## Slide 42
We notice by changing the delay we control the firing angle (alpha).
When we increased the delay, alpha also increased so, the lightening decreased.
If we increase alpha beyond this value we see that the lamp turns off delay.

## Slide 43
Thank you