## Slide 1
An-Najah National University
Faculty Of Engineering
Civil Engineering Department
Foundation design for high rise building
Prepared by :
Faisal Mohammad Hassouna
Submitted to:
Dr. Sami Hijjawi

## Slide 2: Chapter One General Definition of the Project
The aim of this project is to design a foundation of a residential building (AL-khalel housing project) which consists of six Flores.
A sample unit of the housing project was designed.
The site has an area of 8950 m2 and the proposed building will have a plan of about 462 m2.

## Slide 3: Chapter Two Review Of Engineering Foundations
It’s function is to transfer the load of the structure to the soil on which it’s resting.

## Slide 4: Types of Foundation
There are two main types of foundations:
Shallow Foundations:
    Isolated (Spread) Foundations.
    Combined Foundation.
    Continuous(Wall) Foundation.
    Strip Foundation.
    Mat Foundation.
  Deep Foundations:
      Piles.

## Slide 5: Chapter 3:Summary of laboratory test results
Allowable bearing capacity = 2.5 Kg/cm2.
Cohesion= 8 Kg/cm2.
Angle of internal friction ф= 23o
Unconfined compressive strength of the rock located 8m under ground level= 27500 KN/m2 .

## Slide 6: Chapter four Structural calculations
The main objective of this chapter is to find the loads applied on columns using two methods which are:
Tributary area method and analysis using software called SAP2000 v14.

## Slide 8: Plan for unit building

## Slide 9
The loads on each column:
Wu (1.2D + 1.6 L ) Kn | Service load (Kn) | Column#
816 | 720 | 1
929.4 | 774.6 | 2
932.4 | 774 | 3
919.44 | 778.8 | 4
919.44 | 778.8 | 5
932.4 | 774 | 6
929.4 | 774.6 | 7
803.4 | 711 | 8
876 | 732 | 9
882 | 630 | 10
1134 | 810 | 11
1722 | 1230 | 12(shear wall)
1134 | 810 | 13
882 | 630 | 14
817.2 | 690 | 15
806.4 | 672 | 16

## Slide 10
Wu (1.2D + 1.6 L ) Kn | Service load (Kn) | Column#
823.2 | 588 | 17
789.6 | 564 | 18
1688.4 | 1314 | 19(shear wall)
1688.4 | 1314 | 20(shear wall)
789.6 | 564 | 21
1033.2 | 738 | 22
764.4 | 642 | 23
816 | 720 | 24
996 | 828 | 25
1014.6 | 843 | 26
1014.6 | 843 | 27
996 | 828 | 28
803.4 | 711 | 29

## Slide 11: Chapter five Design mat and piles foundation
Mat foundation:
To design Mat Foundations, the thickness of the mat has to be found from punching shear equation manually. Then, the maximum moment in (X) and (Y) directions, area of steel and settlement are found from SAP.

## Slide 12: Design mat foundation
To find the thickness of foundation, the punching shear equation is used.
фVc = 0.75 *(1/3) * bo * d > Vu
d= 60 cm
h= d+10 cm = 70cm

## Slide 13: Sketch for the Mat Foundation in the SAP2000

## Slide 14: Settlement
The maximum value is 1.35 cm and this value is acceptable.

## Slide 15: moment in (X) and (Y)directions
Moment in (x) direction M11.

## Slide 16
Moment in (y) direction M22.

## Slide 17
Summary Of Reinforcement in Y-Direction
Reinforcement in (Y)direction |  |  |  | 
Zone # | strip width(m) | Top steel / Bottom steel | length(m) | ф
1 | 1 | Top steel | 9.75 | 5ф18
 |  | Bottom steel | 9.75 | 5ф18
2 | 1.85 | Top steel | 9.75 | 9ф18
 |  | Bottom steel | 9.75 | 9ф18
3 | 1.5 | Top steel | 9.75 | 7ф18
 |  | Bottom steel | 9.75 | 7ф18
4 | 1.8 | Top steel | 9.75 | 9ф18
 |  | Bottom steel | 9.75 | 9ф18
5 | 1.5 | Top steel | 9.75 | 7ф18
 |  | Bottom steel | 9.75 | 7ф18
6 | 1.9 | Top steel | 9.75 | 9ф18
 |  | Bottom steel | 9.75 | 9ф18
7 | 4.6 | Top steel | 9.75 | 23ф18
 |  | Bottom steel | 9.75 | 27ф20

## Slide 18
Summary Of Reinforcement in X-Direction
Reinforcement in (x)direction |  |  |  | 
Zone # | strip width(m) | Top steel / Bottom steel | length(m) | ф
1 | 1 | Top steel | 3.6 | 5ф20
 |  |  | 16.5 | 5ф18
 |  |  | 3.6 | 5ф20
 |  | bottom steel | 23.7 | 5ф18
2 | 2.1 | Top steel | 23.7 | 11ф18
 |  | bottom steel | 23.7 | 11ф18
3 | 1.1 | Top steel | 23.7 | 6ф18
 |  | bottom steel | 23.7 | 6ф18
4 | 1.1 | Top steel | 23.7 | 6ф18
 |  | bottom steel | 23.7 | 6ф18
5 | 1.1 | Top steel | 23.7 | 6ф18
 |  | bottom steel | 9 | 6ф18
 |  |  | 5.8 | 7ф20
 |  |  | 9 | 6ф18
6 | 2.35 | Top steel | 23.7 | 12ф18
 |  | bottom steel | 9 | 12ф18
 |  |  | 5.8 | 14ф20
 |  |  | 9 | 12ф18
7 | 1 | Top steel | 23.7 | 5ф18
 |  | bottom steel | 23.7 | 5ф18

## Slide 19: Design pile foundation
Number of piles |  |  | Pile bearing capacity (Kn) |  |  | Load(kn) | Column#
50cm | 60cm | 80cm | 50cm | 60cm | 80cm |  | 
3 | 2 | 1 | 350 | 510 | 910 | 720 | 1
3 | 2 | 1 | 350 | 510 | 910 | 774.6 | 2
3 | 2 | 1 | 350 | 510 | 910 | 774 | 3
3 | 2 | 1 | 350 | 510 | 910 | 778.8 | 4
3 | 2 | 1 | 350 | 510 | 910 | 778.8 | 5
3 | 2 | 1 | 350 | 510 | 910 | 774 | 6
3 | 2 | 1 | 350 | 510 | 910 | 774.6 | 7
3 | 2 | 1 | 350 | 510 | 910 | 711 | 8
3 | 2 | 1 | 350 | 510 | 910 | 732 | 9
2 | 2 | 1 | 350 | 510 | 910 | 630 | 10
3 | 2 | 1 | 350 | 510 | 910 | 810 | 11
4 | 3 | 2 | 350 | 510 | 910 | 1230 | 12
3 | 2 | 1 | 350 | 510 | 910 | 810 | 13
2 | 2 | 1 | 350 | 510 | 910 | 630 | 14

## Slide 20: Design pile foundation
Number of piles |  |  | Pile bearing capacity (Kn) |  |  | load | Column#
50cm | 60cm | 80cm | 50cm | 60cm | 80cm |  | 
3 | 2 | 1 | 350 | 510 | 910 | 690 | 15
2 | 2 | 1 | 350 | 510 | 910 | 672 | 16
2 | 2 | 1 | 350 | 510 | 910 | 588 | 17
2 | 2 | 1 | 350 | 510 | 910 | 576 | 18
4 | 3 | 2 | 350 | 510 | 910 | 1314 | 19
4 | 3 | 2 | 350 | 510 | 910 | 1314 | 20
2 | 2 | 1 | 350 | 510 | 910 | 576 | 21
3 | 2 | 1 | 350 | 510 | 910 | 738 | 22
2 | 2 | 1 | 350 | 510 | 910 | 642 | 23
3 | 2 | 1 | 350 | 510 | 910 | 720 | 24
3 | 2 | 1 | 350 | 510 | 910 | 828 | 25
3 | 2 | 1 | 350 | 510 | 910 | 843 | 26
3 | 2 | 1 | 350 | 510 | 910 | 843 | 27
3 | 2 | 1 | 350 | 510 | 910 | 828 | 28
3 | 2 | 1 | 350 | 510 | 910 | 711 | 29

## Slide 21: Design pile
Design the Pile for axial
Pd = фλ*(0.85* 𝑓c*(Ag-As) + Fy*As)
As= 25.12 cm2
So USE 10ф18 mm
Design the Pile for Shear
USE spiral ф10 mm / 10 cm

## Slide 22: Design of Piles Cap
Dimensions 1.2 *1.2*0. 65 cm for all column
Design of One Pile Cap
Design for axial .
As =0.0018*b*d
Use 6ф16 mm in two directions.
Design cap for shear wall
Use 5ф16 mm/m in two directions

## Slide 23: Plan for piles foundation

## Slide 24: Cost of foundations
Cost of mat foundation :
Total cost =85000 NIS
Cost of pile foundation:
Total cost =101500 NIS

## Slide 25: Conclusion and Recommendations
After designing the two alternative choices (Piles and Mat) and surveying the quantities for steel and concrete and drilling. find that the cost of the Mat Foundation is less than the cost of the Pile Foundation.
So it is recommend that the mat Foundation is more useful and it is cheap with respect to the cost of the piles.

## Slide 26: THANKS FOR LISTENING