## Slide 1: 3d dynamic design of sky face hotel
Prepared by :Ahmad AL-Nuirat
Islam Zuhd
Supervisor: D.Abdul Razzaq Touqan

## Slide 2: Tips to be covered
Introduction
Preliminary Design And Checks
Static design
Dynamic checks and design

## Slide 3: Chapter 1 : Introduction

## Slide 4: Introduction :
Sky face hotel :
A four story, Nablus city.
story area = 2000 m2.
The first story is 5.5 m height (reception, wedding hall, security, offices, restaurant, prayers room and services).
The upper three stories are 4m height for each, contain 26 living unit, and 18 sweat.
The roof contains a swimming pool ,coffee shop.

## Slide 5: Introduction :

## Slide 6: Introduction :

## Slide 7: Introduction :

## Slide 8: Introduction :
    Site and geology:
    Hard lime stone, bearing capacity = 400kN/m2.
    Design codes:
    ACI -2008 (American Concrete Institute Code 2008 ).
    IBC 2006 (international building code 2006).

## Slide 9: Introduction :
    Materials :
    Structural materials: Non structural materials:
    columns and shear
    walls f’c = 30 MPa.
    beams and slabs f’c = 24 MPa.
    For footing f’c = 40 MPa.
    Steel yield strength fy = 420 MPa.
    weight per unit
    volume fo concrete = 25 kN/m3
    density =2.55 ton/m3

## Slide 10: Introduction :
    Structural system :
The structural systems
were used one
way solid slab and
two way with
drop beams in
both directions.

## Slide 11: Introduction :
    Loading:
    Vertical loads:
    Dead loads: it consists of weight of all permanent construction
    super imposed dead load = 5.4kN/m2
    Live load :from table 4-1 in ASCE/SEI 7-05 code. For this building, LL = 2 kN/m2 for slab1,2,3 , LL =4.8 kN/m2 for slab roof 4 , and LL=10 kN/m2 for slab roof 5.
    Lateral load from water pressure .

## Slide 12: Introduction :
Computer programs was used :
SAP2000 (v14.2.4) program.
    Loads combination:
    Wu= 1.4D.L
    Wu= 1.2D.L+ 1.6L.L
    Wu= 1.2D.L +1.0L.L ±1.0E
    Wu= 0.9D.L ±1.0E

## Slide 13: Chapter 2: Preliminary Design And Checks

## Slide 14: Preliminary Design And Checks
  Slabs
  Min thickness:
  Table 9.5(a) in ACI-Code318-11:
  The most critical span is 5 m length
  For one end cont. span: hmin = Ln /24
  For both end cont. span: hmin = Ln /28
  210 mm thickness for slabs1,2,3,roof4 , and 250mm for slab roof5

## Slide 15: Preliminary Design And Checks
Check slab for shear:
Own weight of slab1,2,3,roof4 =5.25 KN/m².
Own weight of slabroof5 =6.25 KN/m².
Wu for slab 1,2,3 = 15.98 KN/m²
Wu slab roof 4 = 20.46 KN/m².
Wu slab roof 5 = 29.98 KN/m².
slabroof4 Vu =50.85 KN. ΦvC =97.98 KN
slabroof5 Vu =73.3 KN. ΦvC =122.47 KN
Vu< ØVc____________ OK.

## Slide 16: Preliminary Design And Checks
beams depths:
From table 9.5(a) in ACI-Code318-11:

## Slide 18: Preliminary Design And Checks
Columns dimensions:
column( k17) :
The ultimate load = 6136.59 KN
Pu =Øδ (0.85*f’c*Ac + fy*As)
reinforcement ratio ρ = 0.01.
Ag = 400822.52
Root foot Ag = 633.11 mm
Use column dimensions of 800x800.

## Slide 20: Preliminary Design And Checks
  Checks and SAP model Verification:
  Compatibility:
  The compatibility of the model was checked and it was OK

## Slide 21: Preliminary Design And Checks
Checks and SAP model Verification:
Equilibrium :
Equilibrium in the vertical direction (due to gravity loads )
Thus, the errors between hand solution and SAP results are very small and less than 5%, so accept results.
Load type | Hand results (KN) | SAP results (KN) | Error %
live load | 15729.804 | 16264.172 | 3.28
SID load | 20069.856 | 20614.71 | 2.64
dead load | 42479.38 | 42057.665 | 1
Load type | Hand results (KN) | SAP results (KN) | Error %
live load | 11991.84 | 11921.736 | 0.5
SID load | 24943.68 | 25461.972 | 2.03
dead load | 43109.816 | 45355.04 | 4.9
water load | 3000 | 3000 | 0

## Slide 22: Preliminary Design And Checks
Checks and SAP model Verification:
Equilibrium :
Equilibrium in lateral direction
From hand calculation both x and
Y force =0.

## Slide 23: Preliminary Design And Checks
Checks and SAP model Verification:
Stress-strain Relationship:

## Slide 24: Preliminary Design And Checks
panel ID | panel location | (left) |  | (right) | M average | wl2/8 | error%
s1 |  | 33 | 21 | 19 | 47 | 49.94 | -6.25
 |  | 42 | 27 | 31 | 63.5 | 63.94 | -0.7
 |  | 60 | 46 | 33 | 92.5 | 93.69 | -1.2
s2 |  | 38 | 15 | 31 | 49.5 | 49.94 | -0.89
 |  | 66 | 22 | 23 | 66.5 | 63.94 | 3.84
panel ID | panel location |  |  |  | M average | wl2/8 | error%
s1 |  | 33 | 21 | 19 | 47 | 49.94 | -6.25
 |  | 42 | 27 | 31 | 63.5 | 63.94 | -0.7
 |  | 60 | 46 | 33 | 92.5 | 93.69 | -1.2
s2 |  | 38 | 15 | 31 | 49.5 | 49.94 | -0.89
 |  | 66 | 22 | 23 | 66.5 | 63.94 | 3.84
beam ID | beam location | (left) |  | (right) | M average | wl 2/ 8 | Error%
beam 1 |  | 1617.75 | 880 | 1569.5 | 2473.625 | 2430.47 | 1.74
 |  | 2002.03 | 1064 | 2039.87 | 3084.95 | 3035.52 | 1.6
 |  | 3003.19 | 1777 | 2463.37 | 4510.28 | 4308.29 | 4.48
beam 2 |  | 655.44 | 393 | 689.44 | 1065.44 | 1072.25 | -0.64
 |  | 756.78 | 502 | 725.7 | 1243.24 | 1352.25 | -8.76
beam ID | beam location |  |  |  | M average | wl 2/ 8 | Error%
beam 1 |  | 1617.75 | 880 | 1569.5 | 2473.625 | 2430.47 | 1.74
 |  | 2002.03 | 1064 | 2039.87 | 3084.95 | 3035.52 | 1.6
 |  | 3003.19 | 1777 | 2463.37 | 4510.28 | 4308.29 | 4.48
beam 2 |  | 655.44 | 393 | 689.44 | 1065.44 | 1072.25 | -0.64
 |  | 756.78 | 502 | 725.7 | 1243.24 | 1352.25 | -8.76

## Slide 25: Chapter 3: Static design

## Slide 26: Static design
Slab design
Column design
Footing design
Pool design
Stair case

## Slide 27: Static design
    Slab Design:
    Check Deflection:
    The max deflection due to dead load was found at the middle of the panel between grid lines 14 and 16 that is 41.6mm.

## Slide 28: Static design
    Slab Design:
    Check Deflection:
Δ dead = 4.386 mm.
Δ Live = 4.178 mm.
    Δ long term = 17.128 mm.
    The allowable deflection = L /240 = 5000 /240 = 20.83 mm.
    So the slab deflection = 17.128 mm. < allowable long term def. =20.83mm OK.

## Slide 29: Static design
    Slab Design:
check slab for shear :
ØVc= 122.47 KN. ,Vu slab roof4 = 78.65 KN/m.
122.47 ≥ 78.65 OK
ØVc= 97.98 KN. ,Vu slab roof4 = 56.47 KN/m.
122.47 ≥ 56.47 OK

## Slide 30
Design for bending moment:
-ve &+ve moment m11 for slabs roof5

## Slide 31
reinforcement for slab roof5

## Slide 32
-reinforcement for slab roof4 northern part

## Slide 33
reinforcement for slab roof4 southern part

## Slide 34
reinforcement for slabs 1,2,3 northern part

## Slide 35
reinforcement for slabs 1,2,3 southern part

## Slide 36: Static design
Design of columns:
For un-braced column:-
Kl/r≤ 22 ……........Short column.
Kl/r≥ 22 ………….Long column

## Slide 37: Static design
M min =Pu*e min
e min =0.015+0.03c
Moment M min = 51.78 1 KN.m
Pu =1918 KN , Mc =62.14KN.m
Use =0.01 , fc =30 MPa
Cover in column =0.04m ,ɤ=0.8
Pu/bh =1.74Ksi , Mn/bh2 =0.141Ksi.
From interaction diagram the section is adequate to carry the load and moment .

## Slide 40
Grouping name | column ID | Dimension(m) | Column identification using grid formation | Longitudinal reinforcement
col0.4 | col0.4-1 | 0.4*0.4 | A-1,A-4-A-18,B-3,B-10,B-13,B-18 | 8Ø16
 |  |  | C-1,C-10,C-13,C-18,D-1 | 8Ø16
 |  |  | F-1,F-10,F-13,G-13,J-13,I-1,K-1, K-10,K-13 | 8Ø16
 |  |  | M-1,N-1,N-10 | 8Ø16
 |  |  | O-1,O-10,P-1,P-10,P-13 | 8Ø16
 | col0.4-2 | 0.4*0.4 | B-1 | 16Ø16
col0.5 | col0.5-1 | 0.5*0.5 | B-14,B-16,B-17,C-3,C-14,C-16,C-17 | 12Ø18
 |  |  | F-3,G-15,J-15,K-15,P-18 | 12Ø18
 | col0.5-2 | 0.5*0.5 | N-18,O-13,O-18,N-13 | 14Ø18
col0.6 | col0.6-1 | 0.6*0.6 | B-6,B-7,B-9,F-9,F-16,G-14,I-3,1-7, I-9,K-3 | 16Ø18
 |  |  | K-6,K-7,K-9,K-18,F-14,F-18,N-3,N-6, N-7,N-9 | 16Ø18
 | col0.6-2 | 0.6*0.6 | B-4,N-4,F-17 | 20Ø18
 | col0.6-3 | 0.6*0.6 | P-3,P-4,P-6,P-7,P-9 | 22Ø20
col0.8 | col0.8-1 | 0.8*0.8 | F-,F-7,I-6,K-17 | 14Ø25
 | col0.8-2 | 0.8*0.8 | K-14,K-16,P-14,P-16,P-17 | 22Ø32

## Slide 41: Static design
footing:
Bearing capacity of the soil=400KN/m2.
Design of footing for column B-3:
Column dimensions = 0.4x0.4 m
Compressive strength of concrete (fc) = 40MPa.
service load =1640 KN
Area=
Area of footing =4.1m2
The root of area =2.03m L= 2.5 m.

## Slide 42: Static design
For design:
Area of footing =6.25m2
Check wide beam shear
ØVc = 0.75fc^0.5 L*d/6
ØVc= 830.09 KN
Vu = qu[ L/2– (c/2+d) ]
Vu= 483.34 KN
Vu < ØVc. Wide beam shear OK.

## Slide 43: Static design
Check punching shear:
Qu=306.88KN /m2
ØVcp=0.75 fc^0.5 L*d/3
ØVcp=2178.17 KN
Vup=Pu –(c+d)2 qu Vup =1803 KN
Vup< ØVcp Punching is OK.

## Slide 44: Static design
Flexural design:
Mu =422.92 KN.m
=0.00257
As= *L*d
As =2699mm2 So use As 13ɸ18
As shrinkage= 2250mm2

## Slide 45: Static design
grouping name | footing ID | dimension | Column identification using grid formation | reinforcement
f1 | f1-1 | 1.5*1.5 | A-1,C-1,D-1,F-1,G-13,J-13,K-1,M-1,N-1,P-1 | 8ɸ16
f2 | f2-1 | 2*2 | A-3,A-4,A-5,A-8,A-9,A-16,A-17, A-18,B-1,C-18,J-15,O-1,P-18 | 10ɸ16
 | f2-2 | 2*2 | I-1,B-18 | 10ɸ18
f3 | f3-1 | 2.5*2.5 | A-14,B-3,B-7,B-9,B-14,B-16,B-17,C-3,C-14, | 13ɸ18
 |  |  | C-16,C-17,F-14,F-18,K-3,N-3,N-9, N-18,O-18,P-3,P-4,P-6,P-7,P-9 | 
 | f3-2 | 2.5*2.5 | K-18 | 13ɸ20
f4 | f4-1 | 3*3 | B-4,B-6,F-16,F-17,I-3,N-4,N-6,N-7 | 15ɸ20
 | f4-2 | 3*3 | F-3,K-14 | 15ɸ25
f5 | f5-1 | 3.3*3.3 | P-14,P-16,P-17 | 17ɸ20
f6 | f6-1 | 3.8*3.8 | K-16,K-17 | 19ɸ20

## Slide 46: Static design
Design of footing F7 carrying O-10 and O-13 :
Column ID | service load KN(Ps) | Ultimate load KN (Pu)
O-10 | 838 | 1059
O-13 | 1359 | 1751
 | C.S 1.25m | M.S 1.25m | C.S 1.5m | M.S 1.5m
moment/C.S or/M.S | 385 | 295 | 370 | 225
 | 0.0047 | 0.0036 | 0.0037 | 0.0023
As | 2468 | 1890 | 2331 | 1449
As. Bars | 13ɸ16 | 13ɸ14 | 15ɸ14 | 15ɸ12

## Slide 47: Static design
Check wide beam shear was satisfied
Check punching shear was satisfied
footing f7 | dimensions | Reinforcement in long direction . | Reinforcement in short direction .
O-10,O-13 | 3*2.5 | 26ɸ16 | 30ɸ14
A-10,A-13 | 3*2.5 | 26ɸ16 | 30ɸ14
C-10,C-13 | 3*2.5 | 26ɸ16 | 30ɸ14
N-10,N-13 | 3*2.5 | 26ɸ16 | 30ɸ14
B-10,B-13 | 3*2.5 | 26ɸ16 | 30ɸ14
P-10,P-13 | 3*2.5 | 26ɸ16 | 30ɸ14
F-10,F-13 | 3*2.5 | 26ɸ16 | 30ɸ14
K-10,K-13 | 3*2.5 | 26ɸ16 | 30ɸ14

## Slide 48: Static design
Design of raft footing f8 :
The KN and the size of mish =0.3m .
stress == 325.89 KN/m2
where < 400 KN/m2 OK
Check wide beam shear:
h=700mm d=620mm.
ØVc = 490 KN/m
Check punching shear:
ØVcp =5568.14 KN
Pu on column F6= 4643 KN

## Slide 49: Static design

## Slide 50: Static design
Design of combined footing f9:
h= 60cm and d = 52cm.
L = 4m. B=3 m.

## Slide 51: Static design
Check for wide beam shear:
ØVc= 1233.29 KN/m
ØVc > Vu OK.
Check for punching shear:
Column k-14:
Pu=3666.83 KN
ØVcp =4341 KN
ØVcp> Pu OK.

## Slide 52: Static design
Longitudinal 20ɸ20, 20ɸ16
TraversUse 26 ɸ20

## Slide 53: Static design
Pool design :
Pool Wall:
Vu , V13= 13KN/m
V23=50KN/m, both less than 164.3 KN/m Ok.
Flexural design:

## Slide 54: Static design
Mu design =Mu from analysis *Sd*
Sd =
: 0.9 fy: Steel yield strength
: factor for ultimate load which =1.4
H=300mm and assume the distance between bars 20cm then Sd=1.54
fs max :maximum permitted stress in steel to avoid large cracks =175 Mpa
fc 30 Mpa and assume percentage of steel 0.007 then
= 1.044

## Slide 55: Static design
For Mu design =84 KN.m/m
As = 956 mm2/m, So use 7 14/m
For Mu design =10KN.m/m use As min and 4 10/m
Also for horizontal

## Slide 56: Static design
Pool slab:
Check wide beam shear:
ØVc=239.6 KN /m
Design for flexure:

## Slide 57: Static design

## Slide 58
Stair case
2 sections
Dimensions

## Slide 59
Thickness:
Flight span = 6.7m
hmin = = 0.239 m
So, se h=0.25m.
Loads
DL= 6.25 KN/m2
LL= 5 KN/m2
SDL=4.07 KN/m2

## Slide 60
Check for shear: reading shear values from 1D model for both sections
Ø Vc = * =128.6 KN > Vu for both

## Slide 61
Flexure design : moment values from the 1D model as shown for both section , respectively

## Slide 62
Model number | Mu | ρ | As | Reinforcement/m
Model 1 | 87.5 | 0.005558 | 1168 | 8 Ø14
 | 40.57 | 0.002494 | 524 | 4 Ø 14
 | 87.5 | 0.005558 | 1168 | 8 Ø14
Model 2 | 43.29 | 0.002666 | 560 | 4 Ø 14
 | 101.23 | 0.006497 | 1365 | 9 Ø14
Final reinforcement for stair case

## Slide 63
Staircase detail for section 1

## Slide 64
Staircase detail for section 2

## Slide 65: Chapter 4: dynamic design

## Slide 66: Dynamic design
parameters for dynamic analysis and design using IBC2006 design code :
Importance factor (I) = 1.25
Peak Ground Acceleration (PGA)= 0.2g
Area mass = 0.55 ton/m2.
The response spectrum scale factor = .
Time history scale factor = *
The soil class (rock soil) = B
Spectral acceleration at short periods (Ss) =0.5
Spectral acceleration at short periods (S1) =0.2
site coefficients: Fa = 1 Fv = 1
The structural system to be designed is moment resisting frame system. (Intermediate moment frame)
Response modification factor (R):5

## Slide 67: Dynamic design
Period
Period for the structure was taken from SAP checked by Rayleigh method
For the northern part :
Mode |  | period(sec) | MMPR
1 | transition in y | 1.77 | 0.8186
2 | transition in x | 1.58 | 0.8318
3 | Rz | 1.35 | 0.0322
Mode |  | period(sec) | MMPR
1 | transition in x | 1.67 | 0.9084
2 | transition in y | 1.56 | 0.8787
3 | Rz | 1.52 | 0.4199
For the southern part :

## Slide 68: Dynamic design
Earthquake Force:
Methods for determining Earthquake Force :
Equivalent static method.
2. Time history method
3. Response spectrum analysis

## Slide 69: Dynamic design
Equivalent static method
The following calculation for the northern in x-direction
V = Cs*W
SDs = *F a*Ss = *1*0.5 = 0.3333.
SD1 = *F v*S1= *1*0.2 = 0.13333.
Cs = ≤
.
 | SD1 | T(s) | Cs | M(ton) | V(KN)
Northern part x-direction | 0.13333 | 1.59 | 0.01973 | 6489.7 | 1330.57
Southern part x-direction | 0.13333 | 1.66 | 0.02008 | 6748.94 | 1329.44

## Slide 70: Dynamic design
Method | Value(KN)
Manual(equivalent static) southern -x | 1329.44
response-x southern | 1028.07
elcentro-x southern | 1338.89
Manual(equivalent static) northern -x | 1330.57
response-x northern | 2092.2
elcentro-x northern | 2160.03
Earthquake forces for the structure by the 3 methods:

## Slide 71: Dynamic design
Dynamic Design :
consider time history (elcentro earthquake) for the dynamic design.
Load combinations are:
COMB1 = 1.2D.L + 1.6 LL.
COMB2 = 1.4 D.L.
COMB3 = 1.2D.L + L.L + elcentro-x.
COMB4 = 1.2D.L + L.L + elcentro -y.
COMB5 = 0.9D.L + elcentro -x.
COMB6 = 0.9D.L + elcentro -y.

## Slide 72: Dynamic design
Final design :
Slab design
Beams design
Column design
Footing design
Pool design
Shear wall

## Slide 73: Dynamic design
Slab design
we found that the values of shear and moment on slabs due to static or gravity load combination are greater than earthquake combination so: static design governs for slab .

## Slide 74: Dynamic design
Beams design
Final beam design taken from SAP as follows

## Slide 76: Dynamic design
Column design
Grouping name | column ID | Dimension(m) | Column identification using grid formation | Longitudinal reinforcement
col0.4 | col0.4-1 | 0.4*0.4 | A-1-A-17,B-10,B-13,B-18 | 8Ø16
 |  |  | C-1,C-10,C-13,C-18,D-1 | 8Ø16
 |  |  | F-1,F-13,G1-3,J-13,I-1,K-1,K-13 | 8Ø16
 |  |  | M-1,N-1,N-10 | 8Ø16
 |  |  | O-1,P-1,P-10 | 8Ø16
 | col0.4-2 | 0.4*0.4 | B-1,F-10,K-10,O-10 | 16Ø16
col0.5 | col0.5-1 | 0.5*0.5 | B-3,B-14,B-16,B-17,C-3,C-14,C-16,C-17 | 12Ø18
 |  |  | F-3,G-15,J-15,K-15 | 12Ø18
 | col0.5-2 | 0.5*0.5 | N-18,O-13,O-18,N-13 | 14Ø18
col0.6 | col0.6-1 | 0.6*0.6 | B-6,B-7,B-9,F-9,F-6,G-14,I-3,1-7,I-9,K-3 | 16Ø18
 |  |  | K-6,K-7,K-9,K-18,F-14,F-18,N-3,N-6 ,N-7, N-9 | 16Ø18
 | col0.6-2 | 0.6*0.6 | B-4,N-4,F-17 | 20Ø18
 | col0.6-3 | 0.6*0.6 | P-3,P-4,P-6,P-7,P-9 | 22Ø20
col0.8 | col0.8-1 | 0.8*0.8 | F-6,F-7,I-6,K-17 | 14Ø25
 | col0.8-2 | 0.8*0.8 | K-14,K-16,P-14,P-16,P-17 | 22Ø32

## Slide 77: Dynamic design
Footing design
Static design govern in most cases
Some of them was covered by dynamic combinations, and despite that they were within the capacity of previous static design

## Slide 78: Dynamic design
Pool design:
When comparing results, the gravity combinations controlled for analysis and design for both pool slab and pool walls.

## Slide 79: Dynamic design
Shear wall:
Shear wall was designed as a column
Dimensions : (1.5 *0.25 )m
0.01
Within the capacity
Use 16ɸ18 longitudinal
With respect to travers we checked
for shear capacity and required
reinforcement using minimum is
adequate 1ɸ10/250mm

## Slide 80
THANK YOU