## Slide 1
An-Najah National University Faculty of Engineering Building Engineering Department
Graduation Project – 2
Design of an integrated 5-Star Hotel
Prepared By: Alaa Horani
Mosab Hamdan
Nael Sakhen
Yahya Yamin Project supervisor: Eng. Hasan Mather
2015-2016

## Slide 2
CONTENTS
Introduction
Selected Site
Architectural Design
Structural Design
Environmental Design
Electrical Design
Mechanical Design
Safety Design
Estimated Cost

## Slide 3: INTRODUCTION
The main concept of our project was to design an integrated 5-Star Hotel, and our focus has been on Structure, Environmental, Electrical, Mechanical and Safety design to make a comfortable hotel.

## Slide 4: Selected Site
Pelvis No. (رقم الحوض) : 43
Piece no. :18
Site Area : 6770 m2
Rebound from streets : 10m

## Slide 5: Selected Site

## Slide 6: Section A-A
Selected Site

## Slide 7: Selected Site

## Slide 8: ARCHITECTURAL DESIGN

## Slide 9: Site Plan
Site Plan

## Slide 10: Master Plan
Master Plan

## Slide 11: Hotel Plans
B2 plan

## Slide 12: Hotel Plans
B1 Plan

## Slide 13: Hotel Plans
GF Plan

## Slide 14: Hotel Plans
F1 Plan

## Slide 15: Hotel Plans
F2 Plan

## Slide 16: Hotel Plans
F3 Plan

## Slide 17: Plans Hotel
F4-11 Plan

## Slide 18: Elevations
North-Elevation

## Slide 19: Elevations
South-Elevation

## Slide 20: Elevations
East-Elevation

## Slide 21
West-Elevation
Elevations

## Slide 22: Sections
Section A-A

## Slide 23
Section B-B
Sections

## Slide 24: STRUCTURAL DESIGN

## Slide 25
Design Codes
ACI -318-08 for reinforced concrete structural design.
ACI -350-3-01 for seismic design of liquid with concrete structure .
ACI -350-3-06 for seismic design of soil pressure with concrete structure .
UBC -97 for earthquake load combinations.
ASCE for load combinations.

## Slide 26
Compressive strength of Concrete “f′c”.
    For columns and slabs f′c = 28 Mpa
    For all other elements in structure such as blinding and bracing f′c = 12 MPa
Yielding strength of steel fy = 420 MPa.
Material Property
Soil Property
Soil bearing capacity = 400 KN/m2
Soil profile = SB

## Slide 27
Dead loads (D.L): 5 KN/m2
Super Imposed dead load (SI):4 KN/m2
Live Load (L.L): 5 KN/m2 (for first five floor) 3KN/m2 ( for other floors)
Lateral loads consider earthquake load.
Loads

## Slide 28
Column Center Lines Grid

## Slide 29: Design and Reinforcement of Structural Elements
Slab (one way & two way & solid).
Beams ( drop &hidden).
Columns
Shear wall
Basement wall
Stair
Footings
Swimming pool.

## Slide 30
Hotel 3D Model - Etabs

## Slide 31
Model Checks
Compatibility

## Slide 32
Model Checks
Equilibrium

## Slide 33
Model Checks
Internal Forces

## Slide 34
Cv = 0.15
Ca = 0.15
Seismic design
I = 1
R = 5.5
Base shear ( V ) = 6693.1 KN
Soil profile SB
Z = 0.15
From Etabs
Mass participation ratio is larger than 90% in X, Y .

## Slide 35
Footing Reinforcement Details
Single Footing

## Slide 36
Footing Reinforcement Details
Mat Footing

## Slide 37
Basement Retaining Wall Details

## Slide 38
Column Reinforcement Details

## Slide 39
Beam Reinforcement Details

## Slide 40
Slab Reinforcement Details

## Slide 41
Shear Wall Details

## Slide 42
Stair Reinforcement Details

## Slide 43: Swimming pool Reinforcement Details

## Slide 44: Expansion Joint

## Slide 45: Environmental DESIGN

## Slide 46
Floor Properties
Thermal Insulation
Floor Section

## Slide 47
Thermal Insulation
U-Value Of The Other Elements
Elements | U-Value
External wall | 0.51
Ceiling | 0.57
Partition | 2.31
Roof | 0.37
Window | 2.71

## Slide 48
Thermal Insulation
Cooling and heating load for Ground floor
Before add insulation:

## Slide 49
Thermal Insulation
After adding insulation:

## Slide 50
Thermal Insulation
After adding insulation:

## Slide 51
Natural Daylight Analysis

## Slide 52
Shading design
summer
winter

## Slide 53
Shading design

## Slide 54
We used one way ribbed slab with thickness = 400 mm
IIC = 70
Acoustical Design
Sound Transmission Class (STC)
STC-Values Between Different Spaces |  | Recommendation
Bedroom to Bedroom | 52 | > 52
Bedroom to bathroom | 58 | > 56
Corridor To Bedroom | 58 | > 52
Impact Insulation Class (IIC)

## Slide 55
    Acoustical Design
    Reverberation Time (RT60)
    Range RT60 for bedrooms 0.4-0.8
    RT60 values for bedroom before improving :

## Slide 56
    Acoustical Design
    Reverberation Time (RT60)
    Improving RT60 by add Fiberglass board to the wall and Carpet to the floor with
    Different values of absorptions as follow :

## Slide 57
    Acoustical Design
    Reverberation Time (RT60)
    RT60 values for bedroom after improving :

## Slide 58
    Acoustical Design
    Transmission loss (TL)
    TL = 40.6 > 40

## Slide 59: Electrical DESIGN

## Slide 60
    Sockets Arrangement
    Lighting arrangement

## Slide 61
    Artificial Lighting
Bar Lighting:

## Slide 62
    Artificial Lighting

## Slide 63: Mechanical DESIGN

## Slide 64
    Water Supply Design

## Slide 65
    Water Supply System

## Slide 66
    Drainage System
    For Ground Floor

## Slide 67
    Rain Drainage System

## Slide 68
    Rain Drainage System

## Slide 69
    H-VAC System
    VRF system for Bedrooms

## Slide 70
    H-VAC System
    VAV system

## Slide 71: Safety DESIGN

## Slide 72
    Safety Design
    Egress rout for ground floor

## Slide 73
    Egress rout for 4th floor
    Safety Design

## Slide 74
    Safety System

## Slide 75: Estimated Cost

## Slide 76: Estimated Cost
The total cost of the HOTEL is about 26.5 million shekel.
The total cost per meter square for the HOTEL is about 2038 shekel.