## Slide 1
Prepared by:
Ahmad Quzmar
Ahmad Sabobeh
Haitham Estetieh
Omar Al-Qadah
Under the supervision of Dr. Mohammad N. Almasri
The use of WEAP for the assessment of the clustering of the water service providers and the design of a storm water collection network for Anabta

## Slide 2
Water sector faces many problems in quantity
Problem has exacerbated recently
We have roughly 1000 MCM of water recharges each year which led to 170 L/c.d
A considerable number of Palestinians don’t get more than 40 L/c.d
Israeli occupation actions led to Palestinians overuse the groundwater by 120%
Introduction

## Slide 3
Due to the continually changing political situation in the West Bank, we wanted to study the water current and future situation based on some predicted milestones called scenarios
Introduction

## Slide 4
We aim to provide a tool for stakeholders, decision-makers and administrators to handle both current and future situations with preventive procedures
Reduce the problems that the coming generations could go through
Objectives

## Slide 5
“A person who never made a mistake never tried anything new”
“
Figure 1: steps followed in this GP
Problem identification
Data collection
Create the WEAP model
Processing of scenarios
Development of different scenarios
Develop management option per each scenario
Develop the base case scenario using WEAP
Methodology

## Slide 6
Because of the position of the West Bank, the main source for Water is groundwater, which can be found in basins
Three basins: eastern, western and northeastern
Annual renewable recharge for these basins ranges between 675~794 MCM
Study Area Description

## Slide 7
Study Area Description
Basin | Recharge (MCM/year)
Eastern | 318 ~ 420
Western | 125 ~ 195
Northeastern | 145 ~ 170
Table 1: the distribution of recharge in MCM/year for each basin

## Slide 8
Study Area Description
According to Oslo II Accord, the West Bank was divided into temporary areas that differ in predominance
 | Area | %
Area A | 981.97 | 17.37
Area B | 1,035.11 | 18.31
Area C | 3,448.20 | 60.98
Natural Reserves | 166.54 | 2.95
Special Area | 22.40 | 0.40
 | 5,654.21 | 100
 |  | %
Area A | 981.97 | 17.37
Area B | 1,035.11 | 18.31
Area C | 3,448.20 | 60.98
Natural Reserves | 166.54 | 2.95
Special Area | 22.40 | 0.40
 | 5,654.21 | 100
Table 2: area of each category in the West Bank as Oslo II Accord

## Slide 9
Water Evaluation and Planning (WEAP) is a software that was developed by Stockholm Environment Institute (SEI).
WEAP could also be used as a tool to deal with the current situations smartly rather than trying to make changes for inevitable circumstances.
WEAP

## Slide 10
Free
User-Friendly
Available with over 25 languages
Used for future planning of water resources
Easy to learn
Fast technical support
WEAP
Why WEAP?

## Slide 11
Clustering is the process of assembling a bunch of LGUs within one group, called cluster. In our project, we used a 31-cluster map proposed by specialists.
The following are some of the criteria followed by the specialists in establishing the clusters:
Existence of shared water source
Acceptance of LGUs to collaborate and share a certain source
Existence of water infrastructure such as pipelines
Catchment (watershed) boundary
Clusters

## Slide 12
Reduction of the number of water service providers from over 300 to 31 only.
More centralization and independency for each cluster.
More flexibility in the water distribution process.
A decrease in conflicts and disputes.
LGUs will get water impartially as water resources will be controlled more efficiently.
Attracting stakeholders to implement water-related projects in the study area.
Clusters
Advantages

## Slide 13
People in a certain LGU refrain to share water existing under their control with other LGUs.
Conducting the clustering process needs time to persuade people and maybe resorting to intimidate them might be needed.
Clusters
Challenges

## Slide 14
Clusters
The following figure shows the clusters as proposed in the Road Map

## Slide 15
Clusters
Table 1: clusters names and main LGUs
Name (as in WEAP) | Main LGUs | Name (as in WEAP) | Main LGUs
Bethlehem_1 | Bethlehem, Beit Jala, Beit Sahur | Jericho_1 | Al 'Auja, Aqbat Jaber Camp, Jericho
Bethlehem_2 | Nahhalin, Battir, Husan, Wadi Fukin | Jericho_2 | Al Jiftlik, Az Zubeidat
Bethlehem_3 | Beid Falouh, Tuqu', Al 'Ubeidiya, Za'tara | JWU_Jerusalem | Qalandiya Camp, Jerusalem, Al 'Isawiya
Hebron_1 | Surif, Nuba, Bayt Aula, Kharas | JWU_Ramallah | Beituniya, Al Jalazun Camp, Beit Liqya
Hebron_2 | Beit Kahil, Halhul, Beit Ummar, Beit Fajjar | Nablus_1 | Asira ash Shamaliya, Nablus, Beit Furik
Hebron_3 | Sa'ir, Qula Zeita, Ash Shyoukh, Beit 'Einun | Nablus_2 | Aqraba,Qabalan, Beita, Qusra, 'Awarta
Hebron_4 | Ar Rawa'in, Bani Na'im | Qalqilya_1 | Habla, Qalqiliya, Jayyus, Kafr Thulth
Hebron_5 | As Samu', Adh Dhahiriya, Ar Ramadin | Qalqilya_2 | Azzun, Baqat al Hatab, Jinsafut, Hajja
Hebron_6 | Beit 'Amra, Al Karmil, Yatta, Ar Rihiya | Salfit_and_Jama'een | Biddya, Jamma'in, Salfit
Hebron_7 | Taffuh, Hebron, Kharsa, Dura | Tubas_1 | Tubas, El Far'a Camp, Tammun, Tayasir
Hebron_8 | Tarqumiya, Idhna, Beit 'Awwa, Deir Samit | Tubas_2 | Bardala, 'Ein el Beida
Jenin_1 | As Silat al Harithiya, Al Yamun, Jenin | Tulkarm_1 | Anabta, Kafr al Labad, Tulkarm
Jenin_2 | Meithalun, Al Jadida, Siris, 'Aqqaba | Tulkarm_2 | Kafr 'Abbush, Kafr Sur, Kafr Jammal
Jenin_3 | Az Zababida, Qabatiya | Tulkarm_3 | Nazlat 'Isa, Qaffin
Jenin_4 | Ya'bad, Barta'a ash Sharqiya, Arraba | Tulkarm_4 | Illar,'Attil, Deir al Ghusun, Zeita
Jenin_5 | Silat adh Dhahr, Jaba' - Jenin, Kafr Ra'i |  | 

## Slide 16
This type of projects cannot be proceeded without any assumptions because it deals with future predictions
The assumptions we used in this GP were:
We have 31 clusters. We are handling each cluster as an individual entity that represents
Each person in a cluster has the same portion as other people in it
Water in an LGU will be shared within multiple consumers
Assumptions

## Slide 17
The population number of a certain cluster is the population number of all LGUs within it, and the population used is the population of 2017 projected from 2007 with growth rate of (2.24 %).
The demand is constant for all clusters and is taken to be 120 L/c.d according to the PWA reports.
The consumption’s percent is 100%.
Assumptions

## Slide 18
We are going to conduct some management options for the West Bank under 1967 borders while neglecting Israeli settlements.
The loss’s percent is different for each cluster and it's calculated from reports of PWA, as follows:
Assumptions

## Slide 19
Assumptions
Name (WEAP) | Governorate | %loss | Name (WEAP) | Governorate | %loss
Bethlehem_1 | Bethlehem & Hebron | 30.3 | Jericho_1 | Jericho & Al-Aghwar | 32.8
Bethlehem_2 | Bethlehem & Hebron | 30.3 | Jericho_2 | Jericho & Al-Aghwar | 32.8
Bethlehem_3 | Bethlehem & Hebron | 30.3 | JWU_Jerusalem | Ramallah & Al-Bireh, and Jerusalem | 19
Hebron_1 | Bethlehem & Hebron | 30.3 | JWU_Ramallah | Ramallah & Al-Bireh, and Jerusalem | 19
Hebron_2 | Bethlehem & Hebron | 30.3 | Nablus_1 | Nablus | 31
Hebron_3 | Bethlehem & Hebron | 30.3 | Nablus_2 | Nablus | 31
Hebron_4 | Bethlehem & Hebron | 30.3 | Qalqilya_1 | Qalqiliya | 25.6
Hebron_5 | Bethlehem & Hebron | 30.3 | Qalqilya_2 | Qalqiliya | 25.6
Hebron_6 | Bethlehem & Hebron | 30.3 | Salfit_and_Jama'een | Salfit | 18.8
Hebron_7 | Bethlehem & Hebron | 30.3 | Tubas_1 | Tubas | 25.8
Hebron_8 | Bethlehem & Hebron | 30.3 | Tubas_2 | Tubas | 25.8
Jenin_1 | Jenin | 29.3 | Tulkarm_1 | Tulkarm | 38. 5
Jenin_2 | Jenin | 29.3 | Tulkarm_2 | Tulkarm | 38. 5
Jenin_3 | Jenin | 29.3 | Tulkarm_3 | Tulkarm | 38. 5
Jenin_4 | Jenin | 29.3 | Tulkarm_4 | Tulkarm | 38. 5
Jenin_5 | Jenin | 29.3 |  |  | 
Table 3: percentage of loss in each cluster

## Slide 20
Assumptions
There are two main water resources:
The wells under PWA and municipalities control that are used for domestic purposes and excluding all agricultural wells.
The amount of water purchased from Mekorot according to PWA’s reports.

## Slide 21
Name (as in WEAP) | Q Mekorot (MCM/year) | Q well (MCM/year) | Name (as in WEAP) | Q Mekorot (MCM/year) | Q well (MCM/year)
Bethlehem_1 | 3.18 | 5.2 | Jericho_1 | 2 | 0.1
Bethlehem_2 | 0.95 | 0 | Jericho_2 | 0.83 | 0
Bethlehem_3 | 4.13 | 9.51 | JWU_Jerusalem | 6.15 | 1.04
Hebron_1 | 0 | 0 | JWU_Ramallah | 17.68 | 5.36
Hebron_2 | 8.46 | 3.42 | Nablus_1 | 3.8 | 7.69
Hebron_3 | 10.77 | 1.04 | Nablus_2 | 1.03 | 3.82
Hebron_4 | 0 | 0 | Qalqilya_1 | 0 | 3.3
Hebron_5 | 0 | 0.23 | Qalqilya_2 | 1.61 | 0.61
Hebron_6 | 0.46 | 0.47 | Salfit_and_Jama'een | 3.89 | 0
Hebron_7 | 0.19 | 0 | Tubas_1 | 0 | 0
Hebron_8 | 0 | 0 | Tubas_2 | 4.91 | 0
Jenin_1 | 2.08 | 1.97 | Tulkarm_1 | 0.2 | 10.69
Jenin_2 | 0 | 1.05 | Tulkarm_2 | 0.33 | 0.28
Jenin_3 | 0 | 1.2 | Tulkarm_3 | 0 | 0.58
Jenin_4 | 0.56 | 2.12 | Tulkarm_4 | 0 | 1.4
Jenin_5 | 0 | 0 | Subtotal | 73.2 | 61.1
 |  |  | total | 134.3 | 
Table 4: The water amount in m^3 that is either purchased from Mekorot or gained from PWA’s wells per year.

## Slide 22
WEAP Modeling
We added 31 Demand Sites, which represents the 31 clusters under study, 21 Groundwater which represent the withdrawal from the wells, 21 other supply which represent the amount bought from Mekorot for each cluster

## Slide 23
WEAP Modeling
Adding the population of each demand site
Figure 8: Population of 2017 entered to WEAP for each cluster
Adding the growth rate
Figure 9: using a growth rate of 2.4% to predict the population number for each year between 2018 and 2032

## Slide 24
WEAP Modeling
Adding the annual demand rate
Figure 10: water user rate in liters per capita per year
Adding the loss percent for each demand site
Figure 11: loss rate during the years 2017-2032 a percentage

## Slide 25
WEAP Modeling
Adding the annual withdrawal for each demand site.
Figure 12: withdrawal from groundwater in in 2017
Adding the bought amount from Mekorot for each deamnd site.
Figure 13: water from Mekorot for each cluster in CMS

## Slide 26
Data Analysis
It describes the water condition in the West Bank in 2032 assuming no significant change on any parameter, except for the clustering and population growth.
Status quo

## Slide 27
Our main concern in the analysis phase is the amount of unmet demand per capita for each cluster
The values are categorized into 4 classes According to the World Health Organization (WHO):

## Slide 28
Data Analysis
Table 7: per capita consumption in each cluster in 2032

## Slide 29
Data Analysis
Figure 14: unmet demand MCM in clusters with 50-120 L/c.d consumption

## Slide 30
Table 8 unmet demand MCM in clusters with 50-120 L/c.d consumption

## Slide 31
Data Analysis
Figure 15: unmet demand MCM in clusters with 0-50 L/c.d consumption

## Slide 32
Table 9: unmet demand MCM in clusters with 0-50 L/c.d consumption

## Slide 33
A formal document was sent to PWA without any response yet

## Slide 34
Introduction
Because of urbanization, imperviousness increases causing the
generation of runoff. To avoid any related problems we are to design
A storm water network.

## Slide 35
Study Area Description
We chose Anabta because of its vulnerability to floods
Figure 1: Anabta and its neighbouring towns

## Slide 36
We chose the shown part of Anabta, whose area is 10.93 ha
Study Area Description
Figure 2: The 10.93-hectare area

## Slide 37
Figure 3: Contour map for the study area
Study Area Description

## Slide 38
Importance of Work
Figure 4: Floods occur when poor infrastructure exist

## Slide 39
Importance of Work
Figure 5: Floods occur when poor infrastructure exist

## Slide 40
Importance of Work
Figure 6: Floods occur when poor infrastructure exist

## Slide 41
Objectives
We want to design a stom water collection network for part of Anabta.

## Slide 42
Methodology
Figure 7: Methodology
Problem identification
Data collection
Conclusions and recommendations
Delineate catchments and catch basins
SewerGEMS modeling
Selection of study area

## Slide 43
Elements
Runoff
We used the Rational Method
The method depends on:
The average intensity of the storm
The size of the drainage area
The type of the surface of the drainage area

## Slide 44
Catch basins
We used 85 catch basins in our project
Elements
Figure 9: A part of the placed catch basins in our network
Figure 8: Catch basin

## Slide 45
Catch basins
Elements
Figure 10: Catch basin structure design

## Slide 46
Catch basins
Elements
Figure 11: Catch basins design

## Slide 47
Catchments
We used 85 catchments
in our project
Elements
Figure 12: catchments

## Slide 48
Runoff Coefficient (C)
An intersection between the physical plan and the catchments leads to calculating C values
Elements
Land Use | C
Approved Road | 0.8
Commercial "Longitudinal" | 0.7
Residence "D" | 0.5
Roads Pedestrians | 0.8
Table 1: Runoff coefficients for different land uses

## Slide 49
Figure 13: Land use for the 10.93-hectare area

## Slide 50
Figure 14: Anabta’s IDF curve modified from Nablus’s
Elements
Intensity (i)
We modified Nablus’s IDF curve to obtain an IDF curve for Anabta

## Slide 51
Time of concentration ()
The time of concentration is calculated for each catchment, using the Federal Aviation Administration (1970) equation:
Elements

## Slide 52
Figure 15: Sample calculation for Tc

## Slide 53
Elements
Outlet
We used 1 outlet in our project with a flow of 73054
Figure 16: Outfall flex table

## Slide 54
Elements
Conduits
A total of 85 conduits with diameters of 10”, 12”, 15”, 18”, 24”, and 30” were used for the network
Figure 17: Conduits

## Slide 55
Elements
Design Constraints
Design Constraint | Min.. Value | Max. Value
Slope | 1 % | 15 %
Cover | 0.80 m | 4.50 m/
Velocity | 0.90 m/s | 5.00 m/s
Table 2: Design constraints

## Slide 56
Results
Figure 18: Slope trend
Chart: Slope trend

## Slide 57
Results
Figure 19: Velocity trend
Chart: Velocity trend

## Slide 58
Results
Figure 20: Cover trend
Chart: Cover trend

## Slide 59
Profiles
Figure 22: Profile number 1
Figure 21: Profile number 2
Profiles 1 and 2 were taken in the following locations

## Slide 60
Profiles
Figure 23: Profile number 1

## Slide 61
Profiles
Figure 24: Profile number 2

## Slide 62
Profiles
Figure 25: Profile

## Slide 63
Conclusions and Recommendations
Conclusions
Q= 73054
85 catchments → 85 catch basins
The conduit diameters are 10”, 12”, 15”, 18”, 24”, and 30”
In our design we used inlets of type grate, with a 0.5 m width and 0.5 m length and for the structure, the width and length were 0.6 m and 0.6 m, respectively.

## Slide 64
Conclusions and Recommendations
Recommendations
Construction of storm water collection netwrok in Anabta
Cleaning the current culverts in Anabta
Rehabilitation of roads and maintianing a decent cross slope

## Slide 65
Any questions?
Thanks!

## Slide 66
References
[1] | "مقدمة عن المصادر المائية في فلسطين," سلطة المياه, 16 1 2018. [Online]. Available: http://www.pwa.ps/ar_page.aspx?id=NgKPUWa2695364496aNgKPUW.
[2] | "المياه الجوفية في الضفة الغربية," 17 1 2018. [Online]. Available: http://www.pwa.ps/ar_page.aspx?id=LuBJw9a2707737285aLuBJw9.
[3] | U.-W. D. P. o. A. a. C. a. W. S. a. S. C. Council, "The Human Right to Water and Sanitation".

## Slide 67
References
[4] M. N. Almasri, "Hydrology: Lectures," [Online]. Available: https://docs.google.com/viewer?a=v&pid=sites&srcid=ZGVmYXVsdGRvbWFpbnxoeWRyb2xvZ3ltbmF8Z3g6NDg0ZGQ3ZDJmZjBjODE5Nw. [Accessed 2019].
[5] "The Official Website of the State of Indiana," [Online]. Available: https://www.in.gov/dot/div/contracts/standards/dm-Archived/07%20Metric/Part%204%20Vol.%201/Ch%2029/Ch29.pdf. [Accessed 2019].
6] "Pipeline design consideration and standards," [Online]. Available: https://petrowiki.org/Pipeline_design_consideration_and_standards. [Accessed 2019].