## Slide 1
ChocoCup
Tamara AbuAisheh
Raya Break

## Slide 2
01 Introduction
02 The Motivation
03 The Problem & The Solution
04 Stages & Components
05 Challenges
06 Future Work
Overview

## Slide 3
Introduction

## Slide 4
The Motivation
Automatic Process
Hygienic
& Clean
Smart
System
Fast
& Fresh

## Slide 5
1. Manual work is Slow and Tiring
2. No quick Fresh Options
3. High Cost and Waiting Time
for Customization
The Problem

## Slide 6
The Solution
Automated, Customized ChocoCup Machine

## Slide 7
Stages
Input/Output Unit

## Slide 8
Website

## Slide 9
Stages
1. Cup Dispensing
The Hall Effect Sensor resets the System to the Home Position.
Then, the LDR detects the Cup Holder.
After that, the Cup is Dispensed.

## Slide 11
Stepper Motor
Nema 17
H-Bridge L298N
Hall Effect Sensor
Laser
LDR Module
Ultrasonic Sensor
Components

## Slide 12
Stages
2. Biscuits Layer Stage
The Biscuit is Dropped Directly into the Cup

## Slide 14
Stepper Motor
Nema 17
H-Bridge L298N
Laser
LDR Module
Components

## Slide 15
Stages
3. Piston Stage
The Pneumatic Piston will press the Biscuit into one Flat Layer

## Slide 17
Laser
LDR Module
Pneumatic Piston
Air Solenoid Valve
Components

## Slide 18
Stages
4. Melted Chocolate Stage
Chocolate is Melted using a Water Bath to stay Smooth and Shiny

## Slide 20
Laser
LDR Module
Servo Motor
1-Channel Relay
Temperature
Sensor DS18B20
Components

## Slide 21
Stages
5. Topping Stage
One of three Toppings will be Added:
Sprinkles, Pistachios or Chocolate Chips

## Slide 23
Laser
LDR Module
3 Servo Motors
Components

## Slide 24
Components
Arduino Mega 2560
Power Supply
Car Window Motor
4x4 Keypad
20x2 LCD
I2C
4-Channel Relay

## Slide 25
1. Melting the Chocolate at the Right Temperature
2. Adding the Right amount of each Ingredient
3. Designing a Special 3D-Mechanism for the Topping
stage to Deal with Different Sizes
4. Making sure each step works at the Right Time
without Delays or Overlaps
Challenges

## Slide 26
  Implement Automatic Cleaning System for better hygiene and faster reset
  Add more Flavor options for Biscuit, Chocolate and Toppings
  Include a Grinding Mechanism to prepare Fresh Biscuits instead of using pre-powdered ones
Future Work

## Slide 27
Thank You For Your Attention