## Slide 1: Redesign The Directorate of Education in "Hiwarra" –Southern Nablus.
Nablus – Palestine 2018.
An-Najah National University Faculty of Engineering & Information Technology Building Engineering Department
Prepared by:
Taher Eid
Akram Sha'er
Husny Khasati
Supervisor:
Eng. Narmin Al-Barq.

## Slide 2: LAYOUT
Introduction
Methodology
Architectural Aspects
Structural Aspects
Environmental Aspects
Electrical Aspects
Mechanical Aspects

## Slide 3: Introduction
After studying the plans of the Directorate of Education and our selection of the Directorate of Huwara we discovered that the building of the Directorate contains several functions and needs of spaces so it was the beginning of our thinking is creating spaces suitable for each section and on the other hand we tried to create an interactive environment inside the building and give the building a sense of stability as a government building

## Slide 4
Literature review
Mechanical Aspects
Environmental Aspects
Electrical Aspects
Structural Aspects
Architectural Aspects
Water Supply & Drainage
HVAC
Dialux Evo
Standards & codes
Standards & codes
Solar Systems
daylight
Acoustical
Design Builder
Dialux Evo
INSUL
Ecotect
Design Builder
Standards & codes
METHODOLOGY

## Slide 5: Architectural Design

## Slide 6
The site is located in Huwwara village in the south of Nablus city which is located on latitude of 32.2 north and longitude of 35.3 east.
Figure: Site location from GeoMOLG.
Site analysis

## Slide 7: The area of the land is (1512 m2), the contour lines are in that area from 509 m which is the highest region to 500m, so the slope in the site is (20%), As shown in the Figure
Figure: Site location and Area

## Slide 8
Figure: Section of site.

## Slide 9
It’s bordered from the west by (Albaladeh) street, (Alaeen) street from east and building with open spaces(green areas) from north and south, and it is located in an area within the government, it is also free from sources of environmental pollution that is making it a health-friendly, and adequate ventilation.
The time needed to reach the site from Huwwara city center is nearly 5 minutes. The previous Figures and the next Figure explain how to access to the site.
Figure: How to access to the site

## Slide 11: Plans

## Slide 15: elevation

## Slide 18
West elevation

## Slide 19: section

## Slide 21: Problems and solution
The area of book and requirement stories not enough.

## Slide 23: The total area for book & supplies stores in new plans is 214 m2

## Slide 24: The reception area is very small

## Slide 26: The location of the stores in the main façade and not taking into account the places of staff offices from the environmental side

## Slide 28: main staff room

## Slide 30: Rest area and privacy

## Slide 32: parking

## Slide 34: Un useless area

## Slide 35
Structural Design
.

## Slide 36
Modeling

## Slide 37
the Directorate of Education has 4 floor

## Slide 38: Structural Design
Codes and Standards:
ACI -318-11 for reinforced concrete structural design.
UBC -97 for earthquake design.
ASCE 7 2010 for load combinations
For the design of the structure and its elements ETABS , SAP and hand calculations were used .

## Slide 39: Structural Design
Design data:
Concrete strength, f’c=28 MPa for column.
Concrete strength, f’c=24 MPa for slab and beams .
Steel yield strength fy=420 MPa.
Bearing capacity for soil = 220 kN/m2

## Slide 40: Structural Design
Vertical Loads:
Load Type | spaces
Live Load (kN/m2 ) | 5 kN / m2
SID ( kN /m2 ) | 3.5 kN / m2

## Slide 41: Structural Design
Seismic Design data :
The city of structure is Nablus.
The seismic zone factor. Z=0.2.
The soil profile is type SB.
The acceleration seismic coefficient Ca=0.2
The velocity seismic coefficient Cv=0.2.
The Seismic importance factor is 1.
The structural design type is intermediate, R=5.5

## Slide 42: Sections Dimensions
Structural Element | Dimensions
Ribbed Slab | 25 cm thickness
Columns | (60X40) , ( 45 X 45 )
Beams | ( 70X25) , ( 50 X 25 ) , ( 35 X 70 )

## Slide 43: Verification of the model
Compatibility check
Equilibrium check
Internal force check

## Slide 44: Verification of the model
Compatibility check

## Slide 45: Verification of the model
Equilibrium Check
 | Live load ( kN) | SID (kN) | Dead load (kN)
Manual | 13390 | 16603.6 | 21628.76
By ETABS | 13119.7 | 16490.9 | 21192.2
% Error | 2.018671% | 0.678768% | 2.018424%

## Slide 46: Verification of the model
Internal force check
 | Manual | By ETABS | %Error
Column | 3745 kN | 3769.7 kN | 0.6%
beam | 1115.2 kN.m | 1072.6 kN.m | 3.9%
Span of the slab | 110.4 kN.m | 102kN.m | 7.8%

## Slide 47: Design checks
Period Check
0.49 < 0.56 sec
Drift Check
33mm < 36 mm
Deflection check
20mm < 40mm
Modal participating mass ratio check
0.93 > 0.90
Base shear check
3964kN > 3723kN
3818kN > 3723kN

## Slide 48: Slab Reinforcement

## Slide 49: Beams Reinforcement

## Slide 51: Columns Reinforcement

## Slide 53: Footing Reinforcement

## Slide 54: Shear Wall Reinforcement

## Slide 55: Stair Reinforcement

## Slide 56
Environmental Aspects

## Slide 57
Environmental Aspects
Environment & Orientation

## Slide 58
Shading at 8:00 in 15th Jul .

## Slide 59
Thermal
Exterior Wall
U-Value = 0.52 W/.K
Interior Wall
U-Value = 1.6 W/.K

## Slide 60
Thermal
Roof
U-Value = 0.368 W/.K
Glazing
U-Value = 1.49 W/.K
Double grey 3mm/13mm argon LOE (low emittance glass).

## Slide 61
Comfort Analysis

## Slide 62
Energy capacity in the building
 | Total Energy [kWh] | Energy Per Total Building Area [kWh/m2] | Energy Per Conditioned Building Area [kWh/m2]
Total Site Energy | 406208.48 | 267.76 | 273.40
Net Site Energy | 406208.48 | 267.76 | 273.40
Total Source Energy | 1004393.79 | 554.35 | 566.03
Net Source Energy | 1004393.79 | 554.35 | 566.03

## Slide 63
Heating & Cooling
 | District Cooling [kWh] | District Heating [kWh]
Heating | 0 | 188169.69
Cooling | 396693.13 | 0
Interior Lighting | 0 | 0
Exterior Lighting | 0 | 0
Interior Equipment | 0 | 0
Exterior Equipment | 0 | 0
Fans | 0 | 0
Pumps | 0 | 0
Heat Rejection | 0 | 0
Humidification | 0 | 0
Heat Recovery | 0 | 0
Water Systems | 0 | 3506.23
Refrigeration | 0 | 0
Generators | 0 | 0
Total End Uses | 396693.13 | 191675.92

## Slide 64
Daylight

## Slide 65: Electrical Aspects

## Slide 66: lighting aspect
The CIBSE (Charted red Institute of Building Engineers)
The table below shows the recommended lux for different spaces:

## Slide 67
Two simulated spaces in the ground floor.

## Slide 68: Luminaire selection :

## Slide 69: Plans
office plan.
Meeting hall plan.

## Slide 70: simulation Results for the office

## Slide 71: simulation Results for the Meeting hall

## Slide 72
Glare check

## Slide 75: Power and sockets distribution

## Slide 76
Distribution board for ground floor

## Slide 77: MECHANICAL ASPECTS

## Slide 78: Mechanical design
H-VAC System
Firefighting system
Water Supply System
Drainage System

## Slide 79
HVAC System.
VRF system selection units:
Outdoor units
Spilt and cassette indoor units

## Slide 80: Cooling load calculation
Floor | Load as designed(KW)
G.F | 95.21
1st floor | 98.61
2nd floor | 100.74
3rd floor | 102.2

## Slide 81
The required pipe diameter and length for the ground floor.

## Slide 82: HVAC system
Variable Refrigerant Flow (VRF) system

## Slide 83
Return and mechanical ventilation.

## Slide 84: Safety & Fire Fighting system

## Slide 85
Water supply design

## Slide 86
Drainage roof design

## Slide 87
Elevators
Car capacity is 1250kg and its speed 2m/s
RT = 90 sec.
One car
I =RT/N =90/1 =90 sec

## Slide 88: Acoustics Design
The STC for partition must =45 dB or more.

## Slide 89: The value of STC for external wall with window

## Slide 90: The IIC for ceiling

## Slide 91
Note : RT60 range for offices is (0.6 – 1.2)
Reverberation time
STATISTICAL ACOUSTICS - Zone 1 |  |  |  | 
 | TOTAL | SABINE | NOR-ER | MIL-SE
FREQ. | ABSPT. | RT(60) | RT(60) | RT(60)
------- | ------- | ------- | ------- | -------
63Hz: | 17.341 | 0.54 | 0.39 | 0.47
125Hz: | 13.708 | 0.67 | 0.47 | 0.6
250Hz: | 6.231 | 1.21 | 0.71 | 1.16
500Hz: | 3.641 | 1.5 | 1.02 | 1.47
1kHz: | 3.164 | 0.7 | 0.61 | 0.7
2kHz: | 4.276 | 0.42 | 0.4 | 0.42
4kHz: | 6.442 | 0.3 | 0.3 | 0.3
8kHz: | 6.004 | 0.13 | 0.13 | 0.13
16kHz: | 6.947 | 0.14 | 0.14 | 0.14

## Slide 92: Quantities and Survey
stage | Price
Architectural work | 1469275 NIS
structure work | 1743950 NIS
mechanical work | 484800 NIS
electrical work | 320600 NIS
total cost | 4018625 NIS
cost per m2 | 1497.81 NIS