## Slide 1
Al_Najah national university
Faculty of Engineering
Industrial Engineering Department
Haneen Abu Rasis Rabia Tahboosh
Sajeda Sarsoor Yasmeen Aqoobeh
Dr . Ayham Jaaron

## Slide 3
AL-Arz Company
From our humble begging in1950 , producing ice in order to cool water and store food at the time when electricity didn’t exist , Al Arz company has evolved to be the leader of frozen treats market in Palestine . Since its establishment by the late Mohammad Anabtawi in Nablus – Palestine , AL- Arz grew in to a successful producer of high quality extruded ice-cream products.
In 2007 , the company started its first step towards exporting, where Jordan was its first station. That was after it acquired the Palestinian quality certificate .
Tow years later, the company acquired the global food safety certificate HACCP. This achievement was a Palestinian industrial pride, since AL ARZ was the first company that acquires this certificate among the ice cream and dairy manufactures in Palestine and Jordan.
History of Al -Arz Company

## Slide 4
Maintenance
Any activity, such as tests, measurements, replacements, adjustments and repairs, intended to restore or retain a functional in a specified state in which the unit can perform its required function

## Slide 5: Types of Maintenance
Preventive maintenance
Corrective maintenance

## Slide 6: Maintenance Management System in AL-Arz Company
Sources of Data Collection
Data information was taken from Al-Arz company by this ways :
By making frequent visits to the factory and observe the process of maintenance.
By the manager of Research and Development Department (R&D).
By help from maintenance manager (Mechanical engineer).

## Slide 7
Flow Chart

## Slide 8
Turning point for maintenance management system in AL-Arz Company
The turning point that occurred due to this project is to shift maintenance management system in the factory from manually system to an integrated computerized system using the program " Microsoft office Access " , which led to saving time, effort and increase accuracy in the process of information storage and retrieval speed . Plant need for Computerized Maintenance to demonstrates the flow chart from start to finish or from the time of the failures until the system return to work again, explaining the steps and tools and spare parts used and the engineer in charge of maintenance process.
The turning point is to convert (MMS) to (CMMS)

## Slide 9: Performance Analysis

## Slide 10: Types of failures analysis:
This part talks about the types of failures (Mechanical, Electrical, general maintenance services, and Structural).
Type of failure with frequency:
This section shows the relation between each type of failure (Electrical, Mechanical, Structural, and general maintenance services) and their frequencies in general, and the relation between each type of failure with its frequency.

## Slide 11
نوع العطل | التكرارية
ميكانيكي | 107
كهربائي | 12
إنشائي | 3
خدمات عامه | 1

## Slide 12: Mechanical failures:
الفتره الزمنيه | التكراريه
1\1\10-28\2\10 | 20
1\3\10-30\4\10 | 34
1\5\10-30\6\10 | 16
1\7\10-31\8\10 | 16

## Slide 13: Electrical failure
الفتره الزمنيه | التكراريه
1\1\10-28\2\10 | 3
1\3\10-30\4\10 | 6
1\5\10-30\6\10 | 2
1\7\10-31\8\10 | 1

## Slide 14: Structural failure:
الفترة الزمنية | التكرارية
1\2\10-30\3\10 | 2
1\4\10-30\5\10 | 1

## Slide 15: Type of failure in machine with frequency

## Slide 16
اسم الماكنه | التكرارية
الشفاط | 3
ماكنه العيدان | 2
ماكنه التغليف | 17
البركه | 8
مضخه الشراب | 1
نفاش | 23
ماكنه الشوكلاته | 3
ماكنه الديليه هوير | 1
مضخه الزيت | 1
ماكنه الكاسات | 5
مضخه الشوكلاته | 1
مضخه الماء | 1
Mechanical failure (machine name with frequency).

## Slide 17: Electrical failure (machine name with frequency).
اسم الماكنه | التكرارية
النفاشه | 1
ماكنه التغليف | 1
خزان | 2
البركه | 1
ماكنه الشوكلاته | 2
مضخه الشوكلاته | 1

## Slide 18: Machine failure:
All machines, all kinds of failure and time of failure occurrence for each kind of failure
kind of failure for each machine with frequency:
This section shows the relation between all kind of failure for each machines and its frequency.

## Slide 19
الشفاط
العطل | التكرارية
صوت غير طبيعي | 2
كسر بستون | 1

## Slide 20
ماكنه التغليف
تغير السكاكين | 8
خلل بمجموعه سحب الورق | 2
تغير بيل | 3
تغير جنزير | 2
تغير عين | 1
خلل العجلات | 1
قطع قشط | 1
خلل في معايره | 1

## Slide 21: النفاشة
العطل | التكراريه
تسيل | 8
مشكله تبريد | 1
صوت اسفل النفاش | 2
بيل واللبدات | 12
عطل القشط | 1
عطل مضخه | 1
عطل بالحامل السكين | 1

## Slide 22: Period of failure time with frequency

## Slide 23
فترات زمنيه يحدث فيها العطل | التكرارية
1\1\10-28\2\10 | 2
1\3\10-30\4\10 | 1
الشفاط

## Slide 24: ماكنة التغليف
فترات زمنيه يحدث فيها العطل | التكرارية
1\1\10-28\2\10 | 4
1\3\10-30\4\10 | 8
1\5\10-30\6\10 | 3
1\7\10-31\8\10 | 3

## Slide 25: النفاشات
فترات زمنيه يحدث فيها العطل | التكرارية
1\1\2010-30\4\2010 | 10
1\5\2010-30\9\2010 | 5
1\10\2010-28\2\2010 | 5

## Slide 26: Results of analysis:
1-More failures in most time occur on Saturday because in Fridays there is no maintenance for the machines.
2-There are high differences of frequency from period to other because neglecting the documentation of all maintenance reports.
3-More failures are occur in packaging machine andالنفاشه""machine, because this two machine have the highest use in this company.
4-The highest frequency is in the period from (1\1\2010-30\4\2010) because this period are the beginning season (high production), and the machines work for long time in this period

## Slide 27
Recommendation :
1. Al -Arz company is highly advised the new model (CMMS) that can be easily managed by their managers and operators.
2. To Convert manual system of maintenance to computerized system.
3. It must be good documentations of maintenance report.
4. It must be a good contact between Managers and employees.