## Slide 1
Structural analysis and design for Al-Aqsa school in Jerusalem
By:
1. Faraj Ghanem.
2. Mohammad Fahmawi.
3.Qais Khalil.
Under supervision of:
Dr. Abdul Razzaq Touqan
Graduation Project II
2017

## Slide 2
1 Project description.
2 Seismic Design Parameters.
3 Check for Structural Irregularities.
4 Structural System Type.
5 Preliminary Evaluation.
.
6 Frame analysis by direct design method
.
7 Three Dimensional Structural Analysis.
8 ETABS Model Checks.
.
Outline

## Slide 3
Project Description
This school is located in Jerusalem.
Basement
First Floor
Mezzanine
Second, Third and Fourth Floor
This school consists of:

## Slide 4
Materials
Non Structural
Structural
Tile (𝛾 = 26kN/𝑚3 )
Block (𝛾 =12 kN/𝑚3 )
Plaster
(𝛾 = 23 kN/𝑚3 )
Concrete Mortar
(𝛾 = 23kN/𝑚3 )
Aggregate
(𝛾 =20 kN/𝑚3 )
Concrete
Reinforcement
steel

## Slide 5
The Codes used in this project are the following :
  ACI 318-14 (American Concrete Institute).
1
  IBC2015 (International Building Code).
2
  ASCE-7 (2010).
3
The Codes Used in This Project

## Slide 6
Live Load
First Floor and Mezzanine
(3 )
Classes
(3 )
Corridors
(4 )
Roof
(2 )
Super Impose Dead Load
Corridors and Classes
(4 .5)
Mezzanine
(4 )
First Floor
(3 )
Roof (2 )
Slab Own Weight (6)
Gravity loads
Weight of Brick Wall
(3 )

## Slide 7
Risk Category
Seismic Design Parameters

## Slide 8
Seismic Design Category (D)
SDS = 0.48
SD1= 0.32
SMS =
SS x Fa = 0.48
SM1 =
S1 x FV = 0.32
SS =
2.5 x Z
= 0.4
Fa = 1.2
Fv = 1.6
S1=
1.25 x Z
= 0.2
Seismic Zone Factor,
Z = 0.16
Site Class (C)
Importance Factor,
I = 1.25
Seismic Design Parameters

## Slide 9
Check for Structural Irregularities

## Slide 10
Horizontal Irregularities
In x-direction :
1a. Torsional Irregularity
1b. Extreme Torsional Irregularity

## Slide 11
Horizontal Irregularities
In y-direction :
1a. Torsional Irregularity
1b. Extreme Torsional Irregularity

## Slide 12
Horizontal Irregularities
3. Diaphragm Discontinuity Irregularity
2.Reentrant Corner Irregularity

## Slide 13
Horizontal Irregularities
4. Out-of-Plane Offset Irregularity.

## Slide 14
Horizontal Irregularities
5. Nonparallel System Irregularity

## Slide 15
Vertical Irregularities
1b. Stiffness-Extreme Soft Story Irregularity
1a. Stiffness-Soft Story Irregularity

## Slide 16
Vertical Irregularities
In x-direction :
In y-direction :

## Slide 17
2. Weight (Mass) Irregularity
Vertical Irregularities

## Slide 18
Vertical Irregularities
3. Vertical Geometric Irregularity
4. In-Plane Discontinuity in Vertical Lateral Force-Resisting Element Irregularity

## Slide 19
Vertical Irregularities
5a. Discontinuity in Lateral Strength–Weak Story Irregularity.
5b. Discontinuity in Lateral Strength–Extreme Weak Story Irregularity.

## Slide 20
After all the problems of irregularity in the building, a decision was made to change the architectural shape in order to avoid these.

## Slide 21
The new structure
The new plan for all stories
Area = 251.23 m2

## Slide 22
Preliminary Evaluation

## Slide 23
The selected system was two – way solid slab.
Selected slab system:
Slab

## Slide 24
Slab thickness calculated based on the critical span
ℎ Solid = = 0.285 𝑚 , take it 300mm.
Slab

## Slide 25
For all floors the Beam distribution is shown:
1
Beams distribution
Beams

## Slide 26
Beams
2
Beams dimensions
In Y-direction the critical beam is simply supported
In X-direction the critical beam is one end continuous

## Slide 27
In x-direction :
H beam = 6.98 /18.5 = 380 mm, take it 600 mm.
B beam = 6.98 / 20 = 350 mm, take it 400 mm.
Beams

## Slide 28
In y-direction :
H beam = 11.43/16 = 710 mm , take it 900 mm.
B beam = 11.43/(20 ) = 570 mm , take it 600 mm.
Beams

## Slide 29
Columns
For all floors the distribution is shown:
Columns distribution
1

## Slide 30
Columns
2
Dimension of column
The chosen column is that lies on the intersection of gridlines C9, which has a tributary area equal 33.41 Own weight of the column will be assumed to be 5% of the total load.
Pu = 1.05( ultimate dead loads + ultimate live loads)
= 1.05 × (2210.63 + 748.39) = 3106.97 kN
Assume:
ρ = 0.01 ,So As = 0.01 Ag
3106.97× 103 = 0.65 × 0.8 (0.85 × 24 (𝐴𝑔 − 0.01 𝐴𝑔)
𝑆𝑜, 𝐴𝑔 = 244914.91mm2
= 494.88 mm.
Use a square column with 500mm x 500mm.
+ 420 × 0.01 𝐴𝑔)

## Slide 31
Shear Walls
For all floors the distribution was:
Shear wall distribution

## Slide 32
Shear Walls
For all floors the distribution was: For axial capacity, from ACI318-14 code, the axial capacity of the wall is given by the following equation:
Pu on shear wall = load from slaps + own weight
Turbidly area for the shear wall = 3.345*9.9= 33.3
Load on slab = 16 kN /m.
Pu = 16*33.3*5 + 0.25*9.46*17.84*25
= 3774.54 kN.
Shear wall checks

## Slide 33
Shear Walls
∅𝑃𝑛 = 0.55∅𝑓𝑐′ 𝐴𝑔[1-]
Where:
K: Effective length factor from ACI 318-14 table 11.5.3.2, take K = 0.8.
Lc: Maximum vertical length of wall from center to center of joints. = 3.8 m
∅: 0.7.
𝑓𝑐′=24
h:wall thickness = 0.25 m .
Ag: cross section area = 9.96*1000*width of the wall(0.25) = 249,000
∅𝑃𝑛 = 0.7*0.55*24*0.25*9.96*1000(1-() = 19650 kN.
So Pu < ∅𝑃𝑛 … ok
Shear wall checks

## Slide 34
Three Dimensional Structural Analysis

## Slide 35
ETABS Model Checks
Compatibility
Drawing structural model
External equilibrium
Internal equilibrium
Slab shear
Fundamental period
Base shear by ELM
Structural system type
Mass participation ratio
Base shear by Response Spectrum
Slab deflection
Drift
Checks

## Slide 36
ETABS Model Checks
Drawing structural model
1

## Slide 37
2
ETABS Model Checks
Compatibility
All structural members are moving as one unit.

## Slide 38
Load type | Manual results (kN) | ETABS results (kN) | Difference %
Live | 4430.28 | 4432.66 | 0.05
Dead | 18229.76 | 18023.44 | 1.13
SD | 5623.44 | 5627.01 | 0.06
Wall | 2297.55 | 2297.99 | 0.02
3
ETABS Model Checks
External equilibrium
All loads on the structure and reactions are same.

## Slide 39
4.a
ETABS Model Checks
Internal equilibrium ( for frame )
Make a check on third floor slab for SD load (WSD = 4.5 kN/
By Hand:
Mo == = 359.48 kN.m
From ETABS:
Mo = + 177.2 = 349.55 kN.m
Difference % = 2.7 % < 10% then OK.

## Slide 40
4.b
ETABS Model Checks
Internal equilibrium ( for column)
Make a check on column(gridlines E7) for SD
By Hand:
P SD = W SD * Tributary area * No. of stories
P SD = (3* 33.41* 1) + (4.5* 33.41* 3)
+(1.5* 33.41* 1) = 601.38 kN
From ETABS:
P SD = 567.00 kN
Difference% = 5.6 % < 10 % then OK.

## Slide 41
Colors indicate that no shear value
in x-direction more than shear
capacity of slab.
ETABS Model Checks
5.a
Slab shear (V13)
ФVc =
=
= 159.2 kN/m

## Slide 42
ФVc = 159.2 kN/m
Colors indicate that no shear value
in y-direction more than shear
capacity of slab.
.
ETABS Model Checks
5.a
Slab shear (V23)

## Slide 43
Fundamental period
ETABS Model Checks
6
Code:
Ta = Ct
= 0.0466
= 0.623 sec
Upper limit of period = Cu*Ta
=1.4*0.623
= 0.872 sec
ETABS:
Fundamental period = 0.648 sec<0.872 sec

## Slide 44
Structural system type
ETABS Model Checks
7
Building frame system (special reinforced concrete shear walls).
R = 6
= 2.5
Cd = 5

## Slide 45
Base shear by ELM
ETABS Model Checks
8
By Hand:
V = Cs * W
Where: W: effective seismic wieght (Dead load
+ SD + Wall load) = 25948.41 kN
Cs : siesmic response coefficent = 0.10
V = 2594.84 kN
By ETABS:
V = 2505.95 kN
Difference % = 3 % OK

## Slide 46
Mass participation ratio
ETABS Model Checks
8
ASCE7-10 states ” The analysis shall include a sufficient number of modes to obtain a combined modal mass participation of at least 90 percent of actual mass in each of orthogonal horizontal directions of response considered by the model”.

## Slide 47
Base shear by Response Spectrum
ETABS Model Checks
9
Input data of Response Spectrum

## Slide 48
Base shear by Response Spectrum
ETABS Model Checks
9
Results of current dynamic analysis
Results of modified dynamic analysis

## Slide 49
ETABS Model Checks
10
Slab deflection
Make a check on fifth slab in critical panel.
Δ Allowable = L / 240 = 10540/240 = 43.92 mm
Δ Long term = ΔL+ (λ∞ × ΔD) + (λt × ΔSL)
= 38.2 mm < 43.92 mm
Thickness of slab is suitable.

## Slide 50
50
ETABS Model Checks
11
Drift
In x-direction :
In y-direction :

## Slide 51
Design of Structural Elements

## Slide 52
Structural Design
Beams
Slabs
Shear walls
columns
Footings
Stairs
Design

## Slide 53
Slabs Design
1
Flexural Capacity for slab:
∅M = As × 𝑓𝑦 × (d − )
Reinforcement Ratio of steel (𝜌):
𝜌 = 0.85𝑓𝑐′𝐹𝑦 (1-)
𝜌𝑚𝑖𝑛 = 0.0018.
The ultimate minimum moment in both direction X and Y
depth of slap (H)=300 mm
width of slap section (B)= 1000 mm.
effective depth of the slap (d) = 260 mm.
As min = 0.0018 x 1000 x 300 = 540 mm2
a = 540 × 4200.85 × 24 ×1000 = 11.18 mm.
∅M = = 57.7 kN.m
Slabs

## Slide 54
In x-direction :M11
For zone A : As = 5∅18mm.
For zone B : As = 7∅18mm.
Slabs

## Slide 55
Steel Detailing In x-direction
Slabs

## Slide 56
In y-direction :M22
Use the minimum area of steel (5Ф12mm) for the bottom and top steel in Y- direction.
Slabs

## Slide 57
Steel Detailing In y-direction
Slabs

## Slide 58
Shear Wall
  We use = Ф10/200 mm.
Steel Detailing
3

## Slide 59
Columns
Columns distribution

## Slide 60
Code ACI318-14 permits to neglect the slenderness in braced columns if :
≤ 34 – 12
≤ 40
Where:
K: the effective length factor.
Lu: the unsupported height.
r: the radius of gyration which equals to , where I is the moment of inertia and A is the area of the section.
M1: Smaller factored end moment on column.
M2: larger factored end moment on column.
Slenderness check
Columns

## Slide 61
Check slenderness on column C5 in two direction
Assume k=1
Lu = 4m
r = 0.3h = 0.3*0.5 = 0.15m
= = 26.67
36.4 ≤ 34 – 12* = 40.67
≤ 40
36.4 ≤ 34 – 12* = 42.30
≤ 40
Neglect slenderness.
Slenderness check
Columns

## Slide 62
Reinforcement percentages
All values are permitted as ACI318-14.
Columns

## Slide 63
ACI requirements of columns
Columns

## Slide 64
Summery of columns
Columns

## Slide 65
Detailing of column group C-1
Columns

## Slide 66
1
Beams Design
The negative ultimate moment on the section = 726.7 kN.m.
The positive ultimate moment on the section = 598.6 kN.m.
The ultimate shear force on the section = 683.2 kN/m.
ρ = (1-
ρminimum = 0.0033
Top area of steel = 5 Ø 25 mm.
Bottom area of steel = 4 Ø 25 mm.
Stirrups Ø 10 mm were used.
Beams

## Slide 67
1
Beams Design
The ultimate shear force (Vu) obtained from ETABS = 683.2 kN/m.
By calculating the concrete capacity from :
Vu > ФVc, so a shear reinforcement is required that calculation as the following:
Vs
683.2 = 0.75 × ( 305 +Vs )  Vs = 378.2 kN/m.
By substituting in
= minimum (0.5 /mm).
Stirrups Ø 10 mm were used.
Beams

## Slide 68
Beams
2
Beams Detailing

## Slide 69
Beams
2
Beams Detailing

## Slide 70
1
Shear wall design
Internal forces in shear wall:
Vu = 1064 kN
Mu = 7913.2 kN
Pn = 4972 kN
Shear Wall

## Slide 71
= ρl × wall thickness = 0.0025 × 250 = 0.625 mm2 / mm.
* S max = 450 mm.
For two curtains (layers) of reinforcement with Ø 10 mm:
== 0.625 , So S = 251.2 mm, ok.
use 2Ф10/250mm.
For vertical shear reinforcement:
Shear Wall

## Slide 72
= ρt × wall thickness = 0.0025 × 250 = 0.625 mm2 / mm.
S max = 450 mm.
For two curtains (layers) of reinforcement with Ø 10 mm:
= 2∗𝐴𝑟𝑒𝑎 𝑜𝑓 𝑏𝑎𝑟𝑠 = = 0.625, So S = 251.2 mm, ok.
use 2Ф10/250mm.
For horizontal shear reinforcement:
Shear Wall

## Slide 73
Special boundary elements are needed if the stress σ > 0.2 f'c
σ = 0.2 x 24= 4.8 MPa.
To compute stress from σ = + Where:
I: Moment of inertia equal = = 2.05 × mm2
C: Equal 0.5 × Lw = 0.5*9960 = 4980 mm
So, σ = + = 3.89 Mpa. < 4.8 MPa, oK.
Therefore, there is no need for boundary elements.
Shear Wall
Special boundary elements check.

## Slide 74
.
For area of steel = Ф10/250 mm the interaction diagram shown in the figure .
The point intersection of ФPn and ФMn is within the curve so use Ф10/250 mm
Steel Check
2
Shear Wall

## Slide 75
Mat Footing
Single
Footing
Combined Footing
Piles
Wall
Footing
Design of footing

## Slide 76
Footing
Mat Footing was selected
Allowable bearing pressure is small q all = 200 kN /.
Area of single footings and wall footings in the base is more than half ground floor area.
Required area of footing =
Required area of footing = = 152.8
Area of basement = 277.31
Percentage between required area of footing and area of basement equals 0.55, which is greater than 0.50.

## Slide 77
Design of footing

## Slide 78
Pressure under footing check
σ max = 190.8 kN/
Qallowable = 200 kN/>190.8 kN/OK
Design of footing

## Slide 79
Punching shear check
ФVcp
ФVcp = 2931 kN
Vup = Pu – A1 * σult
= 4104.3 – (1.27 *201.94)
= 3847.84 kN > 2931 kN, Not OK.
Increase thickness to 800 mm
ФVcp = 4037 kN > 3847.84 kN, OK.
Design of footing

## Slide 80
Design of footing
Shear V13 check
ФVc =
=
= 447 kN/m
Vu13 = 389.91 kN/m < 447 kN/m
Thickness is suitable in this direction.

## Slide 81
Shear V23 check
ФVc = 447 kN/m
Vu23 = 404.69 kN/m < 447 kN/m
Thickness is suitable in this direction.
 No need for shear reinforcement.
Design of footing

## Slide 82
Design mat footing (M11)
Other values are minimum steel.
min = 0.0018
As min = 0.0018 *1000*800
= 1440 /m (6Ø18/m)
Design of footing

## Slide 83
Design mat footing (M22)
Other values are minimum steel.
min = 0.0018
As min = 0.0018 *1000*800
= 1440 /m (6Ø18/m)
Design of footing

## Slide 84
Section A-A in mat footing
Design of footing

## Slide 85
Design of stairs
Check deflection
Check shear
Thickness of stair = 200 mm
Design moment
M max = 27 kN.m
ρ = 0.00292 > ρmin
As = 0.00292 *1000*170
= 500 /m
Use 4Ø 14 /m
And so on.

## Slide 86
Longitudinal section
Design of stairs

## Slide 87
Thank you