## Slide 1
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project (2)
Structural analysis and design of
Balata health center
Under supervision of Dr. Imad Al-Qasem
By Kareem Kamal

## Slide 2
Outlines
Introduction
Architectural view
Structural system
Preliminary design
3D structural analysis and design
Design of columns
Design of footings
Drawings

## Slide 3
Introduction

## Slide 4
Project description
BALATA HEALTH CENTRE is one of the projects that are recently constructed in the east area in Nablus. This building consists of ground floor, top four floors, reservoir floor, electrical room and staircase.
Floor | Area (m2) | Height (m) | Use of floor
Ground | 609.6 | 3.70 | Receptions and Medical multi-uses
First | 592.1 | 3.64 | Medical multi-uses
Second | 593 | 3.64 | Medical multi-uses
Third | 610 | 3.64 | Medical multi-uses
Fourth (roof) | 274.7 | 3.9 | Meetings, Training and storing
Total | 2679.4 | 18.52 | -

## Slide 5
Structural materials
Concrete
Property | Value
Compressive strength of concrete, (f’c) | 25 Mpa
Modulus of elasticity, (Ec) | 23.5*103 Mpa
Unit weight of plain concrete, (γ) | 23 KN/m3
Unit weight of reinforced concrete, (γ) | 25 KN/m3
Reinforcement steel
Property | Value
Yield strength (fy) | 420 Mpa
Modulus of elasticity, (Ec) | 2.04*105 Mpa
Non-structural elements: Aggregates, Block, Masonry stone, Tiles, Plaster, Concrete mortar

## Slide 6
Soil properties
The soil in the site area is mainly composed of layers of marlstone and clay where footings shall be laid on natural excavated ground.
The allowable bearing capacity of the soil based on the nature of the soil in the site is 200 KN/m2.

## Slide 7
Gravity loads
Dead load
The own weight of structural members
Live load
Floor | Live load (KN/m2)
Ground | 4.79
First | 4.79
Second | 4.79
Third | 4.79
Fourth | 4.79
Roof | 6

## Slide 8
Superimposed dead load
𝑊𝑆𝐷 = 𝑊 𝑡𝑖𝑙𝑒 + 𝑊 𝑚𝑜𝑟𝑡𝑎𝑟 + 𝑊𝑓𝑖𝑙𝑙 +𝑊 𝑝𝑙𝑎𝑠𝑡𝑒𝑟𝑖𝑛𝑔+𝑊𝑝𝑎𝑟𝑡𝑖𝑡𝑖𝑜𝑛𝑠
For partitions, Reinforced block of 10 cm thickness and 25 KN/m3 in addition to plaster will be used.
WSD = 6.23 KN/m2

## Slide 9
Codes and standards
ACI 318-11
Building code requirements of structural concrete and commentary.
IBC2012
For seismic design.

## Slide 10
Architectural view
( Post modern style)

## Slide 11
Southern elevation

## Slide 12
Northern elevation

## Slide 13
Eastern and western elevations

## Slide 14
Structural system

## Slide 15
Solid VS Ribbed
Solid slab is better for seismic design later and has thinner thickness.
Moreover.
One way VS Two way
Two way has larger beams significantly so one way is better
The choice is One-way Solid slab

## Slide 16
Preliminary design

## Slide 17
Plan view

## Slide 18
Slab strips and beams distribution
For floors

## Slide 19
For roof

## Slide 20
Slab
Floors
Roof

## Slide 21
 Use h = 0.2 m
Wu (floor) = 21.14 KN/m2
Wu (roof) = 23.08 KN/m2
WD = 5 KN/m2
Shear check
Floor (strip 1)  Vu = 59.33 KN < = 100 KN
Floor (strip 2)  Vu = 60.25 KN < = 100 KN
Roof (strip 1)  Vu = 66.64 KN < = 100 KN
Roof (strip 2)  Vu = 63.84 KN < = 100 KN
No need for shear reinforcement

## Slide 22
Flexural design
For floors (by take strip 2 as critical)
Mu+ = 34.55 KN  = 0.0037  As = 592 mm2 > Asmin
Mu- = 51.3 KN  = 0.0056  As = 896 mm2 > Asmin
use 6Ø12/m bottom steel and 5Ø16/m top steel
For roof (by take strip 2 as critical)
Mu+ = 40.95 KN  = 0.00442  As = 707 mm2 > Asmin
Mu- = 47.33 KN  = 0.0051  As = 816 mm2 > Asmin
use 5Ø16/m bottom steel and 6Ø16/m top steel

## Slide 23
Interior beams
Secondary beams
Exterior beams of floors
Exterior beams of roof
Dimensions
(mm)
Beams

## Slide 24
Floor’s
Interior
Roof’s
Exterior
Floor’s
Secondary

## Slide 25
Flexural design for floors
Floor | Interior | Exterior | Secondary
Mu+ (KN) | 497.26 | 230.98 | 51.81
p | 0.00296 | 0.00259 | 0.00365
As (mm2) | 1961 | 1343 | 373
As > As min | No | No | yes
As used (mm2) | 2160 | 1728 | 373
Bottom steel | 7Ø20mm | 6Ø20mm | 5Ø10mm
Mu- (KN) | 515.52 | 327.98 | 67.87
p | 0.00833 | 0.0081 | 0.00546
As (mm2) | 2300 | 1750 | 557
As > As min | yes | yes | yes
As used (mm2) | 2300 | 1750 | 557
Top steel | 8Ø20mm | 6Ø20mm | 5Ø12mm

## Slide 26
Roof | Interior | Exterior | Secondary
Mu+ (KN) | 575.14 | 157.51 | 49.51
p | 0.00344 | 0.00375 | 0.00348
As (mm2) | 2279 | 1224 | 355
As > As min | yes | yes | No
As used (mm2) | 2279 | 1224 | 360
Bottom steel | 8Ø20mm | 6Ø16mm | 5Ø10mm
Mu- (KN) | 638.08 | - | 83.02
p | 0.0098 | - | 0.00678
As (mm2) | 2705 | - | 692
As > As min | yes | - | yes
As used (mm2) | 2705 | - | 692
Top steel | 9Ø20mm | - | 7Ø12mm
Flexural design for roof

## Slide 27
Shear design
Floor | Interior | Exterior | Rectangular
Vu (KN) | 472.35 | 301.12 | 85.35
Vs (KN) |  |  | 
Av/s (mm2/mm) | 1.38 | 1.33 | 0.2  use 0.25
S (mm) | 164 | 170 | 904
Smax (mm) | 345 | 270 | 170
S used (mm) | 150 | 150 | 150
Floor | Interior | Exterior | Rectangular
Vu (KN) | 472.35 | 301.12 | 85.35
Vs (KN) |  |  | 
Av/s (mm2/mm) | 1.38 | 1.33 | 0.2  use 0.25
S (mm) | 164 | 170 | 904
Smax (mm) | 345 | 270 | 170
S used (mm) | 150 | 150 | 150
Roof | Interior | Exterior | Rectangular
Vu (KN) | 558.31 | 163.64 | 
Vs (KN) |  |  | 
Av/s (mm2/mm) | 1.76 | 0.46 | 0.26
S (mm) | 128.41 | 491 | 870
S max (mm) | 345 | 170 | 170
S used (mm) | 125 | 150 | 150
Roof | Interior | Exterior | Rectangular
Vu (KN) | 558.31 | 163.64 | 
Vs (KN) |  |  | 
Av/s (mm2/mm) | 1.76 | 0.46 | 0.26
S (mm) | 128.41 | 491 | 870
S max (mm) | 345 | 170 | 170
S used (mm) | 125 | 150 | 150
Vc = 230 KN
Vs max = 920 KN
= 0.33
Øs = 10 mm

## Slide 28
3D Structural analysis and design

## Slide 29
3D model

## Slide 31
Material

## Slide 32
Sections

## Slide 34
Modifiers
Slab
Column
Beam
Shear wall

## Slide 35
Gravity loads

## Slide 36
Seismic loads
Ss = 2.5*Z = 0.5
S1 = 1.25*Z = 0.25

## Slide 37
The site soil classification is D
Fa = 1.4
Fv = 1.9
SMS = Fa * Ss = 0.7
SM1 = Fv * S1 = 0.475
SDS = SMS = 0.7
SD1 = SM1 = 0.475

## Slide 38
The risk category = III
I = 1.25

## Slide 39
Seismic design category is D.
Reduction factor = 3
( ordinary reinforced concrete moment frames)

## Slide 40
Response spectrum

## Slide 41
Scale factor = (I/R) * g
= (1.25/3)*9.81  4.0875

## Slide 43
Design load combination and strength check
1.4D
1.2D+1.6L
1.3D+L+Ex
1.3D+L+Ey
0.8D+Ex
0.8D+Ey
Element | Width (m) | Depth (m)
Floor’s secondary beam | 0.4 | 0.7
Roof’s secondary beam | 0.4 | 0.7
Roof’s interior beam | 0.4 | 1
New dimensions were used. So, there were no red elements and all rebar percentages were within the allowable ranges.

## Slide 44
Checks
Compatibility
( T= 0.23724 )

## Slide 45
Equilibrium
Wdead = Wslab + Wbeam + Wcolumn + Wshear wall
= 12758 + 6673 + 2656 + 5880
= 27967 KN
Wlive = 12529 KN
WSD = 14244 KN
Load type | Hand result (KN) | SAP result (KN) | Differences%
Dead | 27967 | 29010 | 3.73%
SID | 14244 | 13964 | 1.97%
Live | 12529 | 12307 | 1.77%

## Slide 46
Stress-strain relationship
Difference = 1.97% < 10%
M 3D = 33.87
M 1D = 34.55
For slab

## Slide 47
For beam
M avg 3D = 565.5
M avg 1D = 524.39
Difference = 7.84% < 10%

## Slide 48
Deflection (serviceability)
Δ (total dead) = 5.47 mm
Δ (live load) = 2.18 mm

## Slide 49
No compression steel (ρcompression = 0)
Assume 50% sustained live load
, since we assumed that the live load will sustained.
(such that ρ’ is the compression steel ratio, T is a multiplier for long term deflection)
From the figure at time 5 years (60 months), T = 2
 = 2
Δ long-term = (1.5*2.18) + (2*5.47) = 14.21 mm
Length of largest span of slab = 4.65 m
The allowable deflection for all sustained load = L/240 = 4650/240 = 19.38 mm
19.38 > 14.21

## Slide 50
Modal mass participation ratio check
At 100 modes, the X and Y arrived nearly equal percent (67%) which less than 90% and the value of 90% is reached at 500 modes. Moreover, the structure has a lot of shear walls around and internal reinforced partitions so it will not be able to move in X or Y and it is not required to get 90% so I will use 12 modes only. The fundamental mode will be in Z direction.

## Slide 51
Design of Columns

## Slide 52
Columns grouping
columns were classified as groups according to the suggestions of architectural engineer.
Group ID | Max, Pu (KN) | Columns ID
C1 | 1732 | 1,2,3,4,5,6,7,8,9,10,11
C2 | 2032 | 12,13,14,15,16,17,18,23,27,28,32
C3 | 2615 | 24,25,30,31
C4 | 664 | 19,20,21,22

## Slide 53
Column design
Slenderness check 
K= 0.8 (from tables) , L= 3.4 m , r = 0.09 , M1 = 0.4 , M2= 6.7
30.22 < 33.28
so it is short column and neglect slenderness.
Steel ratio ρ = 1% (minimum)
, = 0.8
Asmin= 1% * Ag
Required stirrups spacing according to ACI318-08 is the minimum of:
S≤ 16 db
S≤ 48 ds
Lest dimension of column

## Slide 54
concrete cover = 4cm stirrups of Ø10mm
Group ID | Critical column # | Pu (KN) | Dimension (mm) | Ag (mm2) | As (mm2) | Reinforcement | Ties
1 | 9 | 1732 | 300*600 | 180000 | 1800 | 8Ø18mm | 2Ø10/250mm
2 | 17 | 2032 | 300*600 | 180000 | 1800 | 8Ø18mm | 2Ø10/250mm
3 | 24 | 2615 | 300*1150 | 345000 | 3450 | 18Ø16mm | 3Ø10/250mm
4 | 20 | 664 | 300*500 | 150000 | 1500 | 8Ø16mm | 2Ø10/250mm

## Slide 55
Group 1+2
Group 3
Group 4

## Slide 56
Interaction diagram check
The interaction diagram of column (C24) was drawn (taking the values of M33 vs Pu from SAP)
Moment and axial load on the column are 6.7 KN.m and 2615 KN respectively.
Interaction diagram of column shows that the column section was not economic and that because of large concrete section and restriction on the dimensions from A/E and owner as mentioned before.

## Slide 57
Design of Footings

## Slide 58
Single footings area needed < 50%*Total area of ground floor
 No need for full mat foundation

## Slide 59
Single footings F1&F2
Af = Pservice / qall
Wide-beam shear (one-way shear)
Vu = ØVc
B0 = 2(C1+d) + 2(C2+d)
ꞵ = long column side / short column side
αs= 40 (interior)
h = d + cover

## Slide 60
As = ρ * b * d
As,shrinkage(min) = ρshrinkage * b * d
Steel percentage (ꝭ) =
Group ID | Critical column # | Ps (KN) | Pu (KN) | Dimensions (m) | thickness (m) | Reinforcement
1 | 17 | 1495 | 2032 | 2.75*2.75 | 0.55 | 1Ø16mm/150mm
2 | 24 | 2012 | 2615 | 3.2*3.2 | 0.6 | 1Ø18mm/150mm

## Slide 61
F2 and column 24 were taken as critical in SAP design
9.97 mm < 10 mm
Maximum soil pressure = 200 KN/m2
Qu = reaction / mesh area
= 12/0.0625 = 192 KN/m2

## Slide 62
Vu = 866/3.2 = 271 KN/1m
= 312.5 KN
Vu < ØVc
Vu,p = 686/3.2 = 215 KN/1m

## Slide 63
Mu = {(830+696)/2}/3.2 = 238.44 KN.m/m
Steel percentage (ꝭ) = = 0.00258
As = ρ * b * d
= 0.00258 * 1000 * 500 = 1290 mm2/m
As,shrinkage(min) = ρshrinkage * b * d
= 0.0018 * 1000 * 500 = 900 mm2/m
Astotal = 1290 * 3.2 = 5031 m2
Use As = 20Ø18 mm (bottom steel)

## Slide 65
Longitudinal mat foundation 1&2
Sum (Px*x) = Sum (Px) * X  X
L = 2(X+b1/2)
Af = P/qall
B = Af/L
Vu = ØVc
Vu,p = Pu – qu*A1
B0 = 2(C1+d) + 2(C2+d)
ꞵ = long column side / short column side
h = d + cover

## Slide 66
Mu = from SAP
Steel percentage (ꝭ) =
As = ρ * b * d
 | B | L | d | h | Bottom steel | Top steel | Transverse steel
LMF1 | 4.75 m | 12 m | 0.3 m | 0.35 m | 1Ø25mm /100mm | 1Ø25mm /100mm | 1Ø12mm /250mm
LMF2 | 7 m | 5.5 m | 0.3 m | 0.35 m | 1Ø16mm /200mm | 1Ø32mm /125mm | 1Ø25mm /100mm

## Slide 68
Mat foundation 1&2
P = Sum (p)
Sum (Px*x) = Sum (Px) * X  X
Eccentricity in X direction (Ex) = X –{(c/c)/2}
Sum (Py*y) = Sum (Py) * Y  Y
Eccentricity in Y direction (Ey) = Y –{(c/c)/2}
Mx = P * Ey
My = P * Ex
Check compression < allowable bearing capacity
Check No tension

## Slide 69
Assume d
Vu,p = Pu*load factor
B0 = 2(C1+d) + 2(C2+d)
ꞵ = long column side / short column side
h = d + cover

## Slide 70
Wide-beam shear check
Vu= 3330 KN
= 3900 KN > Vu
Deflection = 9.75 mm < 10 mm
qu=195 KN/m < 200 KN/m

## Slide 71
Values of M11 and M22 are near to each other so, Mu = 1.4(8460/12) = 987 KN.m will be used for X and Y directions design.
Steel percentage (ꝭ) =
As = ρ * b * d
Same procedure for Mat2

## Slide 72
 | B | L | d | h | Reinforcement
MF1 | 12 m | 12 m | 0.52 m | 0.6 m | 1Ø32mm/125mm For Top and Bottom in X and Y directions
MF2 | 12 m | 8.4 m | 0.32 m | 0.4 m (Use 0.6 m) | 1Ø32mm/75mm For Top and Bottom in X and Y directions

## Slide 75
Drawings samples

## Slide 76
Main beam 8
Connection between column group 1 and main beam 3

## Slide 77
Slab of ground, first and second floors

## Slide 78
Shear walls
Stairs

## Slide 79
THANK YOU