## Slide 1: Al Baidar Cultural Center
An-Najah National university Building Engineering Department
Prepared by :
Ala’ Ismail
Issa Obaid Muhammad Tanbouz
Supervisor :
Eng. Hasan Mathar

## Slide 2: The Outlines
Architectural design
Structural Design
Environmental Design
Cost & Quantity
Electro mechanical Design
Conclusion

## Slide 3
Location and Site Analysis
Architectural Plans
Elevations and Sections
Architectural Design

## Slide 4: Architectural Design

## Slide 6: Location and Site Plan
Al Baidar Cultural center is located in Nablus city of distance 530 m east from the center of the city. The area of the land 8700 and it located on 430m above of see level in Al-Haddadin Street.

## Slide 7
Site Plan After
Site Plan Before
Site Plan with Analysis:
Exit
intrance
traffic movement

## Slide 8
Site Analysis
Sun Path in Summer
Wind Direction
Sound Level
80 db
81 db
78db
78 db
75 db
63 db
56 db
65 db
68 db
76 db

## Slide 9
Basement floor before
Basement floor after
Architectural Plans

## Slide 10
Ground Floor Before
Ground Floor After

## Slide 11
First Floor Before
First Floor Before

## Slide 12
Second Floor Before
Second Floor Before

## Slide 13
Third Floor Before
Third Floor Before

## Slide 14: Elevations
Before
After

## Slide 15: Sections
Before
After

## Slide 16
Day Light
Over Shadowing
Thermal Comfort
Environmental Aspects

## Slide 17: Daylight:
First floor after modification
First floor Before modification

## Slide 18: Overshadowing :
In winter at 11AM_21. January
In winter at 1PM_21. January

## Slide 19: Thermal Comfort:
Component | U-value (W/m2 .k)
External wall | 0.375
Roof | 0.26
Glass (Double) | 0.923
External Wall Section
Roof Section

## Slide 20
Comfort Hour
Design capacity (W/m²) | Rating
20-25 | High efficient
26-40 | Good efficient
41-60 | Efficient
61-80 | accepted
Above 80 | Fail( consumes energy)
Cooling Load/floor area (W/m2) | Space | Floor No. | Block No.
35.7 | Reception | G.F | Block (1)
64.2 | Administration |  | 
21.7 | Multipurpose |  | 
37.8 | Library | F.F | 
37.7 | Reception |  | 
43.5 | Cafeteria | S.F | 
37.3 | Kitchen |  | 
44.9 | Cafe | TH.F | 
25.7 | Gallery | G.F | Block (2)
39.2 | Classrooms | F.F | 
42 | Computer room |  | 
45.1 | Corridor |  | 
18.2 | Lobby for theatre | B.F | Block(4)
17.4 | VIP room |  | 
33.7 | North artist rooms |  | 
37.3 | North dressing rooms |  | 
33.7 | South artist rooms |  | 
33.7 | North dressing rooms |  | 
37.3 | South dressing rooms |  | 
65.6 | Corridor |  | 
51.2 | Music rooms | G.F | 
38.5 | Lobby for theatre |  | 
28.6 | Theatre |  | 
62.8 | Stores |  | 
40 | Meeting room | F.F | 
972.8 |  |  | Total

## Slide 21
Cheeks & Design
Detailing
Structural Aspects

## Slide 22: Codes:
ACI-318-14 for reinforcement concert design.
UBC-97 for earthquake design.

## Slide 23: Blocks.
The building divided to four blocks.
Block No1.
Block No2.

## Slide 24: Blocks.
Block No3.
Block No4.

## Slide 25: Design data:
LODAS:
Material:
- Concrete strength
- steel yield strength
Cobiax _(52*52*36) cm.
_(52*52*56) cm.
soil:
Bearing capacity of the soil .
LOADS |  | 
Block No. | LIVE LOAD (Kn/SM) | SID (kN/SM)
Block 1. |  | 
- Floors. | 4.8 | 4
-Stair case. | 2.5 | 2.5
Block 2. |  | 
- Floors. | 4.8 | 4
Block 3. |  | 
- Floor. | 6 | 4
-Ramp. | 4 | 4
Block 4. |  | 
- Floors. | 4.8 | 4
-Roof of theater. | 4.8 | 5
-Amphitheater slab. | 5 | 5
Loads.

## Slide 26: Design data:
Seismic factor:
Seismic zone factor UBS-97
seismic factor
Seismic factor |  | 
The location of the building in Nablus city. |  | 
Seismic zone factor | Z | 0.2
Soil profile |  | SD
Acceleration seismic coefficient | (Ca) | 0.28
Velocity seismic coefficient | (Cv) | 0.4
Seismic importance coefficient | (Ι) | 1
Structure design type |  | Building frame system -shear wall-concret
Over strength factor | (R) | 5.5

## Slide 27: checks:
Compatibility check:
Block No2.
Block No1.

## Slide 28: check:
Compatibility check:
Block No4.
Block No3.

## Slide 29: check:
Equilibrium check:
The %of the error in equilibrium check must be less than 5%.
Equilibrium check |  |  | 
blocks | Value of load (kN) |  | error
Block 1 | Etabs (V16) | manual calculated | % of error
Dead load | 55839.3612 | 55232.2841 | 1.0871849
Live load | 17684.8872 | 17827.23 | -0.804884
SID laad | 18757.8694 | 18968.93 | -1.125184
Block 2 | Etabs (V16) | manual calculated | % of error
Dead load | 25717.75 | 25468.5 | 0.969175
Live load | 9224.875 | 9256.9 | -0.347159
SID laad | 9104.732 | 9037.6 | 0.7373309
Block 3 | Etabs (V16) | manual calculated | % of error
Dead load | 24713.84 | 24670.6 | 0.1750
Live load | 9593.856 | 9593.38 | 0.0050
SID laad | 6825.718 | 6825.3 | 0.0061
Block 4 | Etabs (V16) | manual calculated | % of error
Dead load | 61300.76 | 59969.2 | 2.1722
Live load | 13686.79 | 13686.76 | 0.0002
SID laad | 18987.92 | 18963.36 | 0.1293
Stress-Strain check:
The %of the error in stress strain check must be less than:
10% of column.
25% for beam and slab in two-way system.
5% for beam and slab in one-way system.
Stress strain check |  |  |  | 
blocks |  | Value of load (kN) |  | error
Block 1 | type of load | Etabs (V16) | manual calculated | % of error
Column | ultimate | 1069.18 | 1058.79 | 0.97
Beam | live | 89.5 | 67.1 | 25.03
two way slab | live | 128.5 | 105.3 | 18.05
Block 2 |  | Etabs (V16) | manual calculated | % of error
Column | ultimate | 2099.53 | 2013.66 | 4.089963
Beam | live | 344 | 290 | 15.69767
Two-way slab | live | 242 | 201.88 | 16.57851
Block 3 |  | Etabs (V16) | manual calculated | % of error
Column | ultimate | 2501.3 | 2472.72 | 1.1426
Beam | live | 254 | 241.1 | 5.0787
two-way Slab | live | 260 | 292.8 | -12.6154
Block 4 |  | Etabs (V16) | manual calculated | % of error
Column | ultimate | 539.8 | 578.8 | -7.2249
Beam | live | 132 | 138 | -4.5455
one-way Slab | live | 50.2 | 48.7 | 2.9880

## Slide 30
Seismic Design

## Slide 31: Seismic check:
  Period check:
  Block 1.
T manual= 0.461 sec.
Tx Etabs =0.41 sec.
Ty Etabs =0.35 sec.
  Block 2.
T manual= 0.31 sec.
Tx Etabs =0.295 sec.
Ty Etabs =0.377 sec.

## Slide 32: Seismic check:
  Period check:
  Block 3.
T manual= 0.23 sec.
Tx Etabs =0.126 sec.
Ty Etabs =0.08 sec.
  Block 4.
T manual= 0.46 sec.
Tx Etabs =0.41 sec.
Ty Etabs =0.39 sec.

## Slide 33: Seismic check:
  Mass partition check:
  The summation of Ux and Uy must bee reach 90%.
  Block 1.
  Need a 31 mode.
  Block 2.
  Need a 15 mode
Case | Mode | Period | UX | UY | UZ | Sum UX | Sum UY
 |  | sec |  |  |  |  | 
Modal | 1 | 0.42 | 0.111 | 0.3787 | 0 | 0.111 | 0.3787
Modal | 2 | 0.377 | 0.1843 | 0.1984 | 0 | 0.2953 | 0.577
Modal | 3 | 0.266 | 0.1772 | 0.0217 | 0 | 0.4725 | 0.5988
Modal | 4 | 0.151 | 0.0018 | 0.1785 | 0 | 0.4744 | 0.7772
Modal | 5 | 0.127 | 2.25E-05 | 0.0006 | 0 | 0.4744 | 0.7778
Modal | 6 | 0.114 | 0.0876 | 0.0888 | 0 | 0.562 | 0.8667
Modal | 7 | 0.094 | 0.1532 | 0.0178 | 0 | 0.7152 | 0.8845
Modal | 8 | 0.09 | 0.0728 | 0.028 | 0 | 0.7881 | 0.9125
Modal | 9 | 0.089 | 0.035 | 0.004 | 0 | 0.823 | 0.9165
Modal | 10 | 0.087 | 0.0112 | 2.07E-06 | 0 | 0.8342 | 0.9165
Modal | 11 | 0.073 | 0.0275 | 0.0377 | 0 | 0.8617 | 0.9542
Modal | 12 | 0.071 | 0.0038 | 0.0016 | 0 | 0.8654 | 0.9558
Modal | 13 | 0.068 | 0.0006 | 0.0019 | 0 | 0.866 | 0.9577
Modal | 14 | 0.062 | 0.0223 | 0.0012 | 0 | 0.8884 | 0.9588
Modal | 15 | 0.059 | 0.0141 | 0.0071 | 0 | 0.9025 | 0.9659

## Slide 34: Seismic check:
  Mass partition check:
  The summation of Ux and Uy must bee reach 90%.
  Block 4.
  Need a 50 mode.
  Block 3.
  Need a 50 mode.

## Slide 35: Seismic check:
  Drift check:
  The displacement from Etabs for the two direction must be less than the limit displacement.
  Block 1.
  The manual displacement less than the limit.
  Block 2.
  The manual displacement less than the limit.
story # | h (mm) | distx (mm) | dist y (mm) | drift x (mm) | drift y (mm) | ∆ m x (mm) | ∆ m y (mm) | limit (mm)
1 | 4000 | 0.44 | 1.175 | 0.44 | 1.175 | 1.694 | 4.524 | 80
2 | 4000 | 2.044 | 4.507 | 1.604 | 3.332 | 6.175 | 12.828 | 80
3 | 4000 | 5.22 | 9.36 | 3.176 | 4.853 | 12.22 | 18.684 | 80
story # | h (mm) | distx (mm) | dist y (mm) | drift x (mm) | drift y (mm) | ∆ m x (mm) | ∆ m y (mm) | limit (mm)
1 | 4000 | 0.564 | 0.266 | 0.564 | 0.266 | 2.171 | 1.024 | 80
2 | 4000 | 2.35 | 1.385 | 1.786 | 1.119 | 6.876 | 4.308 | 80
3 | 4000 | 4.51 | 2.778 | 2.16 | 1.393 | 8.316 | 5.363 | 80
4 | 4000 | 6.443 | 4.533 | 1.933 | 1.755 | 7.442 | 6.757 | 80
5 | 4000 | 8.875 | 7.523 | 2.432 | 2.99 | 9.363 | 11.512 | 80

## Slide 36: Seismic check:
  Drift check:
  The displacement from Etabs for the two direction must be less than the limit displacement.
  Block 3.
  The manual displacement less than the limit.
  Block 4.
  The manual displacement less than the limit.
story # | h (mm) | distx (mm) | dist y (mm) | drift x (mm) | drift y (mm) | ∆ m x (mm) | ∆ m y (mm) | limit (mm)
1 | 4000 | 0.141 | 0.301 | 0.141 | 0.301 | 0.543 | 1.159 | 80
story # | h (mm) | distx (mm) | dist y (mm) | drift x (mm) | drift y (mm) | ∆ m x (mm) | ∆ m y (mm) | limit (mm)
1 | 4000 | 0.05 | 0.11 | 0.05 | 0.11 | 0.193 | 0.424 | 80
2 | 4000 | 0.47 | 0.04 | 0.42 | -0.07 | 1.617 | -0.27 | 80
3 | 4000 | 2.8 | 1.4 | 2.33 | 1.36 | 8.971 | 5.236 | 80
4 | 4000 | 6.2 | 4.8 | 3.4 | 3.4 | 13.09 | 13.09 | 80

## Slide 37: Seismic check:
  Base shear check:
  The % of errors in base shear check must be less than 5%.
  Blocks:
Base shear check. |  |  | 
Block No. | V_Etabs (kN) | V_manual (kN) | % of error
Block 1. |  |  | 
EQx | 9949.8 | 9953.6 | -0.04
EQy | 9680.42 | 9953.6 | -2.82
Block 2. |  |  | 
EQx | 4649.39 | 4677.589 | -0.61
EQy | 4456.08 | 4677.589 | -4.97
Block 3. |  |  | 
EQx | 4316.69 | 4319.38 | -0.06
EQy | 4308.16 | 4319.38 | -0.26
Block 4. |  |  | 
EQx | 10433.43 | 10664 | -2.21
EQy | 10459.53 | 10664 | -1.95

## Slide 38: Deflection check:
  Deflection limit = Ln/240.
  After we checks all of the panel in the building, we made sure that there no values ​​from Etabs exceeding the limit.

## Slide 39: Design and detailing of the structure elements:
1.Footings:
We are used three type of footings in this building.
mat footing.
Isolated footing.
Wall footing.

## Slide 40
Mat footing (Block2).
mat footing with thickness 60cm.
Bottom reinforcement.
Bottom reinforcement y-axis:
Bottom reinforcement x-axis:

## Slide 41
Mat footing (Block2).
Top reinforcement.
Top reinforcement y-axis:
Top reinforcement x-axis:

## Slide 42
Matt footing (Block2).
Matt footing 60cm.
SEC A-A

## Slide 43
Isolated footing (Block3).
H_Section F1
V_section F1
Wall footing (Block3).
V_section SW

## Slide 44
2. columns:
We are used two type of columns shape this building, rectangular shape and circular shape with more than one dimension of each shape.
Rectangular column 60*100cm.
Circlular column 120cm.

## Slide 45: Design and detailing of the structure elements:
3. Slabs:
We used different systems of slab in this building.
Voided slab with thickness 50cm.
Voided slab with thickness 70cm.
Two way solid slab with thickness 450cm.
Two way solid slab with thickness 400cm.
Two way solid slab with thickness 350cm.
One way solid slab with thickness 350cm.
Two way solid slab with thickness 270cm.
One way solid slab with thickness 150cm.

## Slide 46
Voided slab with thickness 50cm (Block2):
Basement floor layout.
Section in slab.

## Slide 47
Voided slab with thickness 50cm (Block2):
Basement floor reinforcement.
Bottom reinforcement bars y-axis .
Bottom reinforcement bars x-axis .

## Slide 48
4. Beams:
we designed many different dimension of in this building.
Beams of first floor (Block1)

## Slide 49
.
Detailing of beam B7.

## Slide 50
5. Shear wall:
We are used thickness 30cm for shear wall.
Horizontal section in SW4.
Block 2 walls.

## Slide 51
6. Stair case:
Stair case (Block 1)

## Slide 52: Ramp design: Block (B3)
Section A-A
Reinforcement for top& bottom bars
Block 3.

## Slide 53
HVAV Design
Artificial lighting & Electrical
Acoustical Design
Water Supply & Drainage
Electromechanical Aspects

## Slide 54: HVAC system

## Slide 55: HVAC Design
VRF (Variable Refrigerant Flow) system has been used.
VRF system contains three types of systems:
Cassette unit.
Fan coil unit.
Split unit.
Equipment from different companies (TOSHIBA, LG, METALAIRE,
TROX) has been used.
Cooling Load:
Cooling Load (KW) | Space | Floor No. | Block No.
7.50 | Reception | G.F | Block (1)
6.48 | Administration |  | 
7.50 | Multipurpose |  | 
12.85 | Library | F.F | 
6.15 | Reception |  | 
13.96 | Cafeteria | S.F | 
9.25 | Kitchen |  | 
4.58 | Cafe | TH.F | 
8.51 | Gallery | G.F | Block (2)
2.98 | Classrooms | F.F | 
3.19 | Computer room |  | 
4.06 | Corridor |  | 
1.82 | Lobby for theatre | B.F | Block(4)
0.69 | VIP room |  | 
1.28 | North artist rooms |  | 
1.08 | North dressing rooms |  | 
1.28 | South artist rooms |  | 
1.08 | North dressing rooms |  | 
1.28 | South dressing rooms |  | 
20.86 | Corridor |  | 
3.23 | Music rooms | G.F | 
10.73 | Lobby for theatre |  | 
12.76 | Theatre |  | 
11.49 | Stores |  | 
2.64 | Meeting room | F.F | 
155.23 |  |  | Total

## Slide 56: Outdoor units:
Outdoor unit for split unit.
Outdoor unit for VRF system.

## Slide 57: Indoor units:
Cassette unit.
Fan coil unit.
Fresh air intake.

## Slide 58
Indoor units:
Square diffuser.
Slot linear diffuser.
Split unit.

## Slide 59
The distribution of the HVAC systems in the Basement floor:

## Slide 60
The distribution of the HVAC systems in the Ground floor:

## Slide 61
Artificial lighting Design

## Slide 62
Lighting design for the Theatre:
Distribution of lighting and switches.
Required UGR | UGR design | Required Lux | Lux design | Region | Space
< 25 | 21.2 | 300 | 332 | Stage | Theatre
< 22 | 17.6 | 200 | 291 | Seats | 
Simulation results:
Luminaires selected:

## Slide 63
3D views for the Theatre:

## Slide 64
Luminaires selected:
Simulation results:
Lighting design for the Multipurpose room:
Distribution of lighting and switches.
Required Uniformity | Uniformity design | Required UGR | UGR design | Required Lux | Lux design | Space
0.65 | 0.6 | < 19 | 16.5 | 500 | 582 | Multipurpose room

## Slide 65
3D views for the Multipurpose room:

## Slide 66
Lighting design for the Classroom:
Distribution of lighting and switches.
Simulation results:
Luminaires selected:
Required Uniformity | Uniformity design | Required UGR | UGR design | Required Lux | Lux design | Space
0.60 | 0.6 | < 19 | < 10 | 300 | 368 | Classroom

## Slide 67
3D views for the Classroom:

## Slide 68
Basement floor |  |  |  |  |  | 
Space name | Standard lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Parking | 75 | 92 | - | - | 0.4 | 0.36
Store | 100 | 214 | - | - | 0.40 | 0.46
Mechanical room | 100 | 266 | - | - | 0.40 | 0.68
Service office | 300 | 352 | < 19 | < 10 | 0.60 | 0.63
Lobby for theatre | 150 | 152 | - | - | 0.40 | 0.42
VIP room | 300 | 354 | < 19 | < 10 | 0.60 | 0.57
Corridor | 100 | 201 | - | - | 0.40 | 0.30
WC | 100 | 136 | - | - | 0.40 | 0.52
Dressing room | 300 | 334 | - | - | 0.40 | 0.73
Artists room | 300 | 384 | - | - | 0.40 | 0.41
Lighting design for all the floors:
Ground floor |  |  |  |  |  | 
Space name | Standard lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Multipurpose room | 500 | 582 | < 19 | 16.5 | 0.60 | 0.65
Administration | 300 | 431 | < 19 | 17.2 | 0.60 | 0.58
Reception | 200 | 223 | < 19 | 14.7 | 0.50 | 0.35
WC | 100 | 111 | - | - | 0.40 | 0.38
Music room | 300 | 390 | < 19 | 15 | 0.40 | 0.41
Gallery | 300 | 325 | - | - | 0.40 | 0.43
Retail store | 300 | 316 | - | - | 0.60 | 0.62
Control room | 150 | 147 | < 22 | 18.2 | 0.40 | 0.75
Theatre | Stage 300 | 332 | < 25 | 21.2 | - | -
 | Seats 200 | 291 | < 22 | 19.8 | - | -
First floor |  |  |  |  |  | 
Space name | Standard lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Library | 500 | 532 | < 19 | 17.4 | 0.60 | 0.64
Reception | 200 | 234 | < 19 | 19.6 | 0.50 | 0.47
WC | 100 | 111 | - | - | 0.40 | 0.41
Classroom | 300 | 368 | < 19 | < 10 | 0.60 | 0.60
Meeting room | 300 | 480 | < 19 | 12.6 | 0.50 | 0.52
Computer room | 300 | 392 | < 19 | 14.5 | 0.50 | 0.56
corridor | 100 | 202 | - | - | 0.40 | 0.43
Second floor |  |  |  |  |  | 
Space name | Standard lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Cafeteria | 300 | 419 | < 19 | 10.2 | 0.60 | 0.60
Kitchen | 500 | 514 | < 19 | < 10 | 0.60 | 0.58
WC | 100 | 140 | - | - | 0.40 | 0.33
Third floor |  |  |  |  |  | 
Space name | Standard lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Cafe | 300 | 374 | < 19 | 14.8 | 0.60 | 0.64
WC | 100 | 162 | - | - | 0.40 | 0.33

## Slide 69
Power Design

## Slide 70
Distribution socket for multipurpose & administration space in G.F_Block1.

## Slide 71
G. F | Special load | Normal load | Light load | Total power | I load | I C.B | I cable | C.B | Cable (IEC ) | # No of Power branch | # No of branch for Light | Phase
 | Watt | Watt | Watt | Watt | Amp | Amp | Amp | Amp |  |  |  | 
D.B.1 | 0 | 5250 | 4003.1 | 4777.48 | 24.13 | 27.75 | 31.91 | 30 | (36 A ) 6 mm2 | 5 | 7 | 1
D.B.2 | 0 | 2500 | 648 | 1268.4 | 6.41 | 7.37 | 8.47 | 10 | (18A ) 1.5 mm2 | 2 | 2 | 1
D.B.3 | 0 | 7500 | 3661.4 | 5179.12 | 26.16 | 30.08 | 34.59 | 36 | (36A ) 6 mm2 | 9 | 11 | 1
M.D.B (G.F) |  | Total load |  | 11225 | 18.00 | 20.70 | 23.81 | 25 | (24 A) , 4 mm^2 |  |  | 3
The electrical load of power, lighting system in the ground floor.
Main distribution Board for elevators and escalator |  | unit | Power | I load | I C.B | I cable | C.B | Cable | Phase
Unit |  |  | Watt | Amp | Amp | Amp | Amp | Amp | 
For three elevators |  | D.B.E | 21000 | 33.68 | 38.73 | 44.54 | 40 | (44 A ) 6 mm2 | 3
one escalator |  | D.B.S | 7000 | 11.23 | 12.91 | 14.85 | 16 | (21 A ) 2.5 mm3 | 1
3 phases | Each phase | M.D.B.ES | 9333.3 | 14.97 | 17.21 | 19.80 | 20 | (131 A ) 50 mm2 | 3
The electrical load of elevator and escalator
The electrical load of Hvac
Main distribution Board for Hvac |  | blocks | Power | I load | I C.B | I cable | C.B | Cable | Phase
Unit |  |  | Watt | Amp | Amp | Amp | Amp | Amp | 
Hvac |  | D.B.B1 | 73000 | 117.07 | 134.63 | 154.83 | 160 | (180 A ) 95 mm2 | 3
Hvac |  | D.B.B2 | 45000 | 72.17 | 82.99 | 95.44 | 100 | (97 A ) 35 mm3 | 3
Hvac |  | D.B.B3 | 68000 | 109.06 | 125.41 | 144.23 | 160 | (149 A ) 70 mm3 | 3
3 phases | Each phase | M.D.B.BH | 62000 | 99.43 | 114.35 | 131.50 | 125 | (149 A ) 70 mm2 | 3

## Slide 72
The distribution boards for lighting and socket.

## Slide 73
Acoustical Design

## Slide 74
The spaces that were designed acoustically in the building by using Ecotect program:
The absorption coefficient for the finished material were used in classroom, meeting room
Acoustical Design:
Classroom.
Meeting room.
Finish material | Absorption coefficient at every frequency (HZ) |  |  |  |  |  | 
 | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000
Plaster | 0.04 | 0.05 | 0.07 | 0.08 | 0.04 | 0.06 | 0.05
Wooden floor suspended | 0.07 | 0.2 | 0.41 | 0.49 | 0.51 | 0.54 | 0.53
Glass | 0.1 | 0.06 | 0.04 | 0.03 | 0.03 | 0.03 | 0.04
Door (hollow) | 0.41 | 0.35 | 0.25 | 0.2 | 0.15 | 0.14 | 0.13
Ceiling | 0.15 | 0.2 | 0.15 | 0.1 | 0.15 | 0.1 | 0.15
Terrazzo | 0.01 | 0.01 | 0.04 | 0.04 | 0.04 | 0.07 | 0.07

## Slide 75
Classroom RT60 according to Millington.
Reverberation Time (RT60):
 | Full | 50% | Empty
FREQ. | RT(60) | RT(60) | RT(60)
125Hz: | 1.28 | 1.33 | 1.37
250Hz: | 0.81 | 0.84 | 0.87
500Hz: | 0.57 | 0.59 | 0.61
1kHz: | 0.49 | 0.5 | 0.52
2kHz: | 0.45 | 0.46 | 0.48
4kHz: | 0.39 | 0.4 | 0.41
8kHz: | 0.31 | 0.31 | 0.31
Meeting room RT60 according to Millington.
 | Full | 50% | Empty
FREQ. | RT(60) | RT(60) | RT(60)
125Hz: | 1.84 | 1.88 | 1.91
250Hz: | 1.3 | 1.33 | 1.35
500Hz: | 1.12 | 1.14 | 1.17
1kHz: | 1.04 | 1.06 | 1.08
2kHz: | 0.9 | 0.91 | 0.92
4kHz: | 0.73 | 0.73 | 0.74
8kHz: | 0.5 | 0.49 | 0.49

## Slide 76
Acoustical design for the Theatre:
The absorption coefficient for the finished material were used in the Theatre.
Finish material | Absorption coefficient at every frequency (HZ) |  |  |  |  |  | 
 | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000
Sonogama | 0.8 | 0.72 | 0.85 | 0.87 | 0.78 | 0.8 | 0.8
Wood panel 16 | 0.2 | 0.12 | 0.1 | 0.1 | 0.08 | 0.07 | 0.07
Gypsum 12.5 MMB | 0.05 | 0.05 | 0.05 | 0.03 | 0.02 | 0.02 | 0.02
Carpet heavy | 0.02 | 0.06 | 0.14 | 0.37 | 0.6 | 0.65 | 0.7
Fabric | 0.19 | 0.37 | 0.56 | 0.637 | 0.61 | 0.59 | 0.59
PLYWD 1/2 | 0.3 | 0.25 | 0.2 | 0.17 | 0.15 | 0.1 | 0.1
Plaster | 0.03 | 0.03 | 0.04 | 0.05 | 0.04 | 0.03 | 0.03
Theatre RT60 according to Eyring.

## Slide 77: STC and IIC:
Internal walls
External glazing walls
External walls

## Slide 78: STC and IIC:
Floor
Ceiling

## Slide 79: Loud speaker:
Total Sound pressure level (SPL):
Articulation loss %:
SPL | Type
97 | S112V
136 | MAX2

## Slide 80
Fire fighting system

## Slide 81
The symbols of the fire fighting and evacuation systems in the building.
firefighting plan of the ground floor

## Slide 82
Smoke detector
Heat detector
Fire hose
Stand pipe
Signs and emergency light

## Slide 83
Extinguishers according to the space:
sprinklers according to the space:

## Slide 84
Water Supply System

## Slide 85: Water supply system
Water Tanks Used

## Slide 86: Water consumption
Firefighting consumption
Water Consumption for drinking and domestic:
Irrigation consumption
All cube needed is 181 cubes and 12 cubes for hot water use

## Slide 88
Drainage System

## Slide 89: Pipes used
The total number of fixture units is 369 fu the main diameter for the main stack is
The diameters for the pipes as follows
Horizontal pipe for the water closet is with slope 1%
Horizontal pipe for the lavatory is with slope 2%
Horizontal pipe for the kitchen sink is with slope 2%
The pipe between the manholes is with slope1%
The rain water main vertical stack

## Slide 90
Bath Room Drainage

## Slide 92: Over-lap between all systems
Over –lap for Ground Floor
Over –lap for First Floor

## Slide 93
Quantity Surveying and Cost Estimation

## Slide 94: The total cost of the building is 23,786,709 NIS and the total area of the building is 9700m2 which means that the total unit cost per m2 is 2452 NIS/m2, nearly 800 $/m2.
Earth work = 1,646,590 NIS
Foundation = 5,722,500 NIS
Building (construction) = 4,616,525 NIS
Finishing = 8,998,130 NIS
Electrical = 342,380 NIS
Mechanical = 2,460,584 NIS
Chart: 
| Earth work | Foundation | Construction | Finishing | Electrical | Mechanical
 | 1646590 | 5722500 | 4616525 | 8998130 | 342380 | 2460584

## Slide 95: Team
Ala’ Ismail
Issa Obaid
Muhammad Tanbouz
Thank You