## Slide 1: Design of Sahab building at Palestine-Nablus
Prepared by: Ashraf Abu Azezi
Aqeel Hasson
Khaled Salah
Mohammad Zaiter

## Slide 3: Plan view

## Slide 4: Site Location

## Slide 5: Deflection Check
long term deflections for slab systems
Table of Deflection Limits – ACI318-11

## Slide 6: Long term deflection combination: 2D+2SD+1.5 L

## Slide 7: Check deflection In X direction:
long term deflection allowable deflection =L/240 = (6.305/240) *1000=26.27 mm .
long-term deflections for slab systems at the middle = 15.12 mm
long-term deflections for slab systems at the right side = 3.11 mm
long-term deflections for slab systems at the left side = 10.9 mm
Relative long-term deflection = 15.12 – 3.11+10.9/2 = 8.17< 26.27 it is ok

## Slide 8: Check deflection In Y direction:
long term deflection allowable deflection =L/240 = (6.17/240) *1000=25.7 mm .
long-term deflections for slab systems at the middle = 15.12 mm
long-term deflections for slab systems at the top = 15.17 mm
long-term deflections for slab systems at the bottom = 13.5 mm
Relative long-term deflection = 15.12– 15.17+13.5/2 = 0.78 < 25.7 it is ok

## Slide 9: Design and Check for Gravity and Lateral Loads
The structural members that were designed are:
1- Columns 2- Beams 3- Slabs (One way and two way Ribbed slab) 4- Shear walls 5- Footings 6- Stairs

## Slide 10: Check and design for Columns
We use Bressler’s Reciprocal load method shall be applied to check the column section for the moments

## Slide 11
Figure shown interaction diagram between ØPn and ØMn,2, to check the column capacity for them.
ØPn and ØMn,2
ØPn,3 = 4500 kN
ØPn,2 = 4500 kN
ØPn, o = Ø ƛ (0.85 f’c (Ag-As) + As fy) ØPn
ØPn,o = 4547.4 kN
ØPn=4453.6 KN < 1957.7 KN then its ok

## Slide 12: Check and design for Columns
Figure shown interaction diagram between ØPn and ØMn,3, to check the column capacity for them.

## Slide 13: Design for Columns
column1 (400*800)
column2 (1050*400)
column3 (950*300)

## Slide 14: Design for Column (C1)
Check slenderness
M1=12.3 KN.m, M2=25.7 KN.m
R=0.3*0.4=0.12, Lu=3.1m
K*Lu/r= 25.83
34+12M1/M2= 39.7<40 Then no slenderness, consider a short column.
Pu=2601 KN, ρ From Etabs=0.01
As=0.01*400*850=3400mm ,▲Use 14ø18
Transverse reinforcment:
The spacing between stirrups is as the following
S < 48ds= 48*10=480 mm
< 16dp=16*16=256 mm
< least lateral dimension of column=400 mm
Use 1ø10/250mm.

## Slide 15
Cross section for column 1 ↓
for
General longitudinal section in column ⟶

## Slide 16: Cross section in column 2

## Slide 17: Cross section in column 3
Cross section in column 2

## Slide 18: Check and design for beams
Mu = 84.28 KN.m
The area of steel for this beam due to
the ultimate negative moment = 1011 mm2 .
ρ =0.0051
As = ρ b d = 0.0051× 800 × 240 = 979.2 mm2
. As min= ρ min × b × d = 0.00333 × 800 × 240 = 640 mm2 .
As >As min ,its ok.
𝜌 max.singly = 0.01806
As, max = 0.01806*800*240 = 3476.5 mm2 Ok
Difference percentage between the longitudinal reinforcement from the manual and from ETABS
Difference percentage = 𝑨𝒔 𝒇𝒓𝒐𝒎 𝒎𝒂𝒏𝒖𝒂𝒍−𝑨𝒔 𝒇𝒓𝒐𝒎 𝑬𝑻𝑨𝑩𝑺 /𝑨𝒔 𝒇𝒓𝒐𝒎 𝑬𝑻𝑨𝑩𝑺 * 100% = 3.2%

## Slide 19: Shear Design Verification
Vu = 77.654 kN
Vc =1/6 *√28 *bw*d = 1/6 *√28 *800*240/ 1000 = 169.32 kN
Ø Vc=0.75*169.32= 127 KN
ØVc > Vu then no need for shear reinforcement, use Av/s min
𝐴𝑣/𝑆_𝑚𝑖𝑛 = max of (0.062 √𝑓𝑐∗𝑏𝑤 / fy , 0.35∗𝑏𝑤 /𝑓𝑦)
(0.062 √𝑓𝑐∗𝑏𝑤 /𝑓y = 625 mm^2/m
0.35∗𝑏𝑤 /𝑓𝑦= 666.67 mm^2/m

## Slide 20: Design of beams
H=300,D=240,B=800
As Bottom = 640mm2 .
As Top1 = 640 mm2 .
As Top2 =976 mm2 .
As, min = 0.0033*800*240 = 633.6 mm2 → O.K
𝜌 max.singly = 0.01806
As, max = 0.01806*800*240 = 3467.52 mm2 → O.K.
❖ Longitudinal Reinforcement:
Bottom Steel:
As = 640mm2 → use 4Ø14
Top1 Steel:
As = 640mm → use 4Ø14
Top2 Steel:
As = 976 mm2 → use 5Ø16

## Slide 21
Shear strength:
Av/s=0.6667
Av=2*78.5=157 mm^2
S=235 mm
S max=min of (d/2, 600)=(240/2,600).Then Smax=120mm
Use 2 Ø10 each 120 mm

## Slide 22: Reinforcement for beams

## Slide 23
longitudinal section Cross section For beam3

## Slide 24: Cross section For Beam5 Cross section For Beam2

## Slide 25: Design of Stair
Weight of staircase = 0.02 ∗ 23 + 0.05 ∗ 17 + 0.03 ∗ 27 = 2.12𝐾𝑁/𝑚2 .
Stair width = 30cm and height = 15cm, so:
Wight of concrete triangle of the stair = 0.5∗0.17∗0.3/ 0.345^2 = 0.214𝐾𝑁/𝑚2 .
Total S.D load on the stair= 2.12 + 0.214 = 2.334 𝐾𝑁/𝑚2
Dead load of stair slab= 25 ∗ 0.2 = 5 𝐾𝑁/𝑚2
Wu=1.2𝐷 + 1.6𝐿
𝑊𝑢 = 1.2 ∗ (5 + 2.334) + 1.6 ∗ 5 = 16.8 𝐾𝑁/𝑚𝑚2.
f’c = 28 MPa
fy = 420 MPa
d=160 mm
Assume simply supported slab:
✓ Shear check
𝑉𝑢 = 𝑤𝑢∗𝐿 2 = 16.8∗2.75/ 2 = 23.3𝐾
∅ Vc = ∅/ 6 ∗ 𝜆 ∗ √f’c ∗ 𝑏𝑤 ∗ 𝑑= ∅ /6 ∗ 1 ∗ √28 ∗ 1000 ∗ 160=105.8KN > Vu ,OK
✓ Flexural reinforcement
Mu = 𝑤𝑢∗𝐿^2 /8 = 16.8∗2.75^2/ 8 = 15.88𝐾𝑁. M

## Slide 26: Reinforcement for staircase