## Slide 1: Structural Analysis and Design of Panorama Parking and Mall in Tulkarm-Palestine

## Slide 2: Location 04. 05. 06. 01. 02. 03. Level & Height Site Coordenates Goals Area Floors
Tulkarem Palestine
- Leverl : 83 m above sea Level. -Total Height : 50 m.
X: 152719.36364 Y=191073.39097
Parking, Shopping center and other supplements.
Around 36 000 m2
16 Floors , three of them below ground level

## Slide 3
Internal walls : 300 mm External walls : 400 mm
X: 800*650 mm Y: 700*500 mm
WALLS
BEAMS
Option One : 70 Mpa Concrete Strength Option two : composite, 40 Mpa columns.
COLUMNS
Evaluation of the preliminary design

## Slide 4: 01
Design Verification

## Slide 5: Design Verification
frame
Beam
specification
Shear design verification
column
Bressler’s Reciprocal load method
Flexural design verification

## Slide 6: 4d Smallest Ln BEAMS
X-direction : 2.96 Y-direction : 2.56
X-direction : 4.45 m Y-direction : 6.85 m
Shall be at least 4d

## Slide 7: BEAMS
b is the larger of :
- 0.3h - 250 mm in x-direction : 650 in y-direction : 500

## Slide 8: BEAMS
5667
2670
1579
4560
5641
2658
maximum moment strength:1420 Kn.m
Minimum moment strength : 476 Kn.m
Ratio=0.34>0.25.
steel ratio:
Max : 0.25
Min : 0.00333
0.0168<0.025
bottom moment strength at left and right > 0.5 Their corresponding values at top
øMn at top=1420.38
øMn at bottom=711
Ratio= 0.5

## Slide 9: BEAMS
Strong column Weak beam concept
0.65 < 0.75 m 0.65 < 0.80 m

## Slide 10: Mu ρ manual As Beam Flexural Verification
1420 KN.m
0.0117
Manual : 5655.88 From ETABS : 5667

## Slide 11: Beams Shear Verification
 | ETABS result | Manual result | Different percentage
ΦVc | 317.01 | 313.15 | 1.20%
ΦVs | 399.89 | 398.75 | 0.25%
Vp | 245.54 | 245.55 | 0.004%
Av/s | 1741.75 | 1715.55 | 1.50%

## Slide 12: Pu Mu,2 Mu,3 Column Design Verification
2522.23 KN
250.18 KN.m
114.10 KN.m

## Slide 13: COLUMNS
ØPn,3=16051.8 kN
ØPn,2=16051.8 kN

## Slide 14: COLUMNS
Bressler’s Reciprocal load method:
ØPn,o = Ø ƛ (0.85 f’c (Ag-As) + As fy)
ØPn,o =0.65×0.8× (0.85×40(800000-9505) +9505×420) =17968.05 KN
Then ØPn=14504.88 KN > 17968.05.

## Slide 15: Pier Walls
Wall Thickness 400 mm
Wall Length 7200 mm

## Slide 16: WALLS
Shear check :
Vu
2082.244 KN
Փ Vc
Manual : 1554.4 KN ETABS: 1518.49 KN
Փ Vn
Manual : 3367.87 KN ETABS: 3332.89 KN

## Slide 17: WALLS
Boundary Elements:
Pu
20206.20 KN
Mu
2858.243 KN.m
Stress
Stress : 6.19 Mpa Stress limit : 5.6 Mpa

## Slide 18: Now
Mat Foundation
Allowable Stress : 450 KN/ m2
Thickness : 2200 mm
Footing

## Slide 19: Footing
Soil Pressure
The max soli pressure on the foundation is 430 KN/m2 < 450 KN/m2

## Slide 20: Footing wide beam shear
∅𝑉𝑐
V13
V23
1747.4 KN/m
321.3 KN < ∅𝑉𝑐
822.3 KN < ∅𝑉𝑐

## Slide 21: Punching Check
𝜙𝑉𝑐 = 2.087 ∗ 0.75 = 1.57 𝑀𝑝𝑎
𝑉𝑢 = 1.46 𝑀𝑝a
D/C = 1.46/1.57 = 0.93
Difference = 0%

## Slide 22: Shear Check
∅𝑉c= 100.6𝐾N
Maximum shear = 74 KN
Vu < ∅𝑉c
No need shear reinforcement
SLABS

## Slide 23: STRUCTURAL ELEMENTS DESIGN 02

## Slide 24: BEAM DESIGN

## Slide 25: BEAM DESIGN
4Ø25
4Ø25
4Ø25
4Ø25
Longitudinal Reinforcement

## Slide 26: BEAM DESIGN
9Ø25
9Ø25
8Ø25
No Need
2m
2m
2m
Longitudinal Reinforcement

## Slide 27: BEAM DESIGN
8Ø25
8Ø22
8Ø22
8Ø18
Longitudinal Reinforcement

## Slide 28: BEAM DESIGN
2Ø20
3Ø25
2Ø16
1.6m
1.6m
1.6m
Longitudinal Reinforcement

## Slide 29: BEAM DESIGN
Transverse Reinforcement
Max spacing (So)between stirrups equal the lesser of:
d/4
150mm
6db
(185, 150, 120)
2Ø12 / 120 mm
Confinement length = 3 m

## Slide 30: COLUMN DESIGN

## Slide 31: COLUMN DESIGN
M1 = 865.13 KN.m M2 = 558.50 KN.m
M= 1305.278 + 1318.482 = 2623.760 KN.m
Ratio = 3.03 > 1.2

## Slide 32: COLUMN DESIGN
Flexural Reinforcement
30Ø25

## Slide 33: COLUMN DESIGN
Transverse Reinforcement
3Ø10/120 mm
Lo shall not be less than the largest of:
One-sixth the clear span of the column
Maximum cross-sectional dimension of the column
450 mm
4.08/6=0.68m 1.1m 450mm
Spacing of transverse reinforcement (So) : 120 mm
1Ø10/120 mm

## Slide 34: FOOTING DESIGN
Design Verification
As= 1317.6 mm2 As min = 3888 mm2
As= 3781 mm2

## Slide 35: FOOTING DESIGN
Flexural Design
Minimum Area of Steel = 0.0018*1000*2160 = 3888 mm2 Use Ø25/125 mm in all directions

## Slide 36: FOOTING DESIGN
Flexural Design

## Slide 37: Wall DESIGN
Flexural Design
As from ETABS =
Use Փ14/300mm on each side.
As min
Ls =500mm

## Slide 38: Wall DESIGN
Shear Design
As min =
As from ETABS=
Use Փ20/300mm on each side
Boundary element Design
Width of boundary: b=400mm

## Slide 39: Wall DESIGN

## Slide 40: SLAB DESIGN
Solid Slab
Design Flexure
As,min
use 1Φ14/200mm

## Slide 41: SLAB DESIGN
Solid Slab
Direction1-TOP
As =1351.58 mm2
∴ Use 1Φ14/100 mm.

## Slide 42: SLAB DESIGN
Solid Slab
As 3314.12
∴ Use 1Φ22/100 mm.

## Slide 43: SLAB DESIGN
Solid Slab
Direction2-TOP
As =1203.63 mm2
∴ Use 1Φ14/100 mm.

## Slide 44: SLAB DESIGN
Solid Slab
As =2015.04 mm2
∴ Use 1Φ16/100 mm.
Direction1-Bottom&Direction2-Bottom: No additional reinforcement needed.

## Slide 50: Stairs DESIGN
Flexural Design
As min 360 .
From ETABS, the ultimate moment is 25.699 KN.m, then the steel needed is 208, use min steel.
For Top and Bottom steel As= 360mm2 , use 1Ø12/250 mm
Development length 𝐿𝑑𝑡 ≈ 500 𝑚𝑚.
Vu < ∅Vc, so no need for shear reinforcement.
Shear Design

## Slide 52: THANK YOU