## Slide 1
An-Najah National University Faculty of Engineering Civil Engineering Department
جامعة النجاح الوطنية
كلية الهندسة وتكنولوجيا المعلومات
Graduation Project (II) Structural Analysis and Design of Residential Building in Taybie–Palestine
By:
Abdelqader Alsalhi
Ahmad Jabaly
Mohammad Mawasi
Majd Mawasi
Under supervision of: Dr.Mohammad Sama’neh.

## Slide 2
Jabaly’s Building

## Slide 3
Three-dimensional analysis and design.
3
General Description
1
2
Outline project:
Preliminary Design

## Slide 4
General Description:
Floor | Area(m2) | Height(m) | Function
Ground-11 | 541 | 3.25 | residential
This graduation project presents the structural design for a 12-floor residential building owned by Mr. Hassan Jabaly, located in Taybie , Israel, specifically on plot 18 at basin 7852. The building covers a floor area of 541 square meters, with a staircase landing area of 12 square meters on each floor, and each floor has a height of 3.25 meters. Our objective is to conduct a comprehensive structural analysis and design of the building's main components, including the ceilings, columns, beams, foundations, staircase, and shear walls.

## Slide 5
Project plans

## Slide 8
An inside brief about the project:
The building includes interior and exterior walls which are 30 cm in thickness made of reinforced concrete, the staircase and elevator walls are 20 cm thick and will be constructed as shear wall, and some exterior walls are of 25 cm thick and made of three layers 10 cm block, 10 cm concrete and 5 cm stone, with some openings, which are windows for the building.

## Slide 9
Codes and Standards:
1
ACI-318M-19: which was used in the design of structural elements (Static design).
2
3
ASCE-7-16 Minimum Design Loads and Associated Criteria for Buildings: which was used in the design of the earthquake in the building.
IBC-2016: for seismic loads and design.

## Slide 10
Construction Materials:
1- Structural Elements.
Unit Weight, γc | 25 KN/m3
Modulus of Elasticity, Ec | 24870 MPa
Poisons Ratio, v | 0.2
Compressive Strength, fc | 28 MPa
Flexure | 3.28 MPa
Tensile Strength, ft | 1.75 MPa

## Slide 11
Reinforcing Steel:

## Slide 12
Material | Unit Weight KN/m3
Aggregates | 16
Stone | 24
Tiles | 27
Cement Mortar | 23
Concrete | 25
Rib concrete blocks | 12.54
Block | 16

## Slide 13
LOADS

## Slide 14
A(GRAVITY LOADS:
1) Dead load: self weigh of the structure
2) Live load:The variable load resulting from the use of the building, such as the movement of people, furniture, or temporary equipment.
Floor | Uses for | Live Load | Super dead load
Ground-11th | Residential | 2 KN/m2 | 6.3 KN/m2
3) Superimposed load: Superimposed dead load is the weight of non-structural elements in the structure, such as tiles, glass, plaster, etc.

## Slide 15
2- Seismic loads
According to ASCE 7-16 code to seismic analysis for this structure:
1-Mapped acceleration parameters Ss&S1:
  From Palestine seismic map:
  Ss= 0.3
  S1 = 0.08
2- Site class: Site classification is B

## Slide 16
3- Risk category:
risk category of the building is II

## Slide 17
4- Seismic Design Category : B
5- Importance factor : Ie = 1

## Slide 18
6- Site coefficients: The values of Fa 1.132= and Fv =1.67

## Slide 19
*The maximum considered earthquake Spectral Response Acceleration Parameters SMS and SM1 :
          SMS=Fa * Ss= 0. 9 * 0.3 = 0.27
          SM1= Fv * S1 = 0.8 * 0.08 = 0.064
*Design spectral acceleration (SDS & SD1)
          SDS = 2/3 SMS = 0.18
          SD1 =2/3 SM1 = 0.0426

## Slide 20
7- Type of the lateral forces resisting system:
building frame system: special shear walls
Response modification factor= 5
Overstrength factor Ω = 2.5
Deflection Amplification Factor = 4.5

## Slide 21
8- Seismic Base Shear
V = Cs W
Cs= 0.011
W= D+SD+0.25SL

## Slide 22
CHAPTER 2: Preliminary Design.
1) Slab structural system.
2)Preliminary slab thickness.
4)Preliminary dimensions of columns and walls.
3)Preliminary dimensions of Beams .

## Slide 23
General Notes about dimension
1) The slab structural system used in this building is a one-way&two-way ribbed slab.
3) Use the longest span for calculation
4) For Column dimension,
assuming ρ = 0.01 → As = 0.01 Ag
2) preliminary dimensions were be chosen according to ACI 318-19

## Slide 24
Preliminary dimensions of the structural elements
Structural element | Preliminary dimensions
Slab | Thickness = 250mm
Walls | Thickness = 200&300mm
columns | b = 300 mm & h = 600 mm
Beams | Exterior b = 600 mm & h = 250 mm Interior b = 800 mm & h = 250 mm

## Slide 25
Final dimensions of the structural elements
Structural element | Final dimensions
Slab | Thickness =(250)mm
Walls | Thickness = (300, 200)mm

## Slide 26
Beams:
Beam item | Width(mm) | Thickness(mm)
B1 | 500 | 250
B2 | 600 | 250
B3 | 700 | 250
Final dimensions of the structural elements

## Slide 27
Columns:
Final dimensions of the structural elements
Column item | length(mm) | width(mm)
C1 | 800 | 300
C2 | 900 | 300
C3 | 1000 | 300
C4 | 1100 | 300
C5 | 1000 | 350
C6 | 1000 | 400

## Slide 28
AutoCAD
ETABS
SAFE
Modeling Programs

## Slide 29
AutoCAD 1) Drawing Plans. 2) Drawing Detailed Sections. 3) Illustrate Shop Drawing.
Modeling Programs

## Slide 30
AutoCAD (Outline)

## Slide 31
AutoCAD (Structural Plan)

## Slide 32
AutoCAD (Detailed Section)

## Slide 33
Modeling Programs
ETABS 1) Modeling Structures. 2) Analyzing structures. 3) Design Structures

## Slide 34
ETABS (3D Frame)

## Slide 35
ETABS (3D Model)

## Slide 36
Modeling Programs
SAFE 1) Modeling Foundations. 2) Analyzing Foundations. 3) Design Foundations.

## Slide 37
SAFE Model

## Slide 38
Lateral Load Definition
in this project, the only lateral loads affecting the structure are those induced by seismic (earthquake) forces.

## Slide 39
Cause of Earthquake
The random movements of the tectonic plates are the main natural cause of the earthquake

## Slide 40
History of Earthquake in Palestine
In 1927, a strong earthquake hit Nablus with a volume of 6.2 on the Richter scale which last for a duration of 90 secs.

## Slide 41
Tragedy of Earthquakes

## Slide 42
Provisions By the ASCE 7-16 Code
The design earthquake has a probability of exceedance of 2% every 50 years.
That means every the 2500 years, an earthquake large than the design earthquake will occur.

## Slide 43
Seismic Modeling Methods
Equivalent Static Method (Static).
Response Spectrum Method (Dynamic).
Time History Method (Dynamic).

## Slide 44
Response Spectrum Method
It perform multiple Equivalent Static Method in each mode of the structure and combined them in the end as one force.

## Slide 45
Time History Method
This applies the dynamic forces on the building as a function of time during the earthquake.

## Slide 46
Structural Irregularity
There are two types of Structural Irregularities:
Horizontal Structural Irregularity
Vertical Structural Irregularity

## Slide 47
Horizontal Structural Irregularity

## Slide 48
Vertical Structural Irregularity

## Slide 49
Seismic Checks
1- Base shear check :-total seismic load
2- Torsional Irregularity Ratio:-the displacement deference ratio
3-sum of Mass participation ratio
4- Type of Lateral-resisting system

## Slide 50
Designs of Structural Elements
Steel Reinforcement is used for multiple reasons:
1- To support the concrete with resisting the tension forces mainly
and compression forces.
2- To prevent shrinkage of concrete.
3- To make the concrete a ductile material.

## Slide 51
Designs of Structural Elements
1- Slabs
2- Beams
3- Columns
4- Shear Walls
5- Stairs
6- Foundations

## Slide 52
Design of slabs
One-way
One-way
two-way

## Slide 53
Beams

## Slide 55
Columns

## Slide 56
Columns

## Slide 57
Shear Walls

## Slide 58
Shear Walls

## Slide 59
Shear Walls

## Slide 60
Stairs
The staircase is an important element in the structural elements that connect from one floor to another.

## Slide 61
Stairs

## Slide 62
Foundations
The foundation is the most critical structural element responsible for supporting all building loads.
In order to select the appropriate foundation type, it was necessary to determine the ratio of the total column base areas to the building footprint.
This ratio was calculated to be 68%, which indicated that a mat foundation would be the most suitable choice.
Following several design calculations, the mat foundation was designed with a thickness of 90 cm.

## Slide 68
شكراً لحسن استماعكم و دمتم لنا ذخراً نفتخر بكم دائماً