## Slide 1: Towards More Sustainable Mobility in Nablus City, Palestine

## Slide 2: Introduction
Sustainability :is the ability to continue a defined behavior indefinitely. It contains :
Environmental sustainability : is the ability to maintain rates of renewable resource harvest, pollution creation, and non-renewable resource depletion that can be continued indefinitely.
Economic sustainability : is the ability to support a defined level of economic production indefinitely
Social sustainability : is the ability of a social system, such as a country, to function at a defined level of social well being indefinitely.

## Slide 3: Introduction :
Sustainable Mobility : Sustainable mobility depends on the concept of moving freely without sacrificing other elements such as human, environment and economy .
Environmentally : sustainable system aims to reduce emissions such as CO2 and aims to reduce noise pollution due to traffic.
Economically : sustainable system aims to exploit the different resources particularly human resources and financial resources.
Socially; sustainable system aims to meet the requirement of the users.

## Slide 4: Venn Diagram of sustainable mobility

## Slide 5: Problem Definition :
It is believed the current T.S in Nablus is facing real problems in terms of sustainability, particularly environmental, social, and economical issues.
The first and essential problem is "the environment". The current T.S contributes in Co2 emissions and pollutes the environment.
The social problems : the T.S may not be reliable and it has limited serviceability. Also it doesn’t satisfy citizen's needs like safety and efficiency
Economic problems, it costs the government a lot and the return may not be worth while

## Slide 6: Study Area
A map of Nablus showing the study area

## Slide 7: The Expected Sustainable Mobility Indicators
1) Environmentally:
a) Sound pollution.
b) CO2 emission.
c) Fuel consumption
2) Socially:
a) Safety.
b) Comfort ability.
c) Services levels.
d) Delay.
e) Accessibility.
f) Ability to use non-motorized moods.
3) Economy:
a) Expenditures.
b) Investment .
…etc.

## Slide 8: Methodology
Literature review.
Data collection.
Traffic count studies.
Speed Study.
Official Statistics of the number of vehicles, the population, the densities, percentage of land used as roadways.
Accidents numbers and safety conditions.
Questionnaire.

## Slide 9: Data Type :
Traffic count studies : this study has been done by counting vehicles with their movement to determine the peak hour, peak hourly volume.
Speed Study : the data was collected on (24/11/2015) and it is done by using the radar instrument.
Official Statistics : the official Statistics of the number of vehicles, the population, the densities, percentage of land used as roadways has been taken basically from the (Palestinian Central Bureau of statistics).
Accidents and safety conditions : the accidents occurred in the study area, has been taken into consideration. This data has been collected for the years 2014 and 2015, the accidents are up to Sept 2015 and it is collected from (Police Station).
Questionnaire : a pilot study has been made. However, the result still under processing.

## Slide 10: Data Collection and analysis : Traffic volume analysis
 | West East |  |  | East west |  | Street Name
PHF | Peak hour | Peak Volume | PHF | Peak hour | Peak Volume | 
0.84 | 7.30-8.30 a.m. | 1093 | 0.84 | 2.45-3.45 p.m. | 776 | Haifa street (west- Tunis)
0.9 | 7.15-8.15 a.m. | 1988 | 0.84 | 7.15-8.15 a.m. | 2039 | Faisal street (Police station)
0.9 | 2.30-3.30 p.m. | 810 | 0.93 | 3.00-4.00 p.m. | 808 | Al-Quds street
0.84 | 7.15-8.15 a.m. | 1063 | 0.8 | 7.15-8.15 a.m. | 832 | Rfeedia street(Tunis)

## Slide 11: Data Collection and analysis : Safety analysis
Chart: No. of accidents in year 2014
| Alquds Street | Haifa Street | Rfeedia Street | Faisal Street
 | 50 | 23 | 106 | 91
Chart: No. of accidents in year 2015 (up to September)
| Alquds Street | Haifa Street | Rfeedia Street | Faisal Street
 | 39 | 30 | 93 | 61

## Slide 12: Data Collection and analysis : Safety analysis
Chart: No. of injuries
| Alquds Street | Haifa Street | Rfeedia Street | Faisal Street
2014 | 39 | 27 | 65 | 79
2015 | 45 | 31 | 88 | 52

## Slide 13: Data Collection and analysis : Safety analysis
Chart: %of accidents according to causes in year 2014 on Rfeedia Street
| Wrong rotate | Start ftom static | Moving backward | Deviation from the traffic route | Failure to take safety issues for pedestrians | Not to give the right of priority | Failure to compliance the traffic signal | Failure to maintain the distance
 | 10 | 2 | 3 | 19 | 17 | 6 | 6 | 31

## Slide 14: Data Collection and analysis : Safety analysis
Chart: %of accidents according to causes in year 2015 on Rfeedia Street (up to September)
| Wrong rotate | Start ftom static | Solar on Road | Deviation from the traffic route | Failure to take safety issues for pedestrians | Not to give the right of priority | Failure to compliance the traffic signal | Failure to maintain the distance
 | 10 | 1 | 2 | 10 | 9 | 4 | 9 | 33

## Slide 15: Data Collection and analysis : Environmental analysis
Air pollution : in Nablus city there are about 20,397 vehicles which contribute about 16.8 % of West Bank (Palestinian Central Bureau of statistics, 2010).
Chart: Vehicle Classification Percentage
| Other vehicles | Private cars | Trucks and commercial vehicles | Taxi
المبيعات | 0.76 | 14.2 | 7.3 | 2.5

## Slide 16: Data Collection and analysis : Environmental analysis
Table shows the amount of CO2 resulting from one ton of fuel
Fuel type | Ton CO2 per ton fuel
Gasoline | 3.047
Kerosene | 3.107
Diesel | 3.149

## Slide 17: Data Collection and analysis : Environmental analysis
Preliminary investigation of noise pollution
Ldn = 31.0+10.2 log {ADDT+%T*ADDT/ 20} - 13.9 log D +0.13S
Where:
Ldn: the equivalent sound level during 24 hours period in (dBA).
ADDT: Annual average daily traffic in (vehicles/day).
%T: Average percentage of trucks during a typical day.
D: Distance from edge of pavement to receiver in (m).
S: Average speed of traffic flow during one hour (km/hr.).

## Slide 18: Data Collection and analysis :
Table shows AADT of study area (east west direction)
Street Name | Peak hour volume | K factor | AADT
Haifa Street (west- Tunis) | 776 | 10% | 7760
Haifa Street (east-Al salam mosque) | 834 | 10% | 8340
Faisal Street (Al-watani) | 1837 | 8% | 18370
Faisal Street (police station) | 2039 | 8% | 20390
Al-Quds Street | 808 | 10% | 8080
Rfeedia Street (Tunis) | 832 | 10% | 8320
Rfeedia Street (badawi) | 834 | 10% | 8340

## Slide 19: Data Collection and analysis : Environmental analysis
% Of trucks (East west)
Street Name | East west
Haifa street (west- Tunis) | 4.7
Faisal street (Police station) | 2.4
Al-Quds street | 3
Rafeedia street (Badwi) | 3.5
Average speed(East west)
Street Name | Average Speed (Km/hr)
Haifa Street | 54.38
Faisal Street | 22.67
Al-Quds Street | 40.35
Rfeedia Street | 35

## Slide 20: Data Collection and analysis : Environmental analysis
Sample Calculation for Faisal Street (police station).
Ldn = 31.0+10.2 log {20390+0.024* 25488/ 20} - 13.9 log 1 +0.13*22.67=79.8 dBA
AADT = 2039/8% =24588
% Of Truck = 2.4%
D = 1 m
Avg. speed = 22.76 km/hr

## Slide 21: Conclusion
The sustainable ideas are still not clear. The purpose of the second semester is to develop and improve these ideas and to evaluate the existing indicators and their performance.
It is also expected that a model is needed to be found so that it can be possible to evaluate and design a sustainable system.
It is expected that various assumptions will be made specially when required data is not attainable
This is the first local study related to sustainable transport; therefore, it is expected to pave the road for future advanced work in this area.