## Slide 1
An-Najah National University
Faculty of Engineering and Information Technology
Industrial Engineering Department
Graduation Project (II)
Applying Lean Manufacturing Tools at Al -Karmel Islamic
Company
Supervisor Name:
Dr. Yahya Saleh

## Slide 2: The Team
Lamees Zamel
Sarah Arman
Yazan AL-Qadi
Baraa Yaseen

## Slide 3: Outline
About Graduation-Project (1) - Define Phase
Measuring Phase
Analyze Phase
Controlling Phase
Improvement Phase
Summary of Results
Conclusion and Recommendations

## Slide 4: Al -Karmel Islamic Company
Al-Karmel Islamic Factory was established in 2013 in the town of Dair Al-Ghosoun - Tulkarm . In 2019, the factory was moved to a new building in the same town, and it consists of two buildings, one of which is dedicated to manufacturing operations and the second for storage. The first building contains three main production lines (the production line of mortadella, sausages and pastrami). The total number of machines inside the factory is 15 machines, and 25 workers work inside it throughout the working period
Why Al -Karmel Islamic Company ???

## Slide 5: Products

## Slide 6: Problem Statement
There are several problems in its factory
Waste on raw materials at different levels of the production chain.
lost time and inefficient worker distribution to machines and work processes.
failure to use the full facilities capacity

## Slide 7: Objectives
Reducing the amount of the waste generated.
Increasing efficiency and production.
Reduced total costs.
Effective manpower utilization.
Reduce the amount of waste in weight produced throughout the manufacturing process.

## Slide 10
Define
Identify the project's challenge and objectives.
Measure
Take careful measurements of the current procedure
Analyze
Analyze the data acquired to determine the process's core causes.
Control
Improve
DMAIC
Improve the efficiency of the procedure.
Establish standards and controls to sustain improvements in the long run.

## Slide 11
Factory visits
Machines and production process tracking
Identify problems and set goals for the study
Define Phase

## Slide 12
FLOW PROCESS CHART

## Slide 13: Measuring Phase
Data Collection of Weights
Samples of size n = 4 were taken from the five different types of products at different times with an interval of 5 minutes between each sample
The tolerance for all the products’ weights is 5% of the product weight:
  The tolerance for Hotdog 1000g = 50 g
  The tolerance for Hotdog 400g = 20 g
  The tolerance for Pastrami 200g = 10 g
  The tolerance for Salami 1200g = 60 g
  The tolerance for Salami 800g = 40 g
An Electronic Measuring Scale had used for collecting the data

## Slide 14: Pareto Chart for Salami different Categories
Chart: Pareto Chart for Salami Categories
| Salami 1200 g | Salami 800 g | Salami 180 g | Salami 1000 g | Salami 400 g | Salami 1800 g | Salami 900 g | Salami 2000 g
Quantity | 144000 | 115200 | 90000 | 70000 | 50000 | 30000 | 26000 | 15000
Percent | 0.26657 | 0.47982 | 0.64643 | 0.77601 | 0.86857 | 0.9241 | 0.97223 | 1

## Slide 15: Cause and Effect Diagram for weight waste

## Slide 16
Analyze the collected data for the weight by applying some SPC tools
Normality test
Xbar-R Chart
Process Capability Analysis
Analyze Phase

## Slide 17: salami 800 g
Normality test
X bar – r Chart
Process Capability analysis

## Slide 18: salami 1200 g
Normality test
X bar – r Chart
Process Capability analysis

## Slide 19: Pastrami 200 g
Normality test
X bar – r Chart
Process Capability analysis

## Slide 20: Hotdog 400 g
Normality test
X bar – r Chart
Process Capability analysis

## Slide 21: Hotdog 1000 g
Normality test
X bar – r Chart
Process Capability analysis

## Slide 22: Losses Calculations

## Slide 23: Losses Calculations
Annual Production Quantity for the 5 products
Item | Annual quantity | Cost NIS/Kg
Hotdog 1000 g | 480,000 kg = 480,000 units | 8
Hotdog 400 g | 13,8240 kg = 345,600 units | 8
Pastrami 200 g | 36,000 kg = 180,000 units | 8
Salami 1200 g | 144,000 kg = 120,000 units | 7
Salami 800 g | 115,200 kg = 144,000 units | 7

## Slide 24: Sample Calculations for Hotdog 1000 g
Total annual production quantity for Hotdog 1000 g = 480,000 units
Shift in weight for Hotdog 1000 g = 22.00 g
Annual Losses in Kg = (Annual quantity Shift) / 1000
= (480,000 22.00) / 1000 = 10,560 Kg
Annual Losses in units = (Losses in Kg 1000) / The weight of the Hotdog 1000 g unit (g)
= (10,560 1000)/1000 = 10,560 units
Annual Losses in cost = Losses in Kg cost per Kg (NIS)
= 10,560 8
= 84,480 NIS

## Slide 25: Losses for the 5 products
Product | Annual Quantity |  | Shift in weight (g/unit) | Annual losses in quantity |  | Annual losses in cost (NIS/year)
 | Kg | Units |  | Kg | Units | 
Hotdog 1000g | 480,000 | 480,000 | 22 | 10,560 | 10,560 | 84,480
Hotdog 400g | 138,240 | 345,600 | -5.93 | 1,862 | 4,655 | (14,896)
Pastrami 200g | 36,000 | 180,000 | 24.66 | 4,439 | 22,194 | 35,504
Salami 1200g | 144,000 | 120,000 | 48.91 | 5,869 | 4,891 | 41,083
Salami 800g | 115,200 | 144,000 | 32.26 | 4,645 | 5,807 | 32,515
Total cost / year |  |  |  |  |  | 178,686

## Slide 26: Improvement Phase

## Slide 27: Some suggestions that have been taken and applied to solve the problem
Periodic maintenance of the machine control panels
Preventive maintenance of production machines to avoid sudden breakdowns
Provide workers with the necessary training
Scheduling for daily production

## Slide 30: Hotdog 1000 g After Improvement
X bar – r Chart
Process Capability analysis

## Slide 31: Hotdog 400 g After Improvement
X bar – r Chart
Process Capability analysis

## Slide 32: Pastrami 200 g After Improvement
X bar – r Chart
Process Capability analysis

## Slide 33: Salami 1200 g After Improvement
X bar – r Chart
Process Capability analysis

## Slide 34: Salami 800 g After Improvement
X bar – r Chart
Process Capability analysis

## Slide 35: Losses for the 5 products after Improvement
Product | Annual Quantity |  | Shift in weight (g/unit) | Annual losses in quantity |  | Annual losses in cost (NIS/year)
 | Kg | Units |  | Kg | Units | 
Hotdog 1000g | 480,000 | 480,000 | 5.93 | 2,846 | 2,846 | 22,771
Hotdog 400g | 138,240 | 345,600 | 4.18 | 1,444 | 3,611 | 11,552
Pastrami 200g | 36,000 | 180,000 | 5.71 | 1,027 | 5,135 | 8,216
Salami 1200g | 144,000 | 120,000 | 6.91 | 829 | 690 | 5,803
Salami 800g | 115,200 | 144,000 | 5.89 | 848 | 1,060 | 5,936
Total cost / year after Improvement |  |  |  |  |  | 54,278

## Slide 36: Saving
Annual Savings = Total annual cost before improvement – Total annual cost after improvement
= 178,686 - 54,278
= 124,408 NIS / year

## Slide 37
In the controlling phase, the manufacturer must use the following steps
continuous monitoring
written rules and instructions
commitment.
Controlling Phase

## Slide 38: Summery of Results

## Slide 39
Summary for the 5 products |  |  |  |  |  |  | 
 | Product | Normality | In control | Mean (g) | Cpk | Capability | Losses
Before | Hotdog 1000g | Normal | In control | 1022 | 0.37 | Incapable | 178,686
 | Hotdog 400g | Normal | In control | 394.61 | 0.31 | Incapable | 
 | Pastrami 200g | Normal | In control | 224.66 | -0.38 | Incapable | 
 | Salami 1200g | Normal | In control | 1248.91 | 0.26 | Incapable | 
 | Salami 800g | Normal | In control | 832.26 | 0.24 | Incapable | 
After | Hotdog 1000g | Normal | In control | 1005.93 | 5.04 | Capable | 54,278
 | Hotdog 400g | Normal | In control | 404.18 | 2.00 | Capable | 
 | Pastrami 200g | Normal | In control | 205.71 | 0.51 | Incapable | 
 | Salami 1200g | Normal | In control | 1206.91 | 4.91 | Capable | 
 | Salami 800g | Normal | In control | 805.89 | 3.49 | Capable | 

## Slide 40: Conclusion and Recommendations

## Slide 41
Conclusion

## Slide 42
Recommendations
Continuous random sampling after improvement to guarantee process stability.
Performing regular preventive maintenance
Follow the instructions by conducting work procedures on how to deal with sudden malfunctions that occur to the machines.
Modernization of some machines due to the age and due to the inconsistency in the production capacity of the machines.
Distributing employees with a new organizational structure correspond with their abilities and experience after training.
Adding a monitoring worker to compensate and solve any defect that occurs during work or the default of one of the workers.