## Slide 1: Smart Fuel Theft Detector
Supervisor: Dr. Samer Mayaleh
Prepared by:
Amjad Rabaya Adham Sawafta
An-Najah National University
Faculty of Engineering

## Slide 2: شكر وتقدير

## Slide 3: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 4: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 5: Review
What is smart fuel theft detector ?
Why to use smart fuel theft detector ?

## Slide 6: Review
What is Theft?
The fuel is being stolen from the vehicle's tank through withdrawing using a pipe.
The tank is filled with amount less than written in the bill.

## Slide 7: Review

## Slide 8: Review
Why to use smart fuel theft detector ?
Helps the companies to monitor and identify exactly its fuel consumption periodically and in real-time.
Prevents fuel theft from the vehicles tanks.
Helps identifying the fuel thief (the driver or other people).

## Slide 9: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 10: Limitations & Challenges
The flammability of the fuel
Accurate and Safe Isolation

## Slide 11: Limitations & Challenges
Dynamic motion of the fuel
Multi Readings per Second

## Slide 12: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 13: Solutions
Ultrasonic Sensor
Flammability
no electrical connection between the sensor and the tank.
Spark-Free device
  Accurately closed Tank
Small size, no need to make large holes in the tank.
Dimension: 45mm x 20mm x 15mm

## Slide 14: Solutions
Dynamic motion of the fuel
Averaging and filtration (100 readings)
we did a simple averaging for the values because the normal decreasing of the fuel level is small and so no needed to make a complicated filtering.

## Slide 15: Solutions
  Slope of the roads
  Using LSM303DLH sensor to
  Determine the slope.
  Find the actual level considering the slope of the road.
  It is fitted outside the tank

## Slide 16: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 17: Used Devices
Ultrasonic Sensor (HC-SR04)
Slope Sensor (LSM303DLH)
Microcontroller (PIC16f877)
GPRS Module (not available!)

## Slide 18: Used Devices Ultrasonic Sensor
Fitted on the tank directly
Connected wired to the controller

## Slide 19: Ultrasonic Principle of Work
Transmitter
Receiver
Some Object
Output: Time of Flight (uSec)

## Slide 20: Used Devices Ultrasonic Sensor
Trigger
Echo
5 volt
10 uSec
PWM depends on the distance

## Slide 21
Filters the readings (50 to 1)
Converts the readings to volume
Theft detection
Pass readings to GPRS module
Used Devices
Microcontroller

## Slide 22
Converts from PWM time to digital volume
PWM signal
Digital
Time (uSec)
Volume signal
(Liter)
Used Devices
Microcontroller

## Slide 23
Filtering and averaging
i.e. Microcontroller is
faster than the sensor
3
…
9
10
1
2
1
Give one reading
Used Devices
Microcontroller

## Slide 24
Check For Fuel Theft
NO
YES
Used Devices
Microcontroller

## Slide 25
Receives readings from the microcontroller
Sends it to the company for further processing.
Used Devices
GPRS Module

## Slide 26: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 27: Measuring Scenarios
Flat-Road & Stopping Probable Theft!
Flat-Road & Moving Impossible Theft.
Tilted-Road & Stopping Probable Theft!
Tilted-Road & Moving Impossible Theft.

## Slide 28: Theft Detecting
The principle of Theft-Detecting is based on the Consumption Rate and the Fuel Change of the vehicle.
Fuel Change ≥ Consumption Rate
Fuel Change ≤ Consumption Rate
THEFT
Normal

## Slide 29: Case Study 50-passengers-bus

## Slide 30: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 31: Hardware Tutorial

## Slide 32: OUTLINE
Review
Limitations & Challenges
Solution methods
Used Elements
Measuring & Theft
Hardware Tutorial
Database
The End

## Slide 33: Database

## Slide 34: THANKs For Listening