## Slide 1: Drawbot
Hardware Graduation Project

## Slide 2: Outlines
Introduction.
Hardware.
Software.
Problems.
Future work

## Slide 3: Introduction
What is Drawbot ?
Simply it’s a 2D CNC robot that can draws any thing.
Why Drawbot (a robot for drawing) ?
Advertising, like stores and adv. companies .
Events.

## Slide 4: How it works ?
G-Code
Image
GRBL Sender
Controller
Motors
Drawbot

## Slide 5: Hardware

## Slide 6: Hardware parts
Stepper motors (X & Y axes)
2x NEMA 17 with 50N.cm for Y-axis. (approx. 2A).
1x NEMA 17 with 30N.cm for X-axis. (approx. 1.3 A)

## Slide 7: Hardware parts
Nema 17 mounting L Bracket for stepper motor.
Quantity : 2.

## Slide 8: Hardware parts
3D printed module for x-axis

## Slide 9: Hardware parts
Servo motor (Z axis)

## Slide 10: Hardware parts
3D printed module for servo 3D printed module for pin

## Slide 11: Hardware parts
GT2-6mm open timing belt ,6mm width
Quantity : 3 m.

## Slide 12: Hardware parts
GT2 Timing Pulley 16 teeth Bore 5mm
Quantity : 6.

## Slide 13: Hardware parts
8mm linear shaft
SHF8 8mm Aluminum Linear Rod Rail Shaft Support
SC8UU 8mm Router Motion Slide Unit Block Bearing
Quantity : 2m.
Quantity : 6.
Quantity : 8.

## Slide 14: Hardware parts
Easy drivers (A3967)
L298N driver
Quantity : 3.
Quantity : 3.

## Slide 15: Software

## Slide 16: Software part
Inkscape
It is a professional vector graphics editor for Windows, Mac OS X and Linux. It's free and open source
Image
G-Code
PC

## Slide 17: Software part
GrblPanel (G-Code sender)
It is a professional vector graphics editor for Windows, Mac OS X and Linux. It's free and open source
PC
Arduino
baud rate 115200

## Slide 18: Software part
Grbl servo firmware
An open source, embedded, high performance g-code-parser and CNC milling controller written in C.
G-Code
X step and direction
Y step and direction
Servo angle
Arduino

## Slide 19: Problems

## Slide 20: Problems
Weight of X-axis make high load on stepper motors.
Power of stepper motors.
Friction.
Weight of body (MDF wood).

## Slide 21: Future work

## Slide 22: Future works
Make it light.
Make it scalable.
Communicate wirelessly by mobile App.

## Slide 23: Thanks all