## Slide 1: Graduation Project II Structural Analysis and Design of multi-functional building in Nablus city -Palestine.
An-Najah National University Faculty of Engineering Civil Engineering Department
جامعة النجاح الوطنية
كلية الهندسة ونكنولوجيا المعلومات
By
Abdul-Aziz Al-Kharraz
Ahmad Khasati
Mjd Salameh
Ekrayem Boshnaq
Under supervision of: Dr.Mahmoud Dwaikat.

## Slide 2: Outline : 1. General Description 2. Preliminary Design 3.Three-Dimensional Modeling and Analysis 4.Design 5.Footing

## Slide 3: General Description

## Slide 4: General Description
Location
It is located in Nablus – Palestine, and the coordinates of the project according to the global coordinate system WGS are 32°13′35″N, 35°15′52″E. Location elevation (site level) is +657m AMSL (above mean sea level). Soil Type white limestone (γ = 23.652), very hard to solid and The allowable bearing is 470 KN/m2 (4.7 Kg/cm2).

## Slide 6: General Description
All supports are Pin supporter in the 3D.
As for the external walls, part of them are made of glass walls and the other part are stone walls, and they are added as dead loads on the external beams.
The slab system is two-way ribbed slab.
In preliminary design chapter, a quick preliminary was performed, so the thicknesses of retaining and shear walls were taken from architectural plans.
Seven checks were made include compatibility check, equilibrium check, stress-strain check, time period, base shear ,story drift , and P-delta.
Assumptions

## Slide 7: Architectural Plans

## Slide 8: Basement three

## Slide 9: Basement two

## Slide 10: Basement one

## Slide 11: Ground floor

## Slide 12: floor 1-7

## Slide 13: floor 8-11

## Slide 14: General Description
Floor Number | Height of each floor (m) | Area of each floor (m2)
B3 | 4.50 | 142
B2 | 4 | 290.5
B1 | 2.75 | 362.5
GF | 4.50 | 290.5
F1-7 | 3 | 290.5
F8-11 | 3 | 260.5
Height and Area For Each Floor

## Slide 15: General Description
Codes and Standard.
ASCE 7-16 (American Society of Civil Engineers)
IBC 19 (International Building Code)
ACI 318-19 (American Concrete Institute)

## Slide 16: General Description
Ultimate load combinations:
1.4D
1.2D + 1.6L
1.2D + 1.6L + 0.5(Lr or S or R)
1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
1.2D + 1.0E + 1.0L + 0.2S
0.9D + 1.0W
0.9D + 1.0E
Service load combinations:
D + L
D + 0.75L
D + 0.7E
D + 0.75L + 0.75(0.7E)
0.6D + 0.7E
Load Combinations

## Slide 17: General Description
Ultimate load combinations: (lateral load)
1.4D
1.2D + 1.6L
1.29D + L + Ex
1.29D + L - Ex
1.29D + L + Ey
1.29D + L - Ey
0.9D + 1.0Ex
0.9D - 1.0Ex
0.9D + 1.0Ey
0.9D - 1.0Ey
Load Combinations

## Slide 18: General Description
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, fc | 28 Mpa
Linear modulus of Elasticity,Ec | 4700 = 24870 Mpa
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, fc | 28 Mpa
Linear modulus of Elasticity,Ec | 
Construction Materials
Structural Elements

## Slide 19: General Description
Non- Structural Elements :
Material | Unit weight ɣ(KN/m3)
Masonry stone | 26
Cement mortar &Plaster | 23
Partition blocks | 12
Filing material aggregate | 14
Glass | 25
Tiles | 26
Ytong Block | 5
Reinforce concrete | 25
Construction Materials.

## Slide 20: General Description
Gravity loads :
Dead load
Super imposed dead load
Live load
Lateral loads :
Soil load
Seismic load
Loads

## Slide 21: General Description
The floor layers:
Finishing materials weight = Σ (thickness of layer × unit weight for each layer)
Element | Thickness (cm) | Unit weight (KN/m^3)
Filling | 5 | 14
Mortar | 2 | 23
Tiles | 1.5 | 26
Ytong Block | 17 | 5
Plaster | 1.5 | 23
SD= Tile weight + Mortor weight + Filling weight + Block weight + Plaster weight + SD of Partitions
SD = (0.015×26) + (0.02×23) + (0.05×14) + (0.17×5) + (0.015×23) + 1
= 3.68 KN/m2
Superimposed Dead load calculation

## Slide 22: General Description
Exterior wall load
-Stone wall :
SD masonry wall = unit weight × thickness
= (0.05×26) + (0.085×25) + (0.1×12) + (0.015×23)
= 4.97 KN/m2
- Glass wall :
SD glass = ɣ glass × thickness × story height
= 25 × 0.05 ×4
= 5 KN/m

## Slide 23
Occupancy | Live Load (KN/m2 )
B3 (Storage) | 6
B2 (Warehouse) | 6
B1 (Garage) | 1.92
GF (Commercial) | 2.5
F1-11 (Residential) | 2.5
Live Load

## Slide 24
Lateral Load
Seismic loads:

## Slide 25
Lateral Load
Seismic loads:
According to ASCE 7-22 code to seismic analysis for this structure:
- Risk category: risk category of the building is II

## Slide 26
Lateral Load
Importance factor : (Ie) = 1
Zone factor (Z) for Nablus = 0.2
- Mapped acceleration parameters Ss & S1 :
From Palestine seismic map:
Ss= (2.5Z) *1.5= 2.5 *0.2 *1.5 = 0.75
S1 = (1.25Z) *1.5 = (1.25 *0.2) *1.5 = 0.375
Site Class
Site classification is B

## Slide 27
Site Coefficients
- The values of Fa and Fv According to the site class in this project are 0.90 ,0.80 respectively.

## Slide 28
Seismic Design Category
-The maximum considered earthquake Spectral Response Acceleration
Parameters SMS and SM1:
SMS =Fa SS = 0.90 × 0.75 = 0.675
SM1 = Fv S1= 0.80 × 0.375= 0.30
Design spectral acceleration :
SDS= 2 SMS /3 = 2*0.675/3 =0.45
SD1= 2 SM1 /3 =2*0.300/3 =0.20
Seismic Design Category :
Seismic design category D

## Slide 29
Lateral Force Resisting System
Type of the lateral forces resisting system :
Moment – resisting frame: special reinforced concrete moment frames.
Response Modification Factor (R) = 8
Over-strength Factor (Ωo) = 3
Deflection Amplification Factor (Cd) = 5.5

## Slide 30
Structural Period
for Moment – resisting frame:
Ta = Ct hn x = 0.0466 × 48.75 0.90 = 1.54sec
T from ETABS ≤ Ta Cu
The period is limited to Tu = Ta Cu= 1.54× 1.5= 2.31sec

## Slide 31: General Description
Computer Programs

## Slide 32: Structural Preliminary Design

## Slide 33: 1. Slab System 2.Beam System 3. Column System 4. Wall System
Preliminary Design
Structural Systems for analysis and design

## Slide 34: Slab Preliminary dimensions

## Slide 35: Using two-way ribbed slab, must
Preliminary Design
Slab System
By referring to Table 8.3.1.1 in ACI-318-19:
h = 250mm
Thickness = = = 0.21954 m

## Slide 36
Preliminary Design
Slab System
Check Slab for shear
Vu =14.13 kN/m
ØVc= 20.83 kN/m
Vu < ØVc ----> Ok

## Slide 37: Beams Layout

## Slide 38
Preliminary Design
Beam Layout

## Slide 39
Preliminary Design
Beam System
Beam number | Height (mm) | Width (mm)
B1 | 250 | 700
B2 | 250 | 450
B3 | 250 | 300
B4 | 250 | 250

## Slide 40: Column Layout

## Slide 42
Preliminary Design
Column System
R: Rectangular column
Column | Type | Dimension
C1 | R | 800*300
C2 | R | 1000*400

## Slide 43: Wall Layout

## Slide 44
Preliminary Design
Types of walls in this structure will be used:
1.Basement retaining walls
2. Elevators and staircase walls. (Shear walls).
From architectural plans, elevators and staircase walls have an initial thickness equal to 200 mm , retaining walls have an initial thickness equal to 300 mm
Wall System
Wall name | Wall thickness (mm)
Wall 1 | 200
Wall 2 | 300

## Slide 45: 3D-Modeling and Analysis

## Slide 46: 3D-Modeling and Analysis

## Slide 47: 3D-Modeling and Analysis

## Slide 48: Verification of Structural Analysis

## Slide 49: 3D-Modeling and Analysis
Compatibility Check

## Slide 50: 3D-Modeling and Analysis
Equilibrium Check
1.Dead Load.
1.1.Beam weight.
1.2.Columns weight

## Slide 51: 3D-Modeling and Analysis
Equilibrium Check
1.3.Slab weight.

## Slide 52: 3D-Modeling and Analysis
Equilibrium Check
1.4.Shear wall weight.
Total dead load = 12146.75 + 5944.5 + 10608.836 + 3540.78 = 32240.86 KN.
From ETABS → total dead = 32649.38 KN. See Figure.

## Slide 53: 3D-Modeling and Analysis
Equilibrium Check
2.Super Imposed Dead Load.
SD load on slab = load * total area for slab
= 3.68 KN/m2 *3531.57 m2 = 12996.18 KN
From ETABS → total SD= 12979.15 KN. See figure.

## Slide 54: 3D-Modeling and Analysis
Equilibrium Check
3.Live Load.
From ETABS → 9993.34 KN. See figure.

## Slide 55: 3D-Modeling and Analysis
Equilibrium Check
4.soil Load.
See figure.

## Slide 56: 3D-Modeling and Analysis
Stress Strain Load
From live load =1.92 KN/m2
See figure.
Exterior negative moment = 8.746 KN.m/m
Positive moment = 10.6262 KN.m/m
interior negative moment = 7.411 KN.m/m

## Slide 57: 3D-Modeling and Analysis
Deflection Check
Allowable Deflection = L/240 =
23 mm < 26.25 mm → ok

## Slide 58: 3D-Modeling and Analysis
Verification of the preliminary design

## Slide 59: 3D-Modeling and Analysis
Seismic Analysis Methods
1.Equivalent lateral force method (ELF).
Seismic loading in Y-direction
Seismic loading in X-direction

## Slide 60: 3D-Modeling and Analysis
Seismic Analysis Methods
  2.Modal response spectrum method (MRS).
Definition of MRS in ETABS

## Slide 61: 3D-Modeling and Analysis
Period
Ta=Ct* Hn^x
=0.0466*48.75^0.9=1.54 s.
Tu= Ta *Cu =1.54*1.5=2.31s.
→T from Etabs in X direction =2.708s
T Etabs >Tupper ------Take Tupper.
→ T from Etabs in Y direction =1.356s
T Etabs <Tupper ------Take T Etabs.

## Slide 62: 3D-Modeling and Analysis
Base Shear Check
→ V manually = Cs * Building weight
-Where:
V: seismic base shear.
Cs: seismic response coefficient.
W: effective weight.
W = D+ SD+ 0.25 L =35512.41+12977+0.25*9991.95
=50987 Kn.

## Slide 63: 3D-Modeling and Analysis
Base Shear
Cs=SDS*I/R=0.45*1/8=0.056
Cs min=0.044*SDs*I=0.044*0.45*1=0.0198
Take Cs=0.0198
V=0.0198*50987.39=1009Kn.

## Slide 64: 3D-Modeling and Analysis
Base Shear Check
Base shear from Etabs (X direction) = 993.3074 KN
Base shear from Etabs (Y direction) = 991.7654 KN

## Slide 65: 3D-Modeling and Analysis
Response spectrum
→ Define load case in both directions (Ex and Ey initial)
Factor=9810/R = 9810/8 =1226.25. See figure
The values of dynamic earthquake forces must be approximately equal to the value of earthquake forces in the static method. However, the values were not equal, which led to a change in the scale factor for each of the dynamic earthquake forces in X and Y.

## Slide 66: 3D-Modeling and Analysis
V(EX)= 369.33 V(ELF-X) =993
modified factor=993/369.33=2.688
Total factor=2.688*1226.25 =3296.16.
→ 0.3Ey must be added to Ex =0.3*1581.86 =474.56.
Check base shear from response compared to ELF:
Response spectrum
V(EY)= 763.635 V(ELF-Y) =991
modified factor=991/763.635=1.29
Total factor=1.29*1226.25=1581.86.
→ 0.3Ex must be added to Ey = 0.3*3296.16=988.

## Slide 67: 3D-Modeling and Analysis

## Slide 68: 3D-Modeling and Analysis
Story Drift
𝜕𝑥 =𝐶𝑑 ∗ 𝜕𝑥𝑒/𝐼𝑒
The allowable drift = 0.02 hx

## Slide 69: 3D-Modeling and Analysis
Story Drift
Drift in X-Direction |  |  |  |  | 
Story | Delta(elastic) | H | Drift | allowable | 
15 | 0.001561 | 3 | 0.0085855 | 0.06 | OK
14 | 0.001697 | 3 | 0.0093335 | 0.06 | OK
13 | 0.001802 | 3 | 0.009911 | 0.06 | OK
12 | 0.0105454 | 3 | 0.0579997 | 0.06 | OK
11 | 0.001948 | 3 | 0.010714 | 0.06 | OK
10 | 0.002008 | 3 | 0.011044 | 0.06 | OK
9 | 0.00205 | 3 | 0.011275 | 0.06 | OK
8 | 0.00206 | 3 | 0.01133 | 0.06 | OK
7 | 0.002032 | 3 | 0.011176 | 0.06 | OK
6 | 0.001934 | 3 | 0.010637 | 0.06 | OK
5 | 0.001771 | 3 | 0.0097405 | 0.06 | OK
4 | 0.001249 | 4.5 | 0.0068695 | 0.09 | OK
3 | 0.000272 | 2.75 | 0.001496 | 0.055 | OK
2 | 8.70E-05 | 4 | 0.0004785 | 0.08 | OK
1 | 2.10E-05 | 4.5 | 0.0001155 | 0.09 | OK

## Slide 70: 3D-Modeling and Analysis
Story Drift
Drift in Y-Direction |  |  |  |  | 
Story | Delta(elastic) | H | Drift | allowable | 
15 | 0.000579 | 3 | 0.0031845 | 0.06 | OK
14 | 0.000585 | 3 | 0.0032175 | 0.06 | OK
13 | 0.000587 | 3 | 0.0032285 | 0.06 | OK
12 | 0.003981 | 3 | 0.0218955 | 0.06 | OK
11 | 0.000571 | 3 | 0.0031405 | 0.06 | OK
10 | 0.000558 | 3 | 0.003069 | 0.06 | OK
9 | 0.000536 | 3 | 0.002948 | 0.06 | OK
8 | 0.000506 | 3 | 0.002783 | 0.06 | OK
7 | 0.000468 | 3 | 0.002574 | 0.06 | OK
6 | 0.00042 | 3 | 0.00231 | 0.06 | OK
5 | 0.00036 | 3 | 0.00198 | 0.06 | OK
4 | 0.000264 | 4.5 | 0.001452 | 0.09 | OK
3 | 0.000243 | 2.75 | 0.0013365 | 0.055 | OK
2 | 6.50E-05 | 4 | 0.0003575 | 0.08 | OK
1 | 1.10E-05 | 4.5 | 0.0000605 | 0.09 | OK

## Slide 71: 3D-Modeling and Analysis
Effect of P-delta
The values of θ in X direction less than 0.1neglect effect of P-delta.
P-Delta in X-Direction |  |  |  |  |  | 
Story | Delta(elastic) | H | P | V | Theta | 
15 | 0.001561 | 3 | 3630.8094 | 260.3228 | 0.007257264 | OK
14 | 0.001697 | 3 | 6956.9113 | 409.0381 | 0.009620847 | OK
13 | 0.001802 | 3 | 10283.013 | 490.003 | 0.012605358 | OK
12 | 0.0105454 | 3 | 13652.49 | 536.0515 | 0.089525583 | OK
11 | 0.001948 | 3 | 17471.52 | 577.9581 | 0.019629174 | OK
10 | 0.002008 | 3 | 21290.55 | 629.437 | 0.022640034 | OK
9 | 0.00205 | 3 | 25109.58 | 677.5426 | 0.025324183 | OK
8 | 0.00206 | 3 | 28928.61 | 721.0305 | 0.027549892 | OK
7 | 0.002032 | 3 | 32747.64 | 766.185 | 0.028950016 | OK
6 | 0.001934 | 3 | 36566.67 | 827.5974 | 0.028484035 | OK
5 | 0.001771 | 3 | 40385.7 | 903.9142 | 0.026375319 | OK
4 | 0.001249 | 4.5 | 44158.367 | 972.6869 | 0.01260056 | OK
3 | 0.000272 | 2.75 | 48984.728 | 995.69 | 0.004866007 | OK
2 | 8.70E-05 | 4 | 54108.254 | 1348.8225 | 0.000872505 | OK
1 | 2.10E-05 | 4.5 | 58853.95 | 1420.52 | 0.000193346 | OK
𝜃 =𝑃𝑥∗ ∆ / 𝑉𝑥∗ℎ𝑥

## Slide 72: 3D-Modeling and Analysis
Effect of P-delta
The values of θ in Y direction less than 0.1neglect effect of P-delta.
𝜃 =𝑃y∗ ∆ / 𝑉y∗ℎy
P-Delta in Y-Direction |  |  |  |  |  | 
Story | Delta(elastic) | H | P | V | Theta | 
15 | 0.000579 | 3 | 3630.8094 | 208.7228 | 0.003357306 | OK
14 | 0.000585 | 3 | 6956.9113 | 356.9285 | 0.003800755 | OK
13 | 0.000587 | 3 | 10283.0132 | 445.5816 | 0.004515543 | OK
12 | 0.003981 | 3 | 13652.4901 | 491.5601 | 0.036855828 | OK
11 | 0.000571 | 3 | 17471.5201 | 521.6355 | 0.006374974 | OK
10 | 0.000558 | 3 | 21290.5501 | 553.349 | 0.0071565 | OK
9 | 0.000536 | 3 | 25109.5801 | 595.7701 | 0.007530161 | OK
8 | 0.000506 | 3 | 28928.6101 | 649.4521 | 0.007512936 | OK
7 | 0.000468 | 3 | 32747.6401 | 713.9394 | 0.007155554 | OK
6 | 0.00042 | 3 | 36566.6701 | 788.7751 | 0.006490233 | OK
5 | 0.00036 | 3 | 40385.7001 | 868.4401 | 0.005580447 | OK
4 | 0.000264 | 4.5 | 44158.3665 | 936.9396 | 0.002764985 | OK
3 | 0.000243 | 2.75 | 48984.7283 | 987.2354 | 0.004384434 | OK
2 | 6.50E-05 | 4 | 54108.2544 | 1003.1682 | 0.000876482 | OK
1 | 1.10E-05 | 4.5 | 58853.95 | 1120.25 | 0.000128422 | OK

## Slide 73: Design

## Slide 74: Design
Design of Slab
Check for Shear:
Hand Calculation:
KN/m
KN/m
From Etabs:
KN/m. See figure.
< (No need for Shear Reinforcement).
Design of Moment:
    = 0.0033 , = 150 mm
    d= 210 mm
  As,min =
  = 0.0033 * 150 * 210 = 103.95 mm²/m → 2∅12/m

## Slide 75: Design
Design of Slab
Design of Moment:
→For positive moment
Let a = = =3.34 mm
∅Mn =∅*As *Fy (d- )
= 0.9*103.95*420*(210- ) * /0.55
= 14.88 KN.m/m.
→For negative moment
Let a = =12.22 mm.
∅Mn =∅*As *Fy (d- a/2)
= 0.9*103.95*420*(210- )* /0.55
= 14.56 KN.m/m

## Slide 76: Design
Design of Slab
Design of Moment:
The moment of slab has been shown
between the ranges of minimum moment as shown in figure:
In x direction, all reinforcement is minimum. See figure:
Take 2∅12 for positive moment and negative moment.

## Slide 77: Design
Design of Slab
Design of Moment:
In y-direction, reinforcements for all slab are minimum
except the following panels. See Figures
For panels in figures above for M11, maximum
moment = 35kN.m/m
→For positive moment
∅Mn =∅*As *Fy (d- a/2)
35*0.9 = 0.9*As*420*(210- )* /0.55
As = 220mm2 → Take 2∅12.
→ For negative moment
∅Mn =∅*As *Fy (d- a/2)
35*0.9 = 0.9*As*420*(210- )* /0.55
As= 225 mm2 → Take 2∅12.

## Slide 78: Design
Design of beam
Beam has been selected in fourd story. See figure:
Beam dimensions = 700 X 250mm.
Effective depth = 215 mm.
Flexural Design:
→ For positive moment = 20.444 KN.m
Where: f’c = 28 MPa, Fy = 420 MPa.
𝜌𝑚𝑖𝑛=0.0033
0.0033 > 0.00168 →Take ρ = 0.0033
→ As = ρ *b*d =0.0033*700* 215 = 501 mm2
→ Use 4∅14

## Slide 79: Design
Design of beam
Flexural Design:
→ For negative moment = 43.7448 KN.m
Where: f’c = 28 MPa, Fy = 420 MPa.
𝜌𝑚𝑖𝑛=0.0033
0.0033 < 0.00369 →Take ρ = 0.00369
→ As = ρ *b*d =0.00369*700* 215 = 555 mm2
→ Use 4∅14

## Slide 80: Design
Design of beam
Design beam for shear:
First, we will make sure to calculate the strength of the shear :
→As =569 mm2 from Etabs .
→As =398mm2 from Etabs .

## Slide 81: Design
.
=(1.38*21.9)+9.15+(2*3.15) =46 Kn.
→ Vg= 1.2D+1.6L = (12*20.9)+(1.6*9.15) =39 Kn.
→ The value of shear design = the max value of (V1,V factored ,Vg) = 61 Kn.

## Slide 82: Design
→The value of V from load case (Dead , Live .E, 1.2D+1.6L). See figure:

## Slide 83: Design
→The summary shear details from Etabs. See the figure:

## Slide 84: Design
Calculate of Av /s :
→∅Vc =99.546 KN.
Assume Av = 2 * 78.5 = 157 mm2
→ Take S = 270mm
→Smax = d/2 = 107.5 mm
→ on the side beam :
S max = min (d/4,6db,150mm)
= min (215/4,6*10,150)
Take S= 60mm.
→ at the middle beam :
S = d/2=215/2 =107.5mm. → Take S=100mm. See the figure:

## Slide 85: Design
Design of columns
Column at grid (5G) has been selected. See figure:
Axial load from ETABS = 4475.81 KN See figure:

## Slide 86: Design
Design of columns
Ultimate moment M3 from ETABS = 101.108 KN.m. See figure:
𝜌 𝐹𝑟𝑜𝑚 𝐸𝑇𝐴𝐵𝑆 = 0.01 See figure:

## Slide 87: Design
Design of columns
➔ As = 0.01 * 1000 * 400 =4000 mm2
➔ Use 16∅18.
Shear design for the column:
Use Av /s min =
Assume Av = 2 * 78.5 = 157 mm2
→ S=270mm.
On the side column:
S max = min (b/4, 6db, h/4, Sₒ)
= min (1000/4, 6*18, 400/4, 100)mm.
Take S= 100mm.
at the middle column:
S =6db=6*18=108mm. → Take S=100mm.
→ Distance between reinforcement bars
= (=153mm > 150mm
→All steel bars must be connected with one stirp

## Slide 88: Footing

## Slide 89: Footing
This project is a design for some types of footing, which the Mat foundation and Wall Footing
Ultimate load combinations:
1.4D
1.54D
1.2D + 1.6L
1.32D+1.76L
1.1D+1.1L (Service load)

## Slide 90: Footing
Mat foundation Layout (AutoCAD drawing): See Figures:
→Allowable bearing capacity of soil = 470 Kn/m2
→All dimensions were assumed and checked on Etabs.
Strip name | Thickness(m)
1 | 0.45
2 | 0.75
3 | 0.45
4 | 0.65
5 | 0.35

## Slide 91: Footing
Mat Foundation and Wall footing checks :
Check soil pressure :
The pressure must be less than q allowable =470 kn/m2. → Ok. See figure:

## Slide 92: Footing
Check Punching shear :
Check punching shear for mat foundation (less than (1) to get a high factor of safety ). OK. See figure:

## Slide 93: Footing
Design for Mat Foundation and Wall footing :
Sample calculation:
Strip 1: (h=450mm)
Area of steel (Top in X direction) from Etabs for (Strip1) =Area of steel min
As min = ρ *b*h =0.0018*1000*450=810mm2. →(4∅16/m). See figure
→ All stirps the As min > As from Etabs
→ Take As min.

## Slide 94: Footing
→Table of steel reinforcing for all stirps: See Table below:
Stirps | Direction(x) Top (As min) | Direction(x) Bottom (As min) | Direction(y) Top (As min) | Direction(y) Bottom (As min)
2 | 1386 mm2 (6∅18/m) | 1386 mm2 (6∅18/m) | 1386 mm2 (6∅18/m) | 1386 mm2 (6∅18/m)
3 | 810 mm2 (4∅16/m) | 810 mm2 (4∅16/m) | 810 mm2 (4∅16/m) | 810 mm2 (4∅16/m)
4 | 1080 mm2 (6∅16/m) | 1080 mm2 (6∅16/m) | 1080 mm2 (6∅16/m) | 1080 mm2 (6∅16/m)
5 | 630 mm2 (4∅14/m) | 630 mm2 (4∅14/m) | 630 mm2 (4∅14/m) | 630 mm2 (4∅14/m)