## Slide 1
Graduation project ( 2 )
July 5th, 2020
Students:
Eng. Omair Zanabeet
Eng. Khalil Odetallah
Eng. Amer Omair
AN-NAJAH NATIONAL UNIVERSITY (NNU)
Faculty of Engineering & Information Technology
Presented in partial fulfillment of the requirements for
Bachelor degree in Mechanical Engineering
Supervisor : Eng. Ramez Alkhaldi

## Slide 3
The effect of cooling on the solar PV performance

## Slide 5
1
6
5
2
4
3
What is Pv cell ?

## Slide 6: Introduction
Year _end | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Cumulative | 178.4 | 229.3 | 306.5 | 403.3 | 512 | 633 | 770
Annual new | 40.1 | 59.9 | 76.8 | 99 | 109 | 121 | 121-154
Cumulative growth | 28% | 29% | 32% | 32% | 27% | 24% | 
Recent and estimated capacity in all world (Gwp)

## Slide 7
The percentage of the renewable electricity using at the end of 2017

## Slide 8: Solar Energy Advantages
Saves you money
After the initial investment has been recovered, the energy from the sun is practically FREE.
Environment friendly
Solar Energy is clean, renewable (unlike gas, oil and coal), sustainable and helping to protect our environment. As we see previously ,it does no pollute air.
Low/ no maintenance
Solar Energy systems are virtually maintenance free and will last for decades.

## Slide 9: Solar panel (or) solar array (or) Solar module
The solar panel (or) solar array is the interconnection of number of solar module to get efficient power.
• A solar module consists of number of interconnected solar cells.
• These interconnected cells embedded between two glass plate to protect from the bad whether.
• Since absorption area of module is high, more energy can be produced.

## Slide 10: The internal structure of the PV cells
Frame
Glass cover
Polymer sheet
Cells
Backing material

## Slide 11: Types of Solar cell
3
The film
1
Mono-crystalline silicon
2
Poly-crystalline silicon

## Slide 12: How to connect the solar panel array
1. Series connection

## Slide 13
2. parallel connection

## Slide 14
3. combined connection

## Slide 15: Solar cell problems
Dust :
The dust is conceded from the one of the main problems that can the solar cells suffered from , and that cause of its direct impact on the absorption of the fallen radiations , because the accumulation of dust atoms and accumulation on the glass surface of the cell prevent the arrival of sunlight to the silicon ions inside the cell , which leads to the lack of the activation capacity of the electrons and their inability to convert the fallen rays into electricity adequately
Temperature :
the rise in temperature above the specified rate of the cell directly reduces the efficiency of the cell so that each rise in temperature by one degree leads to reduce efficiency by an estimated of (0.25%-0.45%) , This percentage is considered high if it continues under the influence of high temperatures.

## Slide 16: Solar cell cooling methods
1
Air cooling
2
Water cooling

## Slide 17: Objective of the project
What we aims to do to get rid of temperature problem ?
After reviewing the effect of high temperature on the efficiency of the cell, it was worked to provide the cells with a water cooling system to ensure the preservation of the temperature and prevent its rise to the extent that affects the value of efficiency.
Various designs have been put in place to eliminate these problems
Our project Divided to three parts :
Standard cell
Backward heat extraction by using fluid circulation
Addition of a water box in the rear of the cell

## Slide 18: Solid-work design

## Slide 19: 1. Standard cell

## Slide 20: Objective of standard cell
The importance of the primary cell lies in studying the ideal angles for fixing the solar cell, where three cells of the same type were installed and each of them was installed at a different angle, namely:
So that was taken reading of: the voltages and current, including calculating the electrical power of each.
The study was carried out over three different days, taking into account the climatic conditions for a single day.
The importance of the cell was also important in the process of studying the effect of the water cooling system on the solar cells, so that the process of comparing the values ​​that were taken for each of the cells equipped with the cooling system with the basic values ​​of the basic cell.

## Slide 21: 2. Backward heat extraction by using fluid circulation

## Slide 22: Objective of the cell :
The main principle used in this system is the process of adding background paths to the solar cell, allowing water to move with the direction of the tracks laid, the goal of adding these paths is to allow water to stay as long as possible and is in contact with the surface of the cell, allowing heat to move as far as possible from the surface The cell into the water entering it.
Aluminium sheets were used in making the tracks laid in addition to making sure the cell was closed from the back by an aluminium plate and insulating materials in order to reduce the chance of rising from the water temperature due to the sunlight on the back of the cell, that is, the heat exchange is limited to the water temperature Inlet and cell surface temperature.

## Slide 23: 3. Addition of a water box in the rear of the cell

## Slide 24: Objective of the cell :
The principle of the box is the process of adding an aluminium box to the back of the cell, which is completely immersed in the water entering it so that it comes in contact with the back surface of the cell at the same time, which allows water to stay in contact with the cell surface long enough to effectively cool the cell .

## Slide 25: Main component
Multi-meter
Load
Measuring cup
Wooden stand
Thermometer

## Slide 26
Pipe and fitting
Y-connection
½ inch elbow fit
16mm pipe
Fitting transition from 1/2 to 3/4
1/2 inch inlet fit

## Slide 27: Full connection

## Slide 28: Insulation

## Slide 29: Practical process

## Slide 32: Results
Optimum tilt angle study results :
Day : Sunday date : 14/6/2020 |  |  |  |  |  |  |  |  | 
Hours ( pm ) | Θ = 25 |  |  | Θ = 29 |  |  | Θ = 40 |  | 
 | V | A | P | V | A | P | V | A | P
12:00 | 25.3 | 0.23 | 5.819 | 27 | 0.26 | 7.02 | 25 | 0.24 | 6
12:10 | 30.4 | 0.24 | 7.296 | 32.1 | 0.28 | 8.988 | 32 | 0.26 | 8.32
12:20 | 24.7 | 0.21 | 5.187 | 26.7 | 0.24 | 6.408 | 25.3 | 0.24 | 6.072
12:30 | 25.8 | 0.2 | 5.16 | 27.3 | 0.22 | 6.006 | 26.7 | 0.22 | 5.874
12:40 | 29.3 | 0.28 | 8.204 | 30.8 | 0.29 | 8.932 | 29.1 | 0.27 | 7.857
12:50 | 31.4 | 0.31 | 9.734 | 31.7 | 0.31 | 9.827 | 30.6 | 0.3 | 9.18
1:00 | 27.6 | 0.27 | 7.452 | 30.5 | 0.3 | 9.15 | 28.2 | 0.31 | 8.742
1:30 | 30.2 | 0.28 | 8.456 | 32.3 | 0.32 | 10.336 | 32 | 0.28 | 8.96
2:00 | 29.7 | 0.25 | 7.425 | 31.4 | 0.28 | 8.792 | 30.1 | 0.26 | 7.826
2:30 | 26.6 | 0.24 | 6.384 | 29.7 | 0.27 | 8.019 | 28.9 | 0.25 | 7.225

## Slide 33
Day : Sunday date :14.6.2020 |  |  |  |  |  | 
Power electrical (Pelec) |  |  | Power input (Pin) | Efficiency ( ) |  | 
Θ = 25 | Θ = 29 | Θ = 40 |  | Θ = 25 | Θ = 29 | Θ = 40
5.819 | 7.02 | 6 | 62.0165 | 0.09383 | 0.113196 | 0.096748
7.296 | 8.988 | 8.32 | 62.0165 | 0.117646 | 0.144929 | 0.134158
5.187 | 6.408 | 6.072 | 62.0165 | 0.083639 | 0.103327 | 0.097909
5.16 | 6.006 | 5.874 | 62.0165 | 0.083204 | 0.096845 | 0.094717
8.204 | 8.932 | 7.857 | 62.0165 | 0.132287 | 0.144026 | 0.126692
9.734 | 9.827 | 9.18 | 62.0165 | 0.156958 | 0.158458 | 0.148025
7.452 | 9.15 | 8.742 | 62.0165 | 0.120162 | 0.147541 | 0.140962
8.456 | 10.336 | 8.96 | 62.0165 | 0.136351 | 0.166665 | 0.144478
7.425 | 8.792 | 7.826 | 62.0165 | 0.119726 | 0.141769 | 0.126192
6.384 | 8.019 | 7.225 | 62.0165 | 0.10294 | 0.129304 | 0.116501
Efficiency calculation results :

## Slide 34
Day: Sunday date :14/6/2020 |  | 
Condition | Symbols | Value
Temperature | T(℃) | 27-21
Humidity |  | 57%
Wind speed | V(km/h) | 15
Atm. Pressure | P (hpa) | 1006
Cell area | A( ) | 1015
Flow rate | Q(L/s) | 0.208
Position |  | 32.3,35.0
Conditions :

## Slide 35: Average efficiency of Tilt angle :
Tilt angle | Average Efficiency ( )
Θ = 25 | 0.114674
Θ = 29 | 0.134606
Θ = 40 | 0.122638

## Slide 36: Results of the designs applied to the cells for the first day :
Day : Wednesday date : 17.6.2020 |  |  |  |  |  |  |  |  |  | 
 | Volt (V) |  |  | Current (A) |  |  | Power (W) |  |  | 
Hours | standard | box | circulation | standard | box | circulation | standard | box | circulation | 
1:20 | 25.5 | 26.3 | 26.8 | 0.27 | 0.31 | 0.32 | 6.885 | 8.153 | 8.576 | 
1:50 | 59.3 | 60.3 | 62.1 | 0.28 | 0.32 | 0.35 | 16.604 | 19.296 | 21.735 | 
2:20 | 60.3 | 61.5 | 62.5 | 0.27 | 0.29 | 0.31 | 16.281 | 17.835 | 19.375 | 
2:50 | 51.5 | 53.2 | 54.1 | 0.26 | 0.3 | 0.33 | 13.39 | 15.96 | 17.853 | 
3:40 | 48 | 49.7 | 51.3 | 0.26 | 0.3 | 0.31 | 12.48 | 14.91 | 15.903 | 

## Slide 37: Conditions :
Day: Wednesday date :17.6.2020 |  | 
Condition | Symbols | Value
Temperature | T(℃) | 31-33
Humidity |  | 55%
Wind speed | V(km/h) | 18
Atm. Pressure | P (hpa) | 1012
Cell area | A( ) | 1015
Flow rate | Q(L/s) | 0.20
Position |  | 32.3,35.0

## Slide 38: Flow rate calculation :

## Slide 39: Results for calculation the efficiency for the previous tables :

## Slide 40: Average efficiency of previous table :

## Slide 41: Results of the designs applied to the cells for the first day :

## Slide 42: Conditions :

## Slide 43: Flow rate calculation :

## Slide 44: Results for calculation the efficiency for the previous tables :

## Slide 45: Average efficiency of previous table :

## Slide 46: Results of the designs applied to the cells for the first day :

## Slide 47: Conditions :

## Slide 48: Flow rate calculation :

## Slide 49: Results for calculation the efficiency for the previous tables :

## Slide 50: Average efficiency of previous table :

## Slide 51: Results of the designs applied to the cells for the first day :

## Slide 52: Conditions :

## Slide 53: Flow rate calculation :

## Slide 54: Results for calculation the efficiency for the previous tables :

## Slide 55: Average efficiency of previous table :

## Slide 56: Calculation equations :

## Slide 57
Positions :

## Slide 58: Sample of calculations for the tilt-angel practical study:
For 14/6/2020 at 12:00 pm

## Slide 59: Sample of calculations for the designs applied to the cells :
For 17 /6/2020 at 3:40 Pm