## Slide 1
AN-Najah National University
Faculty Of Engineering
Mechanical Engineering Department
Graduation project2

## Slide 2: Compressed air engine
Prepared by:
Bahaa Ahmad Hamed
Mahmoud A. Kittaneh
Rafeeq Al- Shami
Tareq A. Khraim
Supervisor :
Dr. Iyad Assaf

## Slide 3
Outline:
Introduction
Importance of the project
Components of the project
Design and calculations
Problems and development
Recommendations
Constrains

## Slide 4
Introduction
In the last time all of the manufacturing and development were depend on non renewable energy which mainly cause global warming and pollution for the environment so we need an alternative energy which be environmentally friendly .

## Slide 5
importance of the project
The pneumatic car is environmentally friendly.
It depends on renewable energy.
Cheaper than other renewable energy cars.

## Slide 6
Components of the project
Air compressor
Air motor
bearings
Worm gear
valves

## Slide 7
Air Compressor:
decrease the volume of the air
Increase the pressure of the air

## Slide 8
Air compressor
The main characteristics of the compressor used:
Volume: 25 L
High pressure: 8 bar
Separated head and motor

## Slide 9
Valve:
to control the flow of the air from the compressor to the air motor
Ball valve used:
Ball valve

## Slide 10
Air Motor:
The type of air motor used in this project is (1/2" SQ. Drive Pistol Grip Air Impact Wrench) which is used to assemble the cars wheel's screws.

## Slide 11
Air motor characteristics:
Average air consumption= 5 CFM @ 90 PSI
Housing material is Cast aluminum
Maximum speed (rpm)= 7000 RPM
Maximum Torque (ft. - lbs.)=250 ft. lbs.
Working pressure (psi)=90 PSI
Air inlet size= 1/4 in
Drive size (in.)=1/2 in.
Product Weight=3.7 lb.
Recommended hose size (in.)=1/2 in.

## Slide 12
NRMV Gearbox:
It is worm gear, NRMV040 worm gearbox
It used to have a high torque
Used to convert the rotation from the air motor to the shaft.

## Slide 13
Gear box characteristics:
Gear ratio 20:1
Gearing Arrangement: Worm
Output Torque: 16-53NM
Rated Power: 0.09 kw
Input Speed: 1400rpm
Output Speed: 14-186.7RPM
Material: Aluminum, Cast Iron Housing

## Slide 14
Ball bearings
There are two ball bearings used in the project of the type shown in the figure

## Slide 15
Manufacturing
1. Collecting the parts and establishing the body

## Slide 16
2. air motor selection:
There are a lot of types of air motor in different application:
1/2'' ratchet wrench
High torque
Low velocity
1/2'' impact wrench
High torque
High velocity

## Slide 17
3. First assembly trial:
Making a connection between the air motor and the drive shaft by using chain and chain wheel.
It was used two chainwheels, the drive has diameter of 12cm, where the driven has diameter 4 cm (ratio 3:1).

## Slide 18
But when connecting it we obtained that the project can't move, that is because there is no enough torque to transmit the car.
so we have to find an alternative solution which is using gearbox

## Slide 19
4. Using gearbox
By using the gearbox -which make the same operation of the back axle in normal cars- to have a higher torque .
By applying this idea we obtained that the car moved.

## Slide 20
Design
The dimensions of the project:
Back width = 82cm
Length= 140 cm
Mass = 70kg
diameter of the wheel = 28 cm
Shaft diameter = 18 mm
Front width= 40 cm

## Slide 21
Calculations
shaft velocity = 8m in 29 sec. → Velocity =
Angular velocity, w= = 19.1 R.P.M
→ W worm = 20*2= 40 rad/ sec = 382 rpm
→ Power of worm = 0.09 kw
→ p= T*W → 90= T * 40 → T= 2.25 N.m
→ Gear diameter = 8 cm
→ Worm diameter= 15mm
→ Lead, L= þx * N worm where þx: circular pitch , N: worm teeth
→ þx =
→ L= 0.013* 4 = 0.052 m
→ Lead angle
→ = 14.5

## Slide 22
Gear forces:
Worm (N) | Gear (N)
Wt = 300 | Wt= 308
Wa= 308 | Wa= 300
Wr= 111 | Wr= 111

## Slide 23
Reactions of bearings and gear forces
A
B

## Slide 24
Bearings selection
There is two ball bearings one has thrust force which is A and the other has no thrust force which is bearing B
Bearing A and B:
→ desired radial load is 5000 hours, Nd = 1800 rpm rating life 106 rev., ball bearing, a= 3
For bearing B:
→ Fb =
→ C10=

## Slide 25
The value of C10=2.6 KN, but this value does not exist in the appendix so take the next one higher than it which is 4.94 KN

## Slide 26
For bearing A:
Fe = → Fe= where Az and Ay are the reactions at point A. and Fe is the same of Fr in the equation:
Fe= X2Fr + Y2 Fa → Fe= (0.56)(0.00184)+ (1.63)(0.3) = 0.49KN
C10=
By using appendix 2 , the final value of Y2 and X2 is 1.38 and 0.56 respectively so the final value of Fe and C10 is:
Fe= X2Fr + Y2 Fa → Fe= (0.56)(0.00184)+ (1.38)(0.3) = 0.41KN
→ C10=
It is the same bearing used at point B

## Slide 27
Problems and developments:
There are some problems faced when applying the project like:
Solution | Problem
Using cove for it consist of Rockwool | noise sound exit from the air motor
using dampers and springs | high vibration produced from the system
put two pulleys the large one on the shaft, and the small one connected with the compressor head to charge it when the car moving | no self-charging for the compressor

## Slide 28
Recommendation
To increase the velocity of the car we can use larger compressor ,air motor with higher torque and velocity, in addition to a larger gearbox with smaller gear ratio

## Slide 29
Constrains:
Because of the high cost of the project we could not complete the full idea of this project like putting the Rockwool cover for the air motor and two pulleys between the compressor and the shaft to charge the compressor.
The total cost of the project is 2900 NIS

## Slide 30
Thank you