## Slide 1: Graduation Project
Presentation and Discussion

## Slide 2
An-Najah National University
Chemical Engineering Department
Turning Waste into Wealth: Bioethanol Synthesis from Food Waste
Graduation Project (II) Presentation
Supervised By:
Dr. Majd Eshtaya
Prepared By:
Omnia Atatrah
Roaa Alqasarwa
Sep 19, 2024
Thursday

## Slide 3: Importance of The Research!

## Slide 4: Table of contents 01 03 02 04
Introduction and overview
Objectives
Methodology
Results and findings
Conclusion
05
Future work
06

## Slide 5: Introduction and overview 01

## Slide 6: General Background
Bioethanol as an alternative fuel
Derived from biomass like sugarcane and corn, bioethanol offers a renewable solution amid concerns about diminishing fossil fuel reserves.
Key production steps
1.Feedstock preparation
2. Saccharification: Converting carbohydrates into fermentable sugars.
3. Fermentation: Using yeast or bacteria to produce ethanol.
4. Separation and purification of the final product.
Environmental benefits
Bioethanol emits lower greenhouse gases and is biodegradable, reducing environmental impact.
01
03
02

## Slide 7: Challenges
Food security and land use
Feedstock competition with food crops.
Production costs
Bioethanol must be competitive with fossil fuels.
Conversion efficiency
Maximizing ethanol yield is vital for sustainability.
01
03
02

## Slide 8: Innovations and solutions
Exploring alternative feedstocks
like cellulose-rich materials to avoid food competition.
Research focus
Optimizing processes, reducing waste, and enhancing bioethanol sustainability.
Integration with biorefineries
Maximizing ethanol yield is vital for sustainability.
01
03
02

## Slide 9: What is Brix Meter?

## Slide 10
Measures sugar content in liquids, particularly in food and beverages
Ensures quality control and product consistency in various industries.
1° Brix = 1 gram of sucrose per 100 grams of solution.
Brix scale
Definition
Importance

## Slide 11: Objective 02

## Slide 12
Sub-Objectives:
1. To determine the optimal fermentation time for complete substrate conversion.
2. To investigate the relationship between pH and fermentation efficiency.
3. To evaluate the impact of fermentation time on ethanol yield.
4. To assess the effects of substrate concentration on ethanol production.
Main Objective
To optimize the ethanol production process from dates.
Objectives

## Slide 13: Methodology 03

## Slide 14
1
3
2
4
5
Dates Pretreatment
Periodic Monitoring
Fermentation
Sugar Quantification
Analysis

## Slide 15
Dates Pretreatment
3. The mixture was sieved to separate the pulp and the juice that contains the sugar.
2. The mashed date and water mixture was subjected to thermal hydrolysis by heating at 90°C for about 30 minutes with continuous stirring.
1. Fresh dates were manually destoned, and the pulp was mashed. Then, 740 g of mashed dates was mixed with 1750 mL of deionized water, creating a water-to-date ratio of 2.3:1.
5. The sieved juice was filtered using a vacuum filtration system to separate the liquid phase from any solid residues.

## Slide 16
Sugar Quantification
Refractometry was used to determine the sugar concentration in dates and the extracted solution by measuring the Brix value, representing total soluble solids, mainly sugars. A densitometer (Mettler Toledo) was also used for easier handling, with both devices giving nearly identical readings. To establish a correlation, standard glucose solutions (0-100 g/L) were prepared, and their Brix values were measured to create a calibration curve for estimating glucose concentration in unknown samples.

## Slide 17
Fermentation
Two substrates were prepared: a glucose solution and a date extract solution, both with a Brix value of nearly 8.
Glucose solution: made by dissolving 20 g of anhydrous D-glucose in 200 mL of deionized water.
Date extract solution: prepared similarly after the sugar extraction process.
Saccharomyces cerevisiae (baker’s yeast): 3.5 g added to each solution.
Yeast was mixed thoroughly to ensure uniform fermentation.
Both solutions were incubated at 30°C, the optimal temperature for yeast activity.
This temperature facilitates the conversion of sugars into ethanol and CO2.
Fermentation progress was periodically monitored for sugar consumption and ethanol production.

## Slide 18
Periodic Monitoring
Samples were collected hourly to monitor sugar consumption and ethanol production.
A 10 mL aliquot from each flask was taken every hour for pH and Brix analysis.
Samples were centrifuged at 4,000 rpm for 10 minutes to separate yeast and solids.
pH of the clarified supernatant was measured using a calibrated pH meter.
Brix values, indicating sugar concentration, were measured using a densitometer.

## Slide 19
Analytical Methods
Reduced Sugar Content
Ethanol Distillation
Ethanol Estimation
A stock glucose solution was diluted to 0, 2, 4, 6, 8, 10, and 12 g/L. Each sample was mixed with phenol and sulfuric acid, reacted for 10 minutes, and incubated at 40°C. Absorbance was measured at 490 nm, and a calibration curve was used to determine glucose concentrations in unknown samples.
Ethanol concentration was estimated using the chromic acid method by measuring absorbance at 584 nm. Chromic acid was prepared by dissolving potassium dichromate in water and adding sulfuric acid. 1 mL of ethanol samples was diluted to 5 mL with water, and 5 mL of chromic acid was added. After incubating at 60°C for 20 minutes, absorbance was measured.
After fermentation, a distillation apparatus was assembled, consisting of a heating source, condenser, and collection flask, to separate ethanol from the broth. The clarified broth was heated in the distillation flask, causing ethanol to evaporate first due to its lower boiling point. The vapor then passed through the condenser, where it was cooled and collected in the receiving flask for further analysis or purification.

## Slide 20: Results 04

## Slide 21
1.Calibration Curves
Standard Curve for Glucose (Concentration-Absorbance).
Relationship Between Ethanol Concentration and Density.

## Slide 22
A calibration curve was created by measuring the Brix values of standard glucose solutions with known concentrations. This curve was used to estimate the glucose concentration in unknown samples.

## Slide 23
2. Glucose Consumption Over Time
The sugar consumption rates were measured during glucose and date fermentations. Brix values were recorded hourly, and a direct relationship between sugar concentration and time was determined.

## Slide 24
3. The Behavior of pH
The pH of glucose and date solutions decreased during fermentation. This is typical as sugars are converted to ethanol. Both solutions had similar pH profiles, indicating comparable fermentation dynamics.
Glucose is converted into ethanol and carbon dioxide during fermentation. However, the process also produces small amounts of organic acids, which can lead to a decrease in pH.

## Slide 25
4. Ethanol Distillation
Volume (ml) | Alcohol % | Alcohol Quantity ml
5 | 59.4 | 2.97
8 | 38.3 | 3.064
6 | 22.6 | 1.356
5 | 14.4 | 0.72
6 | 10.3 | 0.618
8 | 4.1 | 0.328
6 | 2 | 0.12
7.5 | 0.9 | 0.0675
51.5 | Total | 9.2435 ml
 | Yield | 17.95%
The distillation process produced 51.5 mL of distillate containing 9.2435 mL of ethanol (17.95% yield). Alcohol concentration was highest in the initial sample and decreased in later fractions, consistent with distillation principles.
Distillation of 100 g/l Glucose Fermented for 24 hrs.

## Slide 26
4. Ethanol Distillation
A 48-hour fermentation yielded 15.02% ethanol, lower than the 17.95% from a 6-hour fermentation. Most of the sugar was consumed within the first 6 hours, and extending fermentation didn't significantly increase ethanol production.
Distillation of 100 g/l Glucose Fermented for 48 hrs.
Volume (ml) | Alcohol % | Alcohol Quantity ml
5 | 45.3 | 2.265
7 | 37.9 | 2.653
9 | 19.2 | 1.728
8 | 12.8 | 1.024
6 | 4.9 | 0.294
5 | 4.2 | 0.21
6 | 2.6 | 0.156
5 | 1 | 0.05
5 | 0.6 | 0.03
56 | Total | 8.41 ml
 | Yield | 15.02%

## Slide 27
4. Ethanol Distillation
Dates (13.8%) produced similar ethanol yields to glucose (15.01%) in the same time, suggesting dates are a promising substrate for bioethanol. This led to an experiment doubling the substrate concentration.
Distillation of 100 g/l Dates Fermented for 48 hrs.
Volume (ml) | Alcohol % | Alcohol Quantity
16 | 34.2 | 5.472
12 | 12.3 | 1.476
10 | 5.3 | 0.53
9 | 3.2 | 0.288
10 | 1 | 0.1
57 | Total | 7.866 ml
 | Yield | 13.8%

## Slide 28
4. Ethanol Distillation
Distillation | Total Distillate (mL) | Ethanol Volume (mL) | Yield (%) | Fermentation Time (hours)
Distillation 1 | 51.5 | 9.24 | 17.90 | 24
Distillation 2 | 56.0 | 8.41 | 15.02 | 48
Distillation 3 | 57.0 | 7.86 | 13.87 | 48
The data shows a decrease in ethanol yield with longer fermentation time. This suggests that most ethanol production occurs within the first 24 hours. The distillation process is efficient, but optimizing fermentation conditions and exploring continuous fermentation could improve ethanol yield.

## Slide 29
5. Doubling The Substrate Concentration (200 g/l) of Glucose
Brix Value: The brix value, a measure of sugar concentration, decreased during fermentation but followed a similar trend to the initial concentration.
pH Decrease: The pH of the fermentation medium gradually decreased over time.

## Slide 30
Ethanol Distillation
Doubling the substrate concentration significantly increased ethanol yield from 15.01% to 34.54%, demonstrating a 129.5% improvement. This is due to increased sugar availability, leading to more efficient yeast metabolism and higher ethanol production.
Distillation of 200g/l Glucose Fermented for 24 hrs.
Volume ml | Alcohol% | Alcohol Quantity ml
4 | 58.8 | 2.352
3.8 | 59.2 | 2.2496
4 | 56.5 | 2.26
4.4 | 23.1 | 1.0164
4 | 7.2 | 0.288
4 | 2.2 | 0.088
4 | 0.6 | 0.024
6 | 0.2 | 0.012
 | Total | 8.29 ml
 | Yield | 34.54%

## Slide 31: Conclusion 05

## Slide 32: Glucose fermentation
A 100 g/L glucose solution was fully metabolized in 6 hours, much faster than the expected 72 hours, showcasing yeast efficiency.
Acidity
Organic acid production lowered pH during fermentation, indicating yeast metabolic activity.
Dates vs. glucose
Dates produced 91.3% of the ethanol yield compared to glucose, though at a slower rate, suggesting dates need further optimization for ethanol production.

## Slide 33: SO!

## Slide 34
Both glucose and dates are viable for ethanol production. Dates require optimization, and future research should focus on enhancing fermentation efficiency and managing higher substrate concentrations.

## Slide 35: Future Work 06

## Slide 36: To enhance biofuel production in the future, focus on these key areas:

## Slide 37
Process Efficiency and Mass Balance
Improve accuracy in CO2 production measurements, and refine sugar consumption and ethanol production rates to enhance efficiency..
Enzymatic Hydrolysis
Optimize hydrolysis conditions by testing different enzymes, concentrations, pH levels, and temperatures to improve sugar yields.
Substrate Exploration
Evaluate alternative feedstocks, such as agricultural and food waste, based on sugar content and fermentation efficiency.
01
03
02

## Slide 38
Analytical Method Development
Use techniques like HPLC to accurately measure sugars, ethanol, and byproducts.
Yeast Growth and Fermentation Optimization
Study yeast growth rates and behavior under various conditions, and optimize fermentation parameters to boost ethanol production.
Rapid Quantification Methods
Develop innovative methods for quick and accurate measurement of key components.
04
06
05

## Slide 39
Thanks!