## Slide 1
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project II
Structural Analysis and Seismic Design of Palestine Mall in Ramallah City
Prepared by :
Ahmad Kittaneh
Muhammad Jarrar
Muhammad Zakarneh
Supervisor :
Munther Diab

## Slide 2: Outline
Background Information.
Preliminary Design.
Project Modeling.
Model Checks.
Design.

## Slide 3: Location: The project addresses is the analysis and design of Palestine mall (12536.54 m2) located in Ramallah.

## Slide 5
Basement Floor

## Slide 6
Ground Floor

## Slide 7
Floors, areas and heights

## Slide 8
Codes and Standards
American Concrete Institute (ACI 318- 2014).
American Society for Civil Engineering – Minimum Design Loads for Buildings and Other Structures (ASCE 7-2010).
International Building Code (IBC- 2015).

## Slide 9
Concrete:
Property | Value
Compressive strength of concrete, (fʹϲ) | 28 MPa
Modulus of elasticity, (Eϲ) | 24.87×10³ 𝑀𝑝𝑎
Unit weight of plain concrete, 𝜸 | 23 𝑘𝑁/
Unit weight of reinforced concrete, 𝜸 | 25 𝑘𝑁/
Property | Value
Compressive strength of concrete, (fʹϲ) | 28 MPa
Modulus of elasticity, (Eϲ) | 24.87×10³ 𝑀𝑝𝑎
Unit weight of plain concrete, 𝜸 | 
Unit weight of reinforced concrete, 𝜸 | 
Reinforced Steel:
Property | Value
Steel Grade | Grade 60
Yield strength (Fy) | 420 𝑀𝑝𝑎
Ultimate strength (Fu) | 620 𝑀𝑝𝑎
Materials
Structural Materials:

## Slide 10
Non Structural Elements:
Material | Unit weight, 𝜸 in KN\m³
Plaster | 23
Tiles | 25
Sand | 16
Masonry stone | 27
Block | 12
Concrete mortar | 23

## Slide 11
Gravity
Lateral
Loads
Dead
Live
Soil
Loads:
Seismic

## Slide 12
  Gravity Load:
I. Dead Load:
  Slab superimposed dead load= 4.6 KN/m².
  Superimposed dead load of external walls = 21 KN/m.
II. Live Load:
  The maximum value of the live load which was obtained from table 4-1 in ASCE7-10 is 4.8 KN/m², But we used a live load value of 5 KN/m²

## Slide 13: Lateral load:
  I .Seismic Loads:
1. Mapped Spectral Response Acceleration Parameters:
Ss and S1 parameters were obtained from Spectral Response (Ss=0.375 and S1 = 0.1875 ).
2. Site Coefficients and Adjusted Maximum Considered Earthquake (MCEᴿ) Spectral Response Accelerations(SMS & SM1):
By assuming Site Class is B, we obtained values of Fa and Fv from tables 11.4-1 and 11.4-2 in ASCE 7-10 where both coefficients equal 1.
SDs = SMS = = 1 × 0.375 = 0.375
SD1 = SM1 = = 1 × 0.1875 = 0.1875

## Slide 14
3.Importance Factor (Ie) and Risk Category:
The risk Category was decided to be Ш from table 1.5-1 in ASCE7-10, so the Importance Factor is equal 1.25 according to table 1.5-2 in ASCE7-10.
4. Seismic Design Category:
According to the tables 11.6-1 and 11.6-2 in ASCE7-10, Since the value of SDs= 0.375, and the Risk Category is Ш. So, it’s found that the seismic design category is C.

## Slide 15
5. Design Coefficients and Factors for Seismic Force-Resisting Systems:
Since the Seismic Design Category is C, considering the type of Seismic Force-Resisting System is Intermediate reinforced concrete moment frame, from table 12.2-1 it’s found that the response modification coefficient (R=5)and over strength factor (Ωo=3) and deflection amplification factor(Cd=4.5).
6. Structure Fundamental Period:
From table 12.8-2 below, it’s found that values of Ct and x equals 0.0466 and 0.9, respectively.
Since = 52 m, then T= = 1.63 sec.
T=Cu*Ta = 1.53 * 1.62 = 2.5 sec.

## Slide 16
  II. Soil Load:
Ɣ = 20 kN/m³
Ø = 30˚
Ko =1-sin (Ø) =1-sin (30) =0.33
the value of the surcharge live load (w) = 15 KN/m²
The figure below shows the total earth pressure on the basement shear wall including seismic earth pressure .

## Slide 17: Load Combinations
Ultimate Load Combinations Service Load Combinations

## Slide 18: Preliminary Design

## Slide 19
The structural system used is two way solid slab
Slab thickness
Slab thickness =220 mm

## Slide 20
Slab

## Slide 21: Beams
Beam | Dimensions (mm)
B1 | 500*800
B2 | 500*1500
B3 | 300*220

## Slide 22
Beam II

## Slide 23
Beam III

## Slide 24: Columns
Columns dimensions are shown in the table:
Group No. | Dimensions (mm)
G1 | 1100*1100
G2 | 400*1800
G3 | 1000*1000
G4 | 900*900

## Slide 25
The following figure shows the distribution of columns in the seventh floor:

## Slide 26: 3-D Modeling
Structural Modeling using ETABS.

## Slide 27: Seismic loading data according to Equivalent Static Method .
X-direction:

## Slide 28: Check Base Shear Equilibrium
Cs = 0.0937
in X-direction = = 0.0432
in Y-direction = = 0.0381
Difference percentage for Vx = × 100% = 1.7 % → OK.

## Slide 29: Response Spectrum Function
X-direction

## Slide 30: Checking for Dynamic Response Spectrum Analysis
X-Direction:
The scale factor = (𝑔 𝐼)/𝑅 = (9810 × 1.25)/5 = 2043.05
After multiplying with the scale factor

## Slide 31
Y-direction:
The scale factor = (𝑔 𝐼)/𝑅 = (9810 × 1.25)/5 = 2043.05
After multiplying with the scale factor

## Slide 32
Drift Check:
Drift limitations under earthquakes are imposed on inelastic displacements. The story drift, , is defined as the relative displacements between adjacent story displacements, . The story displacement, x, at level x is calculated as follows:

## Slide 33
Drift in X-directions:
Story | ᶋxe from etabs | Cd | Height | ᶋx(m) | Allowable (m)
1 | 0.0003 | 4.5 | 4 | 0.00108 | 0.06
2 | 0.00024 | 4.5 | 4 | 0.000864 | 0.06
3 | 0.00244 | 4.5 | 4 | 0.0088 | 0.06
4 | 0.00724 | 4.5 | 4 | 0.0261 | 0.06
5 | 0.0119 | 4.5 | 4 | 0.043 | 0.06
6 | 0.0136 | 4.5 | 4 | 0.0489 | 0.06
7 | 0.0164 | 4.5 | 4 | 0.058 | 0.06
8 | 0.01435 | 4.5 | 4 | 0.051 | 0.06
9 | 0.01377 | 4.5 | 4 | 0.0495 | 0.06
10 | 0.0125 | 4.5 | 4 | 0.045 | 0.06
11 | 0.01189 | 4.5 | 4 | 0.042 | 0.06
12 | 0.0018 | 4.5 | 4 | 0.00648 | 0.06
13 | 0.006 | 4.5 | 4 | 0.0216 | 0.06

## Slide 34
Drift Y-direction
All values of drift are less than 0.015hx, so it is OK.
Story | ᶋxe from etabs | Cd | Height | ᶋx(m) | Allowable (m)
1 | 0.0003 | 4.5 | 4 | 0.00108 | 0.06
2 | 0.0002 | 4.5 | 4 | 0.00072 | 0.06
3 | 0.00069 | 4.5 | 4 | 0.00248 | 0.06
4 | 0.00235 | 4.5 | 4 | 0.00846 | 0.06
5 | 0.0044 | 4.5 | 4 | 0.0144 | 0.06
6 | 0.00487 | 4.5 | 4 | 0.0175 | 0.06
7 | 0.00498 | 4.5 | 4 | 0.0179 | 0.06
8 | 0.00482 | 4.5 | 4 | 0.0173 | 0.06
9 | 0.00444 | 4.5 | 4 | 0.0159 | 0.06
10 | 0.00394 | 4.5 | 4 | 0.0141 | 0.06
11 | 0.00345 | 4.5 | 4 | 0.0125 | 0.06
12 | 0.00278 | 4.5 | 4 | 0.00972 | 0.06
13 | 0 | 4.5 | 4 | 0 | 0.06

## Slide 35: Model Checks
Compatibility Check:
To ensure that the model will behave as one static unit.

## Slide 36
Equilibrium Checks:
To ensure that the model is satisfied Newton’s Law for statics and equilibrium objects.
Load Type | Hand Cal. (KN) | ETABS Results(KN) | Difference %
Dead | 149604.37 | 144143.48 | 3.6
SD | 54908.08 | 54572.48 | 0.6
Live | 59387.5 | 58385.83 | 1.67

## Slide 37
Stress-Strain relationship Check.
To ensure that the load will be distributed in an expected way in both structural element Slabs and Beams.
3(from ETABS) should equal ( manually )
3 = = 159.665 kN.m
= = 165.01 kN.m
Difference equals 3.24% < 10%

## Slide 38
Mass participation ratio check.

## Slide 39: Design
After building the 3D model using ETABS and make the checks, then we can make the design process and preparing the detailing sheets for all members.

## Slide 40
Slab Design:
Check Slab thickness for shear:
ØVc=0.75 ×××b×d
ØVc: design shear capacity (KN).
Vu: ultimate shear at distance d from face of the support(KN) .
d: effective depth(mm)
b:width of the section(mm).
: concrete compressive strength.
ØVc= 0.75 ×××1000×180×10-3 = 119.06 KN .

## Slide 41
Shear Values:
Maximum value of V13

## Slide 42
Maximum Value of V23
The maximum shear value of the slab equals 61.11 kN
ØVc = 119.06 kN > Vu=61.11 kN  The slab thickness is adequate to resist shear.

## Slide 43
Design for Flexure:
Maximum negative value
ρ = (1- ) = 0.0034  Use ρ = 0.0034 As = 0.0034*180 *1000= 612 mm ²  Use 1ø16/25 cm Top steel

## Slide 44
Maximum positive value
ρ = (1- ) = 0.0025
 Use ρ = 0.0025 As = 0.0025*180 *1000= 450 mm ²  Use 1ø16/20 cm Bottom steel.

## Slide 45
The slab should be designed also for axial tension force:
F11 = 217kN.
Tu = 0.9*As*Fy As (top + bottom)= 217*1000/(0.9*420) = 574 mm/1m
As top = As bottom = 287mm2
Total Top steel in slab = 612+287 =899 mm = (5Ø16 mm/1m) = 1 Ø16 mm/20cm.
Total Bottom steel in slab =450+287= 737mm = (4Ø16 mm/1m) = 1 Ø16mm/25cm.

## Slide 46
Openings:
Minimum area of steel was added in the corners of the openings due to the concentrated load over it
Asmin =0.0018 = 396 mm2.
396/154 = 2.57  use 3 Ø14 / 1 m.

## Slide 47
The Maximum spacing between main bars According to ACI 318‐14 SECTION (7.6.5):
Smax
S =250 which is less than 660 and 450 so , using S =250 is OK

## Slide 48
Beam Design.
Design for Flexure:
The value of moment in span 1 of the beam shown in Figure is taken as sample calculation.

## Slide 49
Results from ETABS
Longitudinal Reinforcement:

## Slide 50
Longitudinal Reinforcement for Beam 7 :
Span number | location | As (mm2) | As required ( mm2) | bars
1 | Negative – Left | 3639 | 3639 | 8Ø25
 | Positive | 2069 | 2069 | 5Ø25
 | Negative -Right | 3239 | 3239 | 7Ø25
2 | Negative – Left | 3972 | 3972 | 9Ø25
 | Positive | 2487 | 2487 | 5Ø25
 | Negative -Right | 3909 | 3909 | 8Ø25
3 | Negative – Left | 3535 | 3535 | 8Ø25
 | Positive | 2208 | 2208 | 5Ø25
 | Negative -Right | 3829 | 3829 | 4Ø25

## Slide 51
Shear Reinforcement:

## Slide 52
Span number | location | (Av/s)etabs | (Av/s)min | (Av/s)used | S (mm) | Stirrups
1 | Near Support | 1.12 | 0.42 | 1.12 | 120 | 1 φ 10 /120 mm
 | Middle | 0.54 | 0.42 | 0.54 | 250 | 1 φ 10 /250 mm
 | Near Support | 0.71 | 0.42 | 0.71 | 220 | 1 φ 10 /220 mm
2 | Near Support | 1.2 | 0.42 | 1.2 | 100 | 1 φ 10 /100 mm
 | Middle | 0.54 | 0.42 | 0.54 | 250 | 1 φ 10 /250 mm
 | Near Support | 1.1 | 0.42 | 1.1 | 100 | 1 φ 10 /100 mm
3 | Near Support | 0.9 | 0.42 | 0.9 | 150 | 1 φ 10 /150 mm
 | Middle | 0.6 | 0.42 | 0.6 | 250 | 1 φ 10 /250 mm
 | Near Support | 1.21 | 0.42 | 1.21 | 100 | 1 φ 10 /100 mm
Shear reinforcement for Beam :

## Slide 53
Cross Section for Beam:

## Slide 54
Column Design:
According to ACI Code, a structural element with a ratio of height-to-least lateral dimension exceeding three used primarily to support compressive loads is defined as column.

## Slide 55
Column Layout:

## Slide 56
Slenderness Check
This check is required to find out whether columns are long or short.
= = 6.3 ≤ 34- 12 ≤ 40
Columns have no slenderness, therefore, all columns are shorts columns.

## Slide 57
Seismic Requirements for Columns of Intermediate moment Frames:

## Slide 58
Longitudinal Reinforcement
As =21681 mm2 use 44Ø25 mm
S max= 150 mm
S min = 50 mm or 1.5 db which is larger 50 or (1.5×25=37.5)
S min = 50 mm.
 Use 1Ø25/10 cm.

## Slide 59
Used stirrups Ø10 mm

## Slide 60
Staircase Design:

## Slide 61
1) Dimensions of stairs:
- Riser: 0.166m. - Going: 0.30 m. - Landing length: 3.2 m.
- Step width: 1.5 m.
-Span length= 5.2 m.
- Slab thickness  0.18 m, d= 0.15m.
2) Loads on stairs:
- Live load: 5 KN/m - Super imposed dead load: 4.4 KN/m.
- Dead load: 0.1 x 25 = 2.5 KN/m.

## Slide 62
3) Design of stairs:
Ultimate loads on slab equal (1.2D + 1.6L) = (1.2x (4.4+2.5) + 1.6 x(5)) = 16.28 KN/m2.
kN.m.
-Longitudinal reinforcement ratio (ρ) from equation:
So, the longitudinal area of steel As = 0.0068 x 1000 x 150 = 1020 mm².
As, Shrinkage = 0.0018 x 180 x 1000 = 320 mm²
Use 616/m.
Use 410/m in the other direction.
Vu = Wu x L = 16.28 x 1.5=24.42KN.

## Slide 63
4) Landing design:
- Landing length: 3.2 m.
Ultimate loads on slab equal (1.2D + 1.6L) = (1.2x (4.4+0.18 x 25) + 1.6 (5)) = 18.68 KN/m².
kN.m.
- Longitudinal reinforcement ratio (ρ) from equation:
So, the longitudinal area of steel As = 0.0029 x 1000 x 150 = 431 mm2.
As, Shrinkage = 0.0018 x 180 x 1000 = 324 mm2
Use 1Ø12 /200mm in each direction for top and bottom .
Vu = (Wu x L)/2 =(18.68 x 3.2)/2=29.88 kN.

## Slide 64
Shear wall Design:

## Slide 65
Shear Wall 5
Length=38.4 m which divided into five spans ( 5.8 m ,11 m ,7.5 m,7.5 m and 6.5 m)
width=0.3 m .
height= 4 m for each floor
Vertical rebar area(pl) =28739 mm2
Horizontal rebar area(pt) =750 mm2

## Slide 66
Longitudinal reinforcement:
NO. of vertical bars:
Span 1 = = 19.3 bars
Span 2 = = 36.7 bars
Span 3 = =25 bars
Span 4 = =25 bars
Span 5 = =21 bars
So use 37 bars Ø25 /30 cm along each face of the shear wall.

## Slide 67
Transverse reinforcement:
No. of transverse bars = =13.3 bars.
So use 14 bars Ø 18/30 cm along each vertical face of the shear wall.

## Slide 68
Design of footings

## Slide 69
Mat foundation was used for the building.
The area of the building = 1539 m2
The total area of foundation is > 0.6 of basement area .
P service =265480 kN.
Allowable bearing capacity of soil = 350 kN/m2
Area of footing=total service load /allowable bearing capacity = 265480*1.1/350= 834.4 m2
The total area of mat foundation =1616.14 m2

## Slide 70
Soil Property Definition (Modules of subgrade Reactions (Ks) :
Safety Factor (Sf) = 2 for Granular soil
Allowable Bering Capacity = 350
Modules of subgrade Reactions (Ks) = 40 (Sf) (q all) = 40*2*350 = 28000

## Slide 71
Deflection Check:

## Slide 72
Design of Mat foundation:
By drawing a contour line of moment m11 and m22 between (-1353,0) ,which corresponding to minimum area of steel of section b=1000mm and h=1500mm.

## Slide 73
Minimum steel =0.0018×1000×1500 =2700 mm2
So use 4Ø32 / 1 meter top in both direction.

## Slide 74
By drawing a contour line of moment M11 and M22 between (0,1353) kN.m , which corresponding to minimum area of steel of section b=1000m and h=1500mm

## Slide 75
Maximum positive moment M22

## Slide 76
the maximum moment in the bottom face of mat foundation is more than 1353 kN.m, so the maximum value of moment in both direction is less than 2000 kN.m by reading the value of moment with blue color far away the center of column and shear wall.
= = 0.00268
So , As =0.00268 = 3806 mm2
So , use 5Ø32 / 1 meter bottom in both direction in dark blue area which equal to 1.5m from each face of column and shear wall.