## Slide 1: An-Najah National University Engineering & IT Faculty Civil Engineering Department
Structural Analysis And Design of Sorda Building
By: Alaa Mohammad Anabseh (11105769)
Jihad Abdelnasser AbdelHaq (11106711)
Under supervision of : Dr. Munther Diab

## Slide 2: Outline:
Introduction.
Gravity and Lateral loads.
3D modeling using SAP.
Design of Slab.
Design of Beams.
Design of Columns and Shear walls.
Design of Footings and Ground Beams.

## Slide 3
INTRODUCTION

## Slide 4
Sorda Building
Location : Sorda-Ramallah
6 Floors.
Floor area : 447 m²
Total Area : 2682 m²

## Slide 5: 5

## Slide 6
Floors consists:
Three Residential Apartments.

## Slide 8
Codes
ACI 318-11 (American Concrete Institute)
IBC-2012 (International Building Code)
UBC-97 (Uniform Building Code)
ASCE-2010 (American Society of Civil Engineers).
Jordanian National Building Code.

## Slide 9: Preliminary Design The choice of the system for slab in the building is very important to resist the internal forces and stability.
International Journal of Current Engineering and Technology
Comparison | Solid Slab | Ribbed Slab
Weight | Heavier than ribbed | Light
Area of steel | More | Less
Beams | Bigger | Smaller
framework | Approximately the same | 
Cost | Bigger | smaller

## Slide 10
GRAVITY & LATERAL
LOADS

## Slide 11
Loads
Gravity
Lateral
Seismic
Dead
live
Superimposed

## Slide 13
Shear resisting
system

## Slide 14
SDS=2/3*SMS
SMS= Fa * Ss
R
System
I
Fa→ site class(B), Ss
Ss= 2.5 *Z
Z→ site class(B)→ soil type
Risk category (III)
Use of Buildings and Structures

## Slide 15
Response spectrum
  A response spectrum is a plot of the maximum response amplitude (displacement, velocity, or acceleration) versus the modal period

## Slide 16: Seismic design factors
R= Modification factor
Cd= Deflection Amplification Factor

## Slide 17
Code | Value of base shear (Hand Calc.)(kN)
IBC-2012 | 1415
UBC-97 | 1737

## Slide 18
Load combinations
U = 1.4D
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 19
THREE DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 20
Modifiers for each element
Modifier | Element
0.7 | Column
0.35 | Beam
0.25 | Slab
0.7 | Shear wall

## Slide 23
Rebar percentage
All is okay
Shear & torsion
No red elements
No problems
Strength check

## Slide 24
Compatibility of structural model

## Slide 25
Equilibrium

## Slide 26
Slab moments
The difference percentage is 5.75 %, which is less than 10%, OK.
Stress Strain relationship
(internal equilibrium)

## Slide 27
Beams moments
The difference percentage is 7.01%, which is less than 10%, OK.

## Slide 28
Lateral loads check
Seismic load, IBC

## Slide 29
Period and modal participation ratio

## Slide 31
Structural period( hand calculation)
𝑇𝑥=0.70 Sec
ASCE, Equation 15.4-6

## Slide 32
DESIGN OF SLAB

## Slide 33
Solid slab.
Thickness = 20 cm.
Shear on slab:
Max Vu = 80 kN
Vc = 112.5 kN
112.5 >80 so,
shear is OK
80

## Slide 34
Steel reinforcement:
Using a uniform steel mesh with 4Ø16/ 1m (Top and Bottom) for all floors and roof.
(Negative and positive)
When the moment not exceeds 42 kN.m/m , use 4Ø16/ 1m (Top and Bottom)

## Slide 35
My : All moment less than 42 kN.m/m

## Slide 36
Mx : All moment less than 42 kN.m/m

## Slide 37
DESIGN OF BEAMS

## Slide 39
ACI318-11 Code requirements:
The value of moment and shear
computed by taking twice the
earthquake load in the load
combinations.
The first hoop shall be located not more than 50 mm from the face of a supporting member.
  .

## Slide 40
For shear and torsion |  | For flexure
 |  | As = ρbd
For shear and torsion |  | For flexure
 |  | As = ρbd
Equations:

## Slide 41
Beam ID | Dimension(h/d) | Longitudinal Steel |  | transverse steel until 2h(S1) | transverse steel (S2)
B1 | (800/250) | Top | 6Ø16 | 6Ø10/m | 4Ø10/m
 |  | Torsion | 5Ø16 |  | 
 |  | Bottom | 3Ø16 |  | 
B2 |  | Top | 5Ø16 |  | 
 | (800/250) | Torsion | 4Ø16 | 7Ø10/m | 4Ø10/m
 |  | Bottom | 3Ø16 |  | 
B3 |  | Top | 6Ø16 |  | 
 | (800/250) | Torsion | 3Ø16 | 6Ø10/m | 4Ø10/m
 |  | Bottom | 3Ø16 |  | 
B4 | (600/250) | Top | 5Ø16 | 7Ø10/m | 4Ø10/m
 |  | Torsion | 3Ø16 |  | 
 |  | Bottom | 3Ø16 |  | 
B5 | (800/250) | Top | 4Ø16 | 6Ø10/m | 4Ø10/m
 |  | Torsion | 4Ø16 |  | 
 |  | Bottom | 3Ø16 |  | 
B6 |  | Top | 3Ø16 |  | 
 | (600/250) | Torsion | 4Ø16 | 7Ø10/m | 4Ø10/m
 |  | Bottom | 2Ø16 |  | 
B7 |  | Top | 7Ø16 |  | 
 | (800/250) | Torsion | 3Ø16 | 9Ø10/m | 4Ø10/m
 |  | Bottom | 4Ø16 |  | 
B8 | (800/250) | Top | 3Ø16 | 5Ø12/m | 4Ø12/m
 |  | Torsion | 3Ø16 |  | 
 |  | Bottom | 2Ø16 |  | 
B9 | (800/250) | Top | 7Ø16 | 6Ø10/m | 4Ø10/m
 |  | Torsion | 3Ø16 |  | 
 |  | Bottom | 4Ø16 |  | 
B10 |  | Top | 2Ø16 |  | 
 | (800/250) | Mid | 3Ø16 | 5Ø10/m | 4Ø10/m
 |  | Bottom | 2Ø16 |  | 
Beam 1*0.25 |  | Top | 3Ø16 |  | 
 | (1000/250) | Torsion | 2Ø16 | 5Ø10/m | 4Ø10/m
 |  | Bottom | 2Ø16 |  | 
Beam0.6*0.25 | (6000/250) | Top | 3Ø16 | 5Ø12/m | 4Ø10/m
 |  | Torsion | 4Ø16 |  | 
 |  | Bottom | 3Ø16 |  | 

## Slide 42
Beams section

## Slide 43
DESIGN OF COLUMNS AND SHEAR WALLS

## Slide 45
Two columns in the project:
1. C1: (70x30), 17 columns.
2. C2: (60x25), 18 columns.
3. C3: (90x20), 3 columns.
Design methodology:-
The design based on taking the critical edge, intermediate, and corner columns of C1,C2 and C3.
Drawing the interaction diagram for C1,C2 and C3.
Using SAP to get the axial force and moments on each column.
Choosing the proper steel ratio.
Determining the spacing between hoops.

## Slide 46
ACI318-11 code requirements:
The value of moment and shear computed by taking 3 times the earthquake load in the load combinations.
Hoops Equations (ACI318-11):

## Slide 48
Vu(KN) | Mu(KN.m) | Pu(KN) | Colum ID
24 | 85.5 | 1270 | C1
29.8 | 36 | 2235 | C2
30.5 | 18.5 | 1049 | C3

## Slide 49
The distribution of (M,P) point for check columns on C1,C2and C3 interaction diagram
c3
1%

## Slide 50
Using a steel ratio of 1% is safe and economical for all columns.
The longitudinal steel is:
8 19 for C1 (70 x 30).
8 16 for C2 (60 x 25)
10 16 for C3 (90*20)
Hoops:
For All columns: provide Ø10/10 cm at a distance of 0.85 m from the top
and bottom joints of columns, and Ø10/15cm on mid of column.
Start with hoops at a distance of 5 cm from the face of supports.
Provide a lap splice length = 0.6 m.
The splicing of bars is made on the middle of columns.

## Slide 53
Design of shear wall :

## Slide 54
Minimum reinforcement in shear walls according to ACI318-11
Minimum ratio of vertical reinforcement area area, ρ, shall be:
  0.0012 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Minimum ratio of horizontal reinforcement area, ρ, shall be:
  0.002 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Vertical and horizontal reinforcement shall not be spaced farther apart than three times the wall thickness, nor farther apart than 450 mm.

## Slide 55
Equations:
  Compressive strength:

## Slide 56
Length of SW = 9.1 m.
Thickness of SW = 0.35 m
…. The thickness is accepted
Using SAP :
Vu (kN) | Muy (kN.m) | Mux (kN.m) | Pu (kN) | SW ID
1765 | 10037 | 1216 | 11260 | SW

## Slide 57
Use total cover = 40 mm.
, therefore, use the minimum horizontal steel according to ACI318-11:
Then, for each face of wall, → use 1Ø10/250 mm

## Slide 59
on the two sides.
on each side.
The total longitudinal steel in SW for each side =
→ Use 1Ø19/20cm, or 6Ø19mm/1m.

## Slide 60: DESIGN OF FOOTING

## Slide 61
Soil type : Rock.
Allowable Bearing Capacity: 350 kN/m²
Grouping of footings are shown in table below:
Group Column | Dimensions (m) | Capacity in service load (KN) | Groups ID
c5,c6,c13,c24,c27,c28 . | 1.5x1.5x0.6 | 760 | Group 1 (F1)
C14,c13,c32,c7,c38,c26,c35,c31,c10 | 1.7x1.7x0.6 | 1000 | Group 2 (F2)
C33,c2,c22,c21c37 | 1.9x1.9x0.6 | 1240 | Group 3 (F3)
C25,c17,c18,c16, c15,c30,c34,c12, c20,c29,c19,c11 | 2.1x2.1x0.6 | 1480 | Group 4 (F4)
C4,c9,c8,c3 | 2.3x2.3x0.6 | 1820 | Group 5 (F5)

## Slide 63: Design of Footing F5
Maximum load on F5 comes from C4.
Envelop Ultimate load | Service load(kN) | Live load (kN) | Dead Load | Footing Dim. | Column Dim. | Footing ID | Column ID
2335 | 1814 | 546 | 1268 | 2.3 x 2.3 | 0.7x0.3 | F5 | C4
Ultimate Moment (kN.m) | Service load(kN.m) | Live Moment(kN.m) | Dead Moment(kN.m) | Footing Dim. | Column Dim. | Footing ID | Column ID
2.45 | 2.2 | 1.90 | 0.30 | 2.3 x 2.3 | 0.7x0.3 | F5 | C4

## Slide 64
As(mm²) | Thickness(m) | Vpu (kN) | Vp (kN) | Vu (kN) | Vc (kN) | Footing ID
1764 | 0.60 | 1893 | 2567 | 137 | 324 | F5
As(mm²) | Thickness(m) | Vpu (kN) |  | Vu (kN) |  | Footing ID
1764 | 0.60 | 1893 | 2567 | 137 | 324 | F5
Transvers steel | Longitudinal Steel
8 16 / m (15 bars along 2.3 m) | 8∅16 or 1∅16/ 15cm (15 bars along 2.3 m)
Transvers steel | Longitudinal Steel
 | 8∅16 or 1∅16/ 15cm (15 bars along 2.3 m)

## Slide 65
Cross section in F5

## Slide 66
DESIGN OF GROUND BEAMS

## Slide 67
Ground beams:
- GB : (600/250).
Design philosophy:
By applying a 2 mm displacement at a joint under a footing that have the tallest ground beam.
Then, determine the area of steel by using a half of steel ratio resulting from the moment.

## Slide 68
Transverse steel | Bottom steel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
5 8 / m | 2 16 | 2 16 | 15.3 | 14.3 | GB1
Transverse steel | Bottom steel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
 |  |  | 15.3 | 14.3 | GB1