## Slide 1: Quantity survey and cost estimate for Kafr Ni'ma basic school
Prepared by
1- Adnan I Jardaneh
2- Amr W Zuhud
3- Momen S Salameh
Supervisor: Eng. Reema Nassar

## Slide 2: What is the projects?
According to Saleh Mabrouk A project as ‘‘a temporary endeavor undertaken to create a unique product, service, or result. The key words in this deﬁnition are temporary and unique: any project must have a starting point and an ending point, and it must have a deliverable product or service that is unique.

## Slide 3: Project key participation
1. Owner (client)
2. Design Professional
3. The contractor
4. The subcontractor

## Slide 4: Life cycle of the projects
There are the major phases in the project life cycle
Startup
Planning phase
Design phase

## Slide 5: The design process involves three phases
Schematic design
Design development
Contract documents

## Slide 6: Project Constraints

## Slide 7: Project Delivery System
Project delivery method describes how the relationship is organized between the participants to transforming the idea of owner project to the facility also the method by which project is executed.

## Slide 8: Type of PDS
Traditional
Design-build (Turnkey)
Self-performance system
Professional construction management method (PCM)
Build-Operate-Transfer

## Slide 9: Parties to a Construction Contract
Simplest from: Two parties:
Owner and A/E.
Owner and Contractor.
More complex: multiple parties:
Owner and several contractors simultaneously.
by trade: electrical, mechanical, plumbing, etc.

## Slide 10: Contracts
Types of Contracts:
Lump Sum Contract.
Unit Price Contract.
Cost-Plus Contract.
Guaranteed Maximum Price Contract.

## Slide 11: Project management
Project management is the application of processes, methods, skills, knowledge, and experience to achieve specific project objectives according to the project acceptance criteria within agreed parameters. Project management has final deliverables that are constrained to a finite timescale and budget.

## Slide 12: Why is Project Management important
Project management is important because it ensures what is being delivered, is right, and will deliver real value against the business opportunity.

## Slide 14: Scheduling
You have to ask yourself three questions to start:
What needs to be done?
When will it be done?
Who will do it?

## Slide 15: Scheduling Methods
    Bar charts (Gantt Charts)
    Critical path Method (CPM)
    Line of balance

## Slide 16: Quantity surveying
Quantity takeoff is a process of measuring the work of the project in form of a series of quantified work items. Each item considered in the takeoff is measured according to a uniform set of rules on how to be measured

## Slide 17: Construction costs
Direct cost include
Materials costs
Labor costs
Equipment costs
Indirect cost include
Overhead
Indirect labor
Profits

## Slide 18: Project Introduction
Project delivery system:- Design-Bid-Build.
Project contract:- Unit price.

## Slide 19: Render.

## Slide 25: Quantities Surveying Using Revit Software

## Slide 26: Architectural Model

## Slide 27: Models build up in Revit

## Slide 28: Link CAD Importing for Drawing

## Slide 29: Section definition
Internal Wall 20cm.

## Slide 30: Section definition
Exterior Wall 15cm.

## Slide 31: Section definition
Floor details

## Slide 32: Final Results from Revit

## Slide 33: Sample calculation for footing excavation
R.L=439.7

## Slide 34: Sample calculation for steel reinforcement

## Slide 35: Sample calculation for concrete volume
Depth =0.5m

## Slide 36: BOQ
Item | Measured quantity | Unit
Excavation for footing | 1033.00 | CM
Excavation of tie beam | 120.00 | CM
Backfill works | 1010.00 | CM
Concrete for footing | 88 | CM
Blinding concrete under footings B150 | 21 | CM
Formwork of footings | 5.15 | CM
Steel reinforcement of footings | 6.3 | Ton
Formwork of C.N | 3.93 | CM
Steel reinforcement of C.N | 2.30 | Ton
Concrete for C.N | 32.60 | Ton
stirrups in C.N | 1940 | #
Formwork of G.B | 4.10 | CM
Steel reinforcement of G.B | 0.76 | Ton
Concrete for G.B | 51.75 | CM
stirrups in G.B | 2308 | #
Formwork of S.G | 0.15 | CM
Steel reinforcement of S.G | 0.69 | CM
Concrete for S.G | 86 | Ton
Formwork of G.F slab | 12.92 | CM
Steel reinforcement of G.F slab | 14 | Ton
Blocks 14cm for G.F slab | 3340 | Peace
Concrete placing for G .F slab | 86 | CM
Steel reinforcement of G.F beam,… | 4.6 | Ton
stirrups in beams | 4190 | #
Formwork of 1st.F slab | 28.20 | CM
Item | Measured quantity | Unit

## Slide 37: BOQ
Blocks 14cm for 1st.F slab | 8048 | Peace
Concrete placing for 1st.F slab | 190 | CM
Steel reinforcement of 1st.F lintels,… | 12 | Ton
stirrups in beams | 9492 | #
Formwork of slab | 1.45 | CM
Steel reinforcement of slab | 2 | Ton
Concrete placing for slab roof | 10 | CM
Steel reinforcement of Beam roof | .25 | Ton
stirrups in beams for beam roof | 366 | #
Formwork for column | 55.25 | CM
Steel reinforcement | 1.44 | Ton
Concrete For coulm | 238 | CM
stirrups in all column | 12290 | #
Formwork for stairs | 4.38 | CM
Steel reinforcement | 5 | Ton
Concrete for stairs | 37 | CM
Block 15 | 1088 | Peace
Block 10 | 1253 | Peace
Plastering works | 5976.00 | SM
tile works | 2178.00 | SM
Painting works | 5976.00 | SM
Wood Doors | 115.00 | SM
Steel Doors | 44.00 | SM
Shaved wood door | 45.00 | No.
Shaved steel door | 15.00 | No.
Aluminium | m2 | 205.00
براطيش | m2 | 39.00
stone work | m2 | 1130.00
Item | Measured quantity | Unit
Item | Measured quantity | Unit

## Slide 38: BOQ
Item | Measured quantity | Consultant quantity | Variance reason
Excavation for footing and tie beam | 1353 CM Without allowance =305 CM | 325 | Because we can’t know the exact allowance of the project,
Blinding Concrete B150 under foundations, footings & tie beams. The thickness should be 10cm or according to drawings. | 210 MS | 204 MS | -
Supply and Cast Reinforced Concrete Grade 'B 250' a). Foundations and Wall Footings with column neck | 120CM | 110CM | -
Supply and Cast Reinforced Concrete Grade 'B 250'. For Slab on | 573SM | 536 SM | 
Supply and Cast Reinforced Concrete Grade 'B 300' for 20 cm thick suspended ribbed slabs. Price to include projected beams, | 1455 SM | 1380 SM | Because of the method of evaluating the exact volume of beam and slab

## Slide 39: Time Schedule Using Primavera Software

## Slide 40: The parameters needed to define the project in Primavera software:

## Slide 41: Calendar Definition:

## Slide 42: Currency Definition

## Slide 43: Work breakdown structure

## Slide 44: Project activities

## Slide 45: Project activities

## Slide 46: Project activities

## Slide 47: Project activities

## Slide 48: Resource in P6

## Slide 49: Bar chart

## Slide 50: Bar chart

## Slide 51: Bar chart

## Slide 52: Bar chart

## Slide 53: Schedule (Run)

## Slide 54
Item | Measured quantity | Consultant quantity
Excavation for footing and tie beam | 1353 CM Without allowance =305 CM | 325
Blinding Concrete B150 under foundations, footings & tie beams. The thickness should be 10cm or according to drawings. | 210 MS | 204 MS
Supply and Cast Reinforced Concrete Grade 'B 250' a). Foundations and Wall Footings with column neck | 120CM | 110CM
Supply and Cast Reinforced Concrete Grade 'B 250'. For Slab on | 573SM | 536 SM
Supply and Cast Reinforced Concrete Grade 'B 300' for 20 cm thick suspended ribbed slabs. Price to include projected beams, | 1455 SM | 1380 SM

## Slide 55: Results and Conclusions
Total cost = 646,191 $
The total cost of insurance is about 10 % of the total cost, and taxes are about 5% of the total cost, and 15% of the total cost is included job overhead and operating and profits
Price = 858,303 $
Price per meter square =
The project started on 1/1/2020 and end at 5/8/2020
Total duration for project =184 days
Total duration calendar day =218days