## Slide 1: Artificial Arm Prepared by: Hamza Nassar Ala Sad Aldeen Owais Sawalha Supervisor: Dr. Salameh Abd Alfatah May 2018

## Slide 2: Outline 1-Introduction 2-Design 3-Results 4-Discussion

## Slide 3: Introduction Human arm degree of freedom(DOF) Types of artificial arm control Electromyograph(EMG) sensing Catagories of surface EMG electrodesEMG electrode placment

## Slide 4: Human arm DOF Human arm degree of freedom The human arm has a total of 27 DOF. 21 of them are set in the hand and the rest are in the arm itself.

## Slide 5: Types of atrificial arm control In term of controlling the artificil arm there is two main ways:- 1- Joint linked system. 2- Artificial tendones. 3- Types of artificial tendons control.

## Slide 6: Joint linked system The vast majority of prosthetic fingers are actuated through a joint linkage system powered by DC electric motors.

## Slide 7: Artificial tendons The artificial tendons way is considered to be a more effective way to control the fingers. the major advantage that artificial tendon have over joint linked system is what is known as joint conformity. Joint conformity allows fingers to adapt to the shape of the object they are grasping.

## Slide 8: Electromyograph(EMG) sensing Myoelectric signals are electrical pulses within the body produced by contracting muscles. Myoelectic electrodes are used to detect this pulses, and there is 3 main types of the electrodes which are:- 1-Needle electrodes. 2- Fine wire electrodes. 3- Surface EMG electrodes.

## Slide 9: Catagories of surface EMG electrode There are two categories of surface EMG electrodes:- 1- Passive EMG electrodes. 2- Active EMG electrodes.

## Slide 10: EMG electrode placement The surface EMG electrodes should be placed between the motor unit and the tendons insertion of the muscle, along the longitudinal midline of the muscle.

## Slide 11: Design We have two main part in this section 1- Mechanical design 2- Electrical design

## Slide 12: Mechanical part 1-Early Ideas 2-Design of the hand 3-Manufacturing and Assembling

## Slide 13: Early Ideas After researching several actuation methods for prosthetic arms an artificial tendon design was chosen.

## Slide 14: Design of the hand We take a ready design from an open source,and we improvmed on it using solidwork programme.

## Slide 15: Manufacturing and Assembling 1- 3D ptinter 2- Assembly 3- Final shpe

## Slide 16: Electrical part Actuators Processing Power supply EMG Sensor

## Slide 17: Results 1-Pre-amplification 2-High pass filter 3-Full wave rectification 4-Low pass filter and final amplication 5-Achievable Goals

## Slide 18: Discussion 1-The over all system quality was pretty good 2-Our arm offers a good griping strength but boor speed

## Slide 19: Difficulties 1- occupation 2-Lake of component

## Slide 20: Improvements 1-Mechanichal design 2- Sensory Feedback 3-Advanced EMG Algorithms and Processing

## Slide 21: Conclusion Our project achieved most of the set goal but the benefits to an amputee were not achieved