## Slide 1: Suggestions for Water Drainage in Bal’a Town.
Graduation Project II

## Slide 2: Introduction:
Water in human being life goes through two levels:
Consumption.
Drainage.

## Slide 3: Study Area

## Slide 4: Bal’a Town

## Slide 5: Bal’a Location
Bala’a Town lies on coordinates of 32° 19′ 59.4″ N, 35° 6′ 31.15″ E, in north eastern Tulkarm city in the north of Palestinian West Bank.

## Slide 6: Population
Given from Palestinian Statistics Centre the following data of population and growth rate from 2007 to 2016 in Bal’a.
G.R= (𝑃(𝑙𝑎𝑡𝑒𝑟 𝑦𝑒𝑎𝑟)/𝑃(𝑝𝑟𝑒𝑣𝑖𝑜𝑢𝑠 𝑦𝑒𝑎𝑟) )^(1/𝑛)−1

## Slide 7: After analysis .it appears that the relationship between years and population is linear, with R=99.98%.
Chart: year
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Pop | 6545 | 6671 | 6800 | 6930 | 7063 | 7199 | 7336 | 7473 | 7610 | 7746
Bala'a Pop | 6545 | 6671 | 6800 | 6930 | 7063 | 7199 | 7336 | 7473 | 7610 | 7746

## Slide 8: Terrain
Bal’a lies on four mountains it has an average height of 400 m on sea level and reaches to 500 m on some regions with high variance in elevation from site to site, with high steep slope.

## Slide 9: Contour map for Bal’a Town.

## Slide 10: Rainfall readings
The average annual rainfall in Bal’a is 617.5 mm according to Palestinian Statistics center.
From Palestinian Metrologic Center :
year | 2013/2014 | 2014/2015 | 2016/2017 | 2017/2018
Annual depth(mm) | 366.6 | 655.8 | 457.4 | 376.4
Maximum day depth (mm) | 81 | 72.2 | 53 | 46.5

## Slide 11: Problems Solved in Graduation Project I.
High losses in the existing Water Distribution net Work.
Unfair water distribution in Bal’a zones.
By designing a new Water Distribution Network using an additional Reservoir.

## Slide 12: Problems to be solved in Graduation Project II.
Non Existence of sewer drainage system covers most Bal’a regions.
Floods occurs on Main Streets in Winter.
By
*Designing Sewer drainage system
And *Designing Culverts on Main streets.

## Slide 13: Sewer Drainage system Design for Bal’a Town. By Sewer Cad Software.

## Slide 14: Methodology
Doing calculations to find the expected population of the town in the future
Finding the expected produced waste water in the future
Preparing data as layers of the town
Using sewer cad to design the network depending on layers of (contour, building, road)
Checking the design to achieve the criteria of velocity and cover.

## Slide 15: Criteria of the Design.
Natural water consumption (L/capita/day) | 120
Growth rate (%) | 2
Load distribution method | Equal distribution for each Manhole in planned urban zones
Design period(years) | 35
% product waste | 85%
Maximum velocity in conduits(m/sec) | 3
Minimum velocity in conduits (m/sec) | 0.6
Maximum allowable cover (m) | 6
Minimum allowable cover(m) | 0.8
Minimum allowable slope (%) | 1
Maximum allowable slope (%) | 12
Infiltration (%) | 20
Conduit Material | PVC

## Slide 16: Load Calculations.
Daily Load on each Manhole= overall load/number of manholes
Overall Daily Load=expected population*peak factor*consumption *product waster percent + Infiltration percent*expected population*consumption*product waste
= )7822)*(1+0.2)^36(*3*120*0.85(+)0.2*7822)*(1+0.2)^36(*120*0.85 (
=5208m3/day
Daily Load on each Manhole =5208/562=9.27m3/day

## Slide 17: Suggested Outfalls.
Tow outfalls:
the first is in the south which goes to AL-Zomar Valley
the other is in the west which goes to Ammar Valley which can go with Alsha’rawiya wastewater collection valleys

## Slide 18: Steps
Adding Data

## Slide 19: Drawing Manholes

## Slide 20: Inserting Loads and constrains

## Slide 21: Conduit Catalog

## Slide 22: Results Velocity (m/sec)
98% of conduits has velocities between 0.6 and 3 m/sec but low velocities appeared due to low collection in the first conduit of each branch.

## Slide 23: Cover Start

## Slide 24: Cover Stop

## Slide 25: Conduit Diameters.
All diameters has 8 Inch diameter.
Lengths between each manhole and the other is less than 30 m.

## Slide 26: Sample Profiles

## Slide 27: Culverts’ Design for Bal’a Main Streets. By HY-8 Software.

## Slide 28: Methodology.
Choosing the most critical streets when storm occurs.
Collecting Data of each street dimension and shape.
Suggesting points of culverts locations.
Determining Catchment areas of each suggested location by GIS.
Calculating the peak flow of a 10-year storm for each catchment by HEC-HMS.
Designing the culverts using HY-8.

## Slide 29: Culverts on streets.

## Slide 30: Suggesting four location of culverts by site visit and GIS and the following coordinates are chosen

## Slide 31: Catchments Data by GIS.

## Slide 32: Catchments on each culvert By GIS.

## Slide 33: Sample Calculation for Lag Time.
*Lag time for catchment A.
Lag Time=0.6*Tc
Tc=0.01947*〖865.95〗^0.77*〖0.1527〗^(-0.385)=7.34min
Lag time=0.6*7.34=4.4 min

## Slide 34: Using IDF curve for 10-year return period.
There were no data for Bal’a to make IDF curve, Wadi Ara which lies near OM-Alfahm town is taken for design.
Om Alfahm town which is 20 KM northern Bal’a, has an annually rainfall of 625 mm which is very near of Bal’a’s one which is 617.5 mm, so it is acceptable to take this IDF curve for design.

## Slide 35: IDF Curve used.

## Slide 36: IDF Curve analysis.

## Slide 37: Mass curve
Chart: 
| 0 | 10 | 30 | 60 | 120 | 240 | 360 | 400 | 420 | 420
Accumilative depth(mm) | 0 | 14.5833 | 37.3333 | 57.3958 | 83.0208 | 118.0208 | 142.0208 | 142.0208 | 142.0208 | 142.0208

## Slide 38: Partial duration depth required for HEC-HMS Inserting
Duration (min) | Partial-Duration Depth(mm)
5 | 7.29
15 | 20.2675
60 | 57.39583
120 | 83.0208
180 | 100.52
360 | 142.0208

## Slide 39: Curve Number
A) Bal’a has a clay soil so it has soil type of “C” ACCORDING TO Curve Number classification.
Group C: clay loams, shallow loam, soils low in organic content, and soils usually high in clay
B) Bal’a has an urban area with impervious 10.52 % (the areas of buildings and paved roads)
According to this table it will have a curve number of 77.

## Slide 40: Curve Number Table.

## Slide 41: Simulation By HEC-HMS

## Slide 42: Results from HEC-HMS
CULVERT Number | CATCHMENT OUTLET | Maximum flow (m3/sec)
1 | A | 21.3
2 | B | 14.7
3 | C | 24.4
4 | D | 2.7

## Slide 43: Roads Data on each culvert location.

## Slide 44: By HY-8 .

## Slide 45: Final Suggested Design.
Culvert number | Diameter(mm) | Number of barrels | Slope (%)
1 | 1350 | 5 | 2.09
2 | 1200 | 4 | 3.8
3 | 1550 | 4 | 4.64
4 | 1000 | 1 | 4.57

## Slide 46: Sample Culvert 4.

## Slide 47: Discussions and Recommendations.

## Slide 48
THANK YOU