## Slide 1: Smart Plant
Prepared by
Aseel Eyad
Shayma Abu Saada
Supervisor
Dr.Luai Malhis

## Slide 2: Outline 01 02 03 05 06 04
What is smart plant
Overview
Motivation
Constraints
Methodology
Future Work

## Slide 3: What is smart plant

## Slide 4
The robot allows indoor plants to serve themselves in terms of two primary needs without the intervention of people
Search for the sunniest location in a room
Measure the soil moisture, so when needed, it can get what it needs from the water
Another feature of Smart Plant is that it allows users to identify the movement of a plant using speech through an app.

## Slide 5: Overview

## Slide 6: Smart Plant is driven by two DC motors and controlled by an Arduino Uno microcontroller and esp32. The HC-05 Bluetooth module can be used to move the plant in all directions by registering the direction (left,right,..) to an app With the help of two light detection receptors (LDRs), the robot seeks out sunlight.

## Slide 7
The planter avoids hitting obstacles thanks to ultrasonic range detectors.
The moisture sensor reading is taken on a regular basis. So, when the plant requires water, start the pump and water it until the moisture sensor reads less than 700.

## Slide 8: Methodology

## Slide 9
Movement of the Dc motors and detecting obstacles using ultrasonic range detectors.
Detecting the sunniest spot using LDRs .
Measuring the soil moisture then water system with pump .
Voice detection with bluetooth.
We will talk about four main ideas:

## Slide 10: Robot Movement

## Slide 11
Our robot has 2 wheels each connected to a dc motor and a third wheel which is not connected to a motor (free wheel).
it’s only used for supporting movement in all directions and maintaining the robot stability.
It’s very important to use a driver with the DC motor because it keeps the power that drives the motors separate from the power that is on the arduino.
We used H-bridges to drive the DC motors.
Dc Motors :

## Slide 12
In order for the robot to avoid obstacles we used ultrasonic range detectors in our project.
Ultrasonic sensor detects obstacles while moving forward
When the sensor detects an obstacle within a distance less than 18 cm it go back and rotates trying to find another path.
Ultrasonic range detectors

## Slide 13
We used 2 LDRs that detect the light coming from left and right side .
LDRs

## Slide 14
We read the soil moisture using an automatic sensor which is mainly put in plant also when the plant is too dray the pump (3-5)v start water the plant . In addition the esp wifi controller connected with blynk application and we will have a notification to tell us how is the moisture read for plant.
Starting watering system

## Slide 15
we use bluetooth module hc-05 with softwareserial library to connect the module with aurduino uno to move plant using four words : go , back , left and right to help plant to search for sunshine and to control it.
Voice detection

## Slide 16: Constraints
Lack of time
Connection issues in h-bridge
Pins fault in aurdunio

## Slide 17: Result

## Slide 19: Future Work

## Slide 20
Improve the project's movement by primarily enhancing an algorithm.
Expand on non-household plants and make them self-serve in some way
An extra function that checks the percentage of elements and minerals in the soil to make sure there isn't a deficiency if one exists.

## Slide 21: Demo