## Slide 1
An - Najah National University Faculty of Engineering
Building Engineering Department
“EFFICIENCY OF DOUBLE SKIN FAÇADE
IN SOUTHERN ELEVATION”
Prepared by:
Mohammed Sanuora
Tawfiq Hijjawi
Amr Ramadan
1
0:05

## Slide 2: Content
Introduction
Site description
Architectural Design
Structural Design
Environmental Design
Electrical Design
Mechanical Design
Fire and Safety Design
Operating & Maintenance
Quantity Surveying and Cost Estimation
1:00
2

## Slide 3: Introduction
1:00
3
Double skin façade system has achieved a big fame in commercial constructions due to its advantages in achieving an attractive view along with sound and thermal insulation properties.
This project examines the efficacy of the system at the southern elevation in residential buildings in Palestine.
.

## Slide 4: Site description and analysis
Al Toffah valley

## Slide 5: Site description and analysis
Sun path and wind direction

## Slide 6: Architectural Design

## Slide 7: Architectural Design
Site Plan

## Slide 8: Architectural Design
Floor | Function | Area m^2
Basement | Parking | 1900
Ground floor | Commercial | 1500
1st | Residential | 470
2nd | Residential | 470
3rd | Residential | 470
4th | Residential | 470
5th | Residential | 470
2 X

## Slide 9: Architectural Design
Basement Plan

## Slide 10
Ground floor “commercial” Plan

## Slide 11
Residential floor Plan

## Slide 12
Eastern elevation

## Slide 13
Western elevation

## Slide 14
Southern elevation

## Slide 15: Northern elevation

## Slide 16: Section A-A

## Slide 17: Section B-B

## Slide 18: Architectural Design
3D VIEW

## Slide 19: Architectural Design
3D VIEW

## Slide 20: Architectural Design
3D VIEW

## Slide 21: Architectural Design
3D VIEW

## Slide 22: Architectural Design
3D VIEW

## Slide 23: Structural Design

## Slide 24: Structural Design
Design Data :
Concrete f ‘c= 24MPa for slabs and beams
Concrete f ‘c= 28MPa for columns and footings.
Slabs system used :- Two way ribbed slab. Load :
Super imposed dead load = 4.71 kN/m2
Live load = 3kN/m2 in residential and 5kN/m2 in commercial

## Slide 25: Structural Design
Etabs 3D MODEL

## Slide 26: Structural Design
MODEL CHECKS
Compatibility check
Equilibrium check
Live load : %error = 0.57%
SID load : %error = 1.19%
DEAD load : %error = 2.69%
All of static analysis checks were satisfied

## Slide 27
The soil profile type is “Sc”
Seismic zone factor (Z) = 0.2
Reduction factor (R) = 5.5
Seismic importance factor (I) = 1
Seismic coefficient (Cv) = 0.32
Seismic coefficient (Ca) = 0.24
Nablus lies in zone 2B
UBC 97
Seismic Design Data :

## Slide 28
Structural-Elements
Footing Plan :

## Slide 29
Structural-Elements
Footing Plan :

## Slide 30
Structural-Elements
Tie Beam Plan:

## Slide 31
Structural-Elements
Tie Beam Plan:

## Slide 32
Structural-Elements
Column sections:

## Slide 33
Structural-Elements
Longitudinal Column Sections :

## Slide 34
Structural-Elements
Beam Reinforcement :

## Slide 35
Structural-Elements
Shear Wall Reinforcement:

## Slide 36
Structural-Elements
slab design in basement

## Slide 37
Structural-Elements
slab design in commercial

## Slide 38
Structural-Elements
slab design in residential floor

## Slide 39
Reinforcement around windows:
Structural-Elements

## Slide 40: Environmental Design

## Slide 41: Environmental Design
Environmental simulation has been performed via Design Builder 5.2

## Slide 42: Environmental Design
To discover efficacy of double skin façade system, insulation and both altogether on thermal loads.
Case 1 : Insulated building and DSF building
Case 2 : Insulated building and single skin façade
Case 3 : uninsulated building and single skin façade
Case 4 : uninsulated building and DSF building

## Slide 43: Environmental Design
HEATING LOADS
Total heating design in the building = 150.55 kW
Zone sensible heating = 120.52 KW
Total heating design = 156 kW
Zone sensible heating = 124.83 KW
Total heating design = 258.87 kW
Zone sensible heating = 201.14 KW
Total heating design = 277.76 kW
Zone sensible heating = 222.23 KW
Case 1
Case 2
Case 3
Case 4
Insulated & DSF
Insulated & single skin façade
uninsulated & single skin façade
uninsulated & DSF

## Slide 44: Environmental Design
COOLING LOADS
Total cooling design = 273.8 kW
Total cooling design = 277 kW
Total cooling design = 353.44 kW
Total cooling design = 364.54 kW
Case 1
Case 2
Case 3
Case 4
Insulated & DSF
Insulated & single skin façade
uninsulated & single skin façade
uninsulated & DSF

## Slide 45: Environmental Design
Simulation
Intensity = 114.1 kW/m^2
Direct heating = 92,223 kWh
Direct cooling = 173,373 kWh
Intensity = 137.37kW/m^2
Direct heating = 88,854 kWh
Direct cooling = 235,595 kWh
Intensity = 132.81 kW/m^2
Direct heating = 153,067.21 kWh
Direct cooling = 175,519.84 kWh
Intensity = 156 kW/m^2
Direct heating = 166,384.72 kWh
Direct cooling = 227,269 kWh
Case 1
Case 2
Case 3
Case 4
Insulated & DSF
Insulated & single skin façade
uninsulated & single skin façade
uninsulated & DSF

## Slide 46: Environmental Design
Comfort
-0.5 to 0.5
High comfort
-0.5 to 0.5
High comfort
-1.0 to 1.0
Good comfort
-1.5 to 1.5
Accepted comfort
Case 1
Case 2
Case 3
Case 4
Insulated & DSF
Insulated & single skin façade
uninsulated & single skin façade
uninsulated & DSF

## Slide 47: Environmental Design
Savings
Annual energy consumption = 114.1 kW/m^2
Cost of annual energy consumption = 114 * 3641.88*0.6
= 290,622.024 ILS
Case 1
Case 2
Insulated & DSF
Annual energy consumption = 137.37 kW/m^2
Cost of annual energy consumption
= 350,199.53 ILS
Insulated & single skin façade
The savings = 59,577.506 ILS
About 17%

## Slide 48: Final thoughts on environmental design
1. The system achieved comfort inside the space according to PMV, with and without HVAC.
2. It has been shown that blue glass gives better results with maintain 50% of light transmission. It is the most light-emitting type of colored glass.

## Slide 49: Final thoughts on environmental design
3. Heating and cooling loads are very low in residential apartments with the traditional insulation and almost high in commercial floors. Thus, the double skin façade in residential building is not active as the same level in the commercial floor. This is why its widespread in commercial and offices buildings and in very few residential cases, the impact of the double façade appeared in the commercial floor much more than it is in the residential floors from energy saving and power saving perspectives.

## Slide 50: Daylight calculations
Commercial floor

## Slide 51: Daylight calculations
Residential floor

## Slide 52: Artificial lighting Design

## Slide 53: Artificial lighting Design
All spaces in this project have been designed with DIALux evo 7.1

## Slide 54: Artificial lighting Design
Lighting requirements of each space have been achieved Illuminance, uniformity and Glare
A. Parking

## Slide 55: Artificial lighting Design
A. Parking

## Slide 56: Artificial lighting Design
B. Master Bedroom

## Slide 57: Artificial lighting Design

## Slide 58: Artificial lighting Design

## Slide 59: Artificial lighting Design
Electrical wires plan
Sockets plan

## Slide 60: Acoustics Design

## Slide 61
Acoustics calculations
Noise level: ≈ 68 dB

## Slide 62: STC calculations
1. STC for DSF wall

## Slide 63: STC calculations
2. STC for insulated Palestinian wall

## Slide 64: STC calculations
Insulated
Palestinian wall
DSF wall
VS.
could you please tell me which one is better !
62
54
VS.

## Slide 65: STC calculations
*Double skin façade is weaker in blocking low frequencies like traffic noise from large vehicles, planes and heavy machinery.
Traditional insulted wall is better in blocking low frequencies.
It called resonance, the main reason for this refers to the nature of the material itself and how it behave when exposed to sound waves at different frequency.

## Slide 66: STC calculations
There are parameters should be taken into account: site, cost, function, degree of insulation, noise frequency and what frequencies to be blocked.

## Slide 67: STC calculations
Bedroom calculations
STC composed (external wall) = 49
IIC for bedroom = 58
STC internal wall = 54
remaining passing noise = 19 dB,
it is lesser than 35 dB (maximum allowable background noise in bedrooms )

## Slide 68: STC calculations
RT60 for Bedroom
The transmitted 19 dB also will be distracted by

## Slide 69: Acoustical calculations
To prevent water hammer, flow’s upper limit is
V = 4.89 = 5 ft/s

## Slide 70: Photovoltaic system Design

## Slide 71: Photovoltaic system
The idea was to improve an integrated system that works efficiently in almost all days per year
UTILIZING SUN’S ALTITUDE
Summer
Altitude 89
Winter
Altitude 35

## Slide 72: Photovoltaic system
Summer
Winter
Also shading system
Southern elevation system
Roof flat system

## Slide 73: Photovoltaic system: Integration
# of modules: 256
Pnom total: 73kWp
Produced energy: 118 MWh/year
# of modules: 308
Pnom total: 88 kWp
Produced energy: 90.3 MWh/year

## Slide 74: Photovoltaic system: statistics
Payback period: 30 months
PV system coverage = 60 % in Winter
PV system coverage = 43% in Summer
Total cost of PV systems = $ 77220

## Slide 75: Mechanical Design
Water Supplying System
Drainage Systems
Elevators
HVAC System

## Slide 76: Water Supplying System

## Slide 77: Drainage Systems

## Slide 78: Drainage Systems

## Slide 79: Drainage Systems

## Slide 80: Drainage Systems

## Slide 81: Drainage Systems

## Slide 82: Drainage Systems

## Slide 83: Drainage Systems

## Slide 84: Drainage Systems

## Slide 85: Elevators
elevator {2000 lb, 100 fpm}
The elevator type is motor driven with a sliding door.

## Slide 86: HVAC System Design

## Slide 87: HVAC System Design
Multi split units system has been used.
DAIKIN’s company catalog has been used to choose suitable indoor and outdoor units.

## Slide 88: HVAC drawings

## Slide 89: HVAC drawings

## Slide 90: Fire fighting System

## Slide 91: Fire fighting System

## Slide 92: Fire fighting System

## Slide 93: Fire fighting System

## Slide 94: Fire fighting System

## Slide 95: Fire fighting System

## Slide 96: Fire fighting System

## Slide 97: Fire fighting System

## Slide 98: Operating & maintenance system

## Slide 99: Operating & maintenance system
Operating & maintenance phase forms 60-70% of LC

## Slide 100: Operating & maintenance system

## Slide 101: Quantity surveying & cost estimate

## Slide 102: Quantity surveying & cost estimate
Type of work | Cost ILS
Excavation, backfilling and site | 12057889
Concrete work | 15663505
Stone work | 59292
Concrete block work | 62761
Tiling and marble work | 306759
Plaster work | 195377
Steel work | 1264410
Painting work | 282493
Electrical work | 32755
Mechanical work | 42650
Solar system + PV | 503680
Fire system | 237300
Hvac system | 125000
Double skin façade | 252144
False ceiling | 106020
Glass on walls | 138384
Doors and windows | 247234
Blocks 10 & 20 cm | 153238
Total cost = 7.1 million ILS
Unit cost = 887.5 ILS/m^2