## Slide 1: Implementation of Lean Manufacturing Tools At AL- Majd Furniture Factory
Prepared by:
Abrar Shtayeh Majd Tbealeh Nadwa Salah Suna Jayyousi
Supervised by:
Dr. Tamer Haddad

## Slide 2: Outline
Introduction
Objectives
Methodology
Analysis & results
Conclusions
Recommendations

## Slide 3: Introduction
About factory :
Al MAJD Furniture factory was founded as a family business in Nablus in 1995.
AL-MAJD is specialized in manufacturing all kinds of home and office furniture including luxury's sofa, bedrooms, children's bedroom…etc

## Slide 4: Introduction( some products )
.

## Slide 5: Introduction
What is Lean ?
Lean manufacturing aims to achieve the same output with less input such as less time, less space, less human effort, less machinery, less material, less cost.

## Slide 6
The main goal of this project is to apply a set of lean manufacturing techniques at to reduced the generated wastes especially scrap , in order to enhance the overall performance of plant floor.
Objectives

## Slide 7: Methodology

## Slide 8: Define : (Problem Statement)
ALMAJD factory suffers from many problems:
Large amount of scrap material

## Slide 9: Define : (Problem Statement)
No clear production line

## Slide 10: Define : (Problem Statement)
Un sufficient material handling system

## Slide 11: Define : (Problem Statement)
Lack of engineering scientific and administrative system

## Slide 12: Define ( product )
Due to the wide variety of products we divided the products into two families and we chose one product to express each family where we chose the bed from the family of wood products and the sofa from the family of products that contain fabric

## Slide 13: Define ( product )

## Slide 14: Define : (lean tools & Technique)
1- 5s tools were helped in
• Sort to removed items that are no longer needed
• straighten or set in order to organize the items to optimize efficiency and flow
• Shine to clean the area in order to more easily identify problems
• Standardize to implement color coding and labels to stay consistent with other areas
• sustain to develop behaviors that keep the workplace organized over the long term

## Slide 15: Define : (lean Tools & Technique)
2- Value stream mapping (VSM) tool was implemented to present the current situation of the factory and to identify non value add activates and production process waiting time to reduce and eliminate it
3- layout analysis was implemented based on line balancing technique in order to reduce the idle time for the worker and increase the efficiency of the production line

## Slide 16: Measure ( TIMWOOD wastes)
transportation
motion
Over processing
inventory
defect
waiting
waste through the distance from assembly station to second floor of plant
unnecessary movement of the workers during working shift like searching for tool, walking through plant floor
due to rework or repair of defects, materials used due to defect and rework
the workers carried out many things over the major production process and added many details and aesthetic that the customer does not request them
excessive work in process and raw material
operator waiting time for previous operation to complete its cycle

## Slide 17: Measure (5s chick list )

## Slide 18: Measure (5s chick list )

## Slide 19: Analysis (using cause and effect diagram to analyze type of wastes)

## Slide 20: Analysis ( bed flow chart )

## Slide 21: Analysis ( sofa flow chart )

## Slide 22: Analysis ( sofa value stream mapping )

## Slide 23: Analysis (bed value stream mapping )

## Slide 24: Improved ( solutions )

## Slide 25: Improved 5s tool (S1 – SORT)
To implement the first S the Red-Tag process is commonly employed.

## Slide 26: Improved 5s tool (S2 – SET IN ORDER )
The second S reflects a very popular saying: “A place for everything and everything in its place”.

## Slide 27: Improved : 5s tool (Sort & set and order )
The following figures show the differences between before & after implementing (sort and set in order)

## Slide 28: Improved 5s tool ( Sort & set and order )

## Slide 29: Improved 5s tool (Sort & set and order )

## Slide 30: Improved 5s tool (Sort & set and order )

## Slide 31: Improved 5s tool (Sort & set and order )

## Slide 32: Improved 5s tool (Sort & set and order )

## Slide 33: Improved 5s tool (Sort & set and order )

## Slide 34: Improved 5s tool (S3 - Shine)
The third S stresses on cleanliness because it ensures a more comfortable and safer workplace, as well as better visibility, which reduces retrieval time and ensures higher quality work, product or service

## Slide 35: The following figures show the differences before & after implementing (shine) phase
Improved 5s tool (S3 - Shine)

## Slide 36: Improved 5s tool (S3 - Shine)

## Slide 37: Improved 5s tool (S3 - Shine)

## Slide 38: S4 – STANDARDIZE
The continued employment of the 3S will ensure a high standard of workplace organization
Once the 3S are in place, the next step is to concentrate on standardizing best practices.

## Slide 39: S4 – STANDARDIZE

## Slide 40: S5 – SUSTAIN
A management auditing process should be put into practice to make sure that employees understand that maintaining the level of workplace organization is a top priority

## Slide 43: Improved Layout
After visiting the factory and observing the physical arrangement of the machines and physical measurements were taken for their dimensions the layout sketch of each floor was drawn

## Slide 44: Improved Layout
Ground floor layout

## Slide 45: Improved Layout
First Floor Layout

## Slide 46: Improved Layout(Line balancing(
According to the situation in the factory which there are two floors, the first floor only will be adjusted.
M1(cleaning machine) was excluded because cleaning must done at the first before the processing

## Slide 47: Improved Layout(Line balancing
In our analysis of layout we considered line assembly balance where every worker's task takes the same amount of time
largest candidate rule algorithm was followed in line balancing.
cycle time for beds according to first floor machines is 4.4 hr and for sofa is 4 hr
so production rate (Rp) for bed is 0.22 assembly/hr and for sofa is 0.25 assembly/hr

## Slide 48: Improved Layout(Line balancing
At first, the processing times of each product on each operation (Tk) and the precedence of the operations were collected

## Slide 49: Improved Layout(Line balancing)
the work elements on each machine was listed in descending order based on total time in last Colum also take the precedence into account

## Slide 50: Improved Layout(Line balancing)
as noticed M2 has the largest total work time (1.19) so it would be the base to arrange the machines into stations.

## Slide 51: Improved Layout(Line balancing)
So here we have two stations and the maximum {TTk} = 1.19 so balance efficiency (Eb) =1.19+0.345+…+0.0184/2*1.19 = 0.806 =80.6%
After this analysis a new proposed layout for ground floor was sketched

## Slide 52: Conclusions
According to the inappropriate layout, there is a significant increase in the transfer of materials between machines, which reduces total productivity.
The non-added value activity for sofa before was 15.38 % but after it is 10.85% And for bed before = 26.14 but after = 20.9 % according to the value stream map generated to the carpentry
Factory continuous evaluation, follow 5S chick list and take corrective action when any error was accord

## Slide 53: Conclusions
After applying the safety (signs and PPE), in the factory, the work environment became safer and more safe for workers and visitors, and more comfortable and convenient for work

## Slide 54: Recommendations
Continuous evaluation of the factory by filling in the audit forms to maintain the level of
improvement.
There is a relationship between implementation .of 5s and the enhancing in the factory
we suggest purchasing the CNC machine because it will save costs and increase profits
on the long run.
Compliance with safety instructions, as well as wearing personal protective equipment, maintaining ventilation