## Slide 1
Structural Design of Nazareth Gate in Nazareth-City Palestine
An-Najah National University
Faculty of Engineering
Civil Engineering Department
جامعة النجاح الوطنية
كلية الهندسة ونكنولوجيا المعلومات
Graduation Project I
1

## Slide 2
Prepared by:
Marah Mosleh
Shimaa Ali
Tala Jamous
Under supervision: Dr.Ibrahim Arman
2

## Slide 3
Outline:
1. General Description
2. Preliminary Design
3. 3-D Modeling and Analysis
4-Verification of structural design
5- Structural design
3

## Slide 4
Member
4

## Slide 5
General Description
5

## Slide 6
General Description
6
Project Description:
  Location:
Near Galilee Street,
in Nazareth City,
Palestine.
  Level and Height:
> on 412 meters above the sea level.
> Total height = 63 m.
  Site coordinate:
lines of longitude and latitude 35°18'39"E 32°42'25"N .
  Complex include:
parking lots, and offices.
serving as a multifunctional building.
  Area:
Around 17,600 m2.
  Floors:
15 floor : Basement, Ground floor and 13 story
  Bearing capacity and Soil Classification:
> Bearing Capacity =
450 kN/m2
> Soil Classification: class B

## Slide 7
7
Location and elevation of proposed Nazareth Gate building.

## Slide 8
Floor No. | Height (m) | Usage
Basement | 4 | Parking and water tanks
Ground floor | 5.15 | Supermarket
1st | 4.35 | Supermarket
2nd | 4.35 | Children’s toys exhibition
3rd | 4.35 | Sports equipment exhibition
4th | 4.35 | Housewares exhibition
5th | 4.35 | Electrical appliances exhibition
6th - 13 th | 4.35 | Offices
General Description
Floors Information:
8

## Slide 9
Basement
9

## Slide 10
Ground floor
10

## Slide 11
1st floor - 5th floor
11

## Slide 12
6th floor - 13th floor
12

## Slide 13
Compressive strength (fc’) for slab | 36 MPa
Compressive strength (fc’) for columns and foundation | 36 MPa
Reinforcing Steel Grade | 60 (A572)
General Description
Structural Materials:
13

## Slide 14
Loads:
Gravity Loads:
Lateral Loads:
Soil loads
General Description
14
Dead loads
Superimposed dead loads
Live loads
Snow loads
Seismic loads

## Slide 15
Floor No. | Usage | Live load (kN/m2)
Basement | Parking | 3.5
Ground floor to 5th | Supermarket and stores | 5
6th - 13th | Office rooms | 3
0.20 kN/m2
15
  Snow Load:
General Description
Gravity Loads:
  Live Load:

## Slide 16
Non-Structural elementts | Weight per unit area (kN/m2)
Tiles | 3.11
False ceiling | 0.25
Exterior walls (glass) | 0.55
Floor No. | Floor height (m) | Line load (kN/m)
Ground | 5.15 | 2.83
1st - 13th | 4.35 | 2.4
Gravity Loads:
  Superimposed Dead Load
General Description
16
Line load at building perimeter

## Slide 17
General Description
Lateral Load:
17
• Soil Load:
- Earth pressure:
p =k × γs × z =0.5 × 16 × 4=32 kN/m2
- Seismic earth pressure:
∆p = 0.4 × kh × γs ×z=0.4 × 0.252 × 16 × 4 = 6.45 kN/m2
-Surcharge load:
∆p = k × γs × heq=∆p = 0.5 × 16 × 0.61 = 4.88 kN/m2

## Slide 18
Mapped acceleration parameters | Ss | 0.7
Mapped acceleration parameters | S1 | 0.14
Mapped acceleration parameters | T | 7
Site coefficient | Fa | 0.9
Site coefficient | Fv | 0.8
Design spectral acceleration | SDS | 0.42
Design spectral acceleration | SD1 | 0.074
Risk categoryof the building | III | III
18
General Description
Lateral Load:
• Seismic Load:

## Slide 19
Importance factor | Ie | 1.25
Seismic design category | C | C
Lateral forces resisting system: | Dual system with intermediate moment frame | Dual system with intermediate moment frame
Response modification factor | R | 5.5
Overstrength factor | Ωo | 2.5
Deflection amplification factor | Cd | 4.5
Structural Period | 1.87 | 1.87
19
General Description
Lateral Load:
• Seismic Load:

## Slide 20
20
General Description
Computer Programs:

## Slide 21
Structural Preliminary Dimension
21

## Slide 22
22
Using two-way solid slab
slab thickness (h) = 200 mm.
Preliminary Design:
Slab Layout:

## Slide 23
23
Preliminary Design:
Beam and column Layout:
Beams | Thickness | Width
B1 | 600 | 400
B2 | 600 | 500
B3 | 1000 | 700

## Slide 24
Group No. | Columns' Dimensions (mm) | Columns' Dimensions (mm)
Group 1 (Basement - 1st) floor | center | 1200 x 1200
Group 1 (Basement - 1st) floor | edge | 800 x 800
Group 2 (2nd - 4th) floor | center | 1050 x 1050
Group 2 (2nd - 4th) floor | edge | 700 x 700
Group 3 (5th - 7th) floor | center | 900 x 900
Group 3 (5th - 7th) floor | edge | 600 x 600
Group 4 (8th - 10th) floor | center | 750 x 750
Group 4 (8th - 10th) floor | edge | 500 x 500
Group 5 (11th - 13th) floor | center | 600 x 600
Group 5 (11th - 13th) floor | edge | 400 x 400
24
Preliminary Design:
Preliminary Dimensions of Columns:

## Slide 25
3-D Modeling and Analysis
25

## Slide 26
Walls
26
Evaluation of the Preliminary Design:
Beams
Columns

## Slide 27
27
Beams | New Beams' Dimensions (mm)
B1 | 400 x 700
B2 | 700 x 600
B3 | 500 x 600
B4 | 1000 x 700
B5 | 900 x 700
B6 | 1300 x 800

## Slide 28
28
Group No. | Old Columns' Dimensions (mm) | Old Columns' Dimensions (mm) | New Columns' Dimensions (mm) | New Columns' Dimensions (mm)
Group 1 (Basement - 1st) floor | center | 1200 x 1200 | center | 1000 x 1000
Group 1 (Basement - 1st) floor | edge | 800 x 800 | edge | 900 x 900
Group 2 (2nd - 4th) floor | center | 1050 x 1050 | center | 900 x 900
Group 2 (2nd - 4th) floor | edge | 700 x 700 | edge | 900 x 900
Group 3 (5th - 7th) floor | center | 900 x 900 | center | 800 x 800
Group 3 (5th - 7th) floor | edge | 600 x 600 | edge | 700 x 700
Group 4 (8th - 10th) floor | center | 750 x 750 | center | 800 x 800
Group 4 (8th - 10th) floor | edge | 500 x 500 | edge | 700 x 700
Group 5 (11th - 13th) floor | center | 600 x 600 | center | 800 x 800
Group 5 (11th - 13th) floor | edge | 400 x 400 | edge | 700 x 700

## Slide 29
29

## Slide 30
30

## Slide 31
Verification of Structural Analysis
31

## Slide 32
Verification of Structural Analysis:
Check of compatibility

## Slide 33
 | Calculated Total weight KN | ETAPS KN | Difference %
Check equilibrium for self-weight load | 15035.65 | 14840.67 | 1.3%
Check equilibrium for superimposed dead loads (SD) | 89660.706 | 90161.9983 | 0.56%
Check equilibrium for live loads | 85616.16 | 85669.7112 | 0.06%
33
Verification of Structural Analysis:
Check equilibrium:

## Slide 34
 | Calculated Value | ETAPS | Difference %
Internal check for slab and beam (Mo) | 1034.15 kN.m | 955.75 kN.m | 8.2%
Internal check for column (axil load) | 126 kN | 128.77 kN | 2.15%
34
Verification of Structural Analysis:
Check of internal forces:

## Slide 35
Verification of Structural Analysis:
Deflection computation:
Long term deflections for slab systems:
Selected panel of ground floor deflection.

## Slide 36
Verification of Structural Analysis:

## Slide 37
37
1-Check mass participation ratio:
the value in X and Y -direction is 98% which is good.
Verification of Structural Analysis:
Seismic Check:

## Slide 38
38
From ETABS
the value equal to 7702.6172 kN
Diffrence (%) =(7796-7702.6)/7796 x100%=1.15% <10% (OK)
Verification of Structural Analysis:
Seismic Check:
2-Check equilibrium of base shear:
Manual calculation of base shear in x-direction and y-direction:
V = Cs×W=7796 KN

## Slide 39
39
Difference (%)=(2.5-2.5)/2.5*100% = 0%
The value from ETABS =2.5
Manual calculation:
in X-direction
Verification of Structural Analysis:
Seismic Check:
3-Check time period by Rayleigh method:
Difference (%)=(2.7-2.7)/2.7*100% = 0%
The value from ETABS =2.7
Manual calculation:
in Y-direction

## Slide 40
40
Verification of Structural Analysis:
Seismic Check:
4-Check Story Forces:

## Slide 41
41
Verification of Structural Analysis:
Seismic Check:
5-Type of Lateral Force Resisting System:
Total force =7681 KN
Force from wall =4974
4974/7681=0.6........60%
This indicates that the system is dual system

## Slide 42
42
Seismic design category is C
Verification of Structural Analysis:
Structural Irrigularity:
1-Horizantal Irregularity:
Type | Commentary
1 | Does not exist
2 | Not applicable
3 | Not applicable
4 | Does not exist
5 | Exist
Type | Commentary
1 a | Not applicable
1 b | Not applicable
2 | Not applicable
3 | Does not exist
4 a | Not applicable
4 b | Does not exist
2- Vertical Irregularity:

## Slide 43
43
If θ < 0.1 ----> the effect of P-delta
will be neglected
θ in both directions < 0.1
SO, the effect of P- delta neglected
Verification of Structural Analysis:
Effect of P-delta:

## Slide 44
44
:beam’s dimensions
width =400mm , depth =600mm ,
length =6.95 m
Verification of Structural Design:
Beam design verification:

## Slide 45
45
Mu = 316.26 kN.m.
ρ = 0.0075
As = 1631 mm2
As From ETABS = 1634 mm2
Difference (%) = ((1634 / 1631)-1) * 100% = 0.18%< 10% %
Verification of Structural Design:
Beam design verification:
1- Flexural design check:

## Slide 46
46
Verification of Structural Design:
Beam design verification:
2- Shear design check:

## Slide 47
47
Vg = 1.2 (76.3 + 44.92) + 1.6 (145.8) = 378.744 kN.
∅Vc = 247.54 kN
Vs = 257.54 kN
Difference % = (1.135-1.297)/1.135=5.7%
Verification of Structural Design:
Beam design verification:
2- Shear design check:

## Slide 48
48
Tu = 38.33 kN.m
Difference % = (0.475-0.457)/0.475 =3.8%
Verification of Structural Design:
Beam design verification:
3- Torsion design check:

## Slide 49
49
Verification of Structural Design:
Column design verification:
Bresler equation:
1- Longitudinal reinforcement:

## Slide 50
50
∅Pn = 15000 kN > Pu = 14971 kN --> OK

## Slide 51
51
Verification of Structural Design:
Column design verification:
2- shear reinforcement:
∅Vc = 3174 kN
Vu (from ETABS) = 33.75 kN
∅Vc > Vu ⟶ No need for shear reinforcement

## Slide 52
52
:pier’s dimensions
width = 350 mm , height = 4.35 m ,
length = 7 243 mm
Verification of Structural Design:
Shear wall design verification:

## Slide 53
53
AS from ETABS = 6337 mm2.
Reinforcement = 6337 / (2×7.24) = 437.64 mm2/m.
use 1Φ16mm/250mm.
Verification of Structural Design:
Shear wall design verification:
1- Longitudinal reinforcement:

## Slide 54
Interaction diagram for 0.0025 pier longitudinal reinforcement.
54

## Slide 55
55
Shear design check:
Details of selected pier’s shear design:
Vn = 5248 KN
ф Vn = (0.6) 5248 = 3149 kN.
ф Vn (ETABS) = 3088.6 kN.
Difference % = 2% < 10% (OK).
Ф Vc = 1551.5kN.
Ф Vc (ETABS) = 1515.6 kN.
Difference % = 2.3% < 10% (OK) .

## Slide 56
Structural Design
56

## Slide 57
57
Design of slabs:
The selected slabs in the story 5 and story 13 ,will be designed according to ACI 318-19 code.
(Slabs thickness is 200 mm).
Selected slab to be designed in story 5.
Selected slab to be designed in story 13.

## Slide 58
58
Check slabs for punching shear:
All columns in this structure are connected to beams or shear walls,
so there is no punching shear on the slabs.
Check slabs for wide beam shear:
∅Vc = 72.2 kN.
1Ø16 bar every 200 mm was added in both the X and Y directions to increase the slab shear capacity in story 13 .
All values of shear in story 5 lower than ∅Vc, so there is no need for shear reinforcement in floor 5.

## Slide 59
59
Check slabs for wide beam shear:
Ultimate shear force in the slab of story 13 in x-direction, V13.
Ultimate shear force in the slab of story 13 in y-direction, V23.

## Slide 60
60
Design of slabs for flexure:
For flexure design, , additional 1Ø12 /400mm top steel reinforcement was only needed in the x-direction on the 13th floor.
Design of slabs detailing and requirements:
Bar development length , ldt = (0.48 × 420 /√36 )× db , For bars diameter less than 20 mm.
Bar splicing length , ls = 1.3× db
cover = 40 mm.

## Slide 61
61
Design of Shear wall:
Design of piers:
selected pier number 6 in the story 3 .
The pier’s dimensions are :
height = 4.35 m
length = 7.26 m
width = 0.35 m

## Slide 62
62
Design of Shear wall:
1- Longitudinal reinforcement:
Longitudinal reinforcement =
5 ф 12 /m at each face of the wall.
2 -Shear reinforcement:
Shear reinforcement =
4 ф 12/1 m at each face of the wall.

## Slide 63
63
Design of Shear wall:
Cross section of selected pier:

## Slide 64
64
Flexural design
Shear design
Torsion design
Design of Beams:

## Slide 65
65
Design of Beams:
1- Longitudinal reinforcement:

## Slide 66
Design of Beams:
66
2- Transvers reinforcement:
So, use S = 100 mm

## Slide 67
67
Design of Beams:
Longitudinal section :
Cross section :

## Slide 68
68
Design of foundation:
Mat foundation:
Thickness = 1400 mm

## Slide 69
69
Design of foundation:
Mat foundation:
1- Punching check:
This check is to ensure the thickness of footing
All values ​​are less than 1, so the thickness was good.

## Slide 70
70
Design of foundation:
Mat foundation:
2- Pressure check:
The soil pressure on mat foundation was less than 450 kN/m2

## Slide 71
71
Design of foundation:
Mat foundation:
Flexural design:
The design was made using ETAPS:

## Slide 72
72
Design of foundation:
Mat foundation:
Wide beam shear design:

## Slide 73
73
Design of Stairs:
The staircase will be designed and detailed manually.
use thickness=200mm
Live Load = 5 KN.
Superimposed Load =3.9 KN.
Self weight = (0.2) (25) = 5 kN.
Landing:

## Slide 74
74
Design of Stairs:
Staircase, flights:

## Slide 75
75
Design of stairs:
Structural Design :
Staircase, flights.

## Slide 76
-Column dimensions are:
L = 0.9 m,
b = 0.9 m,
h = 4.35 m.
-Longitudinal reinforcement
= 10643 mm2 = 28 ф 22.
-Steel ratio =
= 1.31% < 3% -> OK
76
Design of Columns:
1- Longitudinal reinforcement:
Longitudinal reinforcement

## Slide 77
77
Design of Columns:
1- Longitudinal reinforcement:

## Slide 78
78
Design of Columns:
2- Transverse reinforcement:
ℓo ≥ 1/6 ℓu
≥ Max. cross-sectional dimension of column
≥ 450 mm
s˳ ≤ 8 d/b
≤ 200 mm
≤ 1/2 smallest cross-sectional dimension of column
s1 = 200 mm

## Slide 79
79
Design of water tank:
:Water tank’s dimensions
6.3 m x 6.9 m
4 m height
300 mm thickness
the environmental durability factor (Sd) will be used in the design

## Slide 80
80
Design of water tank:
Vertical direction:
Flexural design:
The design moment = (Mu) (Sd) (seismic factor)
= (32.035) (1.23) (1.4) = 55.16 kN.m
As= ρ b d=(0.0035)(1000)(230)=821.1 mm^2
ρ=0.0028 < ρ min=0.0035 ---> Use ρ min=0.0035
use (1 ∅ 14 /150 mm) at each side of the wall.

## Slide 81
81
Design of water tank:
Vertical direction:
Shear design:
The maximum ultimate shear = 62.7 kN
∅Vc = 112.53 kN
Vu < ∅Vc
No need for shear reinforcement.

## Slide 82
82
Design of water tank:
Horizontal direction:
Flexural design:
The design moment = (Mu) (Sd) (seismic factor)
= (59.5) (1.23) (1.4) = 102.45 kN.m
As= ρ b d=(0.0053)(1000)(230)=1219 mm^2
ρ=0.0053 < ρ min=0.0035 ---> Use ρ =0.0053

## Slide 83
83
Design of water tank:
Horizontal direction:
Torsion design:
The design Torsion = (Pu) (Sd) (seismic factor)
= (730.5) (1.96) (1.4) = 2004.5 kN.m

## Slide 84
Horizontal steel from:
-flexural design= 1219 mm2
-torsional design = 5303 mm2
-minimum horizontal steel at a side = (0.005/2) (1000) (300) = 750 mm2
84
Design of water tank:
Horizontal direction:
use (1 ∅ 28 /150 mm) at inner side of the wall.
Total horizontal steel at side of water = 1219 + (5303/2) = 3871 mm2 < minimum steel
Total horizontal steel at outer side of water = (5303/2) = 2652 mm2 < minimum steel
use (1 ∅ 25 /150 mm) at outer side of the wall.

## Slide 85
85
Design of water tank:

## Slide 86
Thank you
86