## Slide 1
An-Najah National University
Faculty of Engineering
Department Of Mechanical Engineering
Electricity Generation Using Speed Breakers
Submitted to :
Dr. Iyad Assaf
Submitted by:
Ahmad Beshara Bilal Hawawra
Kareem Ahmad Renad Daqqa

## Slide 2
Introduction .
Objectives .
Problem statement
Methodology
Result and analysis .
Recommendation and Conclusions
Outline

## Slide 3
Electricity generation depends mainly on coal, coal burning produce a large amounts of carbon.
The power sources in our world are in continuous decreasing.
Our project provides a new clean source of energy. The speed breaker is generating electricity depending mainly on car’s weight by converting the kinetic energy of the moving car into electrical energy using a DC-generator, and for every car passes on the speed breaker, the generator could generate up to 72 watt.
Introduction

## Slide 4
Speed breaker
Load applied on the speed breaker
The springs compressed
Transitional motion in rack
Rotational motion in the gears
The generator rotates
Generating electricity
Saving energy in UPS
Description of the system

## Slide 5: Objectives of Project
To provide an environmental friendly power source.
Reducing the costs of electricity .
Producing a big amount of energy and storing it to use later when the electricity shut down.
To make cheap and easy maintainable power source.

## Slide 6: Problem statement

## Slide 7
We will apply our project in Nablus ,Precisely in the city
center in the front of the taxis parking lots.
We chose this place as there is a high number of cars
pass over from this region and there is often a big
traffic. Also , the weight of the vehicles pass over is
approximately fixed and suitable for the speed breaker
,so we make sure that failure will not occur. As a result
, a high amount of power is generated and the
efficiency is high .
Methodology

## Slide 8
Parts Assembly

## Slide 9
Component
1-Spring
2-Angular joint & wheel

## Slide 10
Component
3-Hollow pipe
4- spur gear&
Support guide

## Slide 11: 6-Rubber speed breaker
Component
5-Rack

## Slide 12
Component
7-Bolts
8-Generator

## Slide 13
9-ups
10-invertor

## Slide 14
11-Steel plate
Lower plate
upper plate

## Slide 15
Material for each component:
Steel material :
Steel is a strong material that is highly resistant to shaping at normal temperatures but this resistance lessens considerably at higher temperatures
Type of steel : 4140 is a 1% chromium - molybdenum e high tensile steel
this type of steel has a high fatigue life and it can be used for heavy duties
This material used for plate, gear, bolts, angular joint, support guide block, and Hollow pipes

## Slide 16
Chrome-vanadium :
The material will be used is Chrome-vanadium (UNS G61500, AISI 6150 M ASTM 231-41).
This is the most popular alloy spring steel for condition involving higher stresses than can be used with the high-carbon steels and for use where fatigue resistance and long endurance are needed.
Also good for shock and impact loads
This material used for spring.

## Slide 17
Final shape

## Slide 18
How the project workفيديو

## Slide 19
Result and analysis

## Slide 20
Helical compression spring
(Na) Number of active coils.
(Nt) Number of total coils.
(OD) Outside diameter.
(Lo) Free Length
(Ls) Solid Length.
(C) Spring index.
(D) Mean diameter.
(d) Wire diameter.
(K) Spring Rate.
(P) Pitch : distance between coil.
Parameters

## Slide 21
Helical compression spring
Calculation:
The calculation depend on :
weight (maximum) = 2000 kg
Fmax = 2000 * 9.81 = 19620 N
weight (minimum) = 1200 k
Fmin = 1200 * 9.81= 11772 N
But etch spring will have (F /2 ) = 11772/2 = 5885 N
Material of spring Chrome-vanadium, squared and ground
F = 5885 N
G = 77200 Mpa
Lo = 500 mm
Ymax = 150 mm
d = 18 mm
D = mm
From table (10-4) [1]
A = 2005
m = 0.168
Equations that are used :

## Slide 22
we choose a suitable wire diameter to satisfy the standard dimensions (the free length and the solid length , more logical and more safe )

## Slide 23
Helical compression spring design for fatigue loading and fatigue life

## Slide 24
N=841382.54
every car make two cycles in the springs : one by the front wheels and the other by the back wheels , every day 500 cars pass over the speed breaker so we have 1000 cycles in the springs each day
Period that does not happened fatigue
831382.54 / 1000 * 360 = 2 year

## Slide 25
Hollow pipe
Calculation:
Dout
t
upper hollow pipe
Lower hollow pipe
Din spring = D-d =156.5-18=138.5 mm
clearance between lower hollow pipe and spring = 5mm
thickness for hollow pipe = 3mm
Din(lower H.P)= Din spring - 2*clearance -2*thickness
Din lower = 122m
clearance between upper hollow pipe and spring = 2mm
thickness for hollow pipe = 3mm
Din ( upper H.P) = Din spring -2*clearance – 2*thickness
Din upper = 128 mm

## Slide 26
Rack , pinion and spur Gear
Teeth parallel to the shaft, Used to transmitted motion from one shaft to the other shaft.
Spur gear:
Rack & pinion gear:
Rack and pinion gears are used to convert the transitional motion to rotational motion
Pitch Diameter
Diametral Pitch
(N) Number of teeth
Theta : angular rotation

## Slide 27
Calculation:
Rack , pinion and spur Gear
The calculation depend on :
S = 150 mm,
the distance that gear rotat (arc length).
Let N1 (gear) = 40 teeth
Let N2 (pinion) = 24 to 8 teeth
Equations that are used :

## Slide 28
Excel sheet
s
r1 = 96 mm
N1 = 40 teeth
N2 = 8 teeth
r2 = 19mm
To check if r for gear 2 is true ?
If the arc length circumference for ger 2 , its true
S=150 mm

## Slide 29
We will find the thickness of plate depend on
Material of plate : steel – 4140
Tensile strength = 1770 Mpa
Yield strength = 1640 Mpa
Length of plate = 300 mm
Width of plate = 500 m
Factor of safety (n) = 2
Thickness (t)
t
calculation for plate thickness
3000 mm
500 mm

## Slide 30
V=9810 N M= 4905 N/mm
(from shear-moment diagram)
where
t = 4.25 mm
t = .25mm
We will choose the largest thickness >>> t=4mm

## Slide 32
calculate the amount of energy produced daily by generator
For every car passes over the speed breaker , the generator could generate up to 72
watts ,and as the car passes by two levels :by the front wheels and by the back
wheels ,the generator will be able to generate up to 144 watt for every car . From
previous transportation statistics , about 500 cars will pass over the speed
breaker each day , so the amount of power generated each day is : 500*144 =
72000 watt/day

## Slide 33
Recommendation and Conclusions
Conclusion
In our project , the main goal was to provide a new cheap and clean source of energy depends mainly on the moving cars weights , which means it is completely clean. The running cost of the project is zero , and the construction cost is low . so our project is economically feasible and environmental friendly .
Our project is “electricity generation using speed breaker” , it consist of :
1- 2 steel plates
2- 2 helical compression
3- 3 gears (rack , gear and pinion)
4- 4 angular joints
5- rubber speed breaker
6- 2 rods
7- support guide block
8- bolts and welding

## Slide 34
Recommendations
our project is very simple and upgradeable , so anyone can understand the working procedure and modify the project .
2. the speed breaker could generate more power by using more than one generator in the same speed breaker
3. the construction cost is low , the running cost is zero and its easy to maintain
4. you can put multiple speed breakers in the streets , which means generating and saving more power .

## Slide 35
Thank you