## Slide 1: Nablus Municipality
An-Najah National university Building Engineering Department
Prepared by :
Ameen Hamed
Jaser Jamil Qaq Mohammad Sholi
Supervisor :
Eng. Alaa Shaheen

## Slide 2: The Outlines
Architectural design
Structural Design
Environmental Design
Cost & Quantity
Electro mechanical Design
Conclusion

## Slide 3: Architectural Design

## Slide 4: Location and Site Plan
The project is located in Nablus - on Tulkarm Street – opposite to the Tamimi fuel station

## Slide 5
Site Analysis
Surrounding buildings & Entrances
Wind movement & Streets & Noise

## Slide 6
Site Analysis
Sun Path in Summer
Sun Path in Winter

## Slide 7
Site Plan with Analysis:
Site Plan After
Site Plan Before
Architectural Plans

## Slide 8
Basement floor after

## Slide 9
Basement floor before
Basement floor after

## Slide 10
Ground Floor Before
Ground Floor After

## Slide 11
First Floor Before
First Floor after

## Slide 12
Second Floor Before
Second Floor after

## Slide 13
Third Floor Before
Third Floor after

## Slide 14
Fourth Floor Before
Fourth Floor after

## Slide 15
fifth Floor after

## Slide 16
sixth Floor after

## Slide 17
Over Shadowing
Solar Radiation
Thermal Comfort
Environmental Aspects

## Slide 18: Overshadowing: In Summer (21/Jan)
12 pm
8 am
3 pm

## Slide 19: Overshadowing: In Winter (21/Jan)
8 am
3 pm
12 pm

## Slide 20: Shading System
SW
NE

## Slide 21: Solar Radiation:
We made annual solar radiation for the roof, and we made solar radiation for each elevations before and after modification at the different time of the day, By Revit software.
Summary for the solar radiation in Summer after modification
Elevation | At 8 am (Wh/m2) | At 12 pm (Wh/m2) | At 3 pm (Wh/m2)
South | 40 | 210 | 338
North | 300 | 50 | 80
East | 480 | 380 | 100
west | 80 | 200 | 340
Summary for the solar radiation in Winter after modification
Elevation | At 8 am (Wh/m2) | At 12 pm (Wh/m2) | At 3 pm (Wh/m2)
south | 13 | 560 | 600
North | 15 | 60 | 70
west | 10 | 50 | 150
East | 25 | 306 | 20

## Slide 22: Thermal Comfort
(U-value) W/m2.K for our building | Highest thermal transmissivity value (U-value) W/m2.K | Structural elements in the outer shell of the building
0.249 | 0.5 | External wall
0.611 | - | Celling
0.251 | 0.39 | Roof
0.395 | 0.46 | Ground Floor
1.493 | 2.46 | Exterior windows
1.492 | 6 | Exterior doors exposed
Energy status | Design Capacity(W/m2)
Highly energy efficient | 20 - 25
Good energy efficient | 26 - 40
Energy efficient | 41 - 60
Accepted | 61 - 80
Fails (consumes high amount of energy) | > 80

## Slide 23: Heating & Cooling loads (With insulation)
Floors | Zone | Cooling Design Capacity (kW) | Design Cooling Load Per Floor Area(W/m2) | Heating Design Capacity (kW) | Design Heating Load Per Floor Area(W/m2)
Ground floor | corridor | 3.34 | 23.9 | 4.78 | 34.1918
 | Cafeteria | 2.32 | 70.5 | 1.37 | 41.7579
 | counting department | 1.76 | 41.8 | 2.77 | 65.9995
 | Office 3 | 0.93 | 37.5 | 1.18 | 47.8655
 | crowd service | 4.39 | 27.7 | 5.62 | 35.4271
 | Office 1 | 1.92 | 69 | 1.63 | 58.5155
 | Office 2 | 1.98 | 72.1 | 1.55 | 56.3079
 | Security | 0.91 | 44.7 | 0.76 | 37.5584
First floor | crowd service & corridor | 12.8 | 42.2 | 7.78 | 25.6455
 | Office of Elections and Statistics | 2.69 | 53.8 | 3.05 | 60.9291
 | Security | 0.81 | 53.7 | 0.5 | 33.2706
 | Regulatory Office and General Police | 0.77 | 39.9 | 0.69 | 35.5523
 | Disputes and Legal Affairs Office | 2.1 | 56.8 | 2.11 | 56.9539
 | civil status office | 2.52 | 64 | 2.78 | 70.6917
 | Office | 1.99 | 57.7 | 1.99 | 57.5264
Second floor | corridor | 10.33 | 61.3 | 5.38 | 31.9161
 | Restoration office | 2.61 | 52.1 | 2.17 | 43.3347
 | Restoration office 2 | 1.55 | 38.5 | 1.35 | 33.542
 | Building Exploitation Office | 0.55 | 43.6 | 0.45 | 35.3679
 | Maintenance department office | 2.38 | 62.7 | 2.25 | 59.3524
 | Projects Follow-up Office | 3.58 | 62.1 | 2.8 | 48.6815
 | Media interest | 1.91 | 55.3 | 1.54 | 44.7619
 | Warehouse office | 2.17 | 55.5 | 1.73 | 44.1249
 | Office of the Building and Construction Authority | 4.08 | 60 | 3.45 | 50.8228
 | Materiel office | 4.22 | 55.3 | 4.51 | 59.0113
Thermal Comfort

## Slide 24
Floors | Zone | Cooling Design Capacity (kW) | Design Cooling Load Per Floor Area(W/m2) | Heating Design Capacity (kW) | Design Heating Load Per Floor Area(W/m2)
Third floor | corridor | 6.49 | 38.5 | 5.26 | 31.1844
 | Department of Electrical Engineering | 2.57 | 51.2 | 2.17 | 43.2417
 | Office of the director of engineers | 1.56 | 38.7 | 1.63 | 40.3447
 | Engineering File Manager | 0.55 | 43.1 | 0.45 | 35.2347
 | Audit engineers & Archive | 2.43 | 64.1 | 2.24 | 59.0708
 | Department of Civil Engineering | 3.56 | 61.8 | 3.17 | 55.0006
 | Department of Energy Engineering | 1.94 | 56.3 | 1.29 | 37.3276
 | Warehouse office | 2.18 | 55.8 | 1.74 | 44.4435
 | Department of Industrial & Building Engineering | 4.1 | 60.3 | 3.06 | 45.0842
 | Department of Mechatronics Engineering & IT | 4.21 | 55.1 | 4.11 | 53.8051
Fourth floor | corridor | 12 | 51.2 | 7.07 | 30.1805
 | Agricultural Affairs Office | 2.82 | 55.6 | 2.17 | 42.8942
 | Agricultural Affairs Office 2 | 1.45 | 40.4 | 1.2 | 33.2989
 | Social Affairs Office 2 | 0.78 | 40.1 | 0.68 | 34.5707
 | Cultural Affairs Office2 | 2.75 | 53.6 | 3.25 | 63.3839
 | Social Affairs Office | 1.96 | 53 | 2.14 | 57.9216
 | Cultural Affairs Office | 3.5 | 62.7 | 2.6 | 46.671
 | Office of Prevention and Public Health 2 | 2.36 | 59.1 | 2.94 | 73.5028
 | Office of Prevention and Public Health | 2.88 | 68.4 | 2.1 | 49.8085
Thermal Comfort
Heating & Cooling loads (With insulation)

## Slide 25
Floors | Zone | Cooling Design Capacity (kW) | Design Cooling Load Per Floor Area(W/m2) | Heating Design Capacity (kW) | Design Heating Load Per Floor Area(W/m2)
Fifth floor | corridor | 13.14 | 65.4 | 6.52 | 32.4521
 | Office of Movement and Statistics | 3.48 | 69.6 | 2.49 | 49.66
 | Personnel Management Office 1 | 1.69 | 47.6 | 1.44 | 40.5927
 | Personnel Management Office | 0.48 | 38.5 | 0.44 | 35.7586
 | Office of General Inventory & Archive | 2.35 | 63.8 | 1.93 | 52.4599
 | Financial Operations Office, Processing Branch | 3.32 | 65.7 | 2.56 | 50.7056
 | Secretary | 0.81 | 43.8 | 0.63 | 34.0659
 | Office of General Inventory | 2.67 | 63.4 | 1.73 | 41.0339
 | Financial Operations Office, Management Branch | 4.12 | 60.8 | 3.58 | 52.7841
 | Deals office | 1.89 | 62.8 | 2.51 | 83.1936
 | Property Management Office | 1.53 | 56.1 | 1.52 | 55.3853
 | Municipal Property | 1.06 | 60.9 | 1.07 | 61.4125
Sixth floor | Corridor | 8.53 | 72.2 | 4.7 | 39.7975
 | Mayor's Office | 5.67 | 54.6 | 5.73 | 55.1849
 | Secretary 1 | 2.37 | 53.7 | 2.15 | 48.7545
 | Security | 1.09 | 72 | 0.54 | 35.5303
 | Secretary 2 | 1.34 | 52.6 | 1 | 39.3025
 | Deputy Mayor's Office | 1.54 | 54.3 | 1.66 | 58.6627
Total |  | 191.76 |  | 155.66 | 
Thermal Comfort
Heating & Cooling loads (With insulation)

## Slide 26: Thermal Comfort Heating & Cooling loads Design Capacity :
 | Cooling Design Capacity (kW) | Heating Design Capacity (kW)
Without insulation | 289.91 | 359.66
With insulation | 191.76 | 155.66
We get the annual energy consumption rate of the building by using Design builder software and it was about 37 KWh/m2.

## Slide 27: Thermal Comfort PMV of the building

## Slide 28: Baseline
 | Saving
Heating load | 72%
Cooling load | 40%
Interior lighting | 73%

## Slide 29
Cheeks & Design
Detailing
Structural Aspects

## Slide 30
Codes:
ACI-318-14 for reinforcement concert design.
UBC-97 for earthquake design.

## Slide 31: Blocks.
The building divided to two blocks.
Block No1.
Block No2.

## Slide 32: Design data:
Material:
- Concrete strength
- steel yield strength
Cobiax _(42*42*36) cm.
soil:
Bearing capacity of the soil .
Loads.
Loads |  |  | 
block No. | Floor | Live load (KN/SM) | SID (KN/SM)
Block1 | basemnt floorS | 6 | 4
 | GF-6th floor | 5 | 4
 | Stair case | 1 | 2
Block2 | basemnt floorS | 6 | 4
 | GF-6th floor | 5 | 4
 | roof | 2 | 2
 | Stair case | 1 | 2

## Slide 33: Design data:
Seismic factor:
Seismic factor |  | 
The location of the building in Nablus city. |  | 
Seismic zone factor | Z | 0.2
Soil profile |  | SC
Acceleration seismic coefficient | (Ca) | 0.24
Velocity seismic coefficient | (Cv) | .32
Seismic importance coefficient | (Ι) | 1
Structure design type |  | Building frame system -shear wall-concret
Over strength factor | (R) | 5.5
Seismic zone factor UBS-97

## Slide 34: Verification check:
Compatibility check:
Block No1.
Block No2.

## Slide 35: Verification check:
Equilibrium check:
The % of error in equilibrium check must be less than 5%.
Stress-Strain check:
The %of the error in stress strain check must be less than:
10% of column.
30% for beam and slab in two-way system.
10% for beam and slab in one-way system
Equilibrium check |  |  | 
blocks | Value of load (kN) |  | error
Block 1 | Etabs (V16) | manual calculated | % of error
Dead load | 65824.39 | 65058.22 | 1.16
Live load | 22388.91 | 23055.28 | 2.98
SID laad | 26721.91 | 26354.88 | 1.37
Block 2 | Etabs (V16) | manual calculated | % of error
Dead load | 34928.72 | 34212.69 | 2.05
Live load | 12479.32 | 12448.91 | 0.24
SID laad | 11689.6 | 11930.08 | 2.06

## Slide 36: Seismic check: Period check:
Block 2.
  Block 1.
𝑇 𝑝𝑒𝑟𝑖𝑜𝑑 𝑚𝑎𝑛𝑢𝑎𝑙=1.006 𝑠𝑒𝑐
𝑇 𝑝𝑒𝑟𝑖𝑜𝑑 𝐸𝑡𝑎𝑏=1.016 𝑠𝑒𝑐

## Slide 37: Seismic check:
  Mass partition check:
  The summation of Ux and Uy must bee reach 90%.
  Block 1.
  Need a 18 mode.

## Slide 38
  Block 2.
  Need a 63 mode

## Slide 39: Drift check:
The displacement from Etabs for the two directions must be less than the limit displacement
  Block 1.
  The manual displacement less than the limit.
  Block 2.
  The manual displacement less than the limit.

## Slide 40: Seismic check:
  Base shear check:
  The % of errors in base shear check must be less than 5%.
Block No1.
Block No2.
Manual calculated of base shear=5208.21 kN
Etabs result
Manual calculated of base shear=2643 kN
Etabs result

## Slide 41: Deflection check:
  Deflection limit = Ln/240.
  After we checks all of the panel in the building, we made sure that there no values ​​from Etabs exceeding the limit.

## Slide 42: Design and detailing of the structure elements:
1.Footings:
We are used one type of footings in this building.
mat footing.

## Slide 43
Mat footing (Block1).
mat footing with thickness 90cm.
Bottom reinforcement.
Bottom reinforcement x-axis:
Bottom reinforcement y-axis:

## Slide 44
Mat footing (Block1).
Top reinforcement.
Top reinforcement x-axis:

## Slide 45: 2. columns:
We are used three type of columns shape this building, rectangular ,square and circular shape with one dimension of each shape.

## Slide 47
3. Slabs:
We used different systems of slab in this building.
Voided slab with thickness 50cm.
Two way solid slab with thickness 30cm.
One way ribbed slab with thickness 32cm.
One way solid slab with thickness 15cm for stair case.

## Slide 48: Voided slab with thickness 50cm (Block1):
Basement floor layout.
Section in slab.

## Slide 49: Voided slab with thickness 50cm (Block1):
Bottom reinforcement bars y-axis .
Bottom reinforcement bars x-axis .

## Slide 50
top reinforcement bars x-axis .
top reinforcement bars y-axis .

## Slide 51: 4. Beams: we designed many different dimensions in this building.
Block No1.
Block No2.

## Slide 52
Detailing of beam B1 in block 1.

## Slide 53
Detailing of beam B9 in block 2.

## Slide 54: 5. Shear wall: We used thickness 30cm for shear wall.
Block No1.
Block No2.

## Slide 55
HVAV Design
Artificial lighting & Electrical
Acoustical Design
Water Supply & Drainage
Electromechanical Aspects

## Slide 56: HVAC system

## Slide 57: HVAC Design
VRF (Variable Refrigerant Flow) system has been used.
Fan coil unit VRF system has been used.
Equipment from different companies (TOSHIBA, METALAIRE) has been used.
floor name | total clloing load kw
fgroung floor | 12.5
first floor | 19.3
second floor | 25.3
third floor | 31.52
fourth floor | 23.9
fifth floor | `17.5
sixth floor | 16.23

## Slide 58: Outdoor units:
Out door VRF unit system

## Slide 59: Indoor units:
Fan coil unit
Fresh air in take unit

## Slide 60: Indoor units:

## Slide 61: The distribution of the HVAC systems in the Basement floor

## Slide 62: Artificial lighting Design

## Slide 63: Lighting design for the manger room:
Luminaires selected
Simulation result
space | standard lux | lux desgion | ugr standerd | ugr desgion | uniform standerd | uniform desgion
head manager | 300 | 480 | <19 | <10 | 0.6 | 0.63
Lighting disruption swatch for head manger room

## Slide 64: 3D views for the manger room.

## Slide 65: 3D views for the lope room

## Slide 66: Lighting design for lope:
Luminaires selected:
space | standard lux | lux desgion | ugr standerd | ugr desgion | uniform standerd | uniform desgion
loope | 300 | 400 | <19 | <10 | 0.6 | 0.63
Lighting lope disruption
and swatch
Simulation result

## Slide 67: Lighting design for all room :
space name | stnderd lux | Lux design | UGR standard | UGR design | Uniformity standard | Uniformity design
Barcking | 75 | 92 | _ | _ | 0.4 | 0.36
Service office | 300 | 352 | _ | _ | 0.6 | 0.63
Lobby for theatr | 150 | 200 | <19 | <10 | 0.6 | 0.63
Cafeteria | 300 | 480 | _ | _ | 0.6 | 0.6
main head room | 300 | 480 | <19 | <10 | 0.6 | 0.63
WC | 100 | 115 | _ | _ | 0.4 | 0.33
Since all floors have the same spaces,
this table expresses all values ​​for all floors

## Slide 68: Electrical Design

## Slide 70: Electric board for light and socket

## Slide 71: Load distribution and cable area
load | load (w) | total power (w) | I (load) w | IC. B Amp | I cable Amp | C.B Amp | Cable(ice)
light load | 2200 | 2200 | 10 | 11.5 | 13.2 | 16 | 2.5mm^2
socket load | 250 | 6250 | 28.4 | 32.6 | 37.5 | 40 | 8mm^2
The electrical load of elevator
main distribution for elevator | power (w) | I load (Amp) | IC. B (Amp) | I Caple (Amp) | C.B (Amp) | Cable (Amp) | phase
four elevators | 2800 | 44.8 | 50.6 | 57.5 | 60 | 61Amp (16mm^2) | 3
main distrubuation for hvac | power (w) | I load (Amp) | IC.B (Amp) | I caple (Amp) | C.B (Amp) | Cable(Amp) | phase
ground floor | 15300 | 23.5 | 27 | 31.05 | 46 | 46Amp 10mm^2 | 3
first floor | 19000 | 29.3 | 29.7 | 34.155 | 46 | 46Amp 10mm^2 | 3
second floor | 29000 | 40.6 | 46.7 | 53.705 | 61 | 61Amp 10mm^2 | 3
third floor | 25600 | 39.4 | 45.3 | 52.095 | 61 | 61Amp 10mm^2 | 3
fourth floor | 26200 | 40.3 | 46.4 | 53.36 | 61 | 61Amp 10mm^2 | 3
fifth floor | 31600 | 48.6 | 55.9 | 64.285 | 61 | 61Amp 10mm^2 | 3
sixth floor | 17800 | 27.4 | 31.5 | 36.225 | 46 | 46Amp 10mm^2 | 3
Electrical load for first floor
The electrical load of Hvac

## Slide 72: Acoustical Design

## Slide 73: Reverberation Time (RT60):
The spaces that were designed acoustically in the building :
Manger room in sixth floor
The absorption coefficient for the finished material were used.
finishing material | Absorption coefficient at every frequency (HZ) |  |  |  |  |  | 
 | 125 | 250 | 500 | 1000 | 2000 | 400 | 8000
plaster | 0.04 | 0.05 | 0.07 | 0.08 | 0.04 | 0.06 | 0.05
wooden floor | 0.07 | 0.2 | 0.41 | 0.49 | 0.51 | 0.54 | 0.53
glass | 0.1 | 0.06 | 0.04 | 0.03 | 0.03 | 0.03 | 0.04
door (hollow) | 0.14 | 0.35 | 0.25 | 0.2 | 0.03 | .03. | 0.04
calling | 0.15 | 0.2 | 0.15 | 0.1 | 0.15 | 0.1 | 0.15
ceramic | 0.01 | 0.01 | 0.04 | 0.04 | 0.04 | 0.07 | 0.07

## Slide 74: Classroom RT60 according to Millington
 | FULL | 50% | EMPTY
freq (hz) | RT(60) | RT(60) | RT(60)
125 | 1.56 | 1.59 | 1.65
250 | 1.19 | 1.2 | 1.23
500 | 1.11 | 1.13 | 1.16
1 KHZ | 1.01 | 1.04 | 1.08
2KHZ | 0.88 | 0.89 | 0.9
4KHZ | 0.78 | 0.78 | 0.79

## Slide 75: STC and IIC
External walls:
Internal wall
hz | 63 | 125 | 250 | 500 | 1k | 2k | 4k
db | 55 | 65 | 75 | 85 | 86 | 91 | 101
Wall 1*71.2mm European l f5/G +1*100mm concrete +100 mm poliestere(10kg/m^3)+1*100 holly block
hz | 63 | 125 | 250 | 500 | 1k | 2k | 4k
db | 24 | 31 | 40 | 45 | 51 | 52 | 70
10 cm light block + 2mm plaster in both side +50 mm fiber class

## Slide 76: STC and IIC
Ceiling
hz | 63 | 125 | 250 | 500 | 1k | 2k
db | 42 | 48 | 61 | 69 | 74 | 85
1*50rock wall T1 150+1*60mm concrete+ 1*330mm concrete +1*70mm concrete savr-60
+Z purlin(700*70)mm empty cavity
Impact insulation class (IIC)
hz | 63 | 125 | 250 | 500 | 1k | 2k | 4k
db | 50 | 54 | 55 | 52 | 44 | 33 | 20
Sand bead under ceramic tile (40mm) +1*50rock wall T1 150+1*330mm concrete + 1*170mm rib slab +1*12.25gypsemna regular

## Slide 77: Loud speaker
The type of speaker was used in the meeting room:
two speakers from Yamaha club Company were used on the walls and the max SPL value for this type is 88 dB

## Slide 78: Fire fighting system

## Slide 79: firefighting plan of the ground floor
The symbols of the fire fighting and evacuation systems in the building

## Slide 80: Contests of fire fitting system
Smoke detector
Heat detector
Sprinkler
Emergency sign
Fire hose
Dry stand pipe

## Slide 81
space name | fire fitting way
office | drw boder extinguisher
computer room | drw boder extinguisher
barcking | water sprinker
lope | water sprinker
caffteria | water sprinker
manger room | dry sprinkler

## Slide 82: Water Supply System

## Slide 83: Water supply system
Water Tanks Used

## Slide 84: Water consumption
Consumption for drinking and domestic Consumption
number of person | person cosume /day(L) | total consume/day(L)
160 | 8 | 1280
Firefighting consumption
tupe of consumption | cosumption (m^3)
fire fitting | 170
Tank volume 4000L to provide the budling water in case of cutoff water

## Slide 85: Water pipe dustrpution

## Slide 86: Drainage System

## Slide 87: Pipes used
The total number of fixture units is 210 fu the main diameter for the main stack is
The diameters for the pipes as follows
Horizontal pipe for the water closet is with slope 1%
Horizontal pipe for the lavatory is with slope 2%
The pipe between the manholes is with slope1%
The rain water main vertical stack
show fu for each floor and for horizontal and vertical pipe

## Slide 88: Bath Room Drainage

## Slide 89: Quantity Surveying and Cost Estimation

## Slide 90: The total cost of the building is 19041028 NIS and the total area of the building is 9700m2 which means that the total unit cost per m2 is1866.518NIS/m2, nearly 600 $/m2
Earth work = 1687770 NIS
Foundation = 838615NIS
Building (construction) = 1549217NIS
Finishing = 6113730NIS
Electrical = 378590NIS
Mechanical =1549217 NIS

## Slide 91: Thank you
Prepared by :
Ameen Hamed
Jaser Jamil Qaq Mohammad Sholi
Supervisor :
Eng. Alaa Shaheen