## Slide 1: Graduation Project 2 Structural Analysis and Design of Educational Research and Development Center in Birzeit
Prepared by:
Mahmoud Ibrahim Daraghmeh
Mustafa Nedal Eleyan
Qais Mofeed Daraghmeh
Qusai Mahmoud Mahmoud
Supervised by:
Eng. Ibrahim Arman
An-Najah National University Nablus - Palestine
Faculty of Engineering Civil Engineering Department
Spring 2020

## Slide 2: Outline
Project Description
Codes and Standards
Materials
Site Investigation
Software
Load Types
Load Combinations
Preliminary Dimensions
Modeling
Irregularities
Checks
Design of structural elements

## Slide 5: Project Description

## Slide 6
The project includes a design of the educational research and development center building which located in Birzeit in Ramallah.
The building consists of six floors. Which are basement floor and five floors above the ground.
The height of each floor is 4.2 m except the basement floor which has a height of 3.5m.

## Slide 7
Floor | Usage | Area (m2)
Basement | Garage, mechanical room and an electrical room. | 912
Ground | Conference hall and the department of education and research. | 792
First | Meeting rooms, administrative deputy unit and department of educational and policies. | 792
Second | Technical deputy unit, head of center and administrative department. | 875
Third | Technical deputy unit. | 819
Fourth | Cafeteria and bedrooms. | 853

## Slide 8: Plan for Basement

## Slide 9: Plan for Ground Floor

## Slide 10: Plan for First Floor

## Slide 11: Plan for Second Floor

## Slide 12: Plan for Third Floor

## Slide 13: Plan for Fourth Floor

## Slide 14: Plan for Roof

## Slide 15: Materials
Materials for structural elements:
Concrete B350 (f’c = 28 MPa) E = 24870.06 MPa, γ = 25 kN/m3
Reinforcing Steel (ASTM A615, Grade 60) Fy = 420 MPa, Fu = 630 MPa Es = 200 GPa

## Slide 16: Materials
Materials for non- structural elements:
Plain concrete (γ = 23kN/m3)
Concrete block (γ = 15kN/m3)
Sand (γ = 18kN/m3)
Tiles (γ = 27kN/m3)
Stone units (γ = 27kN/m3)
Spray foam
False ceiling

## Slide 17: Soil Investigation
According to the types of material that are founded when making the boreholes, the recommended type of foundation is single footings using soil allowable bearing capacity,
q all=400 kN/m^2.

## Slide 18: Soil Investigation
The locations of the boreholes in the site:

## Slide 19: Codes
ACI 318-14: For sections design and detailing.
IBC–2012: For determining loads.
ASCE 7-10:For determining loads.
Jordanian Code for Loads – 2006.

## Slide 20: Software
ETABS 18.1.1.
SAFE 16.0.0.
SAP2000 21.
AUTOCAD 2018.

## Slide 21: Load Types
Dead Loads
It’s the own weight of the structural elements of the structure, which are slabs, beams, columns, walls, footings and dome.
Superimposed Dead Loads
It’s the weight of the non-structural elements, which is distributed on slabs, walls, dome and staircases.

## Slide 22: Load Types
Live Loads
Live loads are produced from the occupancy and movable objects on the building, and their values were determined in consideration to ASCE 7-10.
A uniform live load on all floors, except roof, was taken as 5 kN/m2.
And roof live load = 2 kN/m2.

## Slide 23: Load Types
Snow Load
Snow load was determined in accordance with Jordanian Code 2006 using the following equation.
Sd = μi So, where:
So : Site snow load (kN/m2)
Sd : Snow load on roof (kN/m2)
μi : Snow load shape coefficient.
Sd = 1.125*0.8 = 0.9 kN/m2

## Slide 24: Load Types
Wind Load
The structure was divided to two components with only one direction of wind; because all other cases will give the same results.

## Slide 25: Load Types
Wind Load
P = qh G CN p : wind pressure (N/m2) qh : velocity pressure (N/m2) G : gust-effective factor CN : net pressure coefficient
Wind Speed (V) = 120 km/h
Exposure Category “D”
Topographic Factor (Kzt) = 1
Gust Factor (G) = 0.85

## Slide 26: Load Types
Wind Load
Units of structure:

## Slide 27: Load Types
Wind Load
Wind pressure on Leeward wall of unit 1:
Wind pressure on Leeward wall of unit 2:

## Slide 28: Load Types
Wind Load
Wind pressure on Side wall of unit 1 & 2:
Wind pressure on Windward wall of unit 1 & 2:

## Slide 29: Load Types
Wind Load
Wind pressure on Roof of unit 1:
Wind pressure on Roof of unit 2:

## Slide 30: Load Types
Earthquake Loads (EQ)
Risk Category (III)
Importance Factor (Ie) = 1.25
Site Class “B”
Acceleration Parameter at Short Period (Ss) = 0.44
Acceleration Parameter at 1-SEC Period (S1) = 0.11
Fa = 1
Fv = 1
SDS = 0.44
SD1 = 0.11

## Slide 31: Load Types
Earthquake Loads (EQ)
Seismic Design Category “C”
Modal Response Spectrum Analysis was used.
Redundancy Factor (ρ) = 1.0
Eh = ρ QE = 1.0 QE
Ev = 0.2*SDS*D = 0.088 D

## Slide 32: Load Types
Earthquake Loads (EQ)
Seismic force-resisting system is Bearing Wall System (Ordinary RC Shear Walls), as shear walls resist almost all lateral loads and more than 50% of gravity loads.
Direction | Total Base Shear (kN) | Shear Walls Portion (kN) | Percentage (%)
X | 9945 | 9789.8 | 98.4 %
Y | 10358 | 10264.5 | 99.1 %
Total Gravity Load (kN) | Shear Walls Portion (kN) | Percentage (%)
132534.3 | 91556 | 69 %

## Slide 33: Load Types
Earthquake Loads (EQ)
Response Modification Factor (R) = 4
Overstrength Factor (Ωo) = 2.5
Deflection Amplification Factor (Cd) = 4
Tn,x = 0.4 sec.
Tn,y = 0.38 sec.
Base Shear: V,x = 10232.5 kN V,y = 10585.4 kN

## Slide 34: Load Types
Earth pressure
Pressure of the soil (P) = γ H k0
Ko =1-sin⁡∅
The horizontal component of the pressure of the soil

## Slide 35: Load Types
Surcharge Pressure
The pressure on the basement from the surcharge load is constant and is calculated according to the following equation:
Psurcharge = Surcharge load * Ka = 2* 0.5= 1 KN/m2
Horizontal component of the surcharge load:

## Slide 36: Load Types
The horizontal component of the pressure of the soil and the surcharge load:

## Slide 37: Load Types
Soil Seismic Load
∆P = 0.4 Kh γt H rw.
Where,
∆P: additional earth pressure caused by seismic shaking, which is assumed to be uniform pressure.
Kh: horizontal seismic coefficient in the soil, which may be assumed equal to Sxs/2.5.
γt: Total unit weight of soil.
H rw: height of the retaining wall: and
Sxs: spectral response acceleration parameter (Sxs = Fa Ss).
Sxs = Fa Ss = 1.0*0.44 = 0.44.
Kh = Sxs/2.5 = 0.44/2.5 = 0.176.
∆P = 0.4 Kh γt H rw = 0.4*0.176*20*3.5 = 5 KN/m2.

## Slide 38: Load Types
Soil Seismic Load
The pressure caused by the seismic shaking

## Slide 39: Load Types
Soil Seismic Load
The total earth pressure on the wall consists of the seismic earth pressure and the unfactored static active earth pressure.
The total earth pressure on the wall:

## Slide 40: Load Combinations
There are two types of load combinations, strength (used for design) and service (used for serviceability checks).
D = dead load and super-imposed dead
H = load due to lateral earth pressure, ground water pressure, or pressure of bulk materials.
L = live load
E = earthquake load,
Where (E) consider Horizontal component Eh (both X & Y directions) and Vertical component Ev of seismic load, and directional effect (100% from seismic load acting on some direction and 30% from this load acting in other direction).
Ev = 0.2 SDS D = 0.2*0.44*D
Ev = 0.088 D

## Slide 41: Load Combinations
Ultimate Load Combinations | Service Load Combinations
1.4 D + 1.6 H | D + H
1.2 D + 1.6 L + 1.6 H | D + L + H
1.2 D + Ev + Eh + L + 1.6 H | D + 0.7 Ev + 0.7 Eh + 1.0 H
0.9 D – Ev – Eh + 0.9 H | 1.0 D + 0.525 Ev + 0.525 Eh + 0.75 L + 1.0 H
 | 0.6 D – 0.7 Ev - 0.7 Eh + 0.6 H

## Slide 42: Preliminary Dimensions

## Slide 43: Preliminary Dimensions for Beams
Width of beams = Length of span / 20
Thickness of beams is according to the table:

## Slide 45: Preliminary Dimensions for Beams
Beam | Depth (mm) | Width (mm)
B1 | 700 | 550
B2 | 650 | 600
B3 | 700 | 650
B4 | 350 | 300
B5 | 200 | 200
B6 | 300 | 250
B7 | 250 | 250
B8 | 600 | 450
B9 | 600 | 450

## Slide 46: Preliminary Dimensions for Slabs
Slab thickness for one way slabs are according to the table:
All one way slabs are taken as 200 mm thickness.
 | Cantilever | Simple | One-end continuous | Two-end continuous
Slab Thickness | L / 10 | L / 20 | L / 24 | L / 28

## Slide 47: Preliminary Dimensions for Slabs
Slab thickness for two way slabs are according to the table:
All two way slabs are taken as 200 mm thickness.

## Slide 48: Preliminary Dimensions for Shear walls
It is difficult to determine the thickness of the walls; because it is difficult to know the load that came on them.
All wall thicknesses are assumed to be 300 mm.

## Slide 49: Preliminary Dimensions for Columns
The dimensions of the columns were determined from axial load on it, and it calculated from tributary area around columns, including its own weight.
P = (dead load + live load + super-imposed) * (tributary area) * 1.10
P = ϕPn = ϕ × λ × (0.85 f'c ×Ag × (1- ρ) + fy × ρ ×Ag)

## Slide 51: Preliminary Dimensions for Columns
Column | Dimensions (mm)
C1 | 1700 * 1700 * (300 thickness)
C2 | Diameter = 500
C3 | 1000 * 500
C4 | 600 * 300
C5 | 500 * 400
C6 | 350 * 350

## Slide 52: Preliminary Dimensions for Footings
Type of footings is according to its type, in the meaning that the columns has single footings and wall has continuous footing.
Single and wall footings used because total area of footing needed to distribute load is less than 0.5 area of typical floor.
Area of footing are selected to distribute the load from structure to the soil and make pressure under footings less Bearing Capacity of the soil.
Thickness of footing are selected mainly to resist one way shear and punching shear

## Slide 54: Preliminary Dimensions for Footings
Footing | Length (m) | Width (m) | Thickness (mm)
F1 | Variable | 4.0 | 1000
F2 | 2.3 | 2.3 | 500
F3 | 4.2 | 3.3 | 900
F4 | 3.0 | 2.6 | 700

## Slide 55: Modeling

## Slide 57: Modifiers
For beams
mass and weight
modifiers change
when depth of
beam change

## Slide 58: Modifiers
For columns

## Slide 59: Modifiers
For slabs

## Slide 60: Modifiers
For footings

## Slide 61: Modifiers
For piers

## Slide 62: Modifiers
For spandrels

## Slide 63: Mass source

## Slide 64: Function

## Slide 65: Number of modes

## Slide 66: Load Patterns

## Slide 67: Load Cases

## Slide 68: Load Combinations

## Slide 69: Irregularities
Torsional irregularity:
Torsional irregularity is defined
to exist where the maximum
story drift, computed including
accidental torsion with Ax = 1.0,
at one end of the structure
transverse to an axis is more
than 1.2 or 1.4 times the
average of the story drifts at
the two ends of the structure

## Slide 70: Irregularities
Torsional irregularity:
The structure is irregular due to this type of irregularity, so the eccentricities
were modified to take the effect of torsional irregularity.
The Equivalent Lateral Force method was modified by changing eccentricities
directly.
Dynamic analysis was made to take the torsional irregularity effect on Response
Spectrum Analysis method according to the ASCE Code.

## Slide 71: Irregularities
Reentrant corner irregularity:
Reentrant corner irregularity is defined to exist where both plan projections of
the structure beyond a reentrant corner are greater than 15% of the plan
dimension of the structure in the given direction.
This irregularity determine the type of analysis.
The structure is regular due to this type of irregularity.
Since Design category is (C), type of analysis will not affected by this irregularity,
and all types of analysis is valid.

## Slide 72: Irregularities
Stiffness-soft story irregularity:
Stiffness-soft story irregularity is defined to exist where there is a story in which
the lateral stiffness is less than 70% or 60% of that in the story above or less than
80% or 70% of the average stiffness of the three stories above.
The structure is regular due to this type of irregularity.

## Slide 73: Irregularities
Weight (mass) irregularity (weak story check):
Weight (mass) irregularity is defined to exist where the effective mass of any
story is more than 150% of the effective mass of an adjacent story. A roof that is
lighter than the floor below need not be considered.
The structure is regular due to this type of irregularity.

## Slide 74: Checks 1- Compatibility Check:

## Slide 75: Checks
2- Equilibrium Check
This check for ensure that loads added on model are correct
Dead Load:
Dead (Manual) = 68548 kN
Dead from program = 68498 kN
% error = 0.075 % < 5%
Live Load:
Live (Manual) = 20824.3 KN
Live from program = 21240 kN
% error = 2 % < 5%

## Slide 76: Checks
3- Stress-Strain Check
It was done live loads for different elements.
Slab:
M11 = = = 11.93 KN.m
Moments values from program :
M+ = 7.04 KN.m
M-1 = 5.04 KN.m
M-2 = 5.21 KN.m
(5.04+5.21)/2 + 7.04 = 12.17 KN.m
% error in moment = 2 % < 10 %

## Slide 77: Checks
3- Stress-Strain Check
Beam:
M = = 19.05 KN.m
Moments values from program :
M+ = 115.97 KN.m
M-1 = 164.8 KN.m
M-2 = 185.54 KN.m
(164.8+185.54)/2 + 115.97 = 291.14 KN.m
% error in moment = 6.7 % < 10 %

## Slide 78: Checks
3- Stress-Strain Check
Column:
Axial load (manual) = 292.6 kN
Axial load (ETABS) = 299.12 kN
% error in moment = 2.22 % < 10 %
Footing:
Moment (manual) = 228.63 kN.m
Moment (ETABS) = 253.7 kN.m
% error in moment = 9.8 % < 10 %

## Slide 79: Checks
4- Deflection Check
Long-term deflection:
Deflection from self-weight = 4.69 mm
Deflection from the long-term load combination = 43.47 mm
Deflection = 43.47 – 4.69 = 38.78 mm
Δall = 47.5 mm
Deflection < Allowable deflection, OK

## Slide 80: Checks
5- Check stresses under footings
Allowable bearing capacity for the soil = 400 kN/m2
Maximum stress value under F1 = 348.9 kN/m2 O.K.
Maximum stress value under F2 = 390.6 kN/m2 O.K.
Maximum stress value under F3 = 382.4 kN/m2 O.K.
Maximum stress value under F4 = 391.4 kN/m2 O.K.
All minimum values are larger than zero.

## Slide 81: Checks
6- Slenderness Check
Slenderness ratio =
Where:
k : effective length factor
Lu: unbraced length
r: radius of gyration
k = 1 , Lu,max = 3.95 m
For minimum section dimensions, r = 0.1
= 39.1 < 40
Then, all columns are short columns.

## Slide 82: Checks
7- Drift Check
The deflection at level x (δx) =
Drift was calculated as the difference of the deflections at the centers of mass at the top and bottom of the story.
Δall = 0.015 * story height
Δall for typical floors = 0.015*4200 = 63 mm
Δall for basement = 0.015*3500 = 52.5 mm
Δmax at X-direction = 1.31 mm O.K.
Δmax at Y-direction = 1.28 mm O.K.

## Slide 83: Checks
8- P-delta Check
θ =
When θ ≤ 0.1 , No Need for P-delta
θmax = ≤ 0.25
Where, is the of shear demand to shear capacity for the story. This ratio is permitted to be conservatively taken as 1.0.
So, θmax = = 0.125 < 0.25

## Slide 84: Checks
8- P-delta Check
In X-direction:
In Y-direction:
Story | stability coefficient | Check
Roof | 0.0006 | No Need for P-Delta
Fourth Floor | 0.0007 | No Need for P-Delta
Third Floor | 0.0008 | No Need for P-Delta
Second Floor | 0.0009 | No Need for P-Delta
First Floor | 0.0008 | No Need for P-Delta
Ground Floor | 0.0004 | No Need for P-Delta
Story | stability coefficient | Check
Roof | 0.0006 | No Need for P-Delta
Fourth Floor | 0.0007 | No Need for P-Delta
Third Floor | 0.0008 | No Need for P-Delta
Second Floor | 0.0008 | No Need for P-Delta
First Floor | 0.0009 | No Need for P-Delta
Ground Floor | 0.0003 | No Need for P-Delta

## Slide 85
Design of Structural Elements
Notes: Design results of program was verified on all structural elements, so final design results were taken directly from the program.

## Slide 86: Design of Dome
Dome has a thickness of 12 cm.
Inner face reinforcement:
A net of 1 ∅ 10 / 200 mm in both directions.
Outer face reinforcement (at lower half of the height):
A net of 1 ∅ 10 / 100 mm in both directions.

## Slide 87: Design of Slabs
All slabs are solid slabs and have a thickness of 25 cm, except slab of basement: 15 cm.
Shear check:
Vc = 138.9 kN
Vu in the first floor = 110.21 kN < Vc OK.
Vu in the second floor = 115.25 kN < Vc OK.
Vu in the third floor = 111.35 kN < Vc OK.
Vu in the fourth floor = 119.90 kN < Vc OK.
Vu in the roof floor = 80.97 kN < Vc OK.
Vu in the stairs roof = 30.59 kN < Vc OK.
 No Need for shear reinforcement.

## Slide 88: Design of Slabs
Floor | Bottom steel in direction 1 | Top steel in direction 1 | Bottom steel in direction 2 | Top steel in direction 2
Ground Floor | 1 12 /200 mm. | 1 12 / 200 mm. | 1 12 / 200 mm. | 1 12 / 200 mm.
First Floor | 1 12 / 150 mm. | 1 14 / 120 mm. | 1 12 / 150 mm. | 1 14 / 120 mm.
Second floor | 1 12 / 150 mm. | 1 14/ 120 mm. | 1 12 / 150 mm. | 1 14 / 120 mm.
Third floor | 1 12 / 150 mm. | 1 14 / 120 mm. | 1 12 / 150 mm. | 1 14 / 120 mm.
Fourth floor | 1 12 / 150 mm. | 1 14 / 120 mm. | 1 12 / 150 mm. | 1 14 / 120 mm.
Roof floor | 1 12 / 150 mm. | 1 14 / 120 mm. | 1 12 / 150 mm. | 1 14 / 120 mm.
Stairs roof | 1 12 / 200 mm. | 1 12 / 120 mm. | 1 12 / 200 mm. | 1 12 / 120 mm.
Floor | Bottom steel in direction 1 | Top steel in direction 1 | Bottom steel in direction 2 | Top steel in direction 2
Ground Floor |  |  |  | 
First Floor |  |  |  | 
Second floor |  |  |  | 
Third floor |  |  |  | 
Fourth floor |  |  |  | 
Roof floor |  |  |  | 
Stairs roof |  |  |  | 

## Slide 89: Design of Beams

## Slide 90: Design of Beams
Beam | Span | Width (mm) | Depth (mm) | Stirrups | Top Steel at End-1 | Top Steel at End-2 | Middle Torsion Steel | Bottom Steel
B1 | ـــ | 500 | 750 | 1Ø12/90 | 4Ø32 | 4Ø32 | 4Ø16 | 5Ø25
B2 | span1 | 500 | 750 | 1Ø12/100 | 6Ø32 | 6Ø32 | 4Ø14 | 5Ø32
 | span2 | 300 | 500 | 1Ø10/150 | 2Ø32 | 4Ø18 | 2Ø14 | 4Ø18
 | span3 | 300 | 300 | 1Ø10/130 | 2Ø18 | 2Ø18 | 2Ø10 | 2Ø18
B3 | span1 | 500 | 750 | 1Ø12/100 | 5Ø32 | 6Ø32 | 4Ø14 | 4Ø32
 | span2 | 300 | 500 | 1Ø10/200 | 2Ø32 | 3Ø18 | 0 | 3Ø18
 | span3 | 200 | 300 | 1Ø10/130 | 3Ø18 | 2Ø14 | 2Ø10 | 2Ø14
B4 | ـــ | 300 | 500 | 1Ø10/100 | 3Ø25 | 4Ø25 | 2Ø14 | 3Ø25
B5 | span1 | 300 | 300 | 1Ø10/130 | 3Ø18 | 3Ø14 | 2Ø10 | 3Ø14
 | span2 | 300 | 300 | 1Ø10/130 | 3Ø14 | 3Ø14 | 0 | 2Ø14
 | span3 | 300 | 300 | 1Ø10/130 | 3Ø14 | 3Ø18 | 2Ø10 | 3Ø14
B6 | span1 | 300 | 500 | 1Ø10/150 | 3Ø20 | 3Ø18 | 2Ø14 | 3Ø18
 | span2 | 300 | 500 | 1Ø10/200 | 3Ø18 | 3Ø18 | 2Ø14 | 3Ø18
 | span3 | 300 | 500 | 1Ø10/200 | 3Ø18 | 5Ø20 | 2Ø14 | 3Ø20
B7 | span1 | 300 | 300 | 1Ø10/130 | 2Ø18 | 2Ø18 | 2Ø10 | 2Ø18
 | span2 | 400 | 500 | 1Ø10/100 | 4Ø18 | 3Ø20 | 2Ø14 | 3Ø20
 | span3 | 400 | 500 | 1Ø10/150 | 3Ø20 | 4Ø18 | 2Ø14 | 3Ø20
 | span4 | 300 | 300 | 1Ø10/130 | 2Ø18 | 2Ø18 | 2Ø10 | 2Ø18
B8 | ـــ | 200 | 300 | 1Ø10/130 | 2Ø14 | 2Ø14 | 2Ø10 | 2Ø14
B9 | ـــ | 200 | 300 | 1Ø10/130 | 2Ø14 | 2Ø14 | 2Ø10 | 2Ø14
B10 | ـــ | 300 | 1000 | 1Ø10/100 | 5Ø25 | 5Ø25 | 4Ø12 | 3Ø25
B11 | ـــ | 300 | 500 | 1Ø10/200 | 3Ø14 | 3Ø14 | 0 | 3Ø14
B12 | ـــ | 300 | 1000 | 1Ø10/100 | 4Ø25 | 3Ø25 | 4Ø12 | 3Ø25
B13 | ـــ | 200 | 300 | 1Ø10/130 | 2Ø14 | 2Ø14 | 2Ø10 | 2Ø14
B14 | ـــ | 300 | 500 | 1Ø10/150 | 3Ø18 | 3Ø18 | 2Ø14 | 3Ø18
B15 | ـــ | 400 | 500 | 1Ø10/100 | 3Ø20 | 3Ø20 | 2Ø16 | 3Ø20
B16 | ـــ | 300 | 300 | 1Ø10/130 | 3Ø14 | 3Ø14 | 2Ø10 | 3Ø14
B17 | ـــ | 200 | 300 | 1Ø10/130 | 2Ø14 | 2Ø14 | 2Ø10 | 2Ø14
TB-1 | ـــ | 300 | 400 | 1Ø10/150 | 3Ø16 | 3Ø16 | 0 | 2Ø18
TB-2 | ـــ | 300 | 400 | 1Ø12/90 | 2Ø16 | 2Ø16 | 0 | 3Ø25
TB-3 | All Spans | 300 | 400 | 1Ø10/150 | 4Ø18 | 4Ø18 | 2Ø12 | 2Ø25

## Slide 91: Design of Beams
Beams Detailing:
According to ACI318-14 code, at least two longitudinal bars should be extended along the top and bottom faces of the beam.
Splicing Ls = 1.3 Ldt.
Development length:
Ldt = (0.48 fy)/√(f'c) db , when db < 20 mm.
Ldt = (0.59 fy)/√(f'c) db , when db ≥ 20 mm.
where db is the bar diameter.
Development lengths should be increased by 30% for top steel bars when d ≥ 300 mm.

## Slide 92: Design of Beams
Beam B1:

## Slide 93: Design of Beams
Beam B1:
Section 1-1 Section 2-2

## Slide 94: Design of Columns

## Slide 95: Design of Columns
Check for design was done using interaction diagrams and Bresler’s Reciprocal load method:
>> Pu

## Slide 96: Design of Columns
Column Label | Dimensions (mm, mm) | Longitudinal Reinforcement | L Splice (mm) | Stirrups
C1 | 1700*1700 | 8416 | 800 | 2 12 / 150 mm.
C2 | Diameter = 700 | 1420 | 1000 | 1 12 / 180 mm.
C3 | 1400*500 | 2420 | 1000 | 4 12 / 320 mm.
C4 | 800*400 | 1616 | 800 | 3 12 / 250 mm.
C5 | 600*500 | 1620 | 1000 | 3 12 / 320 mm.
C6 | 350*350 | 814 | 700 | 3 12 / 220 mm.
Column Label | Dimensions (mm, mm) | Longitudinal Reinforcement | L Splice (mm) | Stirrups
C1 | 1700*1700 |  | 800 | 
C2 | Diameter = 700 |  | 1000 | 
C3 | 1400*500 |  | 1000 | 
C4 | 800*400 |  | 800 | 
C5 | 600*500 |  | 1000 | 
C6 | 350*350 |  | 700 | 

## Slide 97: Design of Columns

## Slide 98: Design of Columns
Column C4 cross section:

## Slide 99: Design of Walls
All shear walls have a thickness of 30 cm.
All shear walls are ordinary reinforced shear walls with uniform reinforcing.

## Slide 100: Design of Walls
Pier Group | Piers' Labels
P-G1 | P1, P4, P12, P15, P16, P17, P19, P24, P28, P29, P30, P32, P43, P44, P45, P46, P57, P58, P60, P61, P62, P63, P66, P67, P70, P71, P72, P79, P85, P88
P-G2 | P2, P3, P7, P27, P34, P47, P48, P83, P86
P-G3 | P22, P80
P-G4 | P10, P13, P20, P74, P77
P-G5 | P11, P14, P35, P38, P40, P52, P54
P-G6 | P8, P25, P31, P33, P51, P64, P68, P69, P81
Pier Group | Vertical Reinforcement | Horizontal Reinforcement
P-G1 | 1 ∅ 14 / 200 mm | 1 ∅ 10 / 200 mm
P-G2 | 1 ∅ 14 / 125 mm | 1 ∅ 10 / 200 mm
P-G3 | 1 ∅ 18 / 200 mm | 1 ∅ 12 / 200 mm
P-G4 | 1 ∅ 22 / 100 mm | 1 ∅ 12 / 150 mm
P-G5 | 1 ∅ 22 / 150 mm | 1 ∅ 10 / 200 mm
P-G6 | 1 ∅ 22 / 200 mm | 1 ∅ 10 / 200 mm

## Slide 101: Design of Walls
Pier P1 longitudinal section:

## Slide 102: Design of Walls
Spandrel Group | Spandrels' Labels
S-G1 | S1, S41, S47, S75, S76, S89, S126
S-G2 | S2, S3, S4, S5, S16, S113, S127, S128, S129, S130
S-G3 | S6, S8, S9, S10, S11, S17, S18, S19, S42, S43, S44, S45, S46, S48, S49, S50, S51, S52, S53, S54, S58, S60, S62, S65, S67, S70, S72, S77, S79, S81, S84, S86, S90, S91, S92, S93, S94, S114, S115, S116, S121, S122, S123, S124, S131
S-G4 | S23, S24, S25, S28, S29, S30, S32, S33, S34, S35, S36, S97, S98, S99, S100, S102, S103, S104, S105
S-G5 | S12, S13, S20, S26, S31, S37, S38, S57, S64, S69, S74, S83, S88, S96, S101, S106, S112, S117, S118, S125, S132
S-G6 | S21, S22, S27
Spandrel Group | Top Steel Bars | Bottom Steel Bars | Vertical Reinforcement | Horizontal Reinforcement
S-G1 | 3 ∅ 25 | 3 ∅ 25 | 1 ∅ 12 / 150 | 1 ∅ 10 / 200
S-G2 | 4 ∅ 25 | 4 ∅ 25 | 1 ∅ 12 / 125 | 1 ∅ 10 / 200
S-G3 | 4 ∅ 25 | 4 ∅ 25 | 1 ∅ 10 / 200 | 1 ∅ 10 / 200
S-G4 | 4 ∅ 32 | 4 ∅ 32 | 1 ∅ 10 / 200 | 1 ∅ 10 / 200
S-G5 | 5 ∅ 25 | 5 ∅ 25 | 1 ∅ 10 / 200 | 1 ∅ 10 / 200
S-G6 | 5 ∅ 32 | 5 ∅ 32 | 1 ∅ 10 / 150 | 1 ∅ 10 / 200

## Slide 103: Design of Walls
Spandrels S57, S64, S69:

## Slide 104: Design of Walls
Spandrels S57, S64, S69:

## Slide 105: Design of Footings
> Vu
for punching > Vu, punching

## Slide 106: Design of Footings
Footing | Length (m) | Width (m) | Depth (mm) | Steel along length – top (Length in m) | Steel along length – bottom (Length in m) | Steel along width – top (Length in m) | Steel along width – bottom (Length in m)
F1 | Shown in drawing | Shown in drawing | 800 | Shown in drawing | Shown in drawing | Shown in drawing | Shown in drawing
F2 | 2.3 | 2.3 | 800 | ∅ 18 / 150 (2.8) | ∅ 18 / 150 (2.8) | ∅ 18 / 150 (2.8) | ∅ 18 / 150 (2.8)
F3 | 8.3 | 3.5 | 1000 | ∅ 20 / 150 (8.9) | ∅ 25 / 125 (9.0) | ∅ 20 / 150 (4.1) | ∅ 22 / 150 (4.2)
F4 | 3.0 | 2.6 | 900 | ∅ 18 / 150 (3.5) | ∅ 22 / 150 (3.7) | ∅ 18 / 150 (3.1) | ∅ 20 / 150 (3.2)

## Slide 107: Design of Footings
Section in Footing F2:

## Slide 108: Design of Stairs

## Slide 109: THANK YOU