## Slide 1
SolarX Robot
Intelligent Autonomous Solar Panel Cleaning System
Hala Maree · Wafa Namroti
Supervised by: Dr. Aladdin Masri
An-Najah National University · Computer Engineering · 2025/2026
1
Introduction
Technologies
Features
Constraints
Future Work
Conclusion

## Slide 2
01
INTRODUCTION
The Problem
Solar Energy Dependency
Solar panels are critical for clean energy generation in residential, commercial, and industrial sectors.
Dust Accumulation Problem
Dust, sand, bird droppings and contaminants reduce sunlight reaching PV cells — causing significant efficiency loss.
Manual Cleaning Challenges
Traditional cleaning is time-consuming, costly, and dangerous — especially in large-scale solar farms.
The Solution: SolarX Robot
An autonomous robot that automates the cleaning process using sensors, motors, and a mobile application.
Project Overview
SolarX Robot is an intelligent autonomous solar panel cleaning system developed at An-Najah National University. It integrates embedded systems, wireless communication, sensors, and a Flutter mobile app into one practical solution.
2

## Slide 3
02
TECHNOLOGIES USED
Controllers & Communication
Arduino Mega 2560
Main Controller
• Reads all sensor data
• Controls motors & actuators
• Executes cleaning algorithms
• Manages Manual & Auto modes
• EEPROM state storage
ESP32 Module
Wireless Communication
• Connects robot to mobile app
• Bluetooth Low Energy (BLE)
• Real-time data exchange
• Remote monitoring & control
• UART link to Arduino
Key Sensors
IR Sensors ×4
Edge detection & panel boundary
Ultrasonic ×2
Water level & panel detection
MPU6050
Orientation & 90° turns
DS3231 RTC
Real-time scheduling
3

## Slide 4
02
TECHNOLOGIES USED
Hardware Systems
Mobility System
4 × DC Gear Motors + BTS7960 Drivers
Four 12V DC gear motors with wheels
High-torque for inclined surfaces
BTS7960 for precise speed & direction
Brush System
2 × Paint Rollers + DC Motors
Two paint rollers as cleaning brushes
Rotation motor via pulley + timing belt
Lifting motor raises/lowers brush
Relay module for safe switching
H-Bridge for cleaning motors
Water System
DC Pump + Nozzles + Tank
Water pump draws from onboard tank
Car windshield nozzles distribute water
Relay-controlled pump operation
Diode protects from reverse current
4

## Slide 5
03
FEATURES
Key Features
🕹
Manual Mode
Full directional control via Flutter app: Forward, Back, Left, Right, Stop commands over BLE.
⚡
Auto Mode
Enter panel dimensions & count. Robot autonomously cleans row-by-row, tracking position in real time.
🕐
Scheduled Cleaning
Set cleaning time via app. DS3231 RTC synced with phone triggers automatic cleaning at scheduled time.
📍
Edge Detection
4 × IR sensors and ultrasonic sensors prevent the robot from falling off panel edges.
💧
Water Level Monitor
Ultrasonic sensor checks tank level before each session. Alerts user if water is insufficient.
🔋
EEPROM Save State
Operational state is saved to EEPROM. User can pause, resume and stop robot when they want and continue from where it stoped.
5

## Slide 6
Cleaning Algorithm
Row-by-row zigzag traversal with edge detection
1
Start
▶
2
Move Forward
▶
3
Detect
Edge
▶
▶
▶
▶
Navigation Pattern — Zigzag Row-by-Row
Row 1
Row 2
Row 3
Robot
→
→
←
→
←
6
Turn 90°
5
Shift Row
4
Turn 90°
7
Continue
▶
8
Finish

## Slide 7
03
MOBILE APPLICATION
Flutter Mobile App
Built with Flutter · Communicates via Bluetooth Low Energy (BLE) · Controls & Monitors robot remotely
Manual Control
Directional buttons (F/B/L/R/Stop) send commands directly to the robot in real time.
Auto Mode
User inputs panel dimensions and count. App displays live position map and cleaning progress.
6

## Slide 8
03
MOBILE APPLICATION
Scheduling & Features Control
7
Scheduled Mode
Syncs phone time with DS3231 RTC. User sets a time and the robot auto-starts cleaning.
Features Page
Toggle water pump, brush motor, and brush position individually. Displays water tank level.

## Slide 9
04
CONSTRAINTS
Challenges & Limitations
01
IR Sensor Sensitivity to Sunlight
Operating outdoors means sunlight intensity changes interfere with IR sensor readings. Multiple calibration rounds were required to achieve stable edge detection performance.
02
MPU6050 Hardware Issues
Several MPU6050 sensor modules were damaged during testing and development. Replacing and re-integrating these sensors significantly increased debugging time.
03
Limited Budget
The project was developed with a constrained budget, requiring the use of locally-available, affordable components — which sometimes limited available options.
04
Weight Balance Challenge
The brushes increased front-side weight, causing imbalance. Two Metal Ball Caster Wheels were added to improve stability and maintain a fixed height.
✓ Despite these challenges, the final system was successfully implemented and demonstrated satisfactory performance during testing.
8

## Slide 10
05
FUTURE WORK
Roadmap & Recommendations
Near-term
🛰 GPS Navigation
Integrate GPS-based tracking and navigation for large-scale solar farm deployment.
Near-term
🧠 AI-Powered Scheduling
Use artificial intelligence to optimize cleaning schedules based on weather data and dust accumulation patterns.
Mid-term
☀ Solar Charging
Add onboard solar charging capabilities to extend operating time and make the robot fully energy-independent.
Long-term
🗺 Advanced Path Planning
Develop smarter navigation algorithms for complex solar farm layouts with irregular panel arrangements.
9

## Slide 11
06
CONCLUSION
What We Achieved
✓ Autonomous cleaning in Manual & Auto modes
✓ Real-time position tracking & panel map
✓ Edge detection with IR sensors and ultrasonic
✓ Water level monitoring & wet cleaning
✓ Scheduled operations with DS3231 RTC
✓ BLE-based Flutter mobile application
🌟 SolarX Robot
A practical, low-cost, and efficient autonomous solution for solar panel maintenance. By combining embedded systems, sensor technologies, wireless communication, and a mobile application, SolarX Robot successfully reduces human effort and improves solar energy system efficiency — with a clear roadmap for scaling to commercial installations.
10