## Slide 1
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Structural analysis and design of Tareq Al-Alool building - Nablus
Prepared By:
Yazan saif
Motaz othman
Mohammad masalha
Supervisor: : Dr. Riyad Abd Alkareem

## Slide 2: Outline :
Background information
Analysis and design inputs
Conceptual design
ETABs modeling & checks.
Design.

## Slide 4
Location:
The project addresses is the analysis and design of Tareq Al-Alool building (5500 m2) located in Nablus.

## Slide 5
Basement floor

## Slide 6
Ground floor

## Slide 7
1st floor

## Slide 8
Floor number | Function | Summation of Areas (m2) | Height of floors(m)
Basement (B3) | Parking, | 660 | 3.25
Basement(B2,B1) | Stores | 1115 | B2=3.25 B1=3.5
floors(GF,F1,F2,F3,F4) | Offices | 2240 | GF = 4.5 Floors=3
floors (F5,F6) | Apartments | 810 | 3
Sixth floor roof(F6) | Apartment | 55 | 3
Floors, functions areas and heights

## Slide 9
What we do in GP 11?
Dead
Superimposed
Gravity Load
Live

## Slide 10
    Concrete:
Unit weight of reinforced concrete = 25 kN/m³
Structural element | Fc` (MPs) | Concrete type | Modulus of elasticity(MPs)
Beams, slabs , stairs | 24 | B300 | 23000
Mat, columns, shear walls | 28 | B350 | 24900
Reinforcement steel:
Yielding strength (Fy) = 420MPa.
Modulus of elasticity (Es) = 200GP
Materials:

## Slide 11: .
Soil properties:
Soil investigation indicated that the
bearing capacity of the soil is 250 KN/m2.

## Slide 12
Loads :
Gravity
Lateral
Loads
Dead
Live
Earthquake

## Slide 13
  Load:
Dead Load:
13
Live load:
In this project, a live load of 2.5 kN/m2 will be used for Garage and 5 kN/m2 for corridors and floors according to IBC 2015
  Slab one way ribbed = 3.63 KN/ m2
  Slab two way ribbed =4.82 KN/m2
  Superimposed dead load= 4 KN/m2

## Slide 14: Load combinations: According to the "ACI 318-2011 , the load factors that are used in the analysis and design are:
Load combinations:
U = 1.4D
U = 1.2D + 1.6L
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 15: Computer programs:
  1) ETABS 2016: is used to analyze and design the structural elements.
  2) Sap 2000 for design and checks some of structural elements .
  3) AutoCAD: is used for plans and draw structural detailing.
  4) Other programs such as Excel and word.

## Slide 16
Preliminary design for building:

## Slide 17
Slab :

## Slide 18
For two end continuous ribbed slab thickness of slab h=span length/21 Ribbed slab thickness = 6.75 m/21 = 32 cm

## Slide 19
2. Beam Dimensions :
Beam | Dimensions(mm2)
main beams B2 | 320×1000
secondary beams B1 | 320×350
After making checks, the final beam dimensions are shown in this table:

## Slide 22
3. Column Dimensions :
Critical column is shown below in figure below:

## Slide 23
By using tributary area method,
Tributary area = (6.6 *5.76 ) = 38 m2
= 9239.8kN
Assume ρ =0.01
As= ρ *Ag
= ג×Ø (0.85𝑓𝑐 ′Ac + As × fy)
=0.65*0.8*(0.85*28*(Ag -0.01(Ag)) +420*0.01*Ag)/1000
Ag=460000 mm2 Assume b=h
b=h=700 mm these dimensions consider no moment .
Consider moment use column 800 *800 mm

## Slide 24
Columns dimensions are shown in table:
 | Original dimensions (mm)
C1 | 800*800
C2 | 600*600
C3 | 1000*1000

## Slide 25
Shear Wall
Wall | Thickness (mm)
Wall 1 | 200
Wall 2 | 250
Wall 3 | 300

## Slide 26
Modifiers for area structural element
Modifiers/Section | Slab | Shear walls
Membrane f11 Direction | 1 | 1
Membrane f22 Direction | 1 | 1
Membrane f12 Direction | 1 | 1
Bending m11 Direction | 0.25 | 0.7
Bending m22 Direction | 0.25 | 0.7
Bending m12 Direction | 0.25 | 0.7
Shear v13 Direction | 1 | 1
Shear v23 Direction | 1 | 1
Mass | 1 | 1
Weight | 1 | 1

## Slide 27
.
Modifiers for frame structural element
Modifiers/Section | beams | Columns
Cross Section(axial) Area | 1 | 1
Sheer Area in 2 direction | 1 | 1
Sheer Area in 3 direction | 1 | 1
Torsional Constant | 0.35 | 0.7
Moment of Inertia about 2 axis | 0.35 | 0.7
Moment of Inertia about 3 axis | 0.35 | 0.7
Mass | (Depth-200)/200 | 1
Weight | (Depth-200)/200 | 1

## Slide 28: DYNAMIC ANALYSIS
  Response Spectrum Analysis
Modes and Period
Drift Check

## Slide 29: Definition of mass resource

## Slide 30: Seismic Parameters

## Slide 31: Seismic Zone Factor Z

## Slide 32: Site Classification Sd

## Slide 33
Seismic Coefficient Ca

## Slide 34: Seismic Coefficient Cv

## Slide 35: Seismic Importance Factor I

## Slide 36: Define Of Response Spectrum Function

## Slide 37: Response Spectrum In X-Direction

## Slide 38: Response Spectrum In Y-Direction

## Slide 39: Check Base Shear

## Slide 40
Cs = =0.0945
W= 82044 kN
V= 82044 0.0945 = 7753 kN
Not ok

## Slide 41: After increase scale factor the value become large than V

## Slide 42: Check period
By method A
The period, T is given by:
So,
And from Etabs
Tetab < 1.2 Tcal
Period in mode 1 → T= 0.74 sec.

## Slide 43
Checks
Model check
Deflection check
Structural period T check
Stress strain check
Equilibrium check

## Slide 44: Model check

## Slide 45
compatibility check

## Slide 46: Equilibrium check
Type | ETABS results (KN) | Hand calculation (KN) | Error%
Live | 22200 | 22182 | 0
Superimposed | 21588 | 21574 | 0
Dead | 55643 | 54811 | 0

## Slide 48
M Hand =115.4KN.m
% Difference =33%
We made the internal force check from live load for this beam as following in the figure:
Stress strain check

## Slide 49: Stress strain check
We made the internal force check from live load for this coulmn as following in the figure:
D= (-From hand:
D= (37.46*2.5*3)+(37.46*5*7)=1592KN
1564 KN
Error 0 < 10 % OK

## Slide 50: Stress strain check
We made the internal force check from SD load for slab as following in the figure:
-From hand:
SD =𝑊𝑢×𝑙2/8=(4×6.45^2)/8=20KN.𝑚
From Etab
-(M1 + M2)/ 2 + M3 =(13+12.2)/2 + 8.6= 21.5KN.m.
Error 5 % < 10 OK

## Slide 51
ACI code limitations on immediate and long term deflections
Long term deflection
Deflection check

## Slide 52
immediate term deflection for ribbed slab :
Deflection check
Maximum deflection (Uz) = 22.8-(AVG OF (2.5, 3.56,2.8, 3.9))
=19.61 mm
𝐴𝑙𝑙𝑜𝑤𝑎𝑏𝑙𝑒 𝑑𝑒𝑓𝑙𝑒𝑐𝑡𝑖𝑜𝑛 = 𝐿 /240
=(7.25∗ 1000)/ 240
= 30.2 𝑚𝑚.
19.61 mm < 30.2 → Ok

## Slide 53: Deflection For Beam

## Slide 54
For beam:
Allowable deflection=L / 240= (7.25 *1000)/240= 30.2 mm
Deflection from sap = 9.7- ((3.9+2.3)/2) = 6.6 mm

## Slide 55
Check for shear in slab :
Hand = 0.75X X 1X = 25 kN/Rib
= 46.7 KN/m
  From above Figures it was noticed that ɸVc ≫ Vu so no need for shear reinforcement in slab.

## Slide 56: DESIGN Design of element for flexure

## Slide 57
Design for slab
Asmin = ρ b h
= 0.0033 X 150 X 320 = 140 mm2 (use 2 10/Ribbed)
So, As = 140 mm2 \ 0.55 m
ΦMn= 0.9 X 140X 420 X (280-(19.3/2)) X 10-6
= 14.6 kN.m /0.55m
=26 KN.m\m

## Slide 58: Moment (11)→ bottom and top 2φ10mm/ribbed mm for top steel

## Slide 59: Design for coulmn
From ETABS we found:
The axial force in column =548 kN
M11=113kN.m
M22=195kN.m
At first we will check the slenderness effect (KL/r):

## Slide 60
KL/r = 1 X 3.25 / 0.24 = 13.54 should be less than 34
34so is a short column

## Slide 61
:
M2=113kN.m
Pu=548.5kN.
ϒ=
From interaction diagram
=0.2X 800 X 800 X 7/1000=896kN.

## Slide 62
:
=1254
Pn>Pu
As=0.01800800=6400mm2(17Ø22)

## Slide 63: Design for matt foundation

## Slide 64
Checks:
Bearing capacity of soil
maximum spring load = 40
Bearing capacity = 40/0.5*0.5 = 160 < 250 K.n/m2 ok

## Slide 65: Shear capacity check(punching):
Vu = pu – q (critical section )
bd
Vu = 4954
Vc = 6773 VC>VU Check is ok

## Slide 66: Slab Moment and Area of steel
As min = ρ b h
= 0.0018 × 1000 × 1600 = 2880 mm2 (use 10 20mm)
Φ Mn= 0.9×1880×420× 1500 - (33.1/2)) ×10-6 =1747 kN.m /m

## Slide 67: All value is less than 1747 K.n/m in both m11 & m22 The reinforcement is 10 20mm/m

## Slide 68: Design of stairs:

## Slide 69: Deflection shape

## Slide 70
Based on the long term deflection, max. immediate deflection from SAP2000, ∆ =2.7 mm
Deflection limitation:
𝑎𝑙𝑙𝑎𝑤𝑎𝑏𝑙𝑒 𝐿𝑜𝑛𝑔 𝑡𝑒𝑟𝑚, ∆𝐿 ≤ 𝑙 /240 = 2700/240= 11.25 mm
The long term deflection from SAP found approximately 2.7 mm, which means that is smaller than the allowable deflection → OK

## Slide 71
Check for shear:
Vu13 and Vu23 from SAP analysis = 67 kN and 62 kN respectively.

## Slide 72
VC= 0.75××λ× ×b×d
= 0.75××1000×110/1000 =72.8 kN
Vu= 67 kN
The slab thickness is OK

## Slide 73: Design for flexural:
and from landing analysis by SAP2000 = 9 , 10.6 kN.m respectively.

## Slide 74
Mu max =8 kN.m
ρ = ) =0.00236
As= 0.00236 × 1000×110 =260
=0.0018×1000×150=270 (Consider it as slab)
As > so Use As= 270 (4ɸ10/m in two direction)

## Slide 75
ρ = ) = 0.00191
As=0.00191× 1000×110 =210
=0.0018×1000×150=270
As < so Use As= 270 (4ɸ10/m)
As we defined the stair as one-way solid slab, so the transverse moment is too small, so we used:
For Flight:
from flight analysis by SAP2000=8.6 kN.m

## Slide 76: Design For Interior Panel (B12 ):
:
1-Parameters:
2-Steel Reinforcement:
Mu,max Positive = 120 kN.m >>> 6Ø16 mm.
Mu,max Nevative = 225 kN.m >>> 8Ø20 mm.
Vu = 242 kN >>> / 300 mm.
b (mm) | h (mm) | d (mm) | (Mpa) | fy (Mpa)
1000 | 320 | 240 | 24 | 420
b (mm) | h (mm) | d (mm) |  | fy (Mpa)
1000 | 320 | 240 | 24 | 420

## Slide 77: AutoCAD Details :

## Slide 78: Design For Shear Wall (SW-3 ):

## Slide 79: Notes:
5 internal ultimate forces can be computed; namely, P, Vx, Vy, Mx and My .
Design for V-y in a way similar to beams .
Design for M-y can be carried out by assuming there acts as Couple.
Design for P and Mx in a way similar to columns.
The stresses in the SW-3 are less than 0.1 F`c, there is no need for interaction diagram check.

## Slide 80: Reinforcement For SW-3 :
AS min=0.0025×b×h=0.0025*1000*300 >>> (1Ø12/200mm) on each side.
According to ACI315-04 section 2.10 these rules are following:
Transverse and Longitudinal rebar ratio shall be at least 0.0025
Spacing of reinforcement shall not exceed: mm.
h: the thickness of shear wall (300mm).
So the maximum spacing is 450 mm which is larger than 300 mm, so it is OK.

## Slide 81: Reinforcement For SW-3 :
First : Add Two column to the shear wall , To minimize the moment on shear wall and make Minimum Reinforcement.
Second : Use General Reinforcement At Etabs Pier Design.

## Slide 82: Shear Wall Results :
General Reinforcement:
Define General Reinforcement for Etabs using minimum Reinforcement ,But many Etabs alerts for moment and shear so we increase the Reinforcement.

## Slide 83: Etabs Reinforcement Check Result :

## Slide 84: Shear Wall Reinforcement Results :
 | Vertical reinforcement/m | As/2 | Reinforcement For wall | Horizontal reinforcement/m | Reinforcement For wall | Shear Reinforcement For wall | Vertical reinforcement For Column | Shear Reinforcement for Column
SW-3 | 1600 | 800 | 1φ12/130mm | 850 | 1φ18/200mm | 1φ12/200mm Use 1φ18/200mm | 1φ25/150mm | 2φ10/200mm

## Slide 85: AutoCAD Details :

## Slide 86
Thank you