## Slide 1: Protection and Simulation of 3ph induction motor in Matlab with Direct and Soft starting methods
By Eng Mohanad Hamad
Eng Majdy Jadallah
Eng Oday Radwan
Supervisor
Dr.Falah Hasan

## Slide 2: Overview
General overview about induction motor and existing problems .
Aims and Objectives.
3ph induction motor structure.
Power flow diagram.
Methods of starting induction motors
principle of operation.
Simulating and starting the 3ph induction motor in Matlab.
Hardware procedure
Results.
Comparison between results
Conclusions.

## Slide 3: General overview about induction motor
Asynchronous machines are considered nowadays the most commonly used electrical machines, which are mainly used as electrical induction motors and sometimes as generators. This is mainly due to the simplicity of composition, low price, light weight, high reliability, easy to command and control performance and not containing parts that could easily breakdown compared with DC machines and synchronous machines.
Starting the induction motor is the most important and dangerous step, where the motor properties play a major role in the evaluation of all electrical motors, and these properties are defined by the following factors:

## Slide 4
Starting torque
Starting current
Transient state
Smoothness of the starting
Simplicity and economics of starting

## Slide 5: Existing problems
In this study, a couple of methods of starting three-phase motors will be discussed and compared through curves of currents, torque, speed, efficiency and power factor. These methods are Direct and Soft starting. The discussion will be based on a Matlab simulation of different loading cases of the induction motor. The induction motor model is created according to a group of standard equations (current, voltage, power, efficiency, speed and values developed and edited in the laboratory.

## Slide 6: Aims and Objectives
. Mainly, this project aims to protect three phase induction motor by decreasing starting current through SCR or IGBT ,therefor we keep it from fault as possible.

## Slide 7: 3ph induction motor structure.
A. Stator
B. Rotor
Rotors are sorted in terms of the type of its coils into two types:
B.1.Squirrel cage Rotor

## Slide 8
B.2.Slip Ring Rotor
C.Air-Gap

## Slide 9: Power flow diagram

## Slide 10
Methods of starting induction motors
Direct-On-Line (DOL) Starters
Soft starter by using SCR or mosfet
Starting Of Squirrel Cage Motors
By using primary resistors
Autotransformer
Star-delta switches

## Slide 11: principle of operation.
In this project,we apply the soft starting by controlling the voltage applied in stator winding through using six back to back SCR through firing angle (alpha).

## Slide 12: Simulating and starting the 3ph induction motor in Matlab.

## Slide 13: Direct starting method
Starting currents curves in the No-load case

## Slide 14
Starting torque curve in the No-load case

## Slide 15
Starting speed curve in the No-load case

## Slide 16: Direct starting curves in the 75% of nominal load case:
Starting currents curves in 75% of the nominal load case

## Slide 17
Starting torque curve in 75% of the nominal load case

## Slide 18
Speed curve in 75% of the nominal

## Slide 19: Direct starting curves in the nominal load case:
Starting currents curves in the nominal load case

## Slide 20
Starting torque curve in the nominal load case

## Slide 21
Speed curve in the nominal load case

## Slide 22: Soft staring method:

## Slide 23
Block diagram for the induction motor model in the Soft starting case

## Slide 24: Soft starting curves in the nominal load case:
Starting currents curves in the Soft starting nominal load case

## Slide 25
Torque curve in the Soft starting nominal load case

## Slide 26
Speed curve in the Soft starting nominal load case

## Slide 27: Soft starting curves in the 75% of nominal load case:
Starting currents curves in the Soft starting 75% nominal load case

## Slide 28
Torque curve in the Soft starting 75% nominal load case

## Slide 29
Speed curve in the Soft starting 75% nominal load case

## Slide 30: Hardware procedure
Circuit digrame:

## Slide 31: -Componenets:
1-Rectifire bridge
2-Two capacitors (400volt,470microfarad)
3-Mosfet(20amp)
4-four resister (100ohm)
5-single phase induction motor (pump)(0.5hp)
6-Aurduino dueo with DAC

## Slide 32: Code for generate sinusoidal wave:
static int sinTable[120]=
{
0x7ff, 0x86a, 0x8d5, 0x93f, 0x9a9, 0xa11, 0xa78, 0xadd, 0xb40, 0xba1,
0xbff, 0xc5a, 0xcb2, 0xd08, 0xd59, 0xda7, 0xdf1, 0xe36, 0xe77, 0xeb4,
0xeec, 0xf1f, 0xf4d, 0xf77, 0xf9a, 0xfb9, 0xfd2, 0xfe5, 0xff3, 0xffc,
0xfff, 0xffc, 0xff3, 0xfe5, 0xfd2, 0xfb9, 0xf9a, 0xf77, 0xf4d, 0xf1f,
0xeec, 0xeb4, 0xe77, 0xe36, 0xdf1, 0xda7, 0xd59, 0xd08, 0xcb2, 0xc5a,
0xbff, 0xba1, 0xb40, 0xadd, 0xa78, 0xa11, 0x9a9, 0x93f, 0x8d5, 0x86a,
0x7ff, 0x794, 0x729, 0x6bf, 0x655, 0x5ed, 0x586, 0x521, 0x4be, 0x45d,
0x3ff, 0x3a4, 0x34c, 0x2f6, 0x2a5, 0x257, 0x20d, 0x1c8, 0x187, 0x14a,
0x112, 0xdf, 0xb1, 0x87, 0x64, 0x45, 0x2c, 0x19, 0xb, 0x2,
0x0, 0x2, 0xb, 0x19, 0x2c, 0x45, 0x64, 0x87, 0xb1, 0xdf,
0x112, 0x14a, 0x187, 0x1c8, 0x20d, 0x257, 0x2a5, 0x2f6, 0x34c, 0x3a4,
0x3ff, 0x45d, 0x4be, 0x521, 0x586, 0x5ed, 0x655, 0x6bf, 0x729, 0x794
};
int i = 0;
int step1k=1; // 1 ms for 1000Hz
long nxt_time;

## Slide 33
void setup()
{
analogWriteResolution(12); // set the analog output resolution to 12 bit (4096 levels)
}
void loop()
{
int AV = analogRead(A0);
step1k=AV;
analogWrite(DAC0, sinTable[i]);
analogWrite(DAC1, sinTable[i+60]);
i++;
if(i == 120)
i = 0;
while (micros()<nxt_time); // Hold the sample value for the sample time
nxt_time=micros()+step1k;
}

## Slide 35: Results.
Direct starting method
No load case:
75% of nominal load case:
Ist (pu) | Tst (pu) | Transient (s)
6.1 | 3.95 | 0.6
Ist (pu) | Tst) pu) | Transient (s)
6.3 | 3.8 | 0.4

## Slide 36: Direct starting method
Nominal load:
Ist (pu) | Tst (pu) | Transient (s)
6 | 4.1 | 1.2

## Slide 37: Soft staring method:
nominal load case:
Soft starting 75% nominal load case
Ist (pu) | Tst (pu) | Transient (s)
3.55 | 3.45 | 1.45
Ist (pu) | Tst (pu) | Transient (s)
2.45 | 2.6 | 1.15

## Slide 38
Comparison between results:
Nominal load | 75% of nominal load case | Case / load
6 | 6.1 | Direct starting (Ist)
3.55 | 2.45 | Soft starting (Ist)

## Slide 40: Conclusions
The previous results showed that the Direct starting method requires a large starting current which causes a disturbance to voltages on the supply lines. In other words, the large starting current produces a severe voltage drop which affects the operation of other equipment. Other than that, it is a quite good method because it provides a large starting torque in a short transient state, without the need of external equipment to help starting the motor. The previous features make the Direct starting method the most common one to start a 3ph induction motor.

## Slide 41
The Soft starting method requires a reasonable starting current to generate a small starting torque at a long transient state, not to mention the need of external thyristor voltage regulator which means extra costs. On the other hand, it provides a smooth startup without any jerks along with a controlled flawless acceleration. These features give the Soft starting method a reliable accuracy with less current needed at the expense of stationarity delay and external equipment charges.

## Slide 42: ة1ة ب 1ة ة1