## Slide 1
DONE BY:
Waleed Qartallo
Adnan Abutahnat
Taha Qanazeh
SUPERVISOR:
Dr. Mohammad Abuabiah
m.abuabiah@najah.edu
Graduation Project 2
AN-Najah National University
Faculty of Engineering & Information Technology
Mechanical and Mechatronics Engineering Department
6/25/2025
Integrating Automation Systems into Pharmaceutical Machinery for Enhanced Efficiency

## Slide 2: Motivation
2/28

## Slide 3: Outline
Introduction
Objective
Methodology
Conclusion
3/28

## Slide 4: Introduction
The project aims to digitalize a traditional mixing machine using PLC and HMI technologies.
This digital transformation improves operational efficiency and aligns with Pharma 4.0 standards.
The system enables real-time monitoring through sensors, reducing human intervention and error.

## Slide 5: Objective
Simplify the operation and monitoring of the mixing machine through automation.
Display all critical process values on an HMI screen for real-time monitoring.
Record and store process data in an Excel sheet for documentation and analysis.
Move towards implementing Pharma 4.0 standards by integrating smart and connected technologies.

## Slide 6: Mixing Machine Overview
The mixing machine is a device used to blend and process various materials into a homogeneous mixture. It is essential in many industries, especially in the pharmaceutical and medical fields, where it is used to mix ingredients with high precision to produce high-quality products such as creams, ointments, and medicinal preparations.

## Slide 7: Methodology
Real Machine Phase
The project is structured into two parallel phases:
Prototype Phase

## Slide 8: Prototype System Specification
Characteristics of Prototype Mixing Machine
Specification | Details
Tank Material | Stainless steel with double-jacket design
Mixing System | Two DC-powered mixers
Temperature Sensor | DHT11 sensor
Speed Sensor | Hall Effect sensor
Level Sensor | Ultrasonic sensor (HC-SR04)
Control Unit | Arduino Mega 2560 board housed in a wooden control box
Motor Driver | H-Bridge Motor Driver (e.g., L298N)
User Controls | On/Off buttons and potentiometer for motor speed adjustment
Monitoring Interface | Real-time data display using App Designer GUI
System Interaction | Live feedback and control via graphical user interface

## Slide 9: Prototype System Overview

## Slide 10: Electrical Components
Arduino Mega 2560
/28

## Slide 11: Electrical Components
DC Gear Motors 12V
/28

## Slide 12: Electrical Components
H-Bridge Motor Driver L298N
Relay module
/28

## Slide 13: Sensors
Hall effect sensor
DHT11 sensor
Ultrasonic sensor
/28

## Slide 14: Graphical User interface
14/28

## Slide 15: Methodology
Real Machine Phase
The project is structured into two parallel phases:
Prototype Phase

## Slide 16: Real System Specification
Characteristics of Real Mixing Machine
Specification | Details
Machine Type | Industrial Mixing Machine
Control System | PLC-based with HMI interface
Material Capacity | e.g., 1000 Liters
Motor Type | AC Motor
Speed Monitoring | real-time display on HMI
Temperature Monitoring | RTD pt100 sensors with alarm system
Data Logging | Real-time logging to Excel sheet via PC
Main Structure Material | Stainless Steel (Pharma Grade)
Mixing Mechanism | e.g., Paddle / Homogenizer / Anchor
Automation Level | Semi or Fully Automated
Power Supply | e.g., 220V / 380V, 3 Phase
Safety Features | Emergency stop, Overheat alarm

## Slide 17: Electrical Components
Three-phase Motor
Several types of motors will be used in this project, including:
Anchor motor.
Blade paddle motor.
Homogenizer motor.

## Slide 18: Electrical Components
Variable Frequency Driver (VFD)
Programmable Logic Controller (PLC)

## Slide 19: Sensors
19/28
Pressure transmitter
RTD sensor (pt100)

## Slide 20: PLC Modules
20/28
CB 1241
Analoge input module

## Slide 21: Integrated PLC System

## Slide 22: Human-Machine Interface
22/28

## Slide 23: Data storage
Machine status
Recipe information

## Slide 24: Conclusion
In this project, we focused on developing a monitoring system for an existing pharmaceutical mixing machine.
I designed the mechanical model using SOLIDWORKS, and we selected the sensors, motors, and the appropriate PLC unit for real-time data reading.
We created a user-friendly interface that enables the operator to monitor key variables such as temperature, speed, and liquid level.
We built a complete prototype that integrates the mechanical design, electrical circuits, and programming, and it demonstrated efficiency during practical tests.

## Slide 25: Enhanced Efficiency
Old system | New system
Difficulty taking readings | Readings are displayed in real-time on the HMI screen
Difficulty storing data | Data is automatically logged and saved in an Excel sheet
Difficulty handling the machine | Easier and safer operation through an automated control system
Not knowing if the engines are overheating or not | Real-time temperature monitoring with alerts for overheating

## Slide 26: Bill of Martial for real machine
# | Piece type | Comment | QTY | price (NIS)
1 | CPU | S7-1200 CPU 1215C | 1 | 2740.31
2 | Analog Input | SM 1231 AI – 8x13bit |  | 1750.29
3 | Power supply | SITOP PSU100C – 24V / 2.5A | 1 | 434.42
4 | CB 1241 (RS485) | CB 1241 – Communication board | 1 | 889.28
5 | Pressure transmitter | Autonics TPS20 Series, 0–0.5kg/cm² | 1 | 603.45
6 | RTD pt100 | - | 1 | 222
 |  | Total Price |  | 6639.75

## Slide 27: Bill of Martial for Prototype machine
# | Piece type | QTY | Price (NIS) | # |  | Piece type | QTY | Price (NIS)
1 | DC Motor with Gear | 2 | 130 | 10 |  | H-Bridge Motor Driver L298N | 1 | 25
2 | Arduino Mega 2560 |  | 90 | 11 |  | relay module | 1 | 15
3 | DHT11 sensor | 2 | 25 | 12 |  | Variable resistors | 2 | 3
4 | Prototype Build | 1 | 850 | 13 |  | Magnetic | 2 | 1
5 | Ultrasonic Sensor | 1 | 10 | 14 | Fabric |  | 1 | 48
6 | Hall effect sensor | 2 | 10 | Total Price |  |  | 1457 NIS | 
7 | Push Button(On/Off) | 2 | 5.5 |  |  |  |  | 
8 | Wires | 1 | 30 |  |  |  |  | 
9 | Power Supply | 1 | 40 |  |  |  |  | 

## Slide 28: Thanks !
Any questions ?

## Slide 29: Backup Slides

## Slide 30: Mechanical Design
The mechanical design consists of :
Tank Body: A 1250mm diameter, 1500mm high, and 5mm thick will be used in this project.

## Slide 31: Mechanical Design
Anchor Motor
Anchor
Blade Paddles
Scrapers
Emulsifying head
Shear Homogenizer
Blade Paddles Motor

## Slide 32: Mechanical Design
Tank access platform: This is used to facilitate access to the engines above for maintenance work or to access the maintenance hole.
Screw and bolt: Are used to securely fasten the motors to the tank body in the mixing machine, ensuring a strong and safe attachment of both the motors and the body.
The screws and bolts are tightened using a torque wrench, with a gasket added to prevent leaks.

## Slide 33: Electrical Design
Three-phase Motor
Several types of motors will be used in this project, including:
Gear motor flender (HP5.5 –KW4-VOLT 230/400 -Hz50-4 POLI), called anchor motor
Gear motor flender (HP3-KW2,2 -VOLT 230/400 -Hz50-4 POLI), called blade paddle motor
Electronic motor G160 (KW11/9 -VOLT 230/400 -Hz50-4POLI),
called homogenizer motor

## Slide 34: Recipe information

## Slide 35: Control and monitoring system

## Slide 36: Real-time data graph

## Slide 37: Warning

## Slide 38: Industrial Revolutions