## Slide 1: Transportation Impacts of the Industrial - Crafting Area in Nablus
Prepared by
Najeeb Masri
Mohammad Hamami
Montaser Shaheen
Under the Supervision of
Dr. Khaled Al-Sahili
An-Najah National University
Engineering Collage
Civil Engineering Department

## Slide 2: Presentation Outline
Introduction
Methodology
Data Collection and Analysis
Evaluation and Suggested Actios
Conclusion & Recommendations

## Slide 3: Introduction

## Slide 4: Project Description:
Location:

## Slide 5: Project Description:
Study Area:
Sulaiman Al Nabulsi Street
Al Zoyoot Street
Al Hesbeh Street
Jamal Abdul-Nasser Street
Links:
Intersections:

## Slide 6: Objectives
The main objective: Determine the traffic impact of Industrial Crafting Area Project on the surrounded road network.
Particular Objectives:
Evaluate current traffic conditions.
Estimate future traffic developed by industrial crafting area when it’s completely built.
Evaluation and redesign (geometric and traffic) of the road network intersections and links in the study area.

## Slide 7: Methodology

## Slide 8: Methodology
Collecting Data

## Slide 9: Methodology
Field Inventory
(#1) Al Ghawi Intersection
(#2) Al Hesbeh Roundabout
(#3) Al Maslakh Intersection
(#4) Balata – Al Quds Intersection
(#5) Beit Furik Intersection
(#6) Salem Intersection

## Slide 10: Methodology
Traffic Volume studies:
  Volume Counts
  Peak Hour, Peak Hour Volume (PHV), and Peak Hour Factor (PHF).

## Slide 11: Methodology
Traffic Impact Study (TIS)
  Trip Generation
  Trip Distribution
  Modal Split
  Route Assignment

## Slide 12: Methodology
Level of service (LOS) :
  Existing Traffic Conditions
  Future (Generated) Traffic Conditions - Without the existence of the project - With the existence of the project

## Slide 13: Methodology
Road Network Evaluation
  Expected Problems
  Solutions and Suggested Actions

## Slide 14: Data Collection and Analysis

## Slide 15: Data Collection and Analysis
Existing traffic
  Intersections
Intersection | Status | Peak Hour | PHV | PHF
(#1) Al Ghawi Intersection | Signalized | 2:00 ~ 3:00 PM | 1679 | 0.91
(#2) Al Hesbeh Roundabout | Roundabout | 2:45 ~ 3:45 PM | 723 | 0.96
(#3) Al Maslakh Intersection | Unsignalized | 3:00 ~ 4:00 PM | 831 | 0.94
(#4) Balata – Al Quds Intersection | Signalized | 7:00 ~ 8:00 AM | 2728 | 0.75
(#5) Beit Furik Intersection | Unsignalized | 2:00 ~ 3:00 PM | 707 | 0.90
(#6) Salem Intersection | Unsignalized | 2:45 ~ 3:45 PM | 524 | 0.93

## Slide 16: Data Collection and Analysis
Existing traffic
  Links
Link Name | Status | Peak Hour | Direction | PHV | PHF
Sulaiman Al-Nabulsi | Two-Lane | 2:00 ~ 3:00 PM | Dir. 1 ↑ | 159 | 0.92
 |  |  | Dir. 2 ↓ | 179 | 0.92
Al-Zoyoot | Multi- Lane | 3:00 ~ 4:00 PM | Dir. 1 ← | 314 | 0.88
 |  |  | Dir. 2 → | 356 | 0.88
Al-Hesbeh | Multi- Lane | 2:00 ~ 3:00 PM | Dir. 1 ← | 412 | 0.90
 |  |  | Dir. 2 → | 745 | 0.90
Jamal Abdul Nasser | Multi- Lane | 7:00 ~ 8:00 AM | Dir. 1 ⤶ | 1275 | 0.70
 |  |  | Dir. 2 ⤴ | 753 | 0.80

## Slide 17: Traffic Analysis
Analysis of the existing traffic
  Intersections
Intersection | Status |  |  | Level of Service |  |  | 
 |  |  |  | EB | WB | NB | SB
(#1) Al Ghawi Intersection | Signalized | Lane group |  | C~E | D | C~D | D
(#2) Al Hesbeh Roundabout | Roundabout | V/C | Up B | .37 | .17 | .16 | .11
 |  |  | L B | .44 | .2 | .19 | .14
(#3) Al Maslakh Intersection | Unsignalized | Movement |  | A | A | C~B | C~B
(#4) Balata- Al Quds Intersection | Signalized | Lane Group |  | C~F | D | NA | C
(#5) Beit Furik Intersection | Unsignalized | Movement |  | A | A | C~B | B
(#6) Salem Intersection | Unsignalized | Movement |  | A~C | A~C | A | A

## Slide 18: Traffic Analysis
Analysis of the existing traffic
  Links
Link Name | Status | Direction | LOS
Sulaiman Al-Nabulsi | Two-Lane | Two-Way | B
 |  | Directional | B
Al-Zoyoot | Multi- Lane | Dir. 1 ← | A
 |  | Dir. 2 → | A
Al-Hesbeh | Multi- Lane | Dir. 1 ← | A
 |  | Dir. 2 → | A
Jamal Abdul Nasser | Multi- Lane | Dir. 1 ⤶ | B
 |  | Dir. 2 ⤴ | A

## Slide 19: Traffic Analysis
A value of 3.5% was considered to be used as a traffic growth rate based on previous counts.
Future traffic volume due to natural growth = existing volume × (1 + i)n
Future Traffic Studies
Natural Growth

## Slide 20: Traffic Analysis
Future Traffic Studies
Generated traffic due to the project
Vehicle Trips |  | Phase I Gross Area = 100 Donums | Phase II Gross Area = 250 Donums
AM Peak Hour | Using Avg. Rate | 544 | 1410
 | Using Fitted Curve Eq. | 603 | 1613
PM Peak Hour | Using Avg. Rate | 581 | 1508
 | Using Fitted Curve Eq. | 703 | 1922
Generated Traffic Volumes due to Industrial Crafting Area Project

## Slide 21: Traffic Analysis
Future Traffic Studies
Trip Distribution

## Slide 22: Traffic Analysis
Analysis of the future traffic
Future traffic without the existence of the project (After 5 years).
Future traffic with the existence of the project (Phase I).
Future traffic with the existence of the project (Phase II).

## Slide 23: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#1) Al Ghawi Intersection (Signalized)
  Main Problem : Through movement in the EB direction
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | C~F | D | D~E | D
Phase I | C~F | D | D~E | D
Phase II | D~F | D | D~E | D

## Slide 24: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#1) Al Ghawi Intersection (Signalized)
  Solution : Adjustment of signal timing design
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | D | C~E | D~E | E
Phase I | D | C~E | D~E | E
Phase II | D~E | D~E | D~E | E
  LOS Results after improvement

## Slide 25: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#2) Al Hesbeh Roundabout
Future Traffic | v/c Ratio |  |  |  | 
 |  | EB | WB | NB | SB
Without the existence of the project | Up B | 0.44 | 0.21 | 0.20 | 0.14
 | L B | 0.53 | 0.25 | 0.25 | 0.17
Phase I | Up B | 0.58 | 0.23 | 0.23 | 0.15
 | L B | 0.69 | 0.28 | 0.28 | 0.18
Phase II | Up B | 0.81 | 0.26 | 0.29 | 0.15
 | L B | 0.97 | 0.32 | 0.37 | 0.19

## Slide 26: Evaluations & Suggested Actions
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | A | A | B~C | B~C
Phase I | A | A | B~C | B~C
Phase II | A | B | C~E | B~E
Analysis of the future traffic (Intersections) :
  (#3) Al Maslakh Intersection

## Slide 27: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#4) Balata – Al Quds Intersection (Signalized)
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | D~F | F | NA | C
Phase I | D~F | F | NA | C
Phase II | D~F | F | NA | C

## Slide 28: Evaluations & Suggested Actions
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | A | A | B~D | B~C
Phase I | A | A | C~F | B~D
Phase II | A | B | F | D~F
Analysis of the future traffic (Intersections) :
  (#5) Beit Furik Intersection (Unsignalized)
  Main Problem : (At the beginning of phase I of the project) NB direction and left-turn movement in the EB direction.

## Slide 29: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#5) Beit Furik Intersection (Unsignalized)
  Solution : Design a traffic signal for the intersection with the start of phase I
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Phase I | C | C | D | D
Phase II | E | C | D | D
  LOS Results after improvement

## Slide 30: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#5) Beit Furik Intersection (Unsignalized)

## Slide 31: Evaluations & Suggested Actions
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Without the existence of the project | A~C | A~C | A | A
Phase I | A~F | A~D | A | A
Phase II | A~F | A~F | A | A
Analysis of the future traffic (Intersections) :
  (#6) Salem Intersection (Unsignalized)
  Main Problem : (At the beginning of phase I of the project) Left-turn movement in the EB and WB directions.

## Slide 32: Evaluations & Suggested Actions
Future Traffic | Level of Service |  |  | 
 | EB | WB | NB | SB
Phase I | C~E | C~E | A | A
Phase II (Signalized) | C~E | C | C | D
Analysis of the future traffic (Intersections) :
  (#6) Salem Intersection (Unsignalized)
  Solution : - Separating the left-turn movement in the EB and WB directions. - Design a traffic signal with the start of phase II.
  LOS Results after improvement

## Slide 33: Evaluations & Suggested Actions
Analysis of the future traffic (Intersections) :
  (#6) Salem Intersection (Unsignalized)

## Slide 34: Evaluations & Suggested Actions
Link Name | Status | Direction | LOS |  | 
 |  |  | Without the existence of the project | Phase I | Phase II
Sulaiman Al-Nabulsi | Two-Lane | Two-Way | B | B | C
 |  | Directional | C | C | D
Al-Zoyoot | Multi- Lane | Dir. 1 ← | A | A | A
 |  | Dir. 2 → | A | A | A
Al-Hesbeh | Multi- Lane | Dir. 1 ← | A | A | A
 |  | Dir. 2 → | A | A | A
Jamal Abdul Nasser | Multi- Lane | Dir. 1 ⤶ | C | C | C
 |  | Dir. 2 ⤴ | A | A | B
Analysis of the future traffic (Links) :

## Slide 35: Conclusion and Recommendations

## Slide 36: Conclusion & Recommendations
The importance of transportation impact studies.
Periodic traffic volume counting at the major intersections and links  Accurate value for the growth rate.
Extensive studies on local trip generation rates  Estimate the generated traffic with values very close to the reality
Consider more expensive, large-scale studies and actions in the future.