## Slide 1
بسم الله الرحمن الرحيم
Graduation Project II
Supervisor: Dr. Riyad Awad.
Prepared by: Ahmad Abdel All Omar Barham Zafer Nasrallah
An-Najah National University
Faculty of Engineering
جامعة النجاح الوطنية
كلية الهندسة
Civil Engineering Department
3D-DYNAMIC ANALYSIS AND DESIGN OF ODEH’S HOTEL IN NABLUS

## Slide 2
Outline:
Introduction.
Preliminary dimensions and 3D model.
Dynamic Analysis
Dynamic design.

## Slide 3
Challenges and problems :
 The architect didn’t take any consideration for structural purposes.
 The columns was so scattered so we have a panel of 10 * 7 m,and so a long spans
 The unsymmetrical shape of the building causes an extra load from lateral forces and so the natural period is too high .

## Slide 4
Introduction
Hotel is located in Nablus city.
The Hotel is composed of two Blocks, A and B.
Both of block A,B have a 7 stories
The total area of structure is 5400 m2.

## Slide 5
1) Introduction:
Project description:
Basement
Notes: In this project we’ll design a hotel consist of 7 stories. The total area of the hotel is approximately . The basement contain an indoor pool and some facilities for the hotel.
In this project we’ll design a hotel consist of 7 stories. The total area of the hotel is approximately 5400 𝑚^2. The basement contain an indoor pool and some facilities for the hotel.

## Slide 6
1) Introduction:
Project description:
Ground Floor
Notes: The ground floor contains the reception, the management offices and cafeteria. In this floor there is a mezzanine.

## Slide 7
1) Introduction:
Project description:
Mezzanine

## Slide 8
1) Introduction:
Project description:
First Floor
Notes: A restaurant is located in the first floor.

## Slide 9
1) Introduction:
Project description:
2nd , 3rd and 4th floors
Notes: rooms for hotel guests

## Slide 10
1) Introduction:
Project description:
Story | Elevation | Area
Basement | -4.75 | 805.24
Ground | 0.00 | 805.24
Mezzanine | 3.25 | 482.57
First | 6.00 | 805.24
Second | 9.25 | 805.24
Third | 12.5 | 805.24
Forth | 15.75 | 805.24
Story |  | 
Basement | -4.75 | 805.24
Ground | 0.00 | 805.24
Mezzanine | 3.25 | 482.57
First | 6.00 | 805.24
Second | 9.25 | 805.24
Third | 12.5 | 805.24
Forth | 15.75 | 805.24

## Slide 11
1) Introduction:
Geotechnical information:
Soil layers are close to be soft stone so the design bearing capacity is
Codes and Standards:
IBC 2012
ACI 318M-14
ASCE 2010

## Slide 12
1) Introduction:
Materials:
Rebar Steel: - Yielding strength of used steel (fy) = 420MPa.
- Modulus of elasticity of used steel (Es) = 200GPa.
Concrete: strength: 30 MPa
Type: B375

## Slide 13
1) Introduction:
Loads:
1- Super-imposed dead load:
Zone | Material | Unit Weigh KN/m³ | Thickness cm | Wight (KN/m²) (unit weigh * thickness in m)
A | Ceramic | 0.12 | 1.0 | 1.2 *10‾³
B | Mortar | 23 | 3.0 | 0.69
C | Filling Material | 17 | 7.0 | 1.190
D | Slab Thickness | 25 | - | -
E | Plaster | 23 | 1.5 | 0.345
a. Static load

## Slide 14
1) Introduction:
Loads:
2- Live Load : In Basement, Ground, First floors In 2nd , 3rd and 4th floors
a. Static load

## Slide 15
1) Introduction:
Loads:
b. Lateral loads (seismic)
The hotel is located in Nablus area which is classified zone 2B, according to Palestine seismic zone (z=0.2).

## Slide 16
1) Introduction:
Programs:
1- ETABS 2015
2- SAFE 2014
3- AutoCAD

## Slide 17
Preliminary dimensions and 3D model

## Slide 18
2) Preliminary dimensions and 3D model:
Introduction to structural system.
We divided the project into 2 blocks

## Slide 19
2) Preliminary design and 3D model:
Introduction to structural system.
One-way Voided Slab:

## Slide 20
2) Preliminary design and 3D model:
Block A

## Slide 21
2) Preliminary design and 3D model:
Block B

## Slide 22
2) Preliminary dimensions and 3D model:
Preliminary dimensions:
Column dimensions |  | 
Name: | Cross section: | 
C1 | 60x30 | 
C2 | 80x30 | 
C3 | 40x40 | 
CB | 80x40 | 
Beam dimensions |  | 
B1 | 30x70 | Drop
B2 | 50x30 | Hidden
B3 | 60x30 | Hidden
B4 | 30x30 | Hidden
B5 | 30x90 | Drop

## Slide 23
2) Preliminary dimensions and 3D model:
Materials and modifiers:

## Slide 24
2) Preliminary dimensions and 3D model:
Materials and modifiers:

## Slide 25
2) Preliminary dimensions and 3D model:
Materials and modifiers:

## Slide 26
2) Preliminary dimensions and 3D model:
Materials and modifiers:
Slab modifiers in block A

## Slide 27
2) Preliminary dimensions and 3D model:
Checks
As shown the structure move as a rigid unit (moving together)
1- Checks for Compatibility:

## Slide 28
2) Preliminary dimensions and 3D model:
Checks
2- Equilibrium check (Base reactions):
All less than 5%, OK
Total load: |  |  | 
By hand |  | By model | Error %
Dead | 23181.15 | 22687.28 | 2.18
Live | 7748 | 7553.819 | 2.58
SD | 8227.345 | 8001.932 | 2.82
Wall | 10013.902 | 9614.58 | 4.15

## Slide 29
2) Preliminary dimensions and 3D model:
Checks
3- Checks moment stress-strain relationships:
In our calculations we take slab strip and the interior beam in block A

## Slide 30
2) Preliminary dimensions and 3D model:
Checks
3- Checks moment stress-strain relationships:
And we did the same for a beam
From 1-D analysis:

## Slide 31
2) Preliminary dimensions and 3D model:
Checks
4- Checks for deflection:
We have case 4 that is: L/240

## Slide 32
2) Preliminary dimensions and 3D model:
Checks
4- Checks for deflection:
(we assumed the ∆ sustained live load=)
The value from ACI-code
32.5

## Slide 33
2) Preliminary dimensions and 3D model:
Checks
5- Checks the period:
The fundamental period T=0.472
To check this value, we used Rayleigh analytical
method:

## Slide 34
2) Preliminary dimensions and 3D model:
Checks
5- Checks the period:
Mass calculation:
Element/Story | S1 | S2 | S3 | S4 | S5 | S6 | S7
Slab | 1517.87 | 1517.87 | 1517.87 | 1517.87 | 1517.87 | 1517.87 | 1517.87
Masonry Wall | 1450 | 1450 | 1450 | 1450 | 1450 | 1450 | 1450
SID | 1157.8 | 1157.8 | 1157.8 | 1157.8 | 1157.8 | 1157.8 | 1157.8
Stairs | 179.5 | 179.5 | 179.5 | 179.5 | 179.5 | 179.5 | 89.75
Beams | 696.85 | 696.85 | 696.85 | 696.85 | 696.85 | 696.85 | 696.85
Columns | 257.5 | 186 | 164.625 | 157.625 | 157.625 | 157.625 | 78.8125
Walls | 864.75 | 532 | 532 | 532 | 532 | 532 | 266
Mass (kN) | 6124.27 | 5720.02 | 5698.65 | 5691.65 | 5691.65 | 5691.65 | 5257.08
Mass (ton) | 624.29 | 583.08 | 580.90 | 580.19 | 580.19 | 580.19 | 535.89

## Slide 35
2) Preliminary dimensions and 3D model:
Checks
5- Checks the period:
To find the period in Y:
Drift values due to (1 KN/m2 – in y-direction)
 | delta1 | delta2 | delta3 | delta average (mm)
story 1 | 0.3 | 0.3 | 0.2 | 0.27
story 2 | 0.8 | 0.8 | 0.8 | 0.80
story 3 | 1.4 | 1.4 | 1.4 | 1.40
story 4 | 2.1 | 2.1 | 2.2 | 2.13
story 5 | 2.8 | 2.9 | 3.1 | 2.93
story 6 | 3.6 | 3.7 | 3.9 | 3.73
story 7 | 4.3 | 4.5 | 4.7 | 4.50

## Slide 36
2) Preliminary dimensions and 3D model:
Checks
5- Checks the period:
Period in Y:
 | mass | force | delta | Mass*(delta^2) | force*delta
S1 | 624.29 | 331 | 0.0002667 | 4.44E-05 | 0.088267
S2 | 583.08 | 331 | 0.0008 | 0.000373 | 0.2648
S3 | 580.90 | 331 | 0.0014 | 0.001139 | 0.4634
S4 | 580.19 | 331 | 0.0021333 | 0.002641 | 0.706133
S5 | 580.19 | 331 | 0.0029333 | 0.004992 | 0.970933
S6 | 580.19 | 331 | 0.0037333 | 0.008087 | 1.235733
S7 | 535.89 | 331 | 0.0045 | 0.010852 | 1.4895
Total |  |  |  | 0.028127 | 5.218767

## Slide 37
2) Preliminary dimensions and 3D model:
Checks
5- Checks the period:
Period in Y:

## Slide 38
2) Preliminary dimensions and 3D model:
Checks
6- Check if torsion mode exist in 1st two modes:
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 39
Dynamic Analysis

## Slide 40
3) Dynamic Analysis:
Seismic Parameters
1- Site classifications
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 41
3) Dynamic Analysis:
Seismic Parameters
2- Seismic Zone factor and design seismic spectral acceleration (SD1, SDs):
The hotel located in Nablus city which is in Zone 2B, and has Z = 0.2 g
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 42
3) Dynamic Analysis:
Seismic Parameters
2- Seismic Zone factor and design seismic spectral acceleration (SD1, SDs):
Determine the maximum considered earthquake spectral response accelerations adjusted for site class effects, SMS at short period and SM1 at long period according to IBC 1613.3.3:
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 43
3) Dynamic Analysis:
Seismic Parameters
2- Seismic Zone factor and design seismic spectral acceleration (SD1, SDs):
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 44
3) Dynamic Analysis:
Seismic Parameters
2- Seismic Zone factor and design seismic spectral acceleration (SD1, SDs):
Determine the 5% damped design spectral response accelerations SDS at short period and SD1 at long period in accordance with IBC 1613.3.4.
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 45
3) Dynamic Analysis:
Seismic Parameters
2- Seismic Zone factor and design seismic spectral acceleration (SD1, SDs):
Because of the Z factor is taken from the map (which is probability of exceedance = 10 % and the IBC code is probability of exceedance = 2 %) so we multiply the values of SDs and SD1 by (3/2). NOTE: we want to design the structure as 10 % of exceedance at 50 year exposure time with return design period of 475 years.
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 46
3) Dynamic Analysis:
Seismic Parameters
3- Determination of seismic Design category and importance factor (Ie):
The IBC code classifies the structures according to the nature of occupancy, and the hotel is defined as risk category 2, because it is a normal building.
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 47
3) Dynamic Analysis:
Seismic Parameters
3- Determination of seismic Design category and importance factor (Ie):
Then using ASCE 7-10 to determine the importance factor of the Building from (table 1.5-2: in ASCE)
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 48
3) Dynamic Analysis:
Seismic Parameters
3- Determination of seismic Design category and importance factor (Ie):
So the seismic design category is D
Since all other structures shall be assigned to a seismic design category based on their risk category and the design spectral response acceleration parameters, SDS and SD1. Using ASCE 7-10:
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 49
3) Dynamic Analysis:
Determination of building frame system and Response modification factor (R):
There are 3 types of building frame system according to resistance the gravity and lateral loads:
1- Bearing wall system
2- Building frame system
3- The moment resisting frame system
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 50
3) Dynamic Analysis:
Determination of building frame system and Response modification factor (R):
Walls take 97.75% of lateral loads in y-directions
Walls take 98% of lateral loads in x-directions
From this results and since the building is located in moderate seismic area then the system is building frame system with intermediate reinforcement.
Notes: For modal 1 and 2, both modes are transition, no torsion

## Slide 51
3) Dynamic Analysis:
Determination of building frame system and Response modification factor (R):
So we will use the Ordinary reinforced concrete shear walls system with R = 5, Cd = 4.5 and Ω = 2.5

## Slide 52
3) Dynamic Analysis:
Determinations of Approximate Fundamental Period (Ta):
According to ASCE 7-10 code the analytical periods shall be less than approximate fundamental method (Ta):

## Slide 53
3) Dynamic Analysis:
Determinations of Approximate Fundamental Period (Ta):
Also the code suggests maximizing this value by multiply it by Cu coefficient of upper limits
Notes: The value from ETABS = 0.482 sec which is less than the approximate fundamental Period (Ta)

## Slide 54
3) Dynamic Analysis:
Determination of Seismic Base reactions:
Equivalent static methods
Dynamic methods: Linear modal response spectrum analysis
Notes: The structural analysis shall consist of one of the types permitted in ASCE 7-10 Table 12.6-1, based on the structure’s seismic design category, structural system, dynamic properties and regularity. The analysis procedure selected shall be completed in accordance with the requirements of the corresponding section referenced in (Table 12.6-1 in ASCE).

## Slide 55
3) Dynamic Analysis:
Determination of Seismic Base reactions:
1- Equivalent Static Method
According to ASCE 7-10,
Notes: First we calculated the base reactions manually and from the ETABS models to compare between both of the results.

## Slide 56
3) Dynamic Analysis:
Determination of Seismic Base reactions:
1- Equivalent Static Method
W = 41057.28 kN
Calculating the Seismic Response Coefficient :

## Slide 57
3) Dynamic Analysis:
Determination of Seismic Base reactions:
1- Equivalent Static Method
We assigned equivalent static load in ETABS

## Slide 58
3) Dynamic Analysis:
Determination of Seismic Base reactions:
1- Equivalent Static Method
The following results was obtained:

## Slide 59
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis
Notes: We used ETABS model to calculate the seismic forces from Response spectrum in two directions (X-direction, Y-direction).

## Slide 60
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis
Then, the acceleration of main direction should be
multiplied by a
And the other direction should be multiplied by:
x-directions
Notes: Because the earthquake loads don’t come from one directions, so the structure shall be designed to resist any seismic forces in each direction, then to simulate the reality we add 30% of seismic load in perpendicular direction in addition of the main directions.

## Slide 61
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis

## Slide 62
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis
the response spectrum base shear is less than static base shear so we have to make the response spectrum is the dominant method to make a design by it, to achieve this the ASCE7-10 code scale the forces by multiply the scale factor by
So the scale factor for response in X-direction is:
The scale factor for response in Y-direction is:

## Slide 63
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis
So the base reaction after modification:

## Slide 64
3) Dynamic Analysis:
Determination of Seismic Base reactions:
2- Modal response spectrum analysis
The modal mass participation ratio(MMPR):

## Slide 65
3) Dynamic Analysis:
Load combinations:
Ultimate load combinations | Service load combinations
1.4D | D+L
1.2D+1.6L | 1D+0.75L+0.7E
1.2D+1E +1L | 0.6D+0.7 E
0.9D+1E | 1D+0.7E
Eh including Eh-x and Eh-y
= 1.3

## Slide 66
3) Dynamic Analysis:
Load combinations:

## Slide 67
3) Dynamic Analysis:
Structural Configuration:
1- Plane Configuration
Displacement from mode 3
Notes: The code is trying to make the limits of torsional regularity by dividing it in two cases:
Torsional irregularity.
Extreme torsional irregularity

## Slide 68
3) Dynamic Analysis:
Structural Configuration:
1- Plane Configuration
So there is no torsional irregularity nor extreme torsional irregularity.
Notes: Note that: We didn’t re-do for the rest corners because the plan is nearly square shape after we divided it in two Blocks, in addition the diaphragm is similar in all stories and it is continuous and the opening is less than 50 % of the total area.

## Slide 69
3) Dynamic Analysis:
Structural Configuration:
2- Vertical configuration
The drift values from the ETABS are taken from story 7 and 6 from response in Y-directions:
So there is no story drift nor extreme story drift
Soft story checks
Notes: the soft story is one of the important issues in seismic design effect, we have to avoid it so let’s check it in-out structure. 1- Soft Story. 2- Extreme soft story.

## Slide 70
3) Dynamic Analysis:
Story Drifts Checks and Design of seismic Joint:
Notes: The maximum story drift in a building shall not exceed the allowable story drift as obtained from table 12.12-1 in ASCE 7-10.
The maximum story drift in a building shall not exceed the allowable story drift ∆𝑎 as obtained from table 12.12-1 in ASCE 7-10.

## Slide 71
3) Dynamic Analysis:
Story Drifts Checks and Design of seismic Joint:
Risk category: ΙΙ Structure type: Masonry cantilever shear wall
Allowable story drift
But we have seismic design category D. So, according to 12.12.1.1 in ASCE 7-10, the story drift shall not exceed:

## Slide 72
3) Dynamic Analysis:
Story Drifts Checks and Design of seismic Joint:
Notes: Between 4th and 5th : 2.5mm Y-direction

## Slide 73
3) Dynamic Analysis:
Story Drifts Checks and Design of seismic Joint:
12.12.3 in ASCE 7-10: allow for the maximum inelastic response displacement (𝛿𝑀).
The maximum inelastic story drift (11.25mm) is less than the allowed story drift (25mm)
Notes: 12.12.3 in ASCE 7-10, Separation shall allow for the maximum inelastic response displacement ().
12.12.3 in ASCE 7-10, Separation shall allow for the maximum inelastic response displacement (𝛿_𝑀).

## Slide 74
3) Dynamic Analysis:
Story Drifts Checks and Design of seismic Joint:
The seismic joint:
According to ASCE seismic separation should be SRSS of inelastic displacements by this formula:
so take the seismic joint distance equal 3 cm

## Slide 75
Dynamic design

## Slide 76
Design criteria
Strength
Serviceability and Stability
Cost effective

## Slide 77
3) 3-D analysis and Static design:
Check slab for shear:
From V23 the

## Slide 78
4) Dynamic design
Design of slab for flexure:
The maximum moment is

## Slide 79
4) Dynamic design
Design of slab:

## Slide 80
4) Dynamic design
Design of beams:
Notes: Beam on grid line 2 as example

## Slide 81
4) Dynamic design
Design of beams:
Notes: +As = 1/3 –As shear reinf. S1 = 1.5 (2H) each 9 cm shear reinf S2 = middle each 30 cm

## Slide 82
4) Dynamic design
Design of columns:
Notes: Column A3 as example

## Slide 83
4) Dynamic design
Design of columns:
Notes: At both end … spacing 12 cm for L0= 45 cm
First one not more than 6 cm in the middle …. Spacing 25 cm
Lab splice middle column

## Slide 84
4) Dynamic design
Design of shear wall:
Notes: Sw 5 as example
Sw 5 as example 𝐿𝑤=1400 𝑚𝑚, 𝑇ℎ𝑖𝑐𝑘𝑛𝑒𝑠𝑠=300 𝑚𝑚

## Slide 85
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN
So we don’t need any reinforcement in the 2-direction (weak direction).

## Slide 86
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN

## Slide 87
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN
Notes: biaxial columns and using the reciprocal method for design.
biaxial columns and using the reciprocal method for design. 𝜌𝑙=0.0025

## Slide 88
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN
About Y axis(2-direction):
Then from curve of moment-axial interaction diagram we determine:
So, the
Notes: biaxial columns and using the reciprocal method for design.
biaxial columns and using the reciprocal method for design. 𝜌𝑙=0.0025

## Slide 89
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN
About X axis(3-direction):
Then from curve of moment-axial interaction diagram we determine:
So, the
Pure axial from ACI-code:
Notes: biaxial columns and using the reciprocal method for design.
biaxial columns and using the reciprocal method for design. 𝜌𝑙=0.0025

## Slide 90
4) Dynamic design
Design of shear wall:
Pu | Mu2 | Mu3 | Vu2 | Vu3
3405 kN | 65 KN.m | 160 KN.m | 38.14 KN | 198 KN
So from equation of reciprocal method:
So the assumption is true which is
Notes: biaxial columns and using the reciprocal method for design.
biaxial columns and using the reciprocal method for design. 𝜌𝑙=0.0025

## Slide 91
4) Dynamic design
Design of shear wall:
Check for :
Since,
So,
Notes: Using the section designer on ETABS to draw a bending moment-axial interaction diagram:

## Slide 92
4) Dynamic design
Design of shear wall:

## Slide 93
4) Dynamic design
Design of stairs:
Thickness: 20 cm

## Slide 94
4) Dynamic design
Design of stairs:
1) Loads
The own weight of stairs
L
S

## Slide 95
4) Dynamic design
Design of stairs:
2) Deflection
Long term max. deflection = 7.3 mm
Deflection limitation: “ACI”

## Slide 96
4) Dynamic design
Design of stairs:
3) Shear
, there is no need for shear reinforcement.

## Slide 97
4) Dynamic design
Design of stairs:
4) flexure
longitudinal steel
In flight:
For M22 (positive) = 8.5 KN.m, bottom steel
(4 12 /1m)
For M22 (negative) = 25 KN.m, top steel
Use (4 12 /1m)
In landing:
M22 in the Landing= 25 kN.m and it is negative moment (top steel)
Use (4 12 /1m)

## Slide 98
4) Dynamic design
Design of stairs:

## Slide 99
4) Dynamic design
Design of footings:
To determine the type of footing:
Total load from the building:
Block: | P service (from gravity) | P service (from seismic combination)
Block A | 47857 kN | 47875 kN
Block B | 67089 kN | 68951 kN
Area of footing from gravity loads:
Area of footing from seismic loads:
Notes: So, we used the larger area which come from gravity service loads.
,
It’s preferred to use MAT foundation:
We used CSI SAFE (using finite elements) to analysis and design the MAT footing that consider the footing flexible.
We separated the footing for each block. Below footing A design:
So, we used the larger area which come from gravity service loads.
𝑇ℎ𝑒 𝑟𝑎𝑡𝑖𝑜 𝑜𝑓 𝑎𝑟𝑒𝑎= (𝐴𝑟𝑒𝑎 𝑜𝑓 𝑓𝑜𝑜𝑡𝑖𝑛𝑔)/(𝑎𝑟𝑒𝑎 𝑜𝑓 𝑏𝑢𝑖𝑙𝑑𝑖𝑛𝑔)=460/835=55%,
It’s preferred to use MAT foundation:
We used CSI SAFE (using finite elements) to analysis and design the MAT footing that consider the footing flexible.
We separated the footing for each block. Below footing A design:

## Slide 100
4) Dynamic design
Design of footings:
1) Dimension:
,

## Slide 101
4) Dynamic design
Design of footings:
2) Deflection:

## Slide 102
4) Dynamic design
Design of footings:
3) Soil failure:
Maximum stress on the footing is
200.61 kN/m^2
and there is no tension on the footing.

## Slide 103
4) Dynamic design
Design of footings:
4) Thickness:
based on punching shear
Notes: The punching shear ratio to the capacity
is less than 1 for all columns

## Slide 104
4) Dynamic design
Design of footings:
5) Design:
Design of one strip

## Slide 105
4) Dynamic design
Design of footings:
5) Design:
Column strip
a) Shear:

## Slide 106
4) Dynamic design
Design of footings:
5) Design:
Column strip
b) Flexure:
Moment diagram:
Area of steel (per column strip):

## Slide 107
4) Dynamic design
Design of footings:
5) Design:
Middle strip
Moment diagram:
Total maximum moment
= 1500 kN.m /4.1 strip
For practical use, A mesh reinforcement of 8∅18/m is used (both top and bottom)

## Slide 108
Thanks for your attention.
Any Questions?