## Slide 1: Graduation project 2 Comprehensive study for recycling factory for used Car Tires in West Bank
Group members : Khaled Arafat
Muslem Dawood
Shrooq Khaleeliya
Ali Issam
Supervisor name :Dr. Muwia Tahseen Ramadan

## Slide 2: Introduction
Our project talks about building a factory to recycle used car tires (UCT) and benefit from them in healthy ways and avoid environmental pollution resulting from burning them and other methods that have a negative impact on the environment.

## Slide 3: Available methods for collecting used tires (raw materials)
In this section, we will talk about methods that we can rely on to collect used tires (raw materials) to start recycling them to obtain useful products through the application of supply chain principles that aim to reduce waste wherever possible.
First method:
The used tires are collected in agreement with the owners of the maintenance centers, provided that the tires are taken periodically, and when this proposal was submitted to them, it won a great agreement from them to rid them of the tires that cause them problems in terms of taking an area that can be exploited and distorting the exterior of the maintenance center. And that the assembly process is carried out using a transport cart belonging to the factory, so that the used tires are transported directly from the maintenance centers to the factory from various regions.
The number of used tires (raw materials) expected to be obtained daily 450-500 tire.
Second method:
Represented by the opening of maintenance centers to replace used tires with new ones, so that these centers are affiliated with the factory in particular, and new tires can be sold at cost prices to encourage customers to replace old tires in these centers, and to ensure that the largest possible quantity of used tires is obtained through these centers.
In the beginning, we will be establishing one maintenance center beside the factory.
The number of used tires (raw materials) expected to be obtained daily 10-15 tire per center.

## Slide 4: Third method
Tires are collected by contracting with municipal councils and waste dumps that cover the areas of the West Bank so that they collect tires and supply them to the factory, provided that the transportation costs are paid.
The number of used tires expected to be obtained daily 500-550 tire.
Methodology used to collect tires
After determining the production line, the number of tires required to operate it reached 960 tires per day, and accordingly, the best tire assembly methods were determined. For starters, we will use the first, second and third method, to supply us with 950-1000 tires per day, thus we have obtained the required quantity of tires that meet the needs of the production line and the marketing plan (Demand), as the price of one tire is 3.6 shekels.

## Slide 5: Future plan
The second option for the third method is for the municipal councils to collect tires from all areas of the West Bank and bring them to the factory in exchange for the service provided by the factory from disposing of tires that are difficult to deal with in landfills. After submitting the proposal to the competent authorities in the Ministry of Local Government, we appreciate it highly and can be applied by obtaining support from the competent authorities.
The second method will be adopted as a future plan to collect tires due to its high cost, as the cost of opening a maintenance center , and this constitutes a burden at the beginning of work. But the number of tires at the beginning will be in large quantities, but these quantities will decrease with time and we will need to open these centers to provide the necessary quantity to operate the production line.

## Slide 6: Machines

## Slide 7: Tire Cleaner machine
The first process in the rubber tile manufacturing process
Make the tire clean, and reduce the dust discharge when shred tires.
Advantage: Saving water

## Slide 8: Tire debeader
Disadvantages : Very slow

## Slide 9: Advance tire debeader

## Slide 10: Tire shredder machine
Advantages
Full automat
Disadvantages
high electricity cost because it has two motors, And It works all the time without stopping
Sometimes it requires human intervention to adjust the tire position for chopping

## Slide 11: Advance Tire shredder machine Installing a water system to facilitate the fall of the tire inside the machine

## Slide 12: Rasper machine
Figure 16: output rubber 10-30 mm

## Slide 13: Granulator machine
Figure 19 output of Granulator machine 1-6mm

## Slide 14: Miller
: 10-30 mesh fine rubber

## Slide 15: Big Shaking Screen

## Slide 16: Big magnetic

## Slide 17: Fiber separator
Figure 29: useless fiber 1

## Slide 18: Dryer mixer Machine

## Slide 19: Rubber Tile Press Machine

## Slide 20: Facility layout
The facility layout aim to maximizing the effectiveness of the production process and meeting the needs of customers
The basic layout principle is the flow of work, material, and information through a system
We design and studied the internal and external layout of the facility

## Slide 21: Rough layout
The shape of the layout of the production process is u-shape

## Slide 22: 3D Layout
For studying the detail the distribution of the machine and the movement of workers for every region we make 3D-modeling for the whole industry.
We also calculated the area of each region
The total area for the industry is approximate 908.5579 m2

## Slide 23: 3D Modeling

## Slide 24: Tire store
The truck is putting up tires in the area
The worker arrange the tires and pickup the tires and move it the the next stage
The area = 151m2

## Slide 25: Preparation tire zone
At this stage, the tire is prepared by cleaning with a cleaning machine and removing the wires using a machine
The area is approximate 96.9054 m2

## Slide 26: Powder production line
The area is approximate 213.7325 m2

## Slide 27: Rubber tile production
At this stage, the pure powder is mixed with pigments and glues, and then it is pressed and transformed into a rubber tile
The area is 71.25 m2

## Slide 28: Rubber tile warehouse
The area is 143 m2

## Slide 29: Warehouse layout
Layout of the warehouse is that the warehouse handles orders quickly, efficiently and accurately by taking into consideration, increasing productivity, utilizing space
The principles of warehouse relate to similarity and space utilization

## Slide 30: Offices and tire change station
The area of the offices is 176.67 m2
The area of tire change station 69m2

## Slide 31
Safety at workplace
Safety tools
Human–machine interaction and work design
Occupational Safety

## Slide 32
Safety at work place
Heat, cold and the design of the physical environment
Lighting
Periodic illumination level measurements by light-level meter

## Slide 33
Ventilation system
 | Type | Air In cubic feet per minute
1 | workplace | 60
2 | Offices and management rooms | 20
Periodic velocity of air flow measurements and air pressure by CFM meter device.
Noise and Vibration
noise level shouldn’t exceed 80 Db.
In laboratory, noise level should be between 55-60 dB
In testing, all windows must be closed, measurement is done at a distance of at least 1 meter from walls, 1.2 meter from ground.
Regular maintenance and replacement of worn parts can prevent vibration

## Slide 34
Safety tools
Helmet and Work shoes
Ear protection
Worker's dress
It is not safe to use loose clothes. Especially the wire drawing machine
  Wearing of polyester and cotton is proper
Gloves (Super fabric gloves, consists of nylon or polyester)
Dust mask(miller machine)
Safety Glasses (mixer machine, press machine)

## Slide 35
Human–machine interaction and work design
Tire debeader
Tire shredder machine(The risk should be about 2.7 m from the ground as it is high-risk).
Dryer mixer Machine
Rubber Tile Press Machine

## Slide 36: Economic feasibility study
Market study
Demand: 118,492 tiles/ year
Competitors:
Hebron Factory for Tires Recycling
Tyrec Company for Tires Recycling
Liaoning Birla Carbon Company
Game time company for tire recycling
Target segment: School, Industry and warehouses, Houses, Cows and sheep farms, Kindergartens, Sports clubs
Chart: Market share
| Hebron Factory | Tyrec Company | Game time company | Liaoning Birla Carbon Company
 | 0 | 40 | 35 | 25

## Slide 37: Initial investment
ID | Item | Cost | Annual Depreciation
1 | Building table | 1,087,534 | 9584
2 | Machines | 58,1440 | 35,246
3 | Tire repair station | 9,494 | 774
4 | Tools | 400 | 66.66
5 | Quality Equipment | 4,300 | 230
6 | Safety Equipment | 19,150 | 1,115
7 | Furniture | 39,900 | 2,590
8 | Handling system | 60,175 | 40,17.5
9 | Vehicles | 100,000 | 7,000
10 | Other equipment | 35,450 | 2,045
 | Total | 1,937,843 | 62,668

## Slide 38: Summary of fixed Running cost
ID | Type | monthly cost | Annual cost
1 | Wages | 33,500 | 435,500
2 | Other Electricity | 1000 | 12,000
3 | Other utilities | 1,450 | 17,400
6 | maintenance | 3,500 | 42,000
7 | Rent | 50,000 | 600,000
 | Total | 55950 | 1,757,018

## Slide 39: Summary of Variable Running cost
ID | Cost type | the cost | Cost/ item | monthly cost | Annual cost
2 | Variable cost | Raw materials | 7.6 | 39499 | 900538.2
 |  | Water cost | 0.069 | 1,500 | 18,000
 |  | Packaging and labeling | 0.1 | 41887 | 929202.48
 |  | Machines Electricity | 5.16 | 51,043 | 612,518
 |  | Fuel | 0.99 | 9,800 | 117307
 |  | Advertising | 0.253 | 2500 | 29997
 |  | Total | 12.172 | 146229 | 2607563

## Slide 40: Cost analysis
Total Cost = Fixed cost + Variable cost (Q)
    1,757,018+12.929 (118,492) = 3,289001 Nis/ year
The cost per piece (one Rubber tile) = Total cost / Total demand
    3289001/118492 = 27.75 Nis/ tiles
selling price= cost per unit * profit margin
    27.5* 200% = 55 Nis/tile

## Slide 41: Income
ID | Item | Description | # of Unit | Price | Revenue / month | Revenue / Year
1 | Rubber tiles | - | 9875 tiles | 55 Nis/ tile | 543,125 | 6,517500
2 | Wire Iron | 9875 tiles need 21725 tires, 12% of this tires is wire iron | 2607 kg from wire Iron / month | 912.5 Nis / one ton | 2.85 *912.5 =2600.62 | 31207.44
 |  |  |  | Total | 545,725 NIS | 6,548707 NIS

## Slide 42
  Cost-benefit analysis
Net profit= Total Revenue – Total cost
    6,548707 - 2,677582.348= 3,871124 Nis / year
Rate of return = yearly net profit / Total Investment
    3,871124 / 1,937,843 * 100 = 1.99= 199 %
Payback period (PBP) = Total investment / yearly net profit
    1,937,843/3,871124= 0.5 = 6 month
Break-even point = Total Fixed cost / Price – VC\unit
    1,757,018/ 55-27.75 = 64,478 unit.
ID | Item | monthly | Yearly
1 | Demand | 9875 tiles | 118492 tiles
2 | Initial investment | 1,937,843 Nis | 
3 | fixed Running cost | 151,793 Nis | 1,757,018 Nis
4 | Variable Running cost / unit | 12.929 Nis | 
5 | Income | 545,725 NIS | 6,548707 NIS

## Slide 43: Thank you for your attention