## Slide 1: Operations Improvement For Al- Shakhshir Furniture Factory
Graduation Project 2
By:
Ruba Barmawi
Masa Qadi
Fadi Al-Asaad
Supervisor:
Eng.Suleiman Daifi

## Slide 2: Outline
1
2
4
5
6
Literature
Review
Problem
Statement
Objectives
Methodology
Results
Conclusion & Recommendation
Introduction
3
7

## Slide 3: 01 Introduction
It is structured into three sections: The Smithing section, Upholstery section
and Carpentry section
Two showrooms operated by The Factory :
1- the first one can be found in Nablus.
2- the second one in Al-Bireh – Ramallah.
Al - Shakhshir Furniture Factory Established in 1959 in the city of Nablus.
It’s specializing in the production of office, school, and restaurant furniture.

## Slide 4: 02 Problem Statement
Lack of Documented SOPs
Lack of Production Planning
Lack of Effective Layout
Lack of Inventory Management

## Slide 5: 03 Objectives
02
01
Production Planning Development
New Factory Layout Development
Inventory Management
SOPs Development
03
04

## Slide 6: 04 Literature Review

## Slide 7: Theoretical Background
Documentation
Flowcharts
Forms
SOPs
Production Planning
Facility Layout
Job Description
Inventory Management
Organizational Structure
Flowcharts

## Slide 8: 05 Methodology

## Slide 9
06 Results

## Slide 10: Production Planning

## Slide 11
Pareto Analysis

## Slide 12
Products Selection
Production percentage out of the factory’s total production | Figure | Product
5% |  | Feno chair
6% |  | Guitar chair
3% |  | Student chair
4% |  | Rectangular Table
6% |  | Wooden office desk

## Slide 13
Flow Chart of Feno Chair Production Proces

## Slide 14: Bill Of Material

## Slide 15: Bill Of Material For Feno Chair
Bill of material |  |  | 
Product description :Feno Chair Stock number : (01) |  |  | 
Component |  | Quantity (Amount) required | Source
Stock No. | Description |  | 
32 | Circular Metal rod - (d = 32 mm) | 4 | Purchasing
13 | Circular Metal rod - (d = 13 mm ) | 6 | Purchasing
40 | Wood - (Sandwich) | 1 | Purchasing
3 | Sponge - (t = 3cm) | 1 | Purchasing
1 | Sponge - (t = 1cm) | 1 | Purchasing
50 | Leather | 1 | Purchasing
8 | Screw | 4 | Purchasing
34 | Plastic Base | 4 | Purchasing

## Slide 16: Routing Sheet

## Slide 17: Routing Sheet For Feno Chair
Routing Sheet |  |  |  |  |  |  | 
Product: Feno Chair Part No.: 01 |  |  |  |  |  |  | 
Operation |  | Machine | Aux.Equip. | Setup Time (hr.) | Hr./Pc | Hr./component | Pc/Hr.
No. | Description |  |  |  |  |  | 
1 | Cutting process of metal rod | Cutting machine | Gloves |  | 0.0014 | 0.014 | 360
2 | Bending process | Rod bending machine | Gloves |  | 0.00194 | 0.0194 | 257
3 | Drilling process | Drill press | Gloves |  | 0.00056 | 0.00224 | 900
4 | Polishing process | Polishing machine | Gloves |  | 0.0014 | 0.014 | 360
5 | Welding process | CO2 welding machine | Welding mask, gloves and chair mold. |  | 0.0334 | 0.0334 | 30
6 | Painting process | Painting oven | Spray painting, Gloves | 0.167 (10min) | 0.0167 | 0.0167 | 30
7 | Wood cutting machine | Table Saw machine | - |  | 0.0167 | 0.0167 | 30
8 | Contouring process | Vertical Saw machine | - |  | 0.033 | 0.033 | 15
10 | Upholstery process | - | Electrical Staple gun |  | 0.167 | 0.167 | 3
11 | Assembly process | - | screws |  | 0.0167 | 0.0167 | 30
12 | Packaging and loading | - | - |  | 0.0167 | 0.0167 | 30
Total |  |  |  | 0.167 (10min) |  | 0.35 (21 min) | 

## Slide 18: Demand Forecasting

## Slide 19: Demand Forecasting
A
Checking the accurecy of the forecasting results
Check
D
D
Demand Forecasting using the suitable model
Forecasitng
C
C
Graphical Representation of the data
B
B
The demand data in previous 2 or 3 years
Data
A
Graphical Represintation

## Slide 20: Feno Chair Demand Forecasting

## Slide 21: Feno Chair Demand Forecasting
Simple Exponential Smoothing Model

## Slide 22: MPS For Feno Chair
 |  | Period |  |  |  |  |  |  |  |  |  | 
Product: Feno Chair | On hand | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Forecast |  | 60 | 28 | 102 | 92 | 194 | 319 | 184 | 125 | 249 | 106 | 37
Projected available balance | 60 | 50 | 52 | 50 | 58 | 54 | 52 | 58 | 53 | 54 | 58 | 51
Master production schedule (MPS) |  | 50 | 30 | 100 | 100 | 190 | 320 | 190 | 120 | 250 | 110 | 30
Lot size = 10 |  |  |  |  |  |  |  |  |  |  |  | 
Safety stock = 50 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 23: Consolidated MPS
 | Period |  |  |  |  |  |  |  |  |  |  | 
Product | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | Total
Feno chair | 50 | 30 | 100 | 100 | 190 | 320 | 190 | 120 | 250 | 110 | 30 | 1490
Guitar Chair | 60 | 20 | 100 | 110 | 520 | 420 | 40 | 10 | 20 | 20 | 10 | 30
Rectangular Table | 100 | 50 | 45 | 100 | 50 | 55 | 50 | 215 | 125 | 65 | 25 | 880
Student chair | 27 | 15 | 6 | 37 | 24 | 65 | 305 | 591 | 225 | 11 | 12 | 62
Wooden Office desk | 30 | 38 | 24 | 45 | 25 | 37 | 31 | 62 | 52 | 34 | 23 | 401

## Slide 24: Monthly Production Planning (MPP)
MPP FOR JUN |  |  |  |  | 
Product | Week 1 | Week 2 | Week 3 | Week 4 | Total
Feno chair | 150 | 120 | - | 50 | 320
Guitar chair | 200 | 140 | - | 80 | 420
Rectangular Table | 25 | 15 | - | 15 | 55
Student chair | 20 | 15 | - | 30 | 65
Wooden Office desk | 15 | 15 | - | 7 | 37
Total | 410 | 305 | - | 182 | -

## Slide 25: Inventory Management
Safety Stock Determination
Re-order Point Calculation
Holding Cost Calculation

## Slide 26: Safety Stock Calculation
Product name | Lead time (Hr) |  | SS
Feno chair | 0.68 | 92 | 124
Guitar chair | 0.65 | 179 | 236
Rectangular table | 0.45 | 57 | 62
Wooden office desk | 2.08 | 13 | 30
Student chair | 0.52 | 183 | 216
Product name | Lead time (Hr) |  | SS
Feno chair | 0.68 | 92 | 124
Guitar chair | 0.65 | 179 | 236
Rectangular table | 0.45 | 57 | 62
Wooden office desk | 2.08 | 13 | 30
Student chair | 0.52 | 183 | 216

## Slide 27: Reorder Point Calculation
Product name | Demand(avg) | Lead time | Safety stock | ROP
Feno chair | 125 | 0.68 | 124 | 209
Guitar chair | 113 | 0.65 | 236 | 309
Rectangular table | 74 | 0.45 | 62 | 95
Wooden office desk | 34 | 2.08 | 30 | 100
Student chair | 115 | 0.52 | 216 | 275

## Slide 28: Total amount of raw materials required for the five products
Raw material name | Feno chair | Guitar chair | Rectangular table | Wooden office desk | Student chair
Circular metal rod – d= 32 mm | 4 |  | 4 |  | 2
Circular metal rod – d= 13 mm | 6 |  |  |  | 2
Wooden Boards – sandwich | 1 | 2 | 1 | 22 | 1
Sponge - t =3 cm | 1 |  |  |  | 
Sponge - t =1 cm | 1 | 2 |  |  | 
Leather | 1 | 2 |  |  | 
Screw | 4 | 8 | 8 | 52 | 12
Plastic base | 4 | 4 | 4 | 4 | 4
Rectangular metal rod – 25 mm |  | 5 | 4 |  | 4
Sponge – t = 7 cm |  | 2 |  |  | 
Corner metal brackets |  | 4 | 4 |  | 
Corner braces |  |  |  | 12 | 
Metal drawer slide |  |  |  | 6 | 
Metal drawer handle |  |  |  | 3 | 
Drawer key |  |  |  | 1 | 
Plastic backrest and seat |  |  |  |  | 2

## Slide 29: Raw Material Safety Stock levels
Raw material name | Feno chair | Guitar chair | Rectangular table | Wooden office desk | Student chair | Total SS
Circular metal rod – d= 32 mm | 4(124) |  | 4(62) |  | 2(216) | 1052
Circular metal rod – d= 13 mm | 6(124) |  |  |  | 2(216) | 1176
Wooden Boards – sandwich | 1(124) | 2(236) | 1(62) | 22(30) | 1(216) | 1534
Sponge - t =3 cm | 1(124) |  |  |  |  | 124
Sponge - t =1 cm | 1(124) | 2(236) |  |  |  | 596
Leather | 1(124) | 2(236) |  |  |  | 596
Screw | 4(124) | 8(236) | 8(62) | 52(30) | 12(216) | 7032
Plastic base | 4(124) | 4(236) | 4(62) | 4(30) | 4(216) | 2672
Rectangular metal rod – 25 mm |  | 5(236) | 4(62) |  | 4(216) | 2292
Sponge – t = 7 cm |  | 2(236) |  |  |  | 472
Corner metal brackets |  | 4(236) | 4(62) |  |  | 1192
Corner braces |  |  |  | 12(30) |  | 360
Metal drawer slide |  |  |  | 6(30) |  | 180
Metal drawer handle |  |  |  | 3(30) |  | 90
Drawer key |  |  |  | 1(30) |  | 30
Plastic backrest and seat |  |  |  |  | 2(216) | 432

## Slide 30: Raw Materials ROP
Raw material name | Feno chair | Guitar chair | Rectangular table | Wooden office desk | Student chair | ROP
Circular metal rod – d= 32 mm | 4(209) |  | 4(95) |  | 2(275) | 1766
Circular metal rod – d= 13 mm | 6(209) |  |  |  | 2(275) | 1804
Wooden Boards – sandwich | 1(209) | 2(309) | 1(95) | 22(100) | 1(275) | 3397
Sponge - t =3 cm | 1(209) |  |  |  |  | 209
Sponge - t =1 cm | 1(209) | 2(309) |  |  |  | 827
Leather | 1(209) | 2(309) |  |  |  | 827
Screw | 4(209) | 8(309) | 8(95) | 52(100) | 12(275) | 11768
Plastic base | 4(209) | 4(309) | 4(95) | 4(100) | 4(275) | 3952
Rectangular metal rod – 25 mm |  | 5(309) | 4(95) |  | 4(275) | 3025
Sponge – t = 7 cm |  | 2(309) |  |  |  | 618
Corner metal brackets |  | 4(309) | 4(95) |  |  | 1616
Corner braces |  |  |  | 12(100) |  | 1200
Metal drawer slide |  |  |  | 6(100) |  | 600
Metal drawer handle |  |  |  | 3(100) |  | 300
Drawer key |  |  |  | 1(100) |  | 100
Plastic backrest and seat |  |  |  |  | 2(275) | 550

## Slide 31: Holding cost
Product name | Initial HC (NIS/item) | Labor HC (NIS/item) | Total HC (NIS/item)
Feno chair | 0.175 | 0.87 | 1.04
Guitar chair | 0.175 | 0.87 | 1.04
Rectangular table | 2.6 | 13 | 15.6
Wooden office desk | 1.9 | 9.4 | 11.3
Student chair | 0.97 | 4.8 | 5.77

## Slide 32: SOPs Manual Development Steps
Job and Organizational Descriptions Development
01
02
03
SOPs Flow Charts Development
04
Organizational Structures Development
05
Forms and Reports Development
SOPs Manual Development

## Slide 33: Organizational Structures
Administrative Organizational Structure
Functional Organizational Structure

## Slide 34: Current Administrative Organizational Structure

## Slide 35: New Administrative Organizational Structure

## Slide 36: Functional Organizational Structure

## Slide 37: Organizational Descriptions
            Finance and Administration Affairs Department
            Warehouses Department
Sales, Marketing and Customer Relations Department
            Quality Control and Occupational Health and Safety Department
Production Department
Maintenance Department

## Slide 38
Organizational Description for Production Department

## Slide 39: Job Descriptions

## Slide 40: Job Description for Production Manager

## Slide 41
SOPs Flow Charts Development

## Slide 42: SOPs That Have been Developed:

## Slide 43: After-Sale Maintenance Standard Operating Procedure

## Slide 44: Final Products Delivery to Warehouses Report

## Slide 45: After-Sale Maintenance Form

## Slide 46: Standard Operating Procedures (SOPs) Manual

## Slide 47: Factory Layout Optimization

## Slide 48: Factory Floors
Upholstery Department
Factory-Produced and Imported Products Inventory
Carpentry Department
Showroom Department
Smithing and Assembly Department
Imported Desks Inventory
Third Floor
Second Floor
Ground Floor

## Slide 49: Layout Design of The First Floor
1
2
1
Showroom Department
2
Assembly and Loading Department

## Slide 50: Layout Design of The First Floor
1
2
3
1
Smithing Department
2
Assembly Department
3
Imported Desks
Inventory

## Slide 51
Layout Design of The Second Floor
1
Upholstery Department
2
3
Spare Parts Inventory
1
2
3
4
5
4
5
Factory-Produced Products Inventory
Imported Products Inventory
Assembly Area

## Slide 52
Layout Design of The Third Floor Carpentry Department
1
2
Production and Assembly Area
Empty (unused) Area
1
2

## Slide 53: Factory Layout Type
cellular (or group family) layout

## Slide 54: Spaghetti Diagram
Smithing Department

## Slide 55: Vertical Flow Pattern
Ground Floor
Second Floor
Third Floor

## Slide 56: Systematic Layout Planning Procedure

## Slide 57: 1. Input Data and Activities Operation Process Chart

## Slide 58: 2. Flow of Material Process Flow Chart

## Slide 60: From-To Chart
Product | Component | Production Quantities (per day) | Movement Factor | Equivalent Flows (per day) | Routing
Guitar chair | 1 | 10 | 1 | 10 | A-B-C-D-E
Feno Chair | 2 | 15 | 1 | 15 | A-B-C-D-E
Rectangular Table | 3 | 6 | 2 | 12 | A-B-D-F
Department | Department symbol
Smithing Department | A
Carpentry Department | B
Upholstery Department | C
Assembly Department | D
Chairs Inventory Department | E
Imported desks and tables inventory | F

## Slide 61: From-To Matrix
To From | A | B | C | D | E | F
A |  | 1 - 10 2 - 15 3 - 12 |  |  |  | 1 - 10 2 - 15
B |  |  | 1 - 10 2 - 15 | 3-12 |  | 
C |  |  |  | 1 - 10 2 - 15 |  | 
D |  |  |  |  | 1 - 10 2 - 15 | 3-12
E |  |  |  |  |  | 
F |  |  |  |  |  | 

## Slide 62: 3. Activity Relationships Relationship Chart

## Slide 63: 4. Relationship Diagram

## Slide 64: 5. New Factory Layout Ground Floor - Smithing Department
Detailed Layout
Spaghetti Diagram

## Slide 65: New Factory Layout Second Floor - Inventory Department
Block Layout
Detailed Layout

## Slide 66: New Factory Layout Third Floor - Carpentry and Upholstery Department
Detailed Layout
Block Layout

## Slide 67: 07 Conclusion
Production Planning
System
Optimaized Factory Layout
SOPs
Manual
Inventory
Management
System

## Slide 68: 07 Recommendations
Develop both preventive and corrective maintenance systems
1
Implement the newly developed layout
Improve the organization of warehouse spaces
2
3
Adopt the designed work procedures and the enhanced organizational structure
4
Implement the inventory management calculations developed in the project
5
Apply the production planning system developed in the project
6

## Slide 69
THANKS!
Masa Qadi
Fadi Al-Asaad
Ruba Barmawi